## Slide 1: Plans for FTM test beam in 2022
Antonello Pellecchia
Piet Verwilligen
Dipartimento di Fisica, Università degli studi di Bari
INFN, sezione di Bari
RD51 Mini-week – Feb 10, 2022

## Slide 2: Reminder on FTM layout and goals
Advertisement drawing
Single foil, single pad readout
500 V
0 V
-1000 V
2-layer FTM layout
FTM goal:
Achieve O(100 ps) time resolution fully resistive multi-layer MPGD
Present R&D on:
DLC foil stability to high fields
High enough effective gain (>104)
Good efficiency and R/O capacitance improvements
Multi-layer readout coupling
Dedicated readout electronics
Test beam goals:
Prove good efficiency with muon and pions
Demonstrate time resolution dependency on number of layers on a small surface
Pictures of small FTM prototype to be tested
done!
ongoing

## Slide 3: FTM Status – gain and efficiency
Results on single-layer prototype from results in various gas mixtures
Gain: good 👍 (over 104 in Ne/iC4H10)
Currents measured with picoammeter
Source: laser
We should be able to see MIPs
Maximum achievable gain always lower than μ-RWELL
Efficiency: bad 😕 (5000e- primary charge)
Primary charge measured by picoammeter
Source: laser
Readout: ORTEC 142PC (4 mv/fC)
Cannot see MIPs despite good charge amplification
Evidence of readout coupling issues
OUTDATED
(thank god!)

## Slide 4: Efficiency, Foil deformation and r/o capacitance
We realized the low efficiency is related to readout electrode deformation
→ visible deformation (100 μm)
→ low attachment of R/O to bottom electrode
→ reduced R/O capacitance, signal invisible
Solution: ensuring attachment of R/O to amp bottom by electrostatic force
Ongoing tests to verify efficiency with new HV distribution
Plan in test beam: verifying minimum attachment voltage for good efficiency
Alternative solution: FTM with read-out plane glued with bottom electrode

## Slide 5: FTM test beam setup
FTM
MCP-PMT
MaPMT
MaPMT
FTM
MaPMT
MCP-PMT
Dark box*
* Also useful for hiding from your boss
DAQ PC
HV
Scope
20 GS/s 4 GHz
TRG
Desiderata
Ne:iC4H10 95:5
Vertically moving table if available
Acquisition and analysis
Reference: 2xMaPMT (trigger) + MCP-PMT (timing)
All waveforms saved and analyzed offline
  Local waveform saving on scope: several kHz Real-time transfer to DAQ PC (ethernet): < 200 Hz (??)
  Other options? (USB, GPIB, transfer on separate thread…)

## Slide 6: FTM readout
Cividec C2-HV
Linear amplifier
Fast shaping
Low S/N ratio
Cividec C2-HV
Ortec 142 PC
Ortec 142 PC
Charge amplifier
Long integration time (> 100 ns)
High S/N ratio
Ortec 142 PC
Ortec 142 PC
Scheme 1
Scheme 2
For timing and efficiency
For signal transparency measurement
Top
Bottom
Signal transparency already observed with laser, to be confirmed with MIPs

## Slide 7: On the reference detectors
Single e- charge 1.65 pC
Gain 1.03 × 107
Trigger
H8500 MaPMT (x2)
81 ps time resolution measured with cosmics (2xPMTs in coincidence)
Timing
XP85012 MCP-PMT
106-108 gain measured with UV laser
Could not measure good time performance from MaPMTs (expected 37 ps for single e-)

## Slide 8: Alternative plans
If this does not work…
Getting drunk in the lab

## Slide 9: Backup
????

## Slide 10: Solution for low readout capacitance
If the ground and readout electrodes are put at a high voltage difference, they will stick together preventing the decrease in the readout capacitance → Electrode voltages to be slightly revised

## Slide 11: Outcome of the tests
Test performed on Marcello’s prototype at CERN:
Adhesion test by observing arrachment in clean room en plein air 500 V applied with Megger between ground (kapton XC) and readout (copper)
Signals with x-ray and increasing HV between ground and R/O
Outcome:
No adhesion up to 1 kV However, if we apply less than 500 V between amplification top and ground, we see the amplification foil attaching to the ground. So maybe the R/o foil is too stiff?
No signals with x-ray up to 500 V between ground and R/O However, without laser it is difficult to quantify the point of efficiency (not possible to change primary charge at wish)

## Slide 12: Considerations and plans
Induction tests to be performed on small size prototype (smaller foils, more flexible)
Options for longer term:
Having ground and electrode foils glued
Could the charge collection be improved by having amplification and bottom produced already glued?
Possibility to have all three electrodes already glued? (à la μ-RWELL I think)

## Slide 13: About the u-RWELL mode

## Slide 14: FTM scheme