## Slide 1: FalconD – FEM Analysis Preliminary results
Przemysław Wąchal
TE-MSC-SMT/HNINP
11.01.2022
High Field Magnet Program

## Slide 2: Outline
Introduction
  Basic magnet cross-section – general view
  Changes in the geometry of the magnet structure – proposed configuration
  FEM Analysis
    Assumptions
    Material properties, Loads & BC
    Optimized cases
    Optimized case – Kawasaki SS Pad
    Optimized case - Shims

## Slide 3: Basic magnet cross-section – general view
Basic geometry of the magnet – 2D cross-section
Technical Design Report
INFN/Code-19/001

## Slide 4: Proposed geometry of the magnet structure – general view
Proposed geometry of the magnet– 2D cross-section

## Slide 5: FEM Analysis - assumptions
Description of the design variables
Optimization of the structure – 1st stage
Design variables:
  X coordinate of the horizontal key; 0-60mm
  Y coordinate of the vertical key; 0-60mm
  Length of the horizontal key; 20-30mm
  Length of the vertical key; 20-30mm
  Horizontal key interference; 0.001-0.5mm
  Vertical key interference; 0.001-0.5mm
  Horizontal gap between SS Pad halves;
  0-0.7mm
  Constants:
    Horizontal gap between yoke halves
    Width of the SS Pad
    Height of the SS Pad

## Slide 6: FEM Analysis - assumptions
Optimization of the structure – 1st stage
State variables:
  Azimuthal stress at 1st load step; 10-70 MPa
  Azimuthal stress at 2nd load step; 70-110 MPa
  Azimuthal stress at 3rd load step;110-150 MPa
  Non zero value (above zero) of the contact pressure between coils and SS Pad at pole region; >0 MPa
  Objective function:
    Von Mises stress at 3rd load step – energization; up to 150 MPa
Max contact pressure between coils and SS Pad
  Azimuthal stress at 3rd load step
Assumed stress limit in the coils at energization load step = 150 MPa

## Slide 7: FEM Analysis - assumptions
Tuning of the final parameters – 2nd stage
  Azimuthal stress at 3rd load step
Design variables:
  X coordinate of the horizontal key
  Y coordinate of the vertical key
  Length of the horizontal key
  Length of the vertical key
  Horizontal key interference
  Vertical key interference
  Horizontal gap between SS Pad halves
  Tuning +/- of the design parameter (if needed)
  Final parameters

## Slide 8: FEM Analysis – Materials, Loads&BC
Material | E [GPa]; RT (1.9K) | ν [-] | α *10^-3
Conductor | 25 (25) | 0.3 | 3.8
SS Pad | 191 (210) | 0.28 | 2.8
Al7075 shell | 72 (79) | 0.3 | 4.2
Ferromagnetic iron | 204 (225) | 0.28 | 2.0
Fiberglass | 25 (27.5) | 0.2 | 2.5
Kawasaki SS | 186 (186) | 0.28 | 1.8
  Linear elastic material properties [1,2]
Three load steps:
Assembly – prestress at RT
Cool-down
Energization – EM forces
  Symmetry in X direction
  Constrained one point in Y direction
  Assembly
  Cool-down
  Energization
  Half of the magnet cross section is modeled
EM Force component | Value [kN/m]
Coils | 
Fx | 3575
Fy | -1781
Yoke | 
Fx | -474
Fy | 235

## Slide 9: FEM Analysis – Materials, Loads&BC
Three load steps:
Assembly – prestress at RT
Cool-down
Energization – EM forces
  Assembly
  Cool-down
  Introduce compression
  Introduce traction – counteract EM forces
  Energization

## Slide 10: FEM Analysis – Materials, Loads&BC
Three load steps:
Assembly – prestress at RT
Cool-down
Energization – EM forces
  Assembly
  Cool-down
  Energization
  Closing the cavity
  Al. Shell shrinks more than other components

## Slide 11: FEM Analysis – Materials, Loads&BC
Three load steps:
Assembly – prestress at RT
Cool-down
Energization – EM forces
  Assembly
  Cool-down
  Energization
  Closed cavity and prestress should keep the coils in right position during energization

## Slide 12: FEM Analysis – Materials, Loads&BC
Contact conditions
  µ=0.2

## Slide 13: FEM Analysis – preliminary results
Optimized case 1
Parameter | Value [mm]
Vertical key interference | 0.17
Horizontal key interference | 0.04
Length of the key - vertical | 26
Length of the key - horizontal | 28
X coordinate of the horizontal key | 51
Y coordinate of the vertical key | 16
Horizontal gap dimension between SS Pad halves | 0.28
Horizontal gap dimension between yoke halves | 2
Width of the SS Pad half | 95
Height of the SS Pad half | 95
Azimuthal stress
[Pa]
[Pa]
[Pa]
Cool-down
Assembly – prestress at RT
Energization – EM forces
Minimum Azimuthal stress during load steps | 
Load step | Value [Mpa]
1 | -68.1
2 | -75.1
3 | -132.0

## Slide 14: FEM Analysis – preliminary results
Optimized case 1
Parameter | Value [mm]
Vertical key interference | 0.17
Horizontal key interference | 0.04
Length of the key - vertical | 26
Length of the key - horizontal | 28
X coordinate of the horizontal key | 51
Y coordinate of the vertical key | 16
Horizontal gap dimension between SS Pad halves | 0.28
Horizontal gap dimension between yoke halves | 2
Width of the SS Pad half | 95
Height of the SS Pad half | 95
Cool-down
[Pa]
[Pa]
[Pa]
Contact pressure between coils and SS Pad
Contact pressure between SS Pad halves
Assembly – prestress at RT
Energization – EM forces
Von Mises stress
[Pa]
Maximum VM stress during load steps | 
Load step | Value [Mpa]
1 | 67.3
2 | 79.5
3 | 132.0

## Slide 15: FEM Analysis – preliminary results
Optimized case 2
Parameter | Value [mm]
Vertical key interference | 0.26
Horizontal key interference | 0.21
Length of the key - vertical | 29
Length of the key - horizontal | 28
X coordinate of the horizontal key | 56
Y coordinate of the vertical key | 7
Horizontal gap dimension between SS Pad halves | 0.42
Horizontal gap dimension between yoke halves | 2
Width of the SS Pad half | 95
Height of the SS Pad half | 95
Azimuthal stress
[Pa]
[Pa]
[Pa]
Cool-down
Assembly – prestress at RT
Energization – EM forces
Minimum Azimuthal stress during load steps | 
Load step | Value [Mpa]
1 | -124
2 | -142
3 | -136
Only azimuthal stress at 3rd load step as a State Variable

## Slide 16: FEM Analysis – preliminary results
Optimized case 2
Parameter | Value [mm]
Vertical key interference | 0.26
Horizontal key interference | 0.21
Length of the key - vertical | 29
Length of the key - horizontal | 28
X coordinate of the horizontal key | 56
Y coordinate of the vertical key | 7
Horizontal gap dimension between SS Pad halves | 0.42
Horizontal gap dimension between yoke halves | 2
Width of the SS Pad half | 95
Height of the SS Pad half | 95
Cool-down
[Pa]
[Pa]
[Pa]
Contact pressure between coils and SS Pad
Contact pressure between SS Pad halves
Assembly – prestress at RT
Energization – EM forces
Von Mises stress
[Pa]
Maximum VM stress during load steps | 
Load step | Value [Mpa]
1 | 122
2 | 144
3 | 136

## Slide 17: FEM Analysis – preliminary results
Optimized case – Kawasaki SS Pad
Parameter | Value [mm]
Vertical key interference | 0.20
Horizontal key interference | 0.29
Length of the key - vertical | 29
Length of the key - horizontal | 28
X coordinate of the horizontal key | 56
Y coordinate of the vertical key | 7
Horizontal gap dimension between SS Pad halves | 0.44
Horizontal gap dimension between yoke halves | 2
Width of the SS Pad half | 95
Height of the SS Pad half | 95
Azimuthal stress
[Pa]
[Pa]
[Pa]
Cool-down
Assembly – prestress at RT
Energization – EM forces
Minimum Azimuthal stress during load steps | 
Load step | Value [Mpa]
1 | -111
2 | -103
3 | -129

## Slide 18: FEM Analysis – preliminary results
Parameter | Value [mm]
Vertical key interference | 0.20
Horizontal key interference | 0.29
Length of the key - vertical | 29
Length of the key - horizontal | 28
X coordinate of the horizontal key | 56
Y coordinate of the vertical key | 7
Horizontal gap dimension between SS Pad halves | 0.44
Horizontal gap dimension between yoke halves | 2
Width of the SS Pad half | 95
Height of the SS Pad half | 95
Cool-down
[Pa]
[Pa]
[Pa]
Contact pressure between coils and SS Pad
Contact pressure between SS Pad halves
Assembly – prestress at RT
Energization – EM forces
Von Mises stress
[Pa]
Maximum VM stress during load steps | 
Load step | Value [Mpa]
1 | 109
2 | 104
3 | 153
Optimized case – Kawasaki SS Pad

## Slide 19: FEM Analysis – preliminary results
Optimized case – shims
Parameter | Value [mm]
Vertical key interference | 0.21
Horizontal key interference | 0.08
Length of the key - vertical | 25
Length of the key - horizontal | 27
X coordinate of the horizontal key | 50
Y coordinate of the vertical key | 7
Horizontal gap dimension between SS Pad halves | 0.28
Horizontal gap dimension between yoke halves | 2
Width of the SS Pad half | 95
Height of the SS Pad half | 95
Shim thickness 1st layer | 3
Shim thickness 2nd layer | 3
Azimuthal stress
[Pa]
[Pa]
[Pa]
Cool-down
Assembly – prestress at RT
Energization – EM forces
Minimum Azimuthal stress during load steps | 
Load step | Value [Mpa]
1 | -106
2 | -111
3 | -128

## Slide 20: FEM Analysis – preliminary results
Parameter | Value [mm]
Vertical key interference | 0.21
Horizontal key interference | 0.08
Length of the key - vertical | 25
Length of the key - horizontal | 27
X coordinate of the horizontal key | 50
Y coordinate of the vertical key | 7
Horizontal gap dimension between SS Pad halves | 0.28
Horizontal gap dimension between yoke halves | 2
Width of the SS Pad half | 95
Height of the SS Pad half | 95
Shim thickness 1st layer | 3
Shim thickness 2nd layer | 3
Cool-down
[Pa]
[Pa]
[Pa]
Contact pressure between coils and SS Pad
Contact pressure between SS Pad halves
Assembly – prestress at RT
Energization – EM forces
Von Mises stress
[Pa]
Maximum VM stress during load steps | 
Load step | Value [Mpa]
1 | 105
2 | 114
3 | 128
Optimized case – shims

## Slide 21: Conclusions
New cross section of the magnet was proposed and checked for the dipole in B&K technology
The proposed geometry gives a good possibilities when it comes to stress managements in the coils
Starting with quite high stresses in assembly step, it is possible, however, to obtain stress values in the energization step that are below the limit (still having a safety margin)
After the preliminary results, it can be concluded that the proposed structure allows for a fairly "flexible" way to adjust the parameters of the magnet
The preliminary results are promising and offer the possibility of a deeper study of the proposed magnet structure

## Slide 22: Future plans&work
Including details in the target structure
Collect nonlinear material data and calculate nonlinear coils
Study the effect of the tollerances
Alternative, low numer of pieces cross section
Study of the ‘12 T coil configuration’, double aperture, taking into account the construction of an instrumented mock-up

## Slide 23: Future plans&work
Thank you for your attention!
Including details in the target structure
Collect nonlinear material data and calculate nonlinear coils
Study the effect of the tollerances
Alternative, low numer of pieces cross section
Study of the ‘12 T coil configuration’, double aperture, taking into account the construction of an instrumented mock-up
References:
[1] TDR, INFN/Code-19/001
[2] C. Lanca, D.Perini, CHARACTERISTICS OF THE AUSTENITIC STEELS USED IN THE LHC MAIN DIPOLES,
LHC Project Report 537,