## Slide 1: Crab cavity impedances & RFD HOM Measurements
On behalf of SY-RF-AC and HL-LHC WP4

## Slide 2: Impedance spectra
EDMS 2488213
DQW RFD

## Slide 3
RFD HOM Measurements
RFD 001
RFD 002

## Slide 4: RFD HOM couplers
V-HOMC
Damps HOMs with high Z⊥v and Z∥
100 Wp range
H-HOMC
Damps HOMs with high Z⊥h and Z∥
kWp range
Field Antenna (FA)
Couples 1 W of the 400 MHz signal.
H-HOMC
V-HOMC
FA
… with huge thanks to our colleagues in EN-MME!

## Slide 5: Transmission measurements
S21 measurements taken between the ancillaries. Agrees very well with simulations!
No measurements with Field Antenna for RFD #2 [1].
EDMS 260982 / 2488318

## Slide 6: HOM measurements
EDMS 260982 / 2488318

## Slide 7: Acceptance criteria (concerning WP2)
Crab Cavity HOMs: Details and Qualifications
Measure modes over 10 A line – transmit information to WP2
Report high power mode characteristics to WP2 if outside range

## Slide 8: HOM measurements: Mode over Ioct = 10 A
Mode over 10 A threshold: 1322 MHz
RFD1 Qe: −10 % wrt simulated value
RFD2 Qe: +20 % wrt simulated value

## Slide 9: HOM measurements: High power mode
EDMS 2488213
19th bunch spacing harmonic = 761.52 MHz
… ✓ Inside range!

## Slide 10: Conclusions
RFD an DQW impedance spectra
SPS RFD HOM measurements presented to fulfil acceptance criteria.
  f vs Q
  Mode over threshold
  High power mode: within specs!

## Slide 11: Questions from our side
Could you evaluate the HOM power estimation with SPS beam as a function of frequency (second opinion)? – this impacts the RF connectors we will use.

## Slide 12: Back-up slides

## Slide 13: DQW Impedance Spectra Evolution