## Slide 1: DFM : Engineering Detailed Design
F. Di Ciocchis*, Y. Leclercq*, P. Schneider for WP6a
Engineering Design Review of DFM 18.01.2022

## Slide 2: DFM in Cold Powering System
IP
D1
CP
Q3
Q2b
Q2a
Q1
DSHx
DSHm
140.0 m
89.5 m
DFHM
DFHX
D2
DFM
Service Gallery
D2
DSHM
D2-DFM Interlink
QXL
Jumper
DFM :Boiler module
DFM: Splice module
DFM in HL-LHC Layout
  Part of the WP6a Cold Powering chain
    DFM-DSHM-DFHM
  Installed on either side of ATLAS and CMS
  Interface with DSHM of WP6a, with D2 & QXL of WP3
Components denominations
  DSHm (SCLink D2): from DFHM to DFM
  DFM
    Splice module (SM): electrically connects Interlink to SCLink
    Boiler module (BM) : creates the helium gaseous mass flow
  D2-DFM interlink: connects leads from D2 to DFM leads
  DFM Jumper: connects to cryo-lines
Key Functions
  Electrical interface between DSHM & magnets
  Supply cryogenics to the DSHM

## Slide 3: External overview & interfaces distribution
Rail
IFS Panel
LHe level gauges &
Cryo-instrumentation
Vacuum instrumentation
(Feedthrough)
Rupture disc
D2-DFM Interlink
DSHM
Vac. Valves & Gauges
Pumping system
External frame
Cryo-Instrumentation
Box
Spring loaded valves
Tunnel interface
Jumper interface
Vacuum sleeve to access cryo-lines
Tunnel interface
  Cryostat suspended from tunnel’s roof
Services
  Vacuum & cryo-instrumentation equipment accessible from transport area
DFHM interface
    Vacuum & helium jacket flanges fixed to DFM
DFM-D2 interlink interface
  Vacuum & helium sleeves to access NbTi-NbTi splices
  Hydraulic barrier (plug) separating LHe (DFM side) from superfluid helium (D2 side)
Jumper interface
  Flexible cryo-interconnections
  Vacuum sleeve to access cryo-interconnections
Interconnection sleeve
Bellows free to expand in case of cold leak

## Slide 4: Key design specifications & constraints
Design (nominal) GHe mass flow rate  6.5 (3) g/s
Autonomy in case of LHE supply stop  10 min @ nominal
Gas evacuation through SC Link
Maximum static heat load to 4.5 K  25 W
Absence of condensation  Dew point 12°C
Helium vessel design pressure  3.5 bara
PED Category  II
QXL
D2
DFM Boiler Module
DFM Splice Module
DSHM
DFM Jumper
D2-DFM Interlink
Compliance demonstrated via numerical analyses
Compliance demonstrated via numerical analyses

## Slide 5: Principle of fluid flow & LHe buffers
  Principle (same as Demo 2, successfully validated)
  LHe injection in splice module
  LHe flows downward in beside boiler module by gravity
  Heating line vaporizes LHe in boiler module
  GHe flows upward to splice module
  Level gauges control LHe inlet valve
  Cryogenic
  Splices are immersed in LHe bath
  5 liters of LHe in SP for 10 min @ 20 W
  15 liters of Lhe in BM for 10 min @ 3g·s-1
A
Cable module
IFS Panel
Burst Disc
Cryo-Instrumentation Box
DSHM

Fill reservoir
Inlet reservoir
Nominal Level
Thermal Barrier
Structural Support
Heaters Volume
15 liters
10 min @ 3g.s-1
+50 mm
-50 mm
≈387mm
100mm
LHe inlet
Top splices
Fill reservoir
10 min @ 20 W
5 liters
LHe Overflow
PLUG
Vacuum\Thermal Barrier
Structural Support
Boiler Module
A
Superfluid @ 1.9 K
LHe @ 4.5 K GHe
Heater ops. T sensor
Heater WU
Level gauge
In-vessel supports
He Vessel Vacuum Vessel
MgB2 cables MgB2-NbTi Splices
NbTi cables NbTi-NbTi Splices
A-A
Vacuum\Thermal Barrier
Structural Support
Plug
Hydraulic Barrier
DSHM
Thermal Barrier
Structural Support

## Slide 6: Coldmass design overview
  Two helium vessels hydraulically interconnected
  Splice module (cooling splices)
  Inclined design to perform LHe-GHe separation
  Universal expansion joint connection with D2
  He sleeve to access NbTi-NbTi splices
  Hydraulic barrier @ D2
  Boiler module (vaporizing LHe)
    Horizontal helium tank
    Safety & Cryo-Instrumentation outputs
    Cryo-connection lines to jumper
GHe Line
Cryo-Instrumentation Box
LHe Overflow Line
Manifold Box
Helium
Connection Flange
IFS Bended Pipe
IFS Output
Cryo-Instrumentation Output
Level Gauge
Safety Line
Instrumentation Flexible
LHe Supply Line
IFS Box
CERNOX
Cryo-Instrumentation Box
GHe Discharge Line
Level Gauge
Safety Line
TS Heat Exchanger
WU Electrical Heaters
Wires Guide Tube
CERNOX
GHe Line
Manifold Box
LHe Overflow Line
LHe Supply Line
MgB2 cables
Helium Universal Expansion joint
Helium Sleeve
(access NbTi-NbTi splices)
Plug
(hydraulic barrier)
WU Electrical Heaters
NbTi Cables
NbTi-NbTi Splices
MgB2-NbTi Splices
Gas Deflector
DSHM
NbTi Cables

## Slide 7: In-vessel support system design overview
Vacuum\Thermal Barrier
Slide Support
Ghe Deflector
Electrical Insulator Sleeve
Cable Entry Guide
A
A
  Boiler module
  One point constraint layout
    Fixation point @ the top (suspension layout)
    Dedicated fixtures for supporting cryo-lines
  Splice module
  Two points constraint layout
    Fixation point @ vacuum\thermal barrier
    Slide connection @ helium connection flange
Helium
Connection Flange
Slide Support
Slide Support
Slide Support
Vacuum
Vessel
A - A
Thermal barrier
Fixed support
Thrust Support
Tie Bracket
Boiler Module
Splice Module
Centering ring

## Slide 8: Cryogenic : thermal contraction
0.6 mm
1.5 mm
1.2 mm
1.2 mm
Thermal barrier
Fixed support
SM to BM
cryo-connections
DFM to QXL
cryo-connections
Splice Module
  Fixed point @ SM vacuum barrier & D2 vacuum barrier
  Sliding point @ helium connection flange
  Universal expansion joint between SM & D2
    Structurally “decoupling” D2 from DFM
Boiler Module
  Fixed point @ thermal barrier
Cryo-Connections
  Flexibles in between SM & BM containing extra-length
  Flexibles in between BM & QXL containing extra-length
0.7 mm
1.8 mm
0.02 mm
2.5 mm
Thermal\Vacuum barrier
Fixed support
Thermal\Vacuum barrier
Fixed support
Universal expansion joint
D2
DSHM
Boiler Module
Cable Module

## Slide 9: DFM Splice Module : Slide Support Design
Scope : rigidify cold-mass & avoid overstressing the vacuum barrier
Key design features
  Three independent slide supports distributed around CM circumference
  Slide support
    Spring-preloading system to compensate CM thermal contraction
    PEEK block to insulate CM
Design validation
    Measured of PEEK deformation @ warm under design load
    Verified sliding principle under design load
    Verified mechanical strength of PEEK @ cold under design load
Insulation Block
Peek
Guide Plate
Support Plate
welded to vacuum vessel
Thrust Bracket
welded to cold-mass
Preloading Screw
Belleville Washer Stack (x4)
Anti-Slip V Pad
Bushing
Bronze
Guiding Pin
Spherical Tip Bronze
Mobile Plate
Test @ warm
Test @ cold
Dedicated FEM analysis of the slide support

## Slide 10: Insulation Vacuum & External Interfaces
Insulation vacuum
  Two insulation vacuum volumes
    One in common with DSHM
    One in common with jumper
  Vacuum Barrier with DSHM & D2
  Vacuum equipment
    Ports for installing pumping system & vacuum gauges
    Ports for installing pressure relief devices
    Port for installing vacuum instrumentation (feedthrough)
  Leak tightness
  O-ring Viton seal compressed to 25% to 30%
  Standard commercial solutions where possible
Mechanical design approach
  Vacuum vessel according to EN 13445-3
  Bellows according to EN 14917+A1
Spring relief plates
Insulation vacuum specifications | Unit | Value
Nominal pressure | [mbar] | 1.10-6
Design pressure | [bara] | 1.49
Maximum allowed leak rate at RT acc. to [19] Liquid Helium volume to insulation vacuum Air to insulation vacuum Through DFM-DSHM vacuum barrier | [mbar.l.s-1] | 1.10-9 1.10-8 1.10-8
Spring loaded valves
Interconnection sleeve
Bellows free to expand in case of cold leak
IFS Panel
DSHM
D2-DFM Interlink
Vac. Valves & Gauges
Jumper interface
Vacuum sleeve to access cryo-lines
Pumping system
Feedthrough
Viton O-ring Ø5 mm
25-30 % compression
ISO Clamps
Floating flange with 2nd seal
Interconnection sleeve

## Slide 11: External frame design overview
Design 90% for location 5R
Key design features
  Cryostat suspended from tunnel’s surface
  2 DOFs kinematic requirement for DSHM installation
Support system composed of three units
  Rail : Fastened to tunnel surface
    Aligned wrt referential during fixation to tunnel roof
  Trolley : sliding over the rail by means of wheels
    Locking system to hold the cryostat in position along the rail
    Swivel connection (tie rod end) with SM vacuum vessel
  Tilting cradle : connected to cryostat & trolley
    Primary bolted interface at vacuum connection flange of SM
    Bolted interface with the BM through dedicated extension arm
    Rotatable connection with trolley + push-pull locking system
Titling Cradle
Rail
Trolley
Tunnel Interfaces
Swivel Connection
Titling Cradle
Extension arm
Trolley
Trolley
locking system
Pivoting Axis
Wheel
Bolted connection (Connection vacuum flange)
Connection vacuum flange
Push-Pull
locking system

## Slide 12: Cryogenic : Thermal Performances
Thermal analysis
Convection over surfaces exposed to atmosphere
Forced T 4.5 K over surfaces exposed to LHe & cold GHe
Conservative assumptions
  Perfect thermal conductance between parts
  Conservative convective coefficient 5 W/m2K, bulk temperature 18°C
  Heat load through lambda plate neglected (EDMS 2642887)
No condensation on surfaces facing atmosphere
Heat in-leaks within budget < 25 W
Extracted conductive resultant heat load ≈18.5 W
Estimated radiative heat load ≈ 4.8 W (cold surfaces ≈4 m2)
Operating temperature distribution of the Cable Module
Operating temperature distribution of the Boiler Module
0.5 W
6.9 W
3.9 W
1.2 W/m2
6.2 W
0.5 W
0.5 W
1.2 W/m2
Operating temperature distribution of the vacuum vessel envelope
MIN 12.2 °C
MIN 13.3 °C
MIN 13.3 °C
MIN 14.8 °C
Condensation check
Heat in-leak loads

## Slide 13: Cryogenic : Gas evacuation
Requirement : gas evacuation towards DSHM
Approach (same as for DFX) :
  Cryostat rotated around frame’s pivot axis
  Rotation of 1.4⁰ @ all the installation’s locations
    Same installation procedure @ all installation’s locations
  Looking from transport area towards DFM
    Clockwise rotation @ locations R1 & R5
    Counterclockwise rotation @ locations L1 & L5
  Resulting slope wrt horizontal reference
    0.7⁰ positive slope @ locations R1 & L5
    2.1⁰ positive slope @ locations L1 & R5
  Relative inclination absorbed by helium\vacuum bellows
L5
R5
0.7 ⁰
Slope compensation required
Horizontal Reference
POINT 5
1.4⁰
1.4⁰
L1
R1
POINT 1
1.4⁰
1.4⁰
Horizontal Reference
0.7⁰
Slope compensation required
Frame’s pivot axis
1.4⁰
Vacuum bellows
Plug
(Coldest point)
NbTi-NbTi splices
Helium bellows

## Slide 14: Design compliance with PED
Identification of PED Category  II
  Calculation report in progress
Applicable standard  EN 13445-3
Definition of P-T configurations
  Derivation of load case scenarios
Identifications of design checks according to EN 13445-3
  Thermo-mechanical cycles < 500 (threshold)  not fatigue assessment
  Pre-qualification of non-standard pressure-retaining welds – Annex C
  Verification of structural stability (I-DC) – Annex B
Thermo-structural analyses through FEM
  Methods, safety factors & acceptance criteria according to EN 13445-3
  Application of Finite Element Sub-modeling Technique
    Global model for thermal, buckling & displacement field
    Sub-models for stress distribution at welded connections
P-T Configurations
Transport
Pumping
Pumping insulation vacuum SC Link
Pumping insulation vacuum DFH
Cryogenic circuit purging
Purge of cryogenic circuit without vacuum
Purge of cryogenic circuit with DSHM vacuum
Purge of cryogenic circuit with DFM vacuum
Pressure test
Thermal cycle
Nominal
DESIGN
DFM Cool down
DFM warm up
Non nominal events
Vacuum break DSHM
Vacuum break DFM
Helium break DFM

## Slide 15: Design compliance with PED
Stress linearization – EN 13445-3 – Annex C
Sub-models @ welded connections
Identification of weld’s critical point
Stress linearization & decomposition
Verification of prescribed material stress limits
All pressure-retaining welds verified
Instability design check - EN 13445-3 – Annex B
Determination of linear buckling modes
Mesh pre-deformation according to buckling modes
Assessment of non-linear elastoplastic buckling
Verification of prescribed material strain limit
Instability verified for all loading scenarios
M = 57 < 150 = f
M+B = 154 < 225 = 1.5·f
Lip Weld – GHe Line
Fillet Weld – GHe Line
M = 62 < 150 = f
M+B = 82 < 225 = 1.5·f
Fillet Weld – LHe Supply Line
M = 123 < 150 = f
M+B = 202 < 225 = 1.5·f
Fillet Weld – Helium Tank Neck
M = 109 < 150 = f
M+B = 194 < 225 = 1.5·f
Cable Module
Boiler Module
εTp,max% = 0.16%<< 5%
Load Multiplier ≈ 8.8
Magnification Factor x 60
Cable Module : Vacuum Barrier
Boiler Module : Vacuum Vessel
Load Multiplier ≈ 11.9
Magnification Factor x130
εTp,max% = 0.13% << 5%
Linear Buckling
Non-linear
elasto-plastic buckling

## Slide 16: Conclusions
Functional and technical requirements have been studied and associated technical solutions were developed in the detailed design
The design principle is similar to the one of the Demonstrator DFX of Demo2
3D detailed model is ready to start producing manufacturing drawings
Structural calculations required by the PED are completed, report in progress
The detailed design of the supporting frame needs to be finalized and adapted to the four locations

## Slide 17: Thank you for your attention