## Slide 1: RHA guidelines for electronic equipment for meeting HL-LHC requirements
Andrea Coronetti (CERN, UM)
R2E Annual Meeting – 1-2 March, 2022
https://indico.cern.ch/event/1116677/

## Slide 2: Introduction
Radiation hardness assurance process for CERN
Goal: achieve the availability target requirements for operation of HL-LHC in terms of R2E-related failures
How to achieve it?
  Need to establish links and responsibilities within R2E project (MCWG, RADWG, R2E Leader) and equipment groups
  Need for a traceable development process that allows backtracing R2E-related design choices to the requirements

## Slide 3: Targeted systems
CERN systems are distributed
Cost leverage prevents widespread use of rad-hard parts
COTS preferred
  Shorter lead time
  Higher performance
  Bring significant challenges to the RHA process
    Traceability
Generally ‘Rad-hard’ means TID-tolerant and does not necessarily apply to CERN rad-tolerance

## Slide 4: Targeted systems
Two types of systems are of concern for HL-LHC in the scope of this guideline
Custom-designed systems based on COTS components
  Design within the equipment group
  Full control over architecture and part selection
Fully commercial systems
  Procured externally
  No control over architecture and part selection
  Best scenario: units from same production lot/series

## Slide 5: RHA process for custom-built systems
Red phases directly concern involvement of R2E working groups
Three documents tackle these three topics (only environment doc already published)
Radiation environment and requirements info in RHAPV
Selected parts radiation qualification info in RHAPV
System-level radiation qualification info in RHAPV
Engineering Change Request
Request to RADWG for component-level selection strategy and testing
Functional Specification
Request to MCWG for assessment of radiation environment(s)
Radiation level specifications for HL-LHC (EDMS 2302154)
Best Practices for Radiation Design of Accelerator Equipment
System-level testing guideline
Radiation Hardness Assurance Project Validation (RHAPV) accompanies the radiation-related development of a system throughout the entire lifecycle (EDMS 2028777)
It ensures traceability and compliance with respect to initial requirements
Request to RADWG for system-level test
Engineering and R2E requests to be submitted to the various groups
The RHA process document defines the various phases of a radiation-tolerant development (EDMS 2066950)
Engineering Specification
R2E fault tracking (AFT) and mitigation

## Slide 6: RHA process for COTS systems
Unless employed in R2E-safe areas (< 3 x 106 HEH/cm2/year and < 3 x 107 nth/cm2/year, EDMS 2389056), COTS systems have to be qualified due to the SEE risk
RHA process has less phases
Dealt with in the same documents as for custom-built systems
Need to include relevant information about qualification in the RHAPV

## Slide 7: Radiation requirements
From HL-LHC availability to the single device radiation response
Radiation Environment
LHC availability goals for R2E
R2E Failure Budget given to the equipment
Number of units
System-level SEE cross-sections
Target lifetime of system and parts (TID, TNID)
Number of parts, technology and use
Part-level SEE cross-sections
Design margins if too low
ID | Requirement
SYS-A001 | The target beam dump rate for the system unit is 10-5 dumps/fb-1, for the environment under consideration this will correspond to a system-level cross-section of 10-12 cm2.
DEV-A001 | Device A can suffer from SEFI that can propagate to the system-level forcing a beam dump with a cross-section below 4 x 10-13 cm2.
DEV-A002 | Device A can suffer from SEU that can propagate to the system-level forcing a beam dump with a cross-section below 2 x 10-13 cm2.
DEV-A003 | Device B can suffer from SEL that can propagate to the system-level forcing a beam dump with a cross-section below 1 x 10-13 cm2.

## Slide 8: Part criticality and test strategy
Devices can be classified based on criticality within the system
Class | Radiation response | Sourcing | Part types
C0 | Resistant to radiation or with moderate sensitivity | Easily replaceable with many alterative on the market | Diodes, transistors
C1 | Susceptible to radiation, but not on system critical path | Limited amount of replacements available | Voltage regulators/references, DAC, memory
C2 | Susceptible to radiation and on system critical path | No equivalents on the market | ADC, FPGA, power electronics
Radiation test at part-level for the various radiation effects of concern based on requirements and technology (TID, TNID, SEEs, synergistic effects)
Radiation test at system-level
Credit: S. Uznanski
Part-level tests can be requested to RADWG
Uncompliant C1 part can be replaced for another COTS part with better radiation performance
Uncompliant C2 part may require re-design
  Mitigation (e.g., derating, ECC, filtering, watchdog)
  Review of functional block architecture
System-level tests done by equipment group with RADWG support

## Slide 9: Part-level testing
Mature practice, but many details to bear in mind to get relevant data
Facility to be used
Testing parameters (bias, temperature, etc.)
Setup preparation
# of units to be tested for good level of confidence
Best candidate may depend on specific critical parameter for the system
Testing for each of TID, TNID and SEEs may require applying different entries to the previous parameters
In addition, R2E R&D work shows that standard qualification with HEH may not always suffice, and extra tests or safety margins may need to be applied
Thermal neutrons
Intermediate-energy neutrons
HEH fission with high-Z materials
Low-energy protons
Credit: M. Cecchetto

## Slide 10: Traceability
Part variability exists even for the same reference
Lot-to-lot, Fab-to-fab, Wafer-mask-to-wafer-mask
Intra-lot variability is typically acceptable
Need to ensure that tested parts and parts used in the accelerator belong to the same lot
  May need to re-test also parts in the RADWG database
Need to have units from same production series for COTS systems
Credit: R. Ladbury
Credit: R. Baumann
Credit: M D’Alessio

## Slide 11: System-level testing
Less mature and harder to interpret, unless everything works
Limitations of
stand-alone
system-level
testing
TID worst case analysis
Part-to-part and module-to-module variability
Data portability
ELDRS
Worst case test conditions?
Pass/fail outcome on a system
Limited level of confidence
Tough to apply mitigations/redesigns
Stand-alone system-level testing is used for COTS systems
For custom-built systems it is used after the part-level qualification to verify those radiation effects that could not be verified at part-level
Benefits of system-level
testing
Fault propagation assessment
Dependent faults/failures
Synergistic effects of radiation
Verification of existing radiation mitigations
Implementation of additional radiation mitigations

## Slide 12: R2E development status review
SY/BI
Beam Loss Monitors
Beam Position Monitor
Beam Gas Ionization Monitor
Rad-tol camera
SY/EPC
60A/120A power unit
FGC power unit
BE/CEM
Distributed I/O Tier
TE/CRG
DC Heater
EDA-03296
DI/DO
TE/MPE
CIBU, PIC, WIC
QDS, QPS
Rad-tol fieldbus
Current lead heating controller
600A /13kA energy extraction
Rad-tol AC/DC supply
TE/VSC
Vacuum gauge electronics
EP/CMU
CMS low voltage supply
Closed session of the R2E annual meeting on March 3rd

## Slide 13: Conclusions
Radiation hardness assurance process for CERN
Built upon the strong collaboration between the R2E project (and its working groups) and the equipment groups
Practices are now mature enough to be tailored into a standard RHA process to be followed also for future developments
  First draft of documents in preparation and soon to be reviewed by relevant stakeholders
  But radiation effects bring continuous challenges
    No real limit to extension/revision of current best practices
Equipment groups already implementing the backbone of the RHA process for HL-LHC with careful monitoring of R2E working groups

## Slide 14
Thank you for
your attention!