## Slide 1: LONGITUDINAL beam DYNAMICS in circular accelerators
Frank Tecker CERN, ATS-DO
Introduction to Accelerator Physics
Kaunas, Lithuania, 18/9 - 1/10/2022

## Slide 2
The author consents to the photographic, audio and video recording of this lecture at the CERN Accelerator School. The term “lecture” includes any material incorporated therein including but not limited to text, images and references.
The author hereby grants CERN a royalty-free license to use his image and name as well as the recordings mentioned above, in order to post them on the CAS website.
The material is used for the sole purpose of illustration for teaching or scientific research. The author hereby confirms that to his best knowledge the content of the lecture does not infringe the copyright, intellectual property or privacy rights of any third party. The author has cited and credited any third-party contribution in accordance with applicable professional standards and legislation in matters of attribution.
Copyright statement and speaker’s release for video publishing

## Slide 3: Scope and Summary of the 2 lectures:
Introduction
Circular accelerators: Cyclotron / Synchrotron
Dispersion Effects in Synchrotron
Stability and Longitudinal Phase Space Motion
Hamiltonian
Stationary Bucket
Injection Matching
More related lectures:
  Linacs – David Alesini
  RF Systems - Christine Völlinger
  Electron Beam Dynamics - Lenny Rivkin
  Non-Linear longitudinal Beam Dynamics - Alexandre Lasheen
Hands-on calculations – longitudinal in the second week !!!
The goal of an accelerator is to provide a stable particle beam.
The particles nevertheless perform transverse betatron oscillations.
We will see that they also perform (so-called synchrotron) oscillations in the longitudinal plane and in energy.
We will look at the stability of these oscillations, their dynamics and derive some basic equations.

## Slide 4
160 MeV-> 2 GeV
-> 25 GeV
-> 450 GeV
-> 7 TeV
Linear accelerators scale in size and cost(!) ~linearly with the energy.
Circular accelerators can each turn reuse
  the accelerating system
  the vacuum chamber
  the bending/focusing magnets
  beam instrumentation, …
-> economic solution to reach higher particle energies
But each accelerator has a limited energy range.
Motivation for circular accelerators
4
-

## Slide 5
The accelerating system will depend upon the evolution of the particle velocity: • electrons reach a constant velocity (~speed of light) at relatively low energy
• heavy particles reach a constant velocity only at very high energy
-> need different types of resonators, optimized for different velocities
-> the revolution frequency will vary, so the RF frequency will be changing
-> magnetic field needs to follow the momentum increase
Particle types and acceleration
Particle rest mass m0:
electron 0.511 MeV
proton 938 MeV
239U ~220000 MeV
Relativistic gamma factor:
Momentum:
Total Energy:

## Slide 6
The revolution and RF frequency will be changing during acceleration
Much more important for lower energies (values are kinetic energy - protons).
PS Booster: 50 MeV (b= 0.314) -> 1.4 GeV (b=0.915)
(pre LS2) 602 kHz -> 1746 kHz => 190% frequency increase
(post LS2): 160 MeV (b= 0.520) -> 2 GeV (b=0.948) => 95% increase
PS: 1.4 GeV (b=0.915) -> 25.4 GeV (b =0.9994)
437 KHz -> 477 kHz => 9% increase
(post LS2): 2 GeV (b=0.948) -> 25.4 GeV (b =0.9994) => 5% increase
SPS: 25.4 GeV -> 450 GeV (b=0.999998)
=> 0.06% frequency increase
LHC: 450 GeV -> 7 TeV (b= 0.999999991)
=> only 2 10-6 increase
RF system needs more flexibility in lower energy accelerators.
Question: What about electrons and positrons?
Revolution frequency variation

## Slide 7: Acceleration + Energy Gain
Hence, it is necessary to have an electric field E (preferably) along the direction of the initial momentum (z),
which changes the momentum p of the particle.
In relativistic dynamics, total energy E and momentum p are linked by
The rate of energy gain per unit length of acceleration (along z) is then:
and the kinetic energy gained from the field along the z path is:
To accelerate, we need a force in the direction of motion!
Newton-Lorentz Force on a charged particle:
2nd term always perpendicular to motion => no acceleration
- V is a potential - q the charge
May the force
be with you!

## Slide 8: Unit of Energy
Today’s accelerators and future projects work/aim at the TeV energy range.
LHC: 7 TeV -> 14 TeV
CLIC: 380 GeV -> 3 TeV
FCC: 100 TeV
In fact, this energy unit comes from acceleration:
Basic Unit: eV (electron Volt) keV = 1000 eV = 103 eV
MeV = 106 eV GeV = 109 eV
TeV = 1012 eV
LHC = ~450 Million km of batteries!!!
3x distance Earth-Sun
1 eV (electron Volt) is the energy that 1 elementary charge e (like one electron or proton) gains when it is accelerated in a potential (voltage) difference of 1 Volt.

## Slide 9: Methods of Acceleration in circular accelerators
Electrostatic field limited by insulation, magnetic field doesn’t accelerate at all.
Circular machine: DC acceleration impossible since
The electric field is derived from a scalar potential φ and a vector potential A
The time variation of the magnetic field H generates an electric field E
The solution: => time varying electric fields
- Induction
- RF frequency fields
+
+
+
Vacuum chamber
Insulator
(ceramic)
Voltage
source
-
+
First attracted
Acceleration
Then again attracted
Deceleration
=> no Acceleration

## Slide 10: Acceleration by Induction: The Betatron
It is based on the principle of a transformer:
- primary side: large electromagnet - secondary side: electron beam.
The ramping magnetic field is used to guide particles on a circular trajectory as well as for acceleration.
Limited by saturation in iron (~300 MeV e-)
Used in industry and medicine, as they are
compact accelerators for electrons
Donald Kerst with the first betatron, invented at the University of Illinois in 1940
coil
beam
vacuum pipe
iron yoke
Bf
B
Bf
E
R
beam
side view
top view
time

## Slide 11
Circular accelerators
Cyclotron
Synchrotron

## Slide 12
Circular accelerators: Cyclotron
Courtesy: EdukiteLearning, https://youtu.be/cNnNM2ZqIsc

## Slide 13
Circular accelerators: Cyclotron
Cyclotron frequency
g increases with the energy  no exact synchronism
if v  c  g  1
Synchronism condition
B = constant
wRF = constant
B
RF generator, wRF
g
Ion source
Extraction electrode
Ions trajectory
Used for protons, ions
Animation: https://phyanim.sciences.univ-nantes.fr/Meca/Charges/cyclotron.php

## Slide 14
Circular accelerators: Cyclotron
Courtesy Berkeley Lab, https://www.youtube.com/watch?v=cutKuFxeXmQ

## Slide 15
Synchrocyclotron: Same as cyclotron, except a modulation of wRF
B = constant
  g wRF = constant
wRF decreases with time
The condition:
Allows to go beyond the non-relativistic energies
Cyclotron / Synchrocyclotron
TRIUMF 520 MeV cyclotron Vancouver - Canada
CERN 600 MeV synchrocyclotron
More in
lectures by Mike Seidel

## Slide 16
Synchronism condition
Constant orbit during acceleration
To keep particles on the closed orbit, B should increase with time
w and wRF increase with energy
RF generator
RF cavity
h integer,
harmonic number:
number of RF cycles
per revolution
Circular accelerators: The Synchrotron
RF frequency can be multiple of revolution frequency
B
injection
extraction
r
R=C/2π
E
Bending
magnet
bending radius
h is the maximum number of bunches in the synchrotron.
Normally less bunches due to gaps for kickers, collision constraints,…

## Slide 17
PS (CERN)
Proton Synchrotron
© CERN Geneva
Examples of different proton and electron synchrotrons at CERN
+ LHC (of course!)
LEAR (CERN)
Low Energy Antiproton Ring
© CERN Geneva
© CERN Geneva
EPA (CERN)
Electron Positron Accumulator
Circular accelerators: The Synchrotron

## Slide 18: The Synchrotron – LHC Operation Cycle
The magnetic field (dipole current) is increased during the acceleration.
energy ramp
preparation and access
beam dump
injection phase
coast
coast
L.Bottura
450 GeV
7 TeV
start of the ramp

## Slide 19: The Synchrotron
The synchrotron is a synchronous accelerator since there is a synchronous RF phase for which the energy gain fits the increase of the magnetic field at each turn. That implies the following operating conditions:
Energy gain per turn
Synchronous particle
RF synchronism
(h - harmonic number)
Constant orbit
Variable magnetic field
If v≈c, w hence wRF remain constant (ultra-relativistic e- )
B
injection
extraction
r
R=C/2π
E
Bending
magnet
bending radius

## Slide 20: Common Phase Conventions
For circular accelerators, the origin of time is taken at the zero crossing of the RF voltage with positive slope
Time t= 0 chosen such that:
3. I will stick to convention 1 in the following to avoid confusion
1
f1
For linear accelerators, the origin of time is taken at the positive crest of the RF voltage
2
f2

## Slide 21
Energy ramping by increasing the B field (frequency has to follow v):
With
The synchronous phase depends on
  the change of the magnetic field
  and the RF voltage
Synchronous phase φs changes during energy ramping
The Synchrotron – Energy ramping
r const.
fs

## Slide 22
During the energy ramping, the RF frequency increases to follow the increase of the revolution frequency :
Since the RF frequency must follow the variation of the B field with the law
Hence: ( using )
RF frequency program during acceleration determined by B-field
This asymptotically tends towards when B becomes large compared to which corresponds to
The Synchrotron – Frequency change

## Slide 23
During the energy ramping, the B-field and the revolution frequency increase
Example: PS - Field / Frequency change
time (ms)
B-field
revolution frequency
kinetic
energy
time (ms)
B-field change
‘B-dot’

## Slide 24: Overtaking in a Formula 1 Race
www.formula1.com

## Slide 25: Overtaking in a Formula 1 Race

## Slide 26: Overtaking in a Formula 1 Race
A F1 car wants to overtake another car! It will have a
a different track length due to a ‘dispersion orbit’
and a different velocity.
and =>
The winner depends on the relative change in speed compared to the relative change in track length!
If the relative change in speed is larger than the relative change in track length => the red car will win!
v=speed of the car
R=track physical radius
T=revolution period
fr=revolution frequency
slow
fast
Circumference
2R

## Slide 27: Overtaking in a Synchrotron
A particle slightly shifted in momentum will have a
dispersion orbit and a different orbit length
a different velocity.
As a result of both effects the revolution period T changes with a “slip factor” 𝜂 :
E+E
E
cavity
Circumference
L = 2R
Note: you also find η defined with a minus sign!
p=particle momentum
R=synchrotron physical radius
T=revolution period
The “momentum compaction factor” is defined as relative orbit length change with momentum:

## Slide 28: Momentum Compaction Factor
d
x
The elementary path difference from the two orbits is:
leading to the total change in the circumference:
With ρ=∞ in straight sections we get:
< >m means that the average is considered over the bending magnet only
definition of dispersion Dx
p+dp
p
Property of the transverse beam optics!

## Slide 29: Dispersion Effects – Revolution Period
The two effects of the orbit length and the particle velocity change the revolution period as:
definition of momentum compaction factor
At transition energy, the velocity change and the path length change with momentum compensate each other. So the revolution frequency there is independent from the momentum deviation.
Slip factor:
with
or
Note: you also find η defined with a minus sign!
⇒

## Slide 30: RECAP: Principle of Phase Stability (Linac)
Let’s consider a succession of accelerating gaps, operating in the 2π mode, for which the synchronism condition is fulfilled for a phase s .
is the energy gain in one gap for the particle to reach the next gap with the same RF phase: P1 ,P2, …… are fixed points.
If an energy increase is transferred into a velocity increase => M1 & N1 will move towards P1 => stable M2 & N2 will go away from P2 => unstable (Highly relativistic particles have no significant velocity change)
For a 2π mode, the electric field is the same in all gaps at any given time.
energy gain
late
early
Notes: Edwin McMillan of UC Berkley, and the Russian V.I. Veksler independently discovered Phase stability in 1945.

## Slide 31: Phase Stability in a Synchrotron
From the definition of  it is clear that an increase in momentum gives - below transition (η < 0) a higher revolution frequency (increase in velocity dominates) while
- above transition (η > 0) a lower revolution frequency (v  c and longer path) where the momentum compaction (generally > 0) dominates.
late
early
fs
p-fs
eV
eVs
stable synchr. particle for  > 0
above transition
 < 0
Energy Gain

## Slide 32: Crossing Transition
At transition, the velocity change and the path length change with momentum compensate each other. So the revolution frequency there is independent from the momentum deviation.
Crossing transition during acceleration makes the previous stable synchronous phase unstable. The RF system needs to make a rapid change of the RF phase, a ‘phase jump’.
In the PS: γt is at ~6 GeV
In the SPS: γt= 22.8, injection at γ=27.7
=> no transition crossing!
In the LHC: γt is at ~55 GeV, also far below injection energy
Transition crossing not needed in leptons machines, why?
fs
p-2fs
above transition
below transition

## Slide 33
f2
f2 - The particle is decelerated
- decrease in energy - decrease in revolution frequency
- The particle arrives later – tends toward f0
F1 - The particle B is accelerated
- Below transition, an energy increase means an increase in revolution frequency
- The particle arrives earlier – tends toward f0
f1
f0
Dynamics: Synchrotron oscillations
Simple case (no accel.): B = const., below transition
The phase of the synchronous particle must therefore be f0 = 0.
B

## Slide 34
1st revolution period
V
time
A
B
Synchrotron oscillations
100th revolution period
200th revolution period
300th revolution period
400th revolution period
500th revolution period
600th revolution period
700th revolution period
800th revolution period
Particle B is performing Synchrotron Oscillations around synchronous particle A.
The amplitude depends on the initial phase and energy.
The oscillation frequency is much slower than in the transverse plane. It takes a large number of revolutions for one complete oscillation. Restoring electric force smaller than magnetic force.

## Slide 35
Cavity voltage
Potential well
A
B
The Potential Well
phase

## Slide 36
DE, Dp/p
f
Emittance: phase space area including all the particles
NB: if the emittance contour correspond to a possible orbit in phase space, its shape does not change with time (matched beam)
DE, Dp/p
f
acceleration
deceleration
move
backward
move
forward
The particle trajectory in the phase space (Dp/p, f) describes its longitudinal motion.
reference
Longitudinal phase space
The energy – phase oscillations can be drawn in phase space:

## Slide 37
t (or )
E
higher energy
late arrival
lower energy
early arrival
Particle B oscillates around particle A
This is a synchrotron oscillation
Plotting this motion in longitudinal phase space gives:
Longitudinal Phase Space Motion

## Slide 38
f1
f0
f2
Phase space picture
Synchrotron oscillations – No acceleration
separatrix
stable region
unstable region

## Slide 39
Synchrotron motion in phase space
The restoring force is non-linear.
speed of motion depends on position in phase-space
(here shown for a stationary bucket)
Remark:
Synchrotron frequency much smaller than betatron frequency.

## Slide 40
Bucket area: area enclosed by the separatrix
The area covered by particles is the longitudinal emittance
DE-f phase space of a stationary bucket (when there is no acceleration)
Dynamics of a particle
Non-linear, conservative oscillator  e.g. pendulum
Particle inside the separatrix:
Particle at the unstable fix-point
Particle outside the separatrix:
Synchrotron motion in phase space

## Slide 41
Bucket area = longitudinal Acceptance [eVs]
Bunch area = longitudinal beam emittance (rms) =  σE σt [eVs]
E
t (or )
E
t
Bunch
Bucket
(Stationary) Bunch & Bucket
The bunches of the beam fill usually a part of the bucket area.
Attention: Different definitions are used!

## Slide 42
fs
stable region
unstable region
separatrix
The symmetry of the case B = const. is lost
Synchrotron oscillations (with acceleration)
2
1
Case with acceleration B increasing
Phase space picture
p-fs

## Slide 43: RF Acceptance versus Synchronous Phase
The areas of stable motion (closed trajectories) are called “BUCKET”. The number of circulating buckets is equal to “h”.
The phase extension of the bucket is maximum for s =180º (or 0°) which means no acceleration.
During acceleration, the buckets get smaller, both in length and energy acceptance.
=> Injection preferably without acceleration.

## Slide 44: Longitudinal Motion with Synchrotron Radiation
Synchrotron radiation energy-loss energy dependant:
During one period of synchrotron oscillation:
when the particle is in the upper half-plane, it loses more energy per turn, its energy gradually reduces
- when the particle is in the lower half-plane, it loses less energy per turn, but receives U0 on the average, so its energy deviation gradually reduces
The phase space trajectory spirals towards the origin (limited by quantum excitations)
=> The synchrotron motion is damped toward an equilibrium bunch length and energy spread.
More details in the lectures on Electron Beam Dynamics
U
0
=
4
3
π
r
e,p
m
0
c
2
(
)
3
E
4
ρ
ΔE

## Slide 45: Longitudinal Dynamics in Synchrotrons
Now we will look more quantitatively at the “synchrotron motion”.
The RF acceleration process clearly emphasizes two coupled variables, the energy gained by the particle and the RF phase experienced by the same particle. Since there is a well defined synchronous particle which has always the same phase s, and the nominal energy E0, it is sufficient to follow other particles with respect to that particle. So let’s introduce the following reduced variables:
particle RF phase :  =  - s
particle momentum : p = p – p0
particle energy : E = E – E0
angular frequency : ⍵ = ⍵ – ⍵0
azimuth orbital angle:  =  - s
Look at difference from synchronous particle

## Slide 46: First Energy-Phase Equation
For a given particle with respect to the reference one:
Since:
one gets:
and
particle ahead arrives earlier
=> smaller RF phase
qs
Dq
R
v

## Slide 47: Second Energy-Phase Equation
The rate of energy gained by a particle is:
The rate of relative energy gain with respect to the reference particle is then:
leads to the second energy-phase equation:
Expanding the left-hand side to first order:

## Slide 48: Equations of Longitudinal Motion
deriving and combining
This second order equation is non linear. Moreover the parameters within the bracket are in general slowly varying with time.
We will study some cases in the following…

## Slide 49: Small Amplitude Oscillations
(for small )
with
Let’s assume constant parameters R, p0, 0 and :
Consider now small phase deviations from the reference particle:
and the corresponding linearized motion reduces to a harmonic oscillation:
where s is the synchrotron angular frequency.
The synchrotron tune is the number of synchrotron oscillations per revolution:
Typical values are <<1, as it takes several 10 - 1000 turns per oscillation.
- proton synchrotrons of the order 10-3
- electron storage rings of the order 10-1

## Slide 50
Stability is obtained when s is real and so s2 positive:
Stability condition for ϕs
with
Vrf
cos (fs)
acceleration
deceleration
Stable in the region if
𝛾 < 𝛾t
𝛾 < 𝛾t
𝛾 > 𝛾t
𝛾 > 𝛾t

## Slide 51: Large Amplitude Oscillations
For larger phase (or energy) deviations from the reference the second order differential equation is non-linear:
(s as previously defined)
Multiplying by and integrating gives an invariant of the motion:
which for small amplitudes reduces to:
(the variable is , and s is constant)
Similar equations exist for the second variable : Ed/dt

## Slide 52: Large Amplitude Oscillations (2)
Second value m where the separatrix crosses the horizontal axis:
Equation of the separatrix:
When  reaches -s the force goes to zero and beyond it becomes non restoring. Hence -s is an extreme amplitude for a stable motion which in the
phase space( ) is shown as
closed trajectories.

## Slide 53: Energy Acceptance
This “RF acceptance” depends strongly on s and plays an important role for the capture at injection, and the stored beam lifetime.
It’s largest for s=0 and s=π (no acceleration, depending on ).
It becomes smaller during acceleration, when s is changing
Need a higher RF voltage for higher acceptance.
For the same RF voltage it is smaller for higher harmonics h.
From the equation of motion it is seen that reaches an extreme at .
Introducing this value into the equation of the separatrix gives:
That translates into an energy acceptance:

## Slide 54: RF Acceptance versus Synchronous Phase
The areas of stable motion (closed trajectories) are called “BUCKET”. The number of circulating buckets is equal to “h”.
The phase extension of the bucket is maximum for s =180º (or 0°) which means no acceleration.
During acceleration, the buckets get smaller, both in length and energy acceptance.
=> Injection preferably without acceleration.

## Slide 55: Stationnary Bucket - Separatrix
This is the case sins=0 (no acceleration) which means s=0 or  . The equation of the separatrix for s=  (above transition) becomes:
Replacing the phase derivative by the (canonical) variable W:
and introducing the expression for s leads to the following equation for the separatrix:
with C=2R
W

0

2
Wbk

## Slide 56: Bucket height – bucket area
Setting = in the previous equation gives the height of the stationary bucket:
The bucket area is:
Since:
one gets:
For an accelerating bucket, this area gets reduced by a factor depending on 𝚽s:

## Slide 57: Potential Energy Function
The longitudinal motion is produced by a force that can be derived from a scalar potential:
The sum of the potential energy and kinetic energy is constant and by analogy represents the total energy of a non-dissipative system.

## Slide 58: Hamiltonian of Longitudinal Motion
Introducing a new convenient variable, W, leads to the 1st order equations:
The two variables ,W are canonical since these equations of motion can be derived from a Hamiltonian H(,W,t):

## Slide 59: Hamiltonian of Longitudinal Motion
Contours of H (φ,W)
What does it represent? The total energy of the system!
Surface of H (φ,W )
Contours of constant H are particle trajectories in phase space! (H is conserved)
Hamiltonian Mechanics can help us understand some fairly
complicated dynamics (multiple harmonics, bunch splitting, …)

## Slide 60
Bunch from sending accelerator into the bucket of receiving
Advantages:
Particles always subject to longitudinal focusing
No need for RF capture of de-bunched beam in receiving accelerator
No particles at unstable fixed point
Time structure of beam preserved during transfer
Injection: Bunch-to-bucket transfer

## Slide 61: Effect of a Mismatch
Injected bunch: short length and large energy spread after 1/4 synchrotron period: longer bunch with a smaller energy spread.
W
W


For larger amplitudes, the angular phase space motion is slower (1/8 period shown below) => can lead to filamentation and emittance growth
stationary bucket
accelerating bucket
W.Pirkl
restoring force is non-linear
W
W



## Slide 62: Effect of a Mismatch (2)
Long. emittance is only preserved for correct RF voltage
Matched case
Longitudinal mismatch
Bunch is fine, longitudinal emittance remains constant
Dilution of bunch results in increase of long. emittance

## Slide 63: Effect of a Mismatch (3)
Evolution of an injected beam for the first 100 turns.
For a mismatched transfer, the emittance increases (right).
matched beam
mismatched beam – phase error

## Slide 64
Matched case
Longitudinal mismatch
Longitudinal matching – Beam profile
Bunch is fine, longitudinal emittance remains constant
Dilution of bunch results in increase of long. emittance
H.Damerau

## Slide 65
Find the difference!
-45° phase error at injection
Can be easily corrected by bucket phase
Equivalent energy error
Phase does not help: requires beam energy change
Matching quiz!
H.Damerau

## Slide 66: Phase Space Tomography
We can reconstruct the phase space distribution of the beam.
Longitudinal bunch profiles over a number of turns
Parameters determining s
1st bunch
2nd bunch

## Slide 67: Bunch Rotation
Phase space motion can be used to make short bunches.
Start with a long bunch and extract or recapture when it’s short.
initial beam

## Slide 68: Capture of a Debunched Beam with Fast Turn-On

## Slide 69: Capture of a Debunched Beam with Adiabatic Turn-On

## Slide 70: Generating a 25ns LHC Bunch Train in the PS

## Slide 71
1. Inject four bunches
Wait 1.2 s for second injection
2. Inject two bunches
3. Triple split after second injection
~ 180 ns, 1.3 eVs
~ 0.7 eVs
4. Accelerate from 1.4 GeV (Ekin) to 26 GeV
Production of the LHC 25 ns beam

## Slide 72
5. During acceleration: longitudinal emittance blow-up: 0.7 – 1.3 eVs
6. Double split (h21 → h42)
7. Double split (h42 → h84)
10. Fine synchronization, bunch rotation → Extraction!
~ 0.35 eVs, 4 ns
Production of the LHC 25 ns beam

## Slide 73
Triple splitting after 2nd injection
Split in four at flat-top energy
Inject 4+2 bunches
26 GeV/c
1.4 GeV
gtr
→ Each bunch from the Booster divided by 12 → 6 × 3 × 2 × 2 = 72
h = 7
h = 21
h = 84
Eject 72 bunches
2nd injection
(sketched)
The LHC25 (ns) cycle in the PS

## Slide 74: Triple splitting in the PS
h=7
h=14
h=21

## Slide 75: Two times double splitting in the PS
Two times double splitting and bunch rotation:
Bunch is divided twice using RF systems at h = 21/42 (10/20 MHz) and h = 42/84 (20/40 MHz)
Bunch rotation: first part h84 only + h168 (80 MHz) for final part
h=21
h=42
h=84

## Slide 76: Synchrotron tune measurement
Reminder: Non-linear force => Synchrotron tune depends on amplitude
Principle A: The synchrotron oscillation modulates the arrival time of a bunch.
Use pick-up intensity signal and perform an FFT
The synchrotron tune will appear as sideband of revolution harmonics
Practical approach: Mix the signal with RF signal => proportional to phase offset
Problem for proton machines since the synchrotron tune is very small. The revolution harmonic lines are huge compared to the synchrotron lines, so a very good and narrow bandwidth filter is needed to separate them
Pickup
Mixer
RF
Phase
A-S.Müller
E.Wanvik

## Slide 77: Synchrotron tune measurement – cont.
Principle B: The transverse beam position is modulated through dispersion:
Use horizontal position signal from a BPM in dispersive region + perform FFT
Radial beam position after injection with phase/energy offset (at the PS)
A-S.Müller

## Slide 78: Synchrotron tune measurement – cont.
Principle C: The transverse tune is modulated through chromaticity:
Frequency modulation (FM) of the betatron tunes.
Use horizontal position signal from a BPM + perform FFT
The synchrotron tune will appear as sidebands of the betatron tune.
Tune measurement for positrons (at the SPS)
A Boudzko (EPAC’98)
E.Wanvik

## Slide 79
Summary
Cyclotrons/Synchrocylotrons for low energy
Synchrotrons for high energies, constant orbit, synchronously rising field and frequency
Particles with higher energy have a longer orbit (normally) but a higher velocity
  at low energies (below transition) velocity increase dominates
  at high energies (above transition) velocity almost constant
Particles perform oscillations around synchronous phase
  synchronous phase depending on acceleration
  below or above transition
Hamiltonian approach can deal with fairly complicated dynamics
Bucket is the stable region in phase space inside the separatrix
Matching the shape of the bunch to the bucket is essential

## Slide 80: Bibliography
S.Y. Lee Accelerator Physics (World Scientific, 2011)
M. Conte, W.W. Mac Kay An Introduction to the Physics of particle Accelerators
        (World Scientific, 1991)
P. J. Bryant and K. Johnsen The Principles of Circular Accelerators and Storage Rings
        (Cambridge University Press, 1993)
D. A. Edwards, M. J. Syphers An Introduction to the Physics of High Energy Accelerators
        (J. Wiley & sons, Inc, 1993)
H. Wiedemann Particle Accelerator Physics
(Springer-Verlag, Berlin, 1993)
M. Reiser Theory and Design of Charged Particles Beams
        (J. Wiley & sons, 1994)
A. Chao, M. Tigner Handbook of Accelerator Physics and Engineering
        (World Scientific 1998)
K. Wille The Physics of Particle Accelerators: An Introduction
        (Oxford University Press, 2000)
E.J.N. Wilson An introduction to Particle Accelerators
        (Oxford University Press, 2001)
And CERN Accelerator Schools (CAS) Proceedings In particular: https://arxiv.org/abs/2011.02932
Longitudinal Beam Dynamics in Circular Accelerators

## Slide 81: Acknowledgements
I would like to thank everyone for the material that I have used.
In particular (hope I don’t forget anyone):
- Joël Le Duff (from whom I inherited the course)
- Rende Steerenberg
- Gerald Dugan
- Heiko Damerau
- Werner Pirkl
- Genevieve Tulloue
- Mike Syphers
- Daniel Schulte
- Roberto Corsini
- Roland Garoby
- Luca Bottura
- Berkeley Lab
- Edukite Learning

## Slide 82: Appendix: Relativity + Energy Gain
RF Acceleration
(neglecting transit time factor)
The field will change during the passage of the particle through the cavity => effective energy gain is lower
Newton-Lorentz Force
Relativistics Dynamics
2nd term always perpendicular to motion => no acceleration

## Slide 83: Phase Space Trajectories inside Stationary Bucket
A particle trajectory inside the separatrix is described by the equation:
s=
The points where the trajectory crosses the axis are symmetric with respect to s=
W

0

2
Wbk
Wb

m
2-m

## Slide 84
Energy ramping by increasing the B field (frequency has to follow v).
Stable phase φs changes during energy ramping
The Synchrotron – Energy ramping
late
early
fs
p-fs
eV
eVs
stable synchr. particle for  > 0
above transition
 < 0
Energy Gain

## Slide 85
fs
stable region
unstable region
separatrix
Particles will accumulate energy difference each turn
Transition
2
1
Case with acceleration B increasing
Phase space picture
p-fs