## Slide 1: History of Accelerators
Dr. Suzie Sheehy
University of Melbourne
University of Oxford
CERN Introductory Accelerator School
Kaunas, 2022
Notes: What are accelerators used for?

## Slide 2
Sources and Recommended Books:
Engines of Discovery,
Andy Sessler, Edmund (Ted) Wilson, 2014
The Fly in the Cathedral, Brian Cathcart, 2004
Big Science: Ernest Lawrence and the Invention that Launched the Military-Industrial Complex, Michael Hiltzik, 2016
The Matter of Everything: Twelve Experiments that Changed Our World, Suzie Sheehy, 2022
Fermilab Physics, the Frontier, and Megascience, Lillian Hoddeson, Adrienne W. Kolb, Catherine Westfall, 2011

## Slide 3: Outline
The scientific case for particle accelerators
The early days: the first accelerators up to 1930s
      Electrostatic accelerators, Cyclotron, early LINACs
A creative boom: the 1940s to 1960s
      Betatron, Synchrotron, FFAs
An established field and powerful tool: 1970s to today
      LINACs, superconducting technology, colliders and advances
    A few loose ends:
      The microtron, rhodotron

## Slide 4: The scientific case for particle accelerators

## Slide 5: The early 1900’s…

## Slide 6
Rutherford* gold foil experiment, 1911
*Actually Ernest Marsden and Hans Geiger
E=4.78 MeV

## Slide 7: What is the nucleus?
What is inside? (protons/neutrons not known)
How is it held together?
Why don’t electrons spiral in? (N. Bohr solved this w. QM)
Question: what were the limitations of using natural radioactive sources?

## Slide 8
Ernest Rutherford
Address to the Royal Society, 1927
“it has long been my ambition to have available for study a copious supply of atoms and electrons which have an individual energy far transcending that of the alpha- and beta-particles from radioactive bodies”
Notes: - Why couldn’t they just use radioactive sources?

## Slide 9: The early days: the first accelerators up to 1930s

## Slide 10: The 1920’s
Notes: Put the 1920’s in context!
35% of all homes had electricity, which increased to about 70% at the end of it.
Modern convenience - electric irons, toasters, refrigerators, air-conditioners, radio, television and vacuum cleaners.
In 1922 the BBC began radio broadcasting in the UK and in 1926 Robert Goddard made the first flight of a liquid fuelled rocket.

## Slide 11
Merle Tuve – Carnegie – 3MV Tesla Coil. Allibone also at Cambridge.
Thomas D. Cornell, Physics Today 41, 1, 57 (1988)
Attempts at Electrostatic Accelerators
Tesla Coil
Arno Brasch, Fritz Lange, Kurt Urban, in Italian Alps 1927-28
http://lateralscience.blogspot.com/2012/10/alpine-air-to-produce-30-million-volts.html?m=0
Lightning
Notes: They achieved 15MV and were going to move up to 30 MV when Kurt Urban was killed in a fall. They went back to lab-based transformers instead.

## Slide 12
Van de Graaff accelerator
"Van de Graaff Generator" by Omphalosskeptic
Licensed under CC BY-SA 3.0 via Commons
1930
1933 – 7MV
http://chem.ch.huji.ac.il/~eugeniik/history/graaff.html
Notes: Merle Tuve jumped on the ideas of Van de Graaff as the answer to his dreams!

## Slide 13: Gamow changes the game
George Gamow arrives at Cambridge, UK, 1929 armed with two plots
Predicts < 1MeV and as low as 200 keV sufficient based on quantum tunnelling
John Cockcroft pushes ahead

## Slide 14: The first accelerator at Cambridge
Transformer
Rectifier
Burch pump
Acceleration tube
Notes: 1930 version of the accelerator. Up to 200kV.

## Slide 15
Cockcroft-Walton accelerator: 1932
1.2 MV 6 stage Cockcroft-Walton accelerator at Clarendon Lab, Oxford University in 1948.
±V
2V
4V
Voltage multiplier circuit
https://www.youtube.com/watch?v=ep3D_LC2UzU
Cavendish Lab, Cambridge
Notes: AC signal at a point to above the source before the capacitor. Assume capacitor is charged (1V), have another 1V from the source (at +ve side of cycle). On -ve cycle, diode lets the voltage through and goes to 0 total. So this gives 2V (AC). By adding another capacitor/diode it acts as a rectifier and we get a steady 2V DC.

## Slide 16: Science context
Image: http://ck12.org.uk
Proton: 1909(?) Rutherford
Neutron: 1932, Chadwick
Splitting the atom was announced at same meeting!
NEW YORK TIMES, May 2, 1932
Notes: Shortly after, the positron was found by Carl Anderson in Cosmic Rays

## Slide 17: We missed one… Linear Accelerators (very early)
Rolf Widerøe, 1924
His PhD thesis was to realise a single drift tube with 2 gaps. 25kV, 1MHz AC voltage produced a 50keV kinetic energy beam.
First resonant accelerator (patented)
Historical note: He was influenced by Gustav Ising’s work, which was never realised in practise as Ising didn’t use an AC source.
Ising, Gustav. Arkiv Fuer Matematik, Astronomi Och Fysik 18 (4), 1928
The linear accelerator & it’s AC powering circuit

## Slide 18: Linear Accelerators (2/3)
Remember: there is no field inside a conductor
For high energy, need high frequency RF sources
Weren’t available until after WWII
But Wideroe’s idea was not quite an RF cavity, Alvarez introduced that…
Notes: Higher frequency microwave sources were unavailable until after WWII, a benefit of radar developments for the war.

## Slide 19: Boyhood friends… Ernest Lawrence and Merle Tuve

## Slide 20: Cyclotrons (1)
Cancelling out rho gives:
ie. for constant charge q and mass m, and a uniform magnetic field B, the angular frequency is constant. ie. the rf frequency can be constant. The orbit radius is proportional to speed, v.
Q. What is the issue with this statement?
Ernest Orlando Lawrence
Centrifugal force = magnetic force
Revolution frequency
Lawrence: “R cancels R!”
Notes: Lawrence came across Wideoe’s paper in a German journal and saw the diagrams, inspired with an idea.
Checked the maths: R cancels R! Found the nearest mathematician who couldn’t see a problem with it. Ran across campus screaming how he was going to be famous.
Answer: relativity! relativistic mass breaks this equality.

## Slide 21: Cyclotrons (2)
The Cyclotron, from E. Lawrence’s 1934 patent
E. Lawrence & M. Stanley Livingston
The first cyclotron
Notes: First attempt was by Niels Edelfsen

## Slide 22: A creative boom: the 1940s to 1960s

## Slide 23: Betatron
Like a transformer with the beam as a secondary coil
Usually used for relativistic electrons (so different from a cyclotron).
Max energy achieved 300 MeV
Accelerating field produced by a changing magnetic field that also serves to maintains electrons in a circular orbit of fixed radius as they are accelerated
D.W. Kerst, Phys. Rev. 58, 841 (1940)
Image: http://mysite.du.edu/~jcalvert/phys/partelec.htm#Tron
Equate Faradays law on induction & Lorentz force law gives…
since
http://physics.princeton.edu/~mcdonald/examples/betatron.pdf

## Slide 24: Blewett raises a problem: do electrons radiate?
Ivanenko & Pomeranchuk: upper limit to betatron energy around 500MeV! (1944)
Shwinger also predicted radiation (1945)
Opposing views: electrons in wires don’t radiate?
GE team searched in the radio spectrum… found nothing?

## Slide 25: Synchrotrons
“Particles should be constrained to move in a circle of constant radius thus enabling the use of an annular ring of magnetic field … which would be varied in such a way that the radius of curvature remains constant as the particles gain energy through successive accelerations” - Marcus Oliphant, 1943
Inject
Extract
t
B(t)
Typical synchrotron magnet cycle
Notes: Ernest Lawrence arrived at GE and told them of the idea for the synchrotron

## Slide 26: Synchrotrons - Phase stability
V
b
a
a - synchronous
b - arrives early, sees higher voltage, goes to larger orbit -> arrives later next time
c - arrives late, sees lower voltage, goes to smaller orbit -> arrives earlier next time
c
t
Vladimir Veksler & Ed McMillan

## Slide 27: Discovery of Synchrotron Light
GE, 1947
Goward and Barnes (UK) converted a small betatron into an 8 MeV electron synchrotron
NB. GE team were beaten to ‘first synchrotron’ by a month:
Astrophysical relevance: majority of radio sources in the universe emit via synchrotron processes!

## Slide 28: Proton Synchrotrons
The Cosmotron, BNL

## Slide 29
The Bevatron, Berkeley: discovered the antiproton

## Slide 31
Strong Focusing
Brookhaven, 1952, Livingston: Can we turn around some Cosmotron magnets?
E. Courant & H. Snyder worked out the theory…
It turned out Nikolas Christophilos (Greek engineer) had got there first and patented the idea: they later hired him.
Notes: It turned out Nikolas Chrisophilos had got there first and patented the idea: they later hired him.

## Slide 32: Strong Focusing Synchrotrons
Image courtesy of ISIS, STFC
rf cavity
dipole
magnets
quadrupole
magnets
Notes: We also ramp the quadrupoles in a synchrotron to retain focusing
In 1953, M.G. White and T. Kitigaki separately invented the separated-function strong focusing
accelerator, in which the functions of bending and focusing are done in separate magnets.

## Slide 33: “What about the Midwest?” The tale of MURA

## Slide 34: Fixed Field Alternating Gradient Accelerators (FFAs)
If the field profile is of a particular form, we call this type of FFA* a ‘scaling’ type
Alternating magnets have opposite bending fields
Beam moves radially with energy
Note that this field profile does NOT satisfy isochronicity
Formerly ‘FFAG’

## Slide 35
L. W. Jones, AIP Conference Proceedings, 237, 1 (1991)
1956

## Slide 36: LINACs & klystrons: from radar to accelerators
Russ & Sigurd Varian
Bill Hansen & team

## Slide 37: Linac Structures
F. Gerigk, CERN
DTL: Drift Tube Linac
CCL: Coupled Cavity Linac
Images thanks to Ciprian Plostinar, RAL

## Slide 38: An established field and a powerful tool: 1970s to today

## Slide 39
‘Livingston plot’
Image: http://www.slac.stanford.edu/pubs/beamline/27/1/27-1-panofsky.pdf
M. Stanley Livingston:
advances in accelerator technology increase in energy record by a factor of 10 every six years.

## Slide 40: Colliders
From: G. Pancheri, L. Bonolis, in History of Particle Colliders,
IOP History of Physics Group, 2018

## Slide 41: ISR – first hadron collider
1971 to 1984, CoM energy
62GeV
Also: stochastic cooling invented by Simon Van de Meer

## Slide 42: The Tevatron & superconducting magnets
Alvin Tollestrup
Helen Edwards
“Tevatron”= 1 TeV beam energy

## Slide 44: Accelerators: Nobel-winning pursuit
“28% of the research in physics between 1939 and 2009 has been influenced by accelerator science and that on average accelerator science contributed to a Nobel Prize for Physics every 2.9 years”*
*Haussecker, E.F., Chao, A.W. The Influence of Accelerator Science on Physics Research. Phys. Perspect. 13, 146 (2011).

## Slide 46
suzie.sheehy@physics.ox.ac.uk
suzie.Sheehy@unimelb.edu.au
Twitter: @suziesheehy
www.suziesheehy.com
My contact details:

## Slide 47
Further Reading:
Engines of Discovery,
Andy Sessler, Edmund (Ted) Wilson, 2014
The Fly in the Cathedral, Brian Cathcart, 2004
Big Science: Ernest Lawrence and the Invention that Launched the Military-Industrial Complex, Michael Hiltzik, 2016
The Matter of Everything: Twelve Experiments that Changed Our World, Suzie Sheehy, 2022
Fermilab Physics, the Frontier, and Megascience, Lillian Hoddeson, Adrienne W. Kolb, Catherine Westfall, 2011

## Slide 48
Betatrons: http://web.mit.edu/course/22/22.09/ClassHandouts/Charged%20Particle%20Accel/CHAP11.PDF
FFA history: K. R. Symon, 'The Mura Days’ https://accelconf.web.cern.ch/accelconf/p03/PAPERS/WOPA003.PDF

## Slide 49: A few loose ends:

## Slide 50: Microtron
Uses a linear accelerator structure instead of the dee electrodes of the cyclotron
Mostly used for electrons as assumes constant frequency RF & B field in the ultra relativistic limit.
Images: wikimedia commons
Veksler, I. V. (1944). "A New Method of the Acceleration of Relativistic Particles". Doklady Akad. Nauk SSSR (in Russian) 43: 346.

## Slide 51: Rhodotron
S: particle source
C: coaxial cavity
D: bending magnets
L: focusing lens
Energy gain ~ 1 MeV per crossing
Invented 1989

## Slide 52: FFAs
Proof of Principle machine built in 1999 at KEK, demonstrated 1kHz rep. rate
In the late 90’s and in 2000’s, the FFA idea was re-awakened in Japan,
Particular focus on hadron FFAs of scaling type
Recently non-scaling type driven by UK collaboration
Non-Scaling (chromatic)
EMMA, Daresbury Lab, UK
Scaling (zero-chromatic)