## Slide 1
Lecture based on previous CAS & JUAS contributions by
Daniela Kiselev, Xavier Queralt, Rüdiger Schmidt, Ivan Strasik, Markus Zerlauth...
Machine & People Protection Issues
CAS Introduction to Accelerator Physics
Kaunas, 24th of September 2022
Peter Forck
Gesellschaft für Schwerionenforschnung (GSI)
p.forck@gsi.de
For peace
and freedom

## Slide 2
The author consents to the photographic, audio and video recording of this lecture at the CERN Accelerator School. The term “lecture” includes any material incorporated therein including but not limited to text, images and references.
The author hereby grants CERN a royalty-free license to use his image and name as well as the recordings mentioned above, in order to post them on the CAS website.
The material is used for the sole purpose of illustration for teaching or scientific research. The author hereby confirms that to his best knowledge the content of the lecture does not infringe the copyright, intellectual property or privacy rights of any third party. The author has cited and credited any third-party contribution in accordance with applicable professional standards and legislation in matters of attribution.
Copyright statement and speaker’s release for video publishing

## Slide 3
Introduction and Outline
Reasons for machine protection:
Protection of the environment: Only necessary activation inside &
outside of the facility should be produced
Protection of the accelerator: Prevent for destruction of component,
prevent for down-time, destruction & cost
Enable save operation: Threshold values for reliable operation
Protection of people: Important for workers and general public, following laws
Outline of this talk:
Introduction to risk & destruction potential
Relevant atomic and nuclear physics
Definition of loss categories, passive protection
Measurements by Beam Loss Monitors
Design of Machine Protection System
Overview of personal safety

## Slide 4
What Risk is acceptable?
Risk is a factor to prepare for decisions, it is not a physical quantity:
Risk = probability of an accident x consequences
measured in terms of e.g. money, manpower, accelerator downtime, radiation pollution ....
5 Catastrophic | 5 | 10 | 15 | 20 | 25
4 Major | 4 | 8 | 12 | 16 | 20
3 Severe | 3 | 6 | 9 | 12 | 15
2 Minor | 2 | 4 | 6 | 8 | 10
1 Slight | 1 | 2 | 3 | 4 | 5
 | 1 Negli -gible | 2 Impro- bable | 3 Occa- sional | 4 Pro- bable | 5 Fre- quent
increasing risk [1... 25]
ALARA
limit of tolerance
limit of full acceptance
As Low As Reasonable Achievable
Consequences
Probability
Intolerable or acceptable depends on e.g. maintenance access, destruction level, operation
Different accelerator facilities allows different risks e.g. medical  research facilities
 Risk must be weighted to foreseen usage, goals and possible achievements

## Slide 5
What is the Risk for an Accelerators?
Categories of destruction, consequences and risk:
Heating: Lost beam heats the surrounding by its energy loss (by atomic physics)
Consequence: Material is melted and deformed  proper functionality hindered
 Type of risk: Stop of operation
Example: Destroyed insertions, leak in vacuum chamber, quench of superconducting magnet
Activation: Nuclear reaction by beam particles (nuclear physics)
Consequence: Permanent activation  pollution, human access hindered
 Type of risk: Maintenance impossible, expensive disposal
6cm
6cm
lattice atoms
incident
particle
exciting particle
Frenkel pair: Vacancy and interstitial atom
Rad-damage: Displacement from regular lattice
Radiation damage: Displacement of lattice atoms, destruction of molecules (atomic physics)
Consequence: Degradation of material properties, faulty electronics
 Type of risk: Stop of operation, exchange of equipment

## Slide 6
What is the Risk for an Accelerators?
Categories of destruction, consequences and risk:
Heating: Lost beam heat the surrounding by its energy loss (by atomic physics)
Consequence: Material is melted and deformed  proper functionality hindered
 Type of risk: Stop of operation
Example: Destroyed insertions, leak in vacuum chamber, quench of superconducting magnet
Financial aspects: High cost of additional radiation shield
Consequence: Reconstruction of buildings
 Type of risk: Insufficient budget, loss of operation permit
User requirements: Less beam available for users
 Consequence: Angry or disappointed users
 Type of risk: Cancel financial support for accelerator facility
6cm
Activation: Nuclear reaction by beam particles (nuclear physics)
Consequence: Permanent activation  pollution, human access hindered
 Type of risk: Maintenance impossible, expensive disposal
Radiation damage: Displacement of lattice atoms, destruction of molecules (atomic physics)
Consequence: Degradation of material properties, faulty electronics
 Type of risk: Stop of operation, exchange of equipment
lattice atoms
incident
particle
exciting particle
Frenkel pair: Vacancy and interstitial atom
Rad-damage: Displacement from regular lattice

## Slide 7
Stored Beam Energy at Accelerators
Examples: Energy of 1MJ correspondence:
1 MJ is the kinetic energy of 2600 kg with an velocity of 100 km/h
1 MJ can heat and melt 1.5 kg of copper [equals cube (5.5 cm)3]
1 MJ is liberated by the explosion of 0.25 kg TNT
LINAC: 1 MW delivered within 1 s equals to 1MJ
Beam power on fixed target proton accelerator:
LINACs, cyclotrons or extraction from synchrotrons
Stored beam energy within a synchrotron:
Mainly large circular collider
Courtesy M. Lindroos & R. Schmidt, JIAS 2014 on beam loss, CERN-2016-002
IFMIF
LIPAc
10 MW
1 MW
0.1 MW
0.1
1
10
100
Proton beam energy [GeV]
Average beam current [mA]
10
1
0.1
0.01
damage threshold
Cu
Tmelt=1080 0C
 = 8.9 g/cm3

## Slide 8
Outline
Outline of this talk:
Introduction to risk & destruction potential
Relevant atomic & nuclear physics
Definition of loss categories, passive protection
Measurements by Beam Loss Monitors
Design of Machine Protection System
Overview of personal safety

## Slide 9
Size of nucleus: rnucl  3 fm
 very probable reactions have  geo
Overview: Interaction of Particles and Photons with Matter
Interaction with matter
General:
Charged particles interacts with electrons
 shorter range
Neutrons ionizes only indirectly
 longer range
Atomic processes have larger cross section
than nuclear processes
‘Geometrical‘ cross section:
Hard balls’ ‘geometrical‘ cross section:
geo =  (ra + rb)2 for any ‘reaction’
ra+rb
ra
rb
‘beam’
factor 108
Mean free path:
n target atom density [cm-3], M molar mass,  density, NA Advogadro number
A: e-
N: reac. if E10MeV/u
A: e-, X-ray, 
N: reaction
, e-
e-

A: e-,X-ray, Compton
N: nuclear reaction,
neutron, pair-prod.
e-


e+
n
neutron
recoil p
capture

, ion
E < 10MeV
e-
A: non
N: elastic scattering
nuclear excitation
A: e-
N: nuclear excitation
hadronic shower
spallation
fast proton
& ions
e-

n, p
material
A = atomic reaction
N = nuclear reaction
Cross section geo comparable to size:
Size of atom: rBohr = 0.053 nm

## Slide 10
Range:
with approx. scaling
Source
LINAC, Cycl.
Synchrotron
Energy Loss of Ions in Copper
Numerical calculation for ions
with semi-empirical model e.g. SRIM
Main modification
This is an atomic physics process:
1. Projectile ions liberates fast electrons
2. Thermalization by collisions
with further electrons
3. Transfer of energy to lattice (phonon)
 Heating of target
Bethe-Bloch formula:
(simplest formulation)
Notes: 10

## Slide 11
Energy Loss and Heating: Calculations
General method of calculation (simplified):
1. Differential energy loss: by Bethe-Bloch via codes like SRIM, LISE, FLUKA, MARS...
2. Energy deposition: with N: number of particles , A: cross section
3. Temperature rise: for short bunches; : mat. density, cp specific heat
4. Further material response: Melting, evaporation, pressure and stress .... via e.g. ANSYS
5. Secondary particles: Nuclear reactions, fragmentation, spallation, shower....  discussed later
beam
range R(Ekin)
Proton Ekin = 50 TeV
size x = 0.2 mm
Y. Nie et al., Phys Rev AB 20, 081001 (2017)
Example: Proton in copper target calc. with FLUKA
Proton Ekin = 50 MeV
size x = 0.2 mm
secondary
particle

## Slide 12
Energy Loss and Heating: Calculations
Example: Proton in copper target at central path
r = 0
FCC
LHC
SPS
PS
PS-Booster
LINAC
Proton Ekin = 50 TeV
size x = 0.2 mm
Y. Nie et al., Phys Rev AB 20, 081001 (2017)
Example: Proton in copper target calc. with FLUKA
Proton Ekin = 50 MeV
size x = 0.2 mm
secondary
particle
Remark: Low energetic proton have large energy deposition at short range e.g. Ekin = 50 MeV
Energy deposition [GeV/cm3 ]
Proton:
Ekin = 7 TeV
2808 bunch
380 MJ energy
at center r = 0

## Slide 13
Beam Dump for high Intensity Beams
Extraction of LHC within one turn 86 µs
on the beam dump (simulation):
Beam dump at LHC:
rise time 3 µs
R. Schmidt et al., New J. Phys. 8, 290 (2006)
Beam dump at LHC:
7m long,  0.7 m, graphite
900 tons of concrete shielding
depth 20 cm
Tmax = 750 oC
T [oC]

## Slide 14
Nuclear Physics Processes for Protons
Nuclear reactions via spallation for protons with Ekin  1 GeV (simplified):
Pre-equilibrium phases: -exchange within  10-22 s with Ekin > 20 MeV  hadronic shower
  10-22 s
  10-18 s
forward peaked
Ekin > 100 MeV
D. Kiselev, CAS 2011
General properties:
Binding energy:
 5 MeV outer nucleons
 50 MeV inner nucleons
for Ekin >> 100 MeV
comparable for n & p

## Slide 15
Nuclear Physics Processes for Protons
Nuclear reactions via spallation for protons with Ekin  1 GeV (simplified):
Pre-equilibrium phases: -exchange within  10-22 s with Ekin > 20 MeV  hadronic shower
Inter-nuclear cascade: Evaporation of n, p, d,  within  10-18 s with Ekin  1 – 10 MeV
Fission for heavy nuclei
 &  decay of nuclei with long lifetime  >> 10-9 s
Result on long term t > 1 ms: Radioactive nuclei = activation
  10-22 s
  10-18 s
forward peaked
Ekin > 100 MeV
D. Kiselev, CAS 2011
General properties:
Binding energy:
 5 MeV outer nucleons
 50 MeV inner nucleons
for Ekin >> 100 MeV
comparable for n & p

## Slide 16
Nuclear Physics Processes for Protons
Nuclear reactions via spallation for protons with Ekin  1 GeV (simplified):
Pre-equilibrium phases: -exchange within  10-22 s with Ekin > 20 MeV  hadronic shower
Inter-nuclear cascade: Evaporation of n, p, d,  within  10-18 s with Ekin  1 – 10 MeV
Fission for heavy nuclei
proton kinetic energy Ekin [MeV]
1
100
1.000
10.000
range [cm]
0.1
1
10
100
1.000
nuclear reaction probability [%]
0.1
1
10
100
0.01
Nuclear reaction probability:
10
R.H. Thomas, in Handbook on Acc. Phy. & Eng.
Thick target: Penetration depth comparable to range
forward peaked
Ekin > 100 MeV
Ekin  1 MeV
Neutron yield per proton:
proton kinetic energy Ekin [MeV]
10
100
1.000
10.000
neutrons per proton
10-3
10-4
10-2
10-1
100
101
102

## Slide 17
Nuclear Physics Processes for Protons
Impact of protons with Ekin > 100 MeV at beam pipe or dump:
Hadronic shower
Beam fragmented nuclei, secondary nuclei
Fast and slow n, p, d,  ...
 &  decay of target nuclei
on long time scale
Vacuum pipe might by ‘thick target’
due to gracing incident
Example of cross section for protons on steel beam pipe:
Reaction: Fe + p  54Mn + something
[ 100 mb  geo ]
54Mn lifetime t1/2 = 312 days
Electron capture E = 1.3 MeV to 54Cr (excited)
with X-ray emission of E = 0.54 MeV
54Cr decay via  emission E = 0.83 MeV
activation of beam pipe
Remark: Comparable cross section for fast neutrons
 constant
Coulomb
barrier
nuclear resonances
D. Kiselev, CAS 2011
Courtesy I. Strasik
Coulomb barrier:
Kinetic energy required to overcome the electric potential to reach a distance for nuclear force fm

## Slide 18
Tolerable Beam Losses
Rule of thumb for proton beam with Ekin > 100 MeV:
‘Beam loss below 1 W/m enables hands-on maintenance’
Example: 1 W/m  6 x 109 protons/(ms) at 1 GeV
Care: Most energy is lost by atomic process,
while activation depends on nuclear physics
 dependence on projectile and target
Simulation for 1 W/m losses for 1 GeV/u impact:
100 days irradiation
of stainless steel No. 304
[ Fe(70%), Cr(18%), Ni(10%), Mn(2%) ]
Decrease of activation:
 10% after  1 year
Isotope mixture same for all ions
highly activated material
needs significant ‘cool down’ time
Simulation for 1 GeV proton irradiation:
Stainless steel beam pipe after 1 W/m beam loss for 100 days & 4 h ‘cool down’
I. Strasik et al., Phys Rev AB 13, 071004 (2010)
Natural background |  1 mSv/a
Medical X-ray CT |  3 mSv
Max. for rad. workers | 20 mSv/a
0.3 mSv/h @1m
Rule of thumb: Light targets (C, Al ...) have lower activation for impact of same # particles
irradiation
‘cool down’

## Slide 19
Secondary Particle Production for Electron Beams
Processes for interaction of electrons
For Ekin < 10 MeV:
Mainly electronic stopping  X-rays, slow e−
For Ekin > 10 MeV:
Bremsstrahlungs-, forward peaked E = 5-50 MeV
 e+ + e− or μ± ..  electro-mag. showers
 Excitation of giant resonances Eres  10-30 MeV
via (, n), (, p) or (, np) with
 Fast neutrons emitted
 Neutrons: Long ranges in matter
no ele.-mag. interaction but nuclear reactions
Photo-Pion reaction: d (,0) pn or d (,-) pp
 activation at electron accelerators
LINAC
synch.
+
vi , Ei
vf , Ef
photon:
E = Ei - Ef
nucleus
electron
Bremsstrahlung
collective vibration
protons
neutrons
photon 
Giant resonance
fast n
neutron yield [neutrons/(skW)]
electron energy Ekin [MeV]
heavier
target
R.H. Thomas, in Handbook on Acc. Phy. & Eng.
Photon Energy [MeV]
Cross-section [mb]

## Slide 20
Interaction of high Energy 
At accelerators the  are originated from nuclear reactions or Bremsstrahlung for e-.
Example: Absorption in lead
Mass absorption coefficient
 density, NA Advogadro const., A atomic mass
Atomic physics (Z=target nucl. charge):
Photo-effect:  + atom  e- + atom+
approx. material scaling photo  Z4
Schematic for heavy ion e.g. lead
photo effect
Compton effect
pair
production
giant resonance
K edge
L edge
total
Courtesy C. Grupen, Xavier Queralt, JUAS
Nuclear physics:
Giant resonance:  + nucleus  n + nucleus’
small cross section but create free neutrons

brems
brems

e-
e-
e-
e+
e+
Ele.-mag. shower
material Z
e+
Compton-effect:  + atom  ’ + e- + atom+
approx. material scaling Comp  Z
Pair prod.:  + nucleus  e- + e+ + nucleus
approx. material scaling pair  Z2
Ele.-mag. shower: for high E
  (e-e+)  ’brems  (e-e+)’  ’’Brems  ....

## Slide 21
Interaction of Neutrons
Neutrons don’t interaction with electrons
Nuclear physics processes:
Elastic scattering: X(n,n)X
with X receiving recoil momentum
Radiative capture with  emission: AX (n,) A+1X
Example: Neutron on copper 63Cu
Elastic scattering: Large cross section for thermal n
Absorption: Large cross section at resonances
- emission and activation
For E >> 100 MeV comparable cross section as proton
https://t2.lanl.gov/nis/data/endf/ and Zhukov, BIW 2010
Example: Neutrons on H
e.g. H2O, organic materials
 effective moderator due to equal masses
nucleus
vrecoil
neutron
vfinal < vini
Elastic scattering
Remark: Shielding of n by plastic (‘paraffin’) or concrete
nucleus
neutron
AX (n,) A+1X

elastic:
1H (n,n) 1H
absorption =
radiative capture:
1H (n,) 2H
absorption =
radiative capture
63Cu (n,) 64Cu
64Cu lifetime 13 h
elastic:
63Cu (n,n) 63Cu
 prod.
100 MeV
0.1 MeV

## Slide 22
Outline
Outline of this talk:
Introduction to risk & destruction potential
Relevant atomic and nuclear physics
Definition of loss categories, passive protection
Measurements by Beam Loss Monitors
Design of Machine Protection System
Overview of personal safety

## Slide 23
Relevant Losses for Machine Protection
2. Irregular losses or fast losses by malfunction  avoidable losses, see below
Types of losses:
1. Regular losses or slow losses  unavoidable losses
Caused by lifetime inside synchrotron (residual gas scattering or charge exchange, Touschek ...)
Caused by halo-formation and cleaning, aperture limitation, imperfections, machine errors
Caused by multi-turn injection, slow extraction,.... known loss mechanism
 Occurs in each cycle at characteristic times and/or beam parameters
 Usually a few % of the beam intensity
Protection of sensitive components, beam abortion only required if above a certain level

## Slide 24
Regular Losses from Halo
Halo formation at synchrotrons:
Definition of halo: low density of particle
with large betatron amplitude
Caused by collective effect (e.g. space charge),
resonances or machine errors
Diffusion process (e.g. 1 µm per turn)
unstable particles are lost
Beam loss terminology: ‘uncontrolled regular loss’
Beam halo collimation system at a synchrotron
Goal: Low impurity beam
Warm synchrotron: Protection of sensitive insertions (e.g. septum)
Concentration of loss at few locations
Super-conduction synch: + quench protection of sc magnets
Collider: + well defined condition for detector at IP
 min. exp. background
  Cleaning of collisional halo particles
Concentration of loss at dedicated locations i.e. ‘controlled losses’
Courtesy I. Strasik CAS 2016
LINAC: Halo generation by long. and trans. mismatch
Goal: Quench protection of sc civilities
Remark:
Halo might have other
distribution than core
Halo formation and its
mitigation is an actual topic

## Slide 25
Goal: Beam dump prior to quench !!!
T [K]
B [T]
Jc [A/mm2]
Quench Protection for superconducting Magnets
Nb-Ti, 0.85mm
J ~ 1500-2000 A/mm2
I ~ 400 A, B = 8-9 T
’Rutherford’ cable strand
Superconducting magnets:
Beam particles energy loss
heat wires due to energy loss
Quench: Transition to normal-conducting phase
Courtesy
Gijs van Rijs
See lecture ‘Superconducting Magnets by Gijs van Rijk
Simulation of temperature increase T:
Energy deposition:
N: number of particles , A: cross section
Temperature rise:
: mat. density, cp specific heat
Temperature dependent specific heat:
Insulator:
Normal conductor:
Superconductor:
material constants
Critical temp. TC

## Slide 26
Two Stage Betatron Collimation System = active Collimation
General functionality of cleaning:
Primary stage as thin foil close to beam
 scattering of halo particles
(Coulomb scattering by Moliere formula)
Betatron amplitude increases
Max. extension after
µ  900 or 2700 betatron phase
Secondary collimator as absorber
more distant to beam
Example:
4.7 GeV scattering in L=1 mm Tungsten foil
Courtesy I. Strasik CAS 2016
foil
thickness L
proton

scattered proton

## Slide 27
LHC Collimator Hardware
LHC Collimator system:
Primary stage
Secondary & tertiary stage
Absorbers
in total 110 movable devices
beam
1.2 m
LHC maximal losses for 6.5 TeV protons:
Total stored power 300 MJ
Max. energy deposition in sc magnet: 0.1 J/cm2
Corresponding to 6x107 protons
Or 2x10-7 of the stored beam of 3x1014 protons
Actuation system
RF contact system
Jaw Assembly
Cooling system
Vacuum Vessel
coutesy R.Losito
1.2 m
beam

## Slide 28
LHC Collimator System
1
1
1z
1
1
1
1
1
1
1
3600 BLM
100 Collimators
IP7:
transverse
cleaning
IP3:
long.
cleaning
at
dispersive
region
LHC Collimator system:
Primary stage as close as  5beam  1 mm
Secondary & tertiary stage made of carbon
Absorbers made of tungsten alloy
 in total 110 movable devices
moving e.g. from injection r = 5 mm  1 mm
Test of functionality:
Loss concentrated at collimators
Experimental verification: Single bunch excitation
Result: Main losses concentrated at collimators
IP7
IP1
IP3
IP5
Cleaning efficiency:
 = (protons lost at collimator) / (total beam loss)
Result:  = 99.8 % reached
Courtesy M. Zerlauth, CAS 2018
S. Redaelli, JAS CERN-2016-002

## Slide 29
Collimation at LINACs
Halo development at LINACs caused by:
Higher order magnet fields (e.g. aberration)
Transverse mis-match
Off-momentum particles due to wrong acceleration
Space charge forces
Goal: Halo cutting at low energy to prevent for activation
Collimators:
Cut the beam tail in space
µ = 900 or µ = 450 betatron phase to cut angle
at least two locations required
x’
x
horizontal phase space
Betatron
phase
µ = 900
beam path s
Example: SNS LINAC
Scraping at 3 MeV
profile measurement at 40 MeV
M. Plum, CERN-2016-002
i.e. phase space distribution is not completely cut

## Slide 30
Outline
Outline of this talk:
Introduction to risk & destruction potential
Important atomic and nuclear physics
Definition of loss categories, passive protection
Measurements by Beam Loss Monitors
Design of Machine Protection System
Overview of personal safety

## Slide 31
Basic Idea of Beam Loss Monitors
Basic idea for Beam Loss Monitors B LM:
A loss beam particle must collide with the vacuum chamber or other insertions
Interaction leads to some shower particle:
e−, , protons, neutrons, excited nuclei, fragmented nuclei
Detection of these secondaries by an appropriate detector outside of beam pipe
Relative cheap detector installed at many locations
Remark: Due to grazing angle a thin vacuum chamber might be a ‘thick target’
BLM detector
front-end
electronics
digitalization
& fast analysis
interlock
display
lost beam particle
Secondary products:
Electromagnetic or hadronic shower products
Charged particles
Neutrons or 
vacuum pipe
beam

## Slide 32
Scintillators as Beam Loss Monitors
Example: Analog pulses of plastic scintillator:
 broad energy spectrum
due to many particle species and energies.
Plastics or liquids are used:
Detection of charged particles
by electronic stopping
Detection of neutrons
by elastic collisions n on p in plastics
and fast p electronic stopping.
Scintillator + photo-multiplier:
counting (large PMT amplification)
or analog voltage ADC (low PMT amplification)
Radiation hardness:
plastics 1 Mrad = 104 Gy
liquid 10 Mrad = 105 Gy
Scintillator
2x2x5 cm3
Photo-multiplier
inside
HV base
40 ns
100 mV
Analog pulses U(t)
Pulse high distribution N(U)
50 mV

## Slide 33
Cherenkov Light Detectors as Beam Loss Monitors
Advantage:
Detection of fast electrons only
not sensitive to  & synch. photons
No saturation effects
Prompt light emission
Usage: Mainly at FELs for
short and intense pulses
Cherenkov detectors:
Passage of a charged particle v faster than propagation of light v > cmedium = c /n
Technical: Quartz rod n=1.5 & photomultiplier
Example: Korean XFEL behind undulator
Cherenkov light emission:
For v > cmedium = c /n
light wave-front like a wake
broadband light emission
H. Yang, D.C. Shin, FEL Conf. 2017
beam
11mm
v t

light propagation
beam
120mm

## Slide 34
Ionization Chamber as Beam Loss Monitors
Energy loss of charged particles in gases → electron-ion pairs → current meas.
W is average energy for creation
for one e- -ion pair:
Gas | Ionization Pot. [eV] | W-Value [eV]
Ar | 15.7 | 26.4
N2 | 15.5 | 34.8
O2 | 12.5 | 30.8
Air |  | 33.8
shower particle
Sealed tube Filled with Ar or N2 gas:
Creation of Ar+-e− pairs,
average energy W = 32 eV/pair
measurement of this current
Slow time response
due to  10 μs drift time of Ar+.
Per definition: Direct measurement of dose !
15 cm
Notes: 34

## Slide 35
Ionization Chamber as BLM: TEVATRON and CERN Type
TEVATRON, RHIC type CERN type
15cm,  6 cm size 50 cm,  9 cm
Ar at 1.1 bar gas N2 at 1.1 bar
3 # of electrodes 61
1000 V voltage 1500 V
3 µs reaction time 0.3 µs
# at the synchr.  4000 at LHC
aver. distance 1 BLM each  6 m
15 cm
38 cm

## Slide 36
Ionization Chamber as BLM: CERN Type
CERN type
size 50 cm,  9 cm
gas N2 at 1.1 bar
# of electrodes 61
voltage 1500 V
reaction time 0.3 µs
# at the synchr.  4000 at LHC
aver. distance 1 BLM each  6 m
Simulation of det. efficiency by Geant4:
Most sensitive to protons,
electrons & high energy 
Low sensitive to neutrons
Calculation of lost protons by
integrating of shower composition
 Quench limit estimation
M. Stockner: PhD-Thesis, Tech. Uni. Vienna
A. North et al., HB 2010
600 particle impact
neutron
proton
electron
 ray
38 cm
one turn

## Slide 37
BF3 Proportional Tubes as BLM and for personal Protection
Detection of neutrons only with a ‘REM-counter’:
Physical processes of signal generation:
1. Slow down of fast neutrons by elastic collisions with p
2. Nuclear reaction inside BF3 gas in tube:
10B + n  7Li +  with Q = 2.3 MeV.
3. Electronic stopping of 7Li and  leads to signal.
20cm
Remark: ‘REM-counters’ are frequently used for neutron detection
outside of the concrete shield & in nuclear power plants
moderation by elastic coll. with H
nuclear reaction B(n,)Li
neutron
C. Grupen, Introduction to Radiation Protection

## Slide 38
Comparison of different Types of BLMs
Different detectors are sensitive to various physical processes
very different count rate, but basically proportional to each other
Typical choice of the detector type:
Ionization Chamber:
Advantage:
- Measurement of absolute dose
Disadvantage:
- Low signal (low , eff, no neutron detection),
- Sometimes slow, ion drift time 10 ... 100 µs
 Often used at proton accelerators
38 cm
Scintillator
2x2x5 cm3
Photo-multiplier
inside
HV base
Scintillator, Cherenkov detector:
Advantage:
- Fast current reading or particle counting
- Can be fabricated in any shape, cheap
Disadvantage:
- Need calibration in many cases
- Might suffer from radiation
 Often used at electron accelerators

## Slide 39
Placement of Beam Loss Monitors
Secondary particles and shower produces are emitted within a forward cone
(in rest-frame isotopically but due to Lorentz-transformation forward in lab-frame .
Position of detector at quadruples due to maximal beam size.
High energy particles leads to a shower in forward direction  Monte-Carlo simulation.
Example: Simulation of lost protons
at LHC at 450 GeV of lost protons:
 at focusing quad. D & x maximum
B. Dehning, JAS 2014, CERN-2016-002
dispersion
x-function
y-function
lost
protons
dipole
dipole
0
10
20
30
40
50
Beam path s (m)
quadrupole
Example: Simulation of number
of shower particles
4
Beam path s (m)
0
8
12
Beam Loss Monitors

## Slide 40
Outline
Outline of this talk:
Introduction to risk & destruction potential
Relevant atomic and nuclear physics
Definition of loss categories, passive protection
Measurements by Beam Loss Monitors
Design of Machine Protection System
Overview of personal safety

## Slide 41
Relevant Losses for Machine Protection
Types of losses:
1. Irregular losses or fast losses by malfunction  avoidable losses
Occurs only seldom i.e. have low probability
The whole beam or a significant fraction is lost
Usually within a short period of the operational cycle (e.g. injection, acceleration, extraction, ...)
 Requirement for detector system: large dynamic range
Usually caused by
 Hardware failures, inaccurate settings or control errors (magnets, cavities ...)
 Beam instabilities (wake-fields, resonances, ...)
 Manually initialized improper beam alignment
Beam abortion required to prevent for destruction via interlock generation
2. Regular losses or slow losses  unavoidable losses, discussed above
Caused by lifetime inside synchrotron (residual gas, Touschek ...),
Caused by aperture limitation, beam manipulations .....
Usually a few % of the beam intensity
Remark:
Personal safety system: Simple devices, reliable technology  based on dose threshold [Gy/s]
Machine protection: Appropriate BLMs, device specific loss threshold  might be more complex

## Slide 42
General Layout of a Machine Protection System: Design
Design criteria for a Machine Protection System:
1. Beam based: Choice of BLM detector type
Main type of radiation (protons, neutrons, electrons, muons.....)
Expected radiation level at foreseen location
Required time response (fast particle counts or short beam delivery  medium fast IC  slow IC)
Required dynamic range to detect irregular losses e.g. 6 orders of magnitude!
Required reliability & fail safe
Proton accelerators: Most often IC are used for interlock-generation
& particle counters for relative measurements (after calibration suited for interlock generation)
Electron accelerators: Scintillators and Cherenkov counters (partly due to short pulse operation)
2. Equipment based: Functionality of any relevant device must be guarantied
Magnet power supplier
rf-generators, cavity properties
Super-conducting state of magnet or cavity
Vacuum conditions
Relevant diagnostics instruments
Control system watchdog
...
Remark: In exceptional cases an interlock-source can be masked to allow for acc. operation

## Slide 43
General Layout of a Machine Protection System: Hardware
Design of a protection system:
BLM detector & analog front-end
low input signal under regular losses
large dynamic range for irregular losses
e.g. current-frequency converter
Digitalization
high time resolution (e.g. LHC 1 turn = 89 µs)
Comparison to threshold values
fast, real-time calculation (FPGA, DSP)
Generation & broadcasting of interlock signal
real-time operation required, equipment ok input
Beam permit: if not ok:
 beam abortion kicker@synchr. or chopper@LINAC
 disable next beam production
Data logging
 detailed ‘post mortem ‘storage & archiving
 error display
Generally
robust & fail-safe system required!
challenge: large dynamic range
= analog
= real-time OS
= regular OS
front- end
electronics
BLM
digi-
talization
interlock
control
kicker or chopper
beam dumping
comparison
threshold
value calc.
Accelerator
control
post mortem
achieving
equipment flags
stop beam delivery
further beam
measures
before cycle

## Slide 44
Statistics for Interlock Generation
Beam dump statistics at LHC in year 2015 and 2012 (above injection):
B. Todd et al., CERNACC- 2014-0041
D. Wollmann et al., IPAC 2016, Busan, p. 4203 (2016)
 conclusion
Beam dump LHC year 2015
Beam dump LHC year 2012
Sum: 442 dumps
Sum:536 dumps
 30 % as planned
after  10 h
 30 % due to device failure
 15 % due to increasing beam loss
15 % by
MPS tests
 15 %
unnecessary

## Slide 45
Outline
Cartoons from C. Grupen
Introduction to Radiation Protection,
Springer Verlag 2010
Outline of this talk:
Introduction to risk & destruction potential
Irelevant atomic and nuclear physics
Definition of loss categories, passive protection
Measurements by Beam Loss Monitors
Design of Machine Protection System
Overview of personal safety

## Slide 46
Radiological Quantities and Units for Humans
Basic quantities & units for personal safety:
Absorbed dose:
for each radiation type R and each tissue T
Equivalent Dose:
with weight factor wR for the radiation type R
Effective Dose:
with weight factor wT for the absorption of each tissue T
whole-body irradiation 
Neutrons: Since 2007 smooth function
Example: Organ or tissue | Sensi. | wT
Gonads | High | 0.20
Lung, stomach, colon, lens, hematopoietic &lymphatic system | Inter- mediate | 0,12
Liver, esophagus, chest, skin, muscle, hart, bone surface | Low | 0.05 to 0.01
I will not eat this fish, it has 104 Bq
My fish is fine, it has 0.3 µCi
(physical quantity)
Rad. type R | wR
 all energies | 1
e- , e+ , µ all energies | 1
Protons E > 2 MeV | 5
, heavier nuclei | 20
Neutrons: E < 10 keV 10 keV < E < 100 keV 100 keV < E < 2 MeV 2 MeV < E < 20 MeV E > 20 MeV | 5 10 20 10 5

## Slide 47
Shielding of Accelerators
Shielding of accelerator by rough rule of thumb:
Estimation of shielding by 10th-value 10
with
(disregarding any secondary particle transport)
Material |  [ | 10 [cm]
Earth | 1.8 | 128
Concrete | 2.4 | 100
Heavy concrete | 3.2 | 80
Iron | 7.4 | 41
Lead | 11.3 | 39
Material |  | 10 [cm]
Earth | 1.8 | 128
Concrete | 2.4 | 100
Heavy concrete | 3.2 | 80
Iron | 7.4 | 41
Lead | 11.3 | 39
Further rough rule of thumb:
Protons, electrons & 
are att. by heavy materials
Neutrons are scattered by hydrogen
due to same mass
Concrete contains  10%weight H2O
Nuclear reactions produces further particles
I believe we need a better shielding
Do you think these Beta-Blockers can protect us from -rays?

## Slide 48
Simplified Model Shielding of Accelerators
Simplified FLUKA calculation: 4GeV protons, iron beam dump  1m l=3.5m, concrete 1 or 3 m, 5105 particles
Courtesy S. Udrea
Results:
Primary protons are stopped in dump
 are from beam & neutrons
in the wall  10-3 attenuation at X
Protons produced from neutrons,
but partly stopped in the wall
Neutrons at X  0.3% of 1m.
Equal ‘leakage’ of n,  & p
Neutrons produced, scattered at wall
 10-3 atten. at X by distance & concrete
‘Leakage’ through opening
 well shielded
Protons stopped in wall
X
iron dump 1m
concrete 1m
beam 4 GeV protons
Result:
Mainly neutrons
and µ behind thick shield
neutron

proton
neutron
proton

3 m

## Slide 49
Realistic Example for Shielding of Accelerators
Example shielding of accelerator: Proton beam of 29 GeV for anti-proton production
Assumtion 2.5  1013 protons on 11cm long copper target
Shield: Iron (1.6 m downstream and 1 m transverse)
Concrete  8 m around beam pipe
Goal: Free access region outside i.e. equivalent dose rate H / t < 0.5 µSv/h
K.. Knie et al., IPAC 2012
beam
beam
7.3m
8.2m
15m
concrete
soil
15m
target
dump
Shielding calculations:
Required for safety procedure
Numerical calculation required
atomic, nuclear& particle
physics models
e.g. FLUKA, MARS, PHITS
see lecture by Dan Faircloth
180 m
free access H/t < 0.5 µSv/h
see lecture ‘Secondary Beams and Targets’ by D. Faircloth

## Slide 50
Categories of Locations & maximal Doses
ALARA principle:
As Low As Reasonable Achievable
Simplified categories of radiation areas:
For workers: Assumption 2000 h/a of access
Maximal dose for an radiation exposed worker:
Maximum dose for one year: 20 mSv/a
Maximum total life dose: 400 mSv
(Lethal dose for short term exposure:  4000 mSv)
Remark: Actual limits are given by national laws.
Non-designated, free access
H/t < 1mSv/a (full year) = 0.5µSv/h (for 2000 h)
Supervised zone
H/t < 3 µSv/h
Control zone
H/t < 10 µSv/h
Limit access zone
H/t < 2 mSv/h
Strict ruled access zone
H/t < 25 mSv/h
Prohibited access zone
H/t > 25 mSv/h
Control area
Surveyed radiation area

## Slide 51
Categories of Locations & maximal Doses
Proportional tube for :
30 keV < Eph < 1.3 MeV
Moderated prop. tube for n
1 eV < En < 20 MeV
Display
Status
Moderated thermo-luminescence detector for passive n-detection
Simplified categories of radiation areas:
For workers: Assumption 2000 h/a of access
Non-designated, free access
H/t < 1mSv/a (full year) = 0.5µSv/h (for 2000 h)
Supervised zone
H/t < 3 µSv/h
Control zone
H/t < 10 µSv/h
Limit access zone
H/t < 2 mSv/h
Strict ruled access zone
H/t < 25 mSv/h
Prohibited access zone
H/t > 25 mSv/h
Control area
Surveyed radiation area
 conclusion
Maximal dose for an radiation exposed worker:
Maximum dose for one year: 20 mSv/a
Maximum total life dose: 400 mSv
(Lethal dose for short term exposure:  4000 mSv)
Remark: Actual limits are given by national laws.

## Slide 52
Natural Radiation Exposure
Example of radiation level:
Natural geological dose up to 10 mSv/a:
Mainly due to rare gas Radon from decay chain
without significant increase of diseases
Source: German Bundesamt für Strahlenschutz
C. Grupen, Introduction to Radiation Protection
Natural dose in Germany:
Typical dose natural and artificial composition:
There have been rumors that Black Forest must be evacuated due to 6 mSv/a.
 conclusion
Cosmic radiation
Medical exposure
Radon & thoron
External terrestrial radiation
Ingestion

## Slide 53
Avoidable, but wildly accepted Radiation Exposure
Cosmic ray based radiation effects depend on altitude and latitude
53
Departure | Arrival | Duration | Dose
Frankfurt | San Francisco | 11.5 h | 45 - 110 µSv
Frankfurt | Rio de Janeiro | 11.5 h | 17 - 28 µSv
Source: German Bundesamt für Strahlenschutz
C. Grupen, Introduction to Radiation Protection
 conclusion
Bearth
Radiation from the rock wall is even worse!
This shelter protects against cosmic rays
Radiation at 11 km altitude, year 2013
Dose [Sv/a]
terrestrial ray
cosmic ray
altitude

## Slide 54
Passive Film Badge Dosimeter and TLD
For personal safety a dosimeter should be worn!
Film badge: X-ray sensitive films
photons (typ. 5keV... 9MeV) &
 (typ. > 0.3MeV)
Sensitivity for  & : 0.1 mSv to 5 Sv
Sensitivity for  & : 0.1 mSv to 5 Sv
Thermo-luminescence dosimeter TLD:
Crystal e.g. LiF is excited by radiation and emit light when heated
neutron sensitive via 6Li(n,)T
Sensitivity for  & : 0.1 mSv to 10 Sv
Advantage: Can be archived
Disadvantage: Limited sensitivity, no online display
TLD-100:
LiF:Mg,Ti
5 x 5 mm2
Absorber
Window for -ray

## Slide 55
Active personal Dosimeter
Active dosimeters for online display
Dose measurement with alarm function,
has to be worn when entering a protected area
Ionization chambers or proportional chambers:
Alternative: PIN-diode solid state detector
Photons: typ. 10 keV... 10 MeV
 : 0.25 .... 1.5 MeV
Sensitivity for  & : 0.05 µSv/h to 1 Sv/h
‘Pocket meter’ for -rays:
Scintillator NaI(Tl) + photo-multiplier for  detection
photons (typ. 60 keV... 1.5 MeV)
Sensitivity for : 0.01 µSv/h to 100 mSv/h
Older versions: Proportional tube
Advantage: Alarm functionality, sensitive
can be archived with some efforts
Disadvantage: Expensive
(TLD sensitivity: 100 µSv to 5 Sv, flight above pole: 45...110 µSv)

## Slide 56
Summary
Many accelerator are build to produce radiation, some risk remains
Accelerator components must be protected from overheating (‘atomic physics’)
e.g. super-conducting magnet & cavities
- Particles’ energy loss must be limited and/or steered to dedicated locations
- Passive protection by collimators for protection or localizing
- Active Machine Protection System based on Beam Loss Monitors
Accelerator components must be protected from activation (‘nuclear physics’)
- Losses must be limited to certain locations e.g. collimators & beam dump
- ‘1 W/m criterion’ to limit activation for hand-on maintenance
Shield of the accelerator required
- p, ion &  best shield by high density material, but care for nuclear reactions
- e- shield for light material (lower Bremsstrahlung)
- n light material preferred
ALARA principle: Unnecessary radiation exposure to people should be avoided
Thank you for your attention!

## Slide 57
R. Schmidt (Ed.), Beam Loss and Accelerator Protection, Proc. Joint International Accelerator School
CERN-2016-002
US Particle Accelerator School – Beam Loss & Machine Protection, January 2017
http://uspas.fnal.gov/materials/17UCDavis/davis-machineprotection.shtml
D. Kiselev , Activation and radiation damage in the environment of hadron accelerators &
D. Forkel-Wirth et al., Radiation protection at CERN in R. Bailey (Ed.) Proc. CAS CERN-2013-001
A. Zhukov, BLMs: Physics, Simulation and Application in Accelerator, Proc. BIW 2010, www.jacow.org
C. Grupen, Introduction to Radiation Protection, Springer Verlag 2010
Proceedings of several CERN Acc. Schools (introduction & advanced level, special topics).
Contributions to conferences, in particular to IPAC & IBIC.
General Reading on Machine Protection

## Slide 58
Backup slides

## Slide 59
Dynamic Machine Protection by Transmission Measurement
40 μs/div
Determination of maximal loss between consecutive transformers by ‘differential current measurement’
dynamic beam interruption in case of software-
given threshold overshoot.
FPGA-electronics:
 ADC digitalization
 calculation of difference
digital comparator
chopper control in case of threshold overshoot
Ar1+ at 1.4 MeV/u
Beam chopping
after Q=44 nC
for intersecting BD
dependents on ion type
For E > 50 MeV protons: nuclear nucl quite low
 machine protection by active transmission control
H. Reeg (GSI) et al., Proc. EPAC’06
ADC
ADC
Differ-
ence
com-
parator
limits from
control system
if too high
High current:
t pulse < 10 μs only
to prevent from damage!

## Slide 60
Secondary Electron Monitor as BLM
Ionizing radiation liberates secondary electrons from a surface.
Working principle:
Three plates mounted in a vacuum vessel (passively NEG pumped)
Outer electrodes: biased by U  +1 kV
Inner electrode: connected for current measurement (here current-frequency converter)
 small and cheap detector, very insensitive.
electronics
HV electrodes
Electrode for measured
current
B. Dehning et al., PAC 2007
longitudinal impact
neutron
electron
proton

## Slide 61
D. Forkel-Wirth et al., CAS 2011, CERN-2013-001
Neutron Energy Spectrum

## Slide 62
D. Kiselev, CAS 2011, CERN-2013-001
Radiation Damage Displacements of Atoms
Low energy protons: Nuclear stopping (collision of protons with target nucleus results in recoil energy above binding energy to stopping
For Ekin > 100 MeV nearly equal cross section
Electronic stopping range
Large capture cross section
results in recoil energy

## Slide 63
Radiation Damage of organic Materials
Radiation damage in plastic by ionizing radiation:
Brake of chemical bonds and displacement of atoms
Microscopic defects in the chemical bonds
Displacement of atoms in the structural material
Example: Kapton foil of 125 µm thickness
Direct irradiation by ion beam’s
energy loss dE/dx increases for heavy ions
T. Seidl et al, HB 2010
Rough estimation of maximal dose
Material | Dose [Gy]
Teflon (PTEE) | 103
Mylar | 5104
Cable insulation | 5104
Magnet coil insul. | 106
Kapton (Polyamide) | 107
11 MeV/u

## Slide 64
Microscopic Damage of structural Materials
D. Kiselev, CAS 2011, CERN-2013-001

## Slide 65
Energy Loss and Heating: Experiment
Verification of material interaction by 440 GeV protons:
Destruction of material due to temperature rise
melting, sublimation plasma formation
mechanical stress
verification of simulation
finding proper
dump material
HiRadMat facility
at CERN SPS
Beam: 440 GeV  1013 protons,
x = y  2 mm within t = 50 µs
 Etot  1 MJ
Beam
cut
cylinders
A. Bertarelli, JAS CERN-2016-002.
Experiment with
450 GeV protons:
V. Kain et al.,
PAC’05, 1607 (2005)
6 cm
depth
20cm

## Slide 66
PIN-Diode (Solid State Detector) as BLM
Solid-state detector: Detection of charged particles.
Working principle
About 104 e−-hole pairs are created by a Minimum Ionizing Particle (MIP).
A coincidence of the two PIN reduces the background due to low energy photons.
A counting module is used with threshold value comparator for alarming.
 small and cheap detector.
2 PIN diodes:
7.5 × 20 mm2
0.1 mm thickness.
electronics

## Slide 67
Collimation at LINACs
Halo development caused by
higher order magnet fields (e.g. aberration)
transverse mis-match
off-momentum particles due to wrong focusing
space charge forces
Goal: Halo cutting at low energy to prevent for activation
Collimators:
Cut the beam tail in space
µ = 900 or µ = 450 betatron phase to cut angle
at least two locations required
x’
x
horizontal phase space
Betatron
phase
µ = 900
beam path s
x’
x
horizontal phase space
µ = 450
beam path s
µ=450
µ=450
µ=450
Example: SNS LINAC
Scraping at 3 MeV
profile measurement at 40 MeV
M. Plum, CERN-2016-002
i.e. not completely cut...