## Slide 1: RF Systems
Christine.Vollinger@cern.ch
26 September 2022
CAS - Introduction to Accelerator Physics

## Slide 2
The author consents to the photographic, audio and video recording of this lecture at the CERN Accelerator School. The term “lecture” includes any material incorporated therein including but not limited to text, images and references.
The author hereby grants CERN a royalty-free license to use his image and name as well as the recordings mentioned above, in order to post them on the CAS website.
The author hereby confirms that to his best knowledge the content of the lecture does not infringe the copyright, intellectual property or privacy rights of any third party. The author has cited and credited any third-party contribution in accordance with applicable professional standards and legislation in matters of attribution. Nevertheless the material represent entirely standard teaching material known for more than ten years. Naturally some figures will look alike those produced by other teachers.
Copyright statement and speaker’s release for video publishing

## Slide 3
Introduction
Choice of parameters for an RF system
  Frequency and voltage
RF cavity parameters
  Shunt impedance, beam loading, power coupling
Power amplifiers
  Tube or solid state
Summary
Outline

## Slide 4
Introduction

## Slide 5
Introduction
What is below?
How are RF signals generated which make the beam feel comfortable?
The radiofrequency (RF) system does the actual acceleration - it transforms a string of magnets into an accelerator
Cavity is the most visible part of an RF system
  On top of the RF system food chain
  Interacts directly with beam
  Also RF gymnastics!
Waveguide & Cavity
Power amplifier
Low-level RF
system
Beam
Beam

## Slide 6
Frequency and wavelength ranges
100 kHz 3 km
1 MHz 300 m
10 MHz
30 m
100 MHz
3 m
1 GHz
30 cm
10 GHz 3 cm
100 GHz
3 mm
SPS 200 MHz
PS main RF system
PS longitudi- nal damper
CLIC 12 GHz
Long wave
Medium/ short wave
VHF
Microwave links

## Slide 7
Amplitude ranges
1 mV
1 mV
1 V
1 kV
1 MV
1 GV
LEP: 3.6 GV total
LLRF systems
Signals from beam pick-ups
ILC and CLIC: several TV
LHC: 16 MV
Cooled hadron beams (ELENA)
Electron light
sources
SLS
LHC
Low/Medium energy hadron RF

## Slide 8
Particle velocity depends on its type:
Old television set (30 kV): Electrons at 30% of c0
            Protons just at 0.7%
Small synchrotron (500 MeV): Electrons at 99.99995%
              Protons at 75.8%
Most electron accelerators at ‘fixed’ frequency (example here: accelerator in Bonn, 1996)
Particle velocity
p+
e-
p+
e-

## Slide 9
Parameter choices

## Slide 10
Accelerator type
Linear
(single pass)
RF system for high-energy accelerators
Hadrons
Electron
Maximum RF voltage, constant velocity
Maximum RF voltage, variable velocity
Circular
(multi-pass)
Compensate synchrotron radiation losses
Sweep frequency with beam
Hadrons
Electron
*
*Exceptions (rare) exist,
e.g. “fixed frequency” acceleration in SPS
fRF = h · frev
Li = vi · TRF
Li = Distance between two adjacent gaps

## Slide 11
Choice of frequency (range), or: shall we try high or low RF frequency?

## Slide 12
Advantages | Disadvantages
Large beam aperture Long RF buckets, large acceptance Wide-band or wide range tunable cavities possible Power amplification and transmission straightforward | Bulky cavities, size scales 1/f, volume 1/f3 Lossy material to downsize cavities Moderate or low acceleration gradient Short particle bunches difficult to generate
Advantages | Disadvantages
Large beam aperture Long RF buckets, large acceptance Wide-band or wide range tunable cavities possible Power amplification and transmission straightforward | 
Why choose a low RF frequency?
  RF frequencies
  below ~200 MHz for
Mainly electrons, some hadron linear accelerators
Cyclotrons
Low- and medium energy hadron synchrotrons

## Slide 13
Advantages | Disadvantages
Reasonable cavity size scales 1/f, volume 1/f3 Break down voltage increases High gradient per length Particle bunches are short | Maximum beam available aperture scales 1/f No technology for wide-band or tunable cavities Power amplifiers more difficult Power transmission losses
Advantages | Disadvantages
Why choose a high RF frequency?
  RF frequencies above ~200 MHz used for
  Linear accelerators
  Electron storage rings
  High energy hadron storage rings

## Slide 14
Limits to maximum gradient
Surface electric field in vacuum
…
Kilpatrick 1957,
f in GHz, Ecrit in MV/m
Wang & Loew, SLAC-PUB-7684, 1997
High frequencies preferred for large gradient.
Today also other criteria are used, e.g. considering local field quantity, see: Grudiev et al., PRAB #102001 , 2009, [1] & Wuensch [2]
Ecrit [MV/m]
f [GHz]
E. Jensen
0.01
0.1
1
10
100
1000
500
200
100
50
20
10

## Slide 15
If exact RF frequency not critical, choose standard value
Off-the-shelf RF components easily available in frequency ranges used by industry.
Exchange of developments and equipment amongst research laboratories.
Exchange expertise with colleagues from other labs!
Some standard frequencies = your choice
Accelerator | Frequency
Hadron synchrotrons (PSB, PS, JPARC RCS, MR) | <10 MHz
Hadron accelerators and storage rings (RHIC, SPS) | ~200 MHz
Electron storage rings (LEP, ESRF, Soleil) | 352 MHz
Electron storage rings (DORIS, BESSY, SLS,…) | 499.6…499.8 MHz
Superconducting electron linacs and FELs (X-FEL, ILC) | 1300 MHz
Normal conducting electron linacs (SLAC) | 2856 MHz
High-gradient electron linac (CLIC) | 11.99 GHz

## Slide 16
Required RF voltage

## Slide 17
RF system expected to provide certain energy gain
On-crest acceleration
Used mostly in linear accelerators
Insufficient in a circular accelerator, (stable phase condition)
More voltage provided to avoid on-crest acceleration
Off-crest acceleration
Needed for circular accelerator
Higher voltage for given energy gain
Minimum voltage requirement


## Slide 18
Bucket area dependence on stable phase
In a circular accelerator the area in energy-time phase space (bucket area) depends on the stable phase
Below transition, fS = 0…90°
Above transition, fS = 90°…180°
Typical synchronous phase with respect to 0° or 180°
  Hadron accelerators: < 40°
  Electron storage rings: ~ 20°
H. Damerau

## Slide 19
Minimum voltage requirement (circular)
The RF system must compensate
Energy gain per turn due to changing magnetic field
Energy loss, e.g., due to synchrotron radiation (electrons)
(mp/me)4 = 18364 ~ 1.1 ∙ 1013 times less for protons
Recall talk of F. Tecker
Recall talk of L. Rivkin
Particle energy

## Slide 20
RF system overview
Waveguide & Cavity
Power amplifier
Low-level RF
system
Beam
Beam
Convert RF power into longitudinal electric field
Amplify low-power signal from beam control to kW, MW or GW
Provide RF signals with correct frequency, amplitude and phase

## Slide 21
RF system overview
Waveguide & Cavity
Power amplifier
Low-level RF
system
Beam
Beam
Convert RF power into longitudinal electric field
Amplify low-power signal from beam control to kW, MW or GW
Provide RF signals with correct frequency, amplitude and phase

## Slide 22
RF components:
Waveguide and Cavity

## Slide 23
Source: Zhang, Electromagnetic Theory for Microwaves and Optoelectronics, 2nd ed., Springer
Rectangular waveguide
Circular waveguide
Arbitrarly shaped cross-section waveguide
Waveguides are hollow metallic tubes with uniform cross-sections of different shapes.
The metallic waveguide is a completely enclosed system without any radiation loss.
Waveguides present a one-conductor system, so no TEM-mode propagation is possible. Propagation happens in TE-mode (Transverse-Electric) and TM-mode (Transverse-Magnetic). These modes have a lower frequency limit, the so-called cut-off frequency below which propagation is not possible. The cut-off frequency depends on the dimensions of the waveguide cross-section.
Waveguides
Picture source: www.pasternak.com
Waves are following the waveguide shape, even if it is bend.
Propagating waves need to fulfill boundary conditions on the waveguide walls.

## Slide 24
Rectangular Waveguide
Source: Zhang, Electromagnetic Theory for Microwaves and Optoelectronics, 2nd ed., Springer
z
b
a
a > b
The rectangular waveguide is characterized by a propagation constant, attenuation constant and characteristic impedance.
TE-modes
TE-modes are characterized by a zero electric field in propagation direction. The electric field is in the transverse plane, only.
TM-modes
TM-modes are characterized by a zero magnetic field in propagation direction. The magnetic field is in the transverse plane, only.
Modes have a cut-off frequency (no propagation below this frequency), identical for TE or TM:
The mode with the lowest cut-off frequency is called the dominant mode.
Hybrid mode happens when TE- and TM-modes start to couple.
A waveguide is called overmoded, if more than one mode is propagating in the waveguide at the same time.

## Slide 25
Fundamental and higher waveguide modes and field patterns for TE-modes
TE11-mode
TE21-mode
Simulaton pictures: courtesy E. Jensen, field pattern source: Pozar, Microwave engineering, 4th ed., Wiley
TE10-mode
Rectangular Waveguide
source: Zinke/Brunswig, Hochfrequenztechnik, 5th ed., Springer
E-field ---H-field

## Slide 26
We know the cut-off frequencies for the different modes:
z
R
 Roots of the Bessel-function for TM-mode
 Roots of the derivative of the B.F. for TE-mode
Circular Waveguide
Source: Pozar, Microwave engineering, 4th ed., Wiley
Chart of cut-off frequencies relative to fc of TE11-mode:
TM-mode
TE-mode
Simulaton pictures: courtesy E. Jensen, source pictures and chart: Pozar, Microwave engineering, 4th ed., Wiley
2nd mode is TM01. Magnetic field is transverse.
1st mode is TE11. Electric field is transverse.
Mode has 2 polarisations (orientations of the electrical field).
Notes: In 1897, the physicist John William Strutt, better known as Lord Rayleigh gave the mathematical proof that wave propagation in waveguides must be possible. This was a novum as until then, people believed that two conductors would be necessary for the transfer of electromagnetic energy. Rayleigh also gave the theory of the TE- and TM-mode patterns and the cut-off frequency, he was, however, not able to provide experimental proof at the time. The waveguide was then essentially forgotten again until the 1930s.

## Slide 27
A cylindrical cavity resonator can be seen as a section of circular waveguide shorted at both ends.
From the TE11-mode (dominant mode for circular waveguide)  TE111-mode is the dominant TE-mode for a cylindrical cavity.
TM010-mode is the dominant TM-mode for a cylindrical cavity.
TM010-mode mode is used for acceleration as it has a large electric field along the z-axis.
Electric field is described by Besselfunction J0.
z
Ez
-B
Pillbox cavity is flat compared to a “long” cylindrical cavity.
Also, beam-pipe connection is needed.
Simulation: P. Kramer
Pillbox Cavity Resonator

## Slide 28
Pillbox Cavity Resonator
Source: Pozar, Microwave engineering, 4th ed., Wiley
Resonant chart for a general cylindrical cavity shows the excited modes as a function of cavity dimensions.
1st TE-mode is TE111
1st TM-mode is TM010, and shows up for ratios (2R/h)2 > 1
For the case of the TM010-mode,
we have no dependence on cavity height,
so we get a very simple formulae:
0.383 λTM,010 = R
(2R/h)2
(2Rf)2
Ez
h
R

## Slide 29
Example “true” Pillbox Cavity
Electric field, TM010-mode
Magnetic field, TM010-mode
E. Jensen
Cavity from DORIS Storage ring (1970-ish, very early electron/positron collider)

## Slide 30
Source: Puglisi, RF-CAS 92, CERN
Enhancement of E-field
Source: Puglisi, RF-CAS 92, CERN
PS 80 MHz cavity
In practice, a “pure” pillbox cavity is not very efficient for acceleration. A simple shape modification can be done by using so-called “nose cones”.
Nose cone is a protrusion on the cavity wall that causes a concentration of the electrical field in the gap.
Pillbox Cavity Design Feature
Nose cones also help to improve the Transit-time factor…

## Slide 31
Resonators are classified by their quality factor Q.
The quality factor (or Q-value) can be used as a measure of “how well the cavity is resonating” (more details will come).
High Q-value is desired in accelerating cavities; Q-value is one of the accelerator efficiency figures-of-merit.
Q-value reduces e.g. due to the power dissipated in the metallic walls or other loss mechanisms.
The connection of the cavity resonator to the outer world will reduce its Q-value as well (we say “it loads” the cavity with an additional loss mechanism).
define
= unloaded Q
Cavity Resonators and Q-value (1/2)

## Slide 32
Example: measurements taken on the PS 80MHz pillbox cavity
We tested this cavity for Q-deterioration and shifting of its fundamental mode (~80 MHz).
Q-values obtained from 3-dB-measurement (see dashed red lines).  Plot on the top has a higher Q-value than the plot below.
Cavity Resonators and Q-value (2/2)

## Slide 33
Particle in the harmonic time-varying field will see less energy gain compared to a constant DC field.
This is called transit-time effect and is described by a factor T (so-called transit-time factor).
T =
energy gained in time-varying RF-field
energy gained in a DC field of voltage V0
Distance the particle travelled in one RF-period
Transit Time Factor (1/2)
particle with velocity v
accelerating gap
transit-time factor:

## Slide 34
Transit time factor
= constant
(as it is for an ideal pillbox cavity!)
gap length
To achieve max. energy gain from this formulae, we want that T = 1  g = 0
Leads to design request: gap as small as possible.
But other considerations as: risk of RF electric breakdown also impact on optimum gap geometry.
Note that it is assumed that the particle does not change velocity along the gap length.
Transit Time Factor (2/2)

## Slide 35
Q-value unloaded Q0 - measure of the resonance quality
energy stored in the resonator
energy dissipated in the resonator
Design goal is a high shunt impedance
“R-over-Q” [Ω] Measure of cavity acceleration efficiency at a given frequency – geometry dependent only!
Effective Shunt impedance [MΩ/m] Measure of effectiveness per unit power loss to deliver energy to a particle
Shunt impedance [MΩ] measure of effectiveness to produce an axial voltage V0
Several figures-of-merit are commonly used to characterize accelerating cavities:
Accelerator efficiency figures-of-merit (1/2)

## Slide 36
Typical values for different cavities:
Cavity type | R/Q | Q0 | R
Ferrite loaded cavity (low frequency, rapid cycling) | 4 kW | 50 | 200 kW
Room temperature copper cavity (type 1 with nose cone) | 192 W | 30 * 103 | 5.75 MW
Superconducting cavity (type 2 with large iris) | 50 W | 1 * 1010 | 500 GW
Accelerator efficiency figures-of-merit (2/2)

## Slide 37
At frequency near resonance, the cavity resonator can be modeled by a lumped-element circuit.
For a cavity with the desired high shunt impedance, only a parallel resonant circuit is suited  require to model a large voltage.
R
C
L
V
lossless resonator
power to the resonator
circuit
input impedance
lossy resistor
Power dissipated in the resistor:
Energy stored in capacitor:
Energy stored in inductor:
Cavity equivalent circuit (1/4)

## Slide 38
At frequency near resonance, the cavity resonator can be modeled by a lumped-element circuit.
For a cavity with the desired high shunt impedance, only a parallel resonant circuit is suited  require to model a large voltage.
R
C
L
V
power to the resonator
circuit
Power dissipated in the resistor:
resonance case is:
3 Parameters are sufficient
to describe the cavity
Cavity equivalent circuit (2/4)

## Slide 39
Cavity equivalent circuit (3/4)
The resonance of a cavity can be understood as simple parallel resonant circuit described by R, L, C
Resonant circuit can also be described by R, R/Q, w0 or any other set of three parameters – and this is what cavity designers use.
R
C
L
Z(w)
Dw

## Slide 40
Ez
Ez
TM010
h
a
For the case of the TM010-mode in a pillbox, where we have no dependence on cavity height, we get a very simple formulae:
Pillbox Cavity Resonators
Remember? skindepth is:
frequency
conductivity
permeability
Gives an idea of expected Q for a normal-conducting, single-gap cavity.

## Slide 41
Most common choice by cavity designers w0, R, R/Q – why?
Resonance frequency, w0
  Exactly defined for given application, e.g.,: h · frev
Shunt impedance, rsh or R
  High shunt impedance required to produce a given voltage without beam.
“R-upon-Q”, R/Q
  Defined only by the cavity geometry
  Criterion to optimize a geometry
  Detuning with beam proportional to R/Q
Cavity equivalent circuit (4/4) - Summary

## Slide 42
What about this R/Q-criteria?
Charged particle experiences cavity gap as capacitor
Goal: cavity geometry with small R/Q to reduce beam loading
q
Cavity
Beam induced voltage

## Slide 43
Example: 400 MHz cavities in LHC
Very high beam currents, need to reduce beam loading in RF cavities
Shunt impedance, R is high but small R/Q is needed
 Possible with superconducting cavities in LHC
Bell shape: R/Q ~ 44 W, 400 MHz
28 cavities, 5.3 MV/m
~o

## Slide 44
resonance frequency
unloaded Q
parallel capacitance
and inductance
R
C
L
ideal transformer
coupling loop
to generator (RF amplifier)
Generator impedance (generally complex due to matching requirement)
Zg
Beam is usually modelled as a current source and sees a (generally complex) Zshunt.
Via the transformer, the coupling to the cavity can be adjusted to “matching” / in practice, we would rotate our coupling loop to modify the coupling strength.
Zshunt 
 Zi
So-called: Inductive loading
What is Cavity loading…
z
Ez
B

## Slide 45
Principles of coupling power into a cavity

## Slide 46
Attach inductivity or capacitance of resonator, or combined
Coupling loop forms transformer with resonator inductivity
Coupling power into a cavity
C
Lc
M
RF power
L. Stigelin
Main coupler PSI cyclotron
~1 MW at 50 MHz
By far the most common method, allows also to adopt the matching.
R
L

## Slide 47
Attach inductivity or capacitance of resonator, or combined
Capacitive divider to gap to transform generator impedance to cavity shunt impedance
Advantage: allows to DC isolate the coupler (if required by amplifier).
Disadvantage: coupling is fixed.
Beam also couples capacitively via the gap
Coupling power into a cavity
R
C
L
RF power
Cc
Beam
Coupler of CERN PS 40 MHz
Coupler forms one half of capacitor with the gap

## Slide 48
Coupling through an electric antenna
Capacitive (electric) coupling
Electrical coupler to space
Power coupler of LHC cavities 300 kW at 400 MHz
Coupler antenna transmits directly into the cavity
2 MW at 540 kHz
Used to transmit radio broadcast in Hungarian language around the world.
*claims to have reached Michigan…
https://en.wikipedia.org/wiki/Transmitter_Solt

## Slide 49
Cavity Design Issues

## Slide 50
RF wavelength large below ~10 MHz: >30 m
With a pillbox design, we would need huge cavities  too large for accelerators
Line resonators: l/4 resonator
  Short circuit on one side  Voltage is zero
  Open end on other  No current but voltage
Why is this resonator so common in particle accelerators?
RF cavities in low frequency range
Voltage
Current
Transmission line, impedance ZL
l/4 length
Zin(w)
Short- circuit
Electric Open side

## Slide 51
Coaxial structure with inner conductor as beam pipe
RF cavities in low frequency range
Zin(w)
Beam axis
Short- circuit
Still rather long geometry, 7.5 m at 10 MHz
E-field
---H-field
Beam axis
Ceramic gap = electric Open
This side acts like a capacitor, we speak of capacitive loading.

## Slide 52
Coaxial structure with inner conductor as beam pipe
RF cavities in low frequency range
Add more capacitive or inductive loading
Plate capacitor
Ferrite inductivity
resonance frequency

## Slide 53
Capacitive loading in real world
Add capacitor at gap of cavity to shorten the resonator
Significantly reduces cavity size
Fixed frequency only
Adds small losses due to capacitor
Advantage: entire cavity in vacuum
NSLS, 52.88 MHz
DESY PIA, 10.4 MHz, inner cond.
Outer cond.
~1 m
ACOL, 9.53 MHz
M. Nagl

## Slide 54
Inductive loading with magnetic material shortens resonator from tens of meters to a device, lossy though
Inductive loading in real world
CERN PSB Finemet cav., 0.6-18 MHz
CERN PS, double gap, 2.8-10 MHz
Additional advantage: permeability of ferrite can be controlled by DC bias current  variable inductivity
  Cavity with programmable resonance frequency
  Essential for hadron acceleration in low-energy accelerators
M. Paoluzzi

## Slide 55
Booster Cavity, below 20 MHz
Tunable cavities – the PSB

## Slide 56
Remove inductive or capacitive loading
C. C. Friedrichs et al., PAC91, p. 1020
R. L. Madrak, IPAC16, p. 130
SSC Low Energy Booster, ~47 MHz to 60 MHz
FNAL Booster 2nd harmonic, 76 MHz – 106 MHz, 100 kV
Tunable cavities at higher frequencies
Upper frequency limit for cavities with large tuning range

## Slide 57
Tunable cavities at higher frequencies
Garnets are ferrites with a magnetic field-dependent relative permeability.
Exposed to a (slowly varying) magnetic field, their µ-value covers a certain range until they saturate.
Problems are the garnet losses (cannot be in vacuum) and the limited Q-value of the material (reduces the cavity Q).
From: Smythe, IEEE, TNS [3]
Parallel bias (= Hmag,bias is parallel HRF)
Perpendicular bias (= Hmag,bias is perpendicular HRF)

## Slide 58
Can that also work on a single-gap cavity?
Perp. bias
Par. bias

## Slide 59
tuning range
Can that also work on a single-gap cavity?

## Slide 60
Coupler to cavity
Support structure
Applying the tuning principle to a single-gap cavity
Ferrite-filled part (makes use of area of homogeneous magnetic field)

## Slide 61
RF cavities in linear accelerators
Beam only passes once  Maximize gradient
Many accelerating cells to best reuse RF voltage
Cavity is the contrary to ‘one size fits all’
Many, many more variants
SuperHILAC, ~70 MHz, Berkley
CLIC, 12 GHz, ~100 MV/m

## Slide 62
RF system overview
Cavity
Power amplifier
Low-level RF
system
Beam
Beam
Convert RF power into longitudinal electric field
Amplify low-power signal from beam control to kW, MW or GW
Provide RF signals with correct frequency, amplitude and phase

## Slide 63
Power amplifiers

## Slide 64
Power to accelerate beam  Wanted
Compensate beam-induced voltage  Refl. P
Compensate electrical losses in cavity  Heat
Compensate electrical losses in distribution  Heat
How much power is required?
(ideally)

## Slide 65
Basically
Pout = g ∙ Pin or Vout = ∙ Vin
The ideal power amplifier
  Large bandwidth: amplifies all frequencies equally
  No saturation, infinite power
  Zero delay
  No added noise
  Unconditionally stable and resistant to reverse power
  Radiation-hard
Unfortunately such a device has not been invented yet
Let us have a look at some real amplifiers
Power amplifiers

## Slide 66
Cathode and filament
Vacuum tube
Heater + Cathode
  Heated cathode
    Coated metal, carbides, borides,…
  thermionic emission
  Electron cloud
Anode
Diode
e-
e-
e-
e-
e-
Ua*
anode
e-
e-
e-
e-
e-
e-
Basics of grid tube
Ia
From diode to tetrode amplifier
E. Montesinos
*For tube amplifier designs voltages are named U instead of V

## Slide 67
Ia
Cathode and filament
Vacuum tube
Heater + Cathode
  Heated cathode
    Coated metal, carbides, borides,…
  thermionic emission
  Electron cloud
Anode
Diode! (but no amplification …yet)
e-
e-
e-
Ua
anode
Basics of grid tube
From diode to tetrode amplifier
E. Montesinos

## Slide 68
Cathode and filament
e-
e-
e-
Ua
anode
Ug1 control grid
e-
e-
e-
e-
From Diode to Triode
  Adding a negatively charged control grid (e- won’t catch)
  Modulating the grid voltage proportionally modulates the anode current
  Transconductance
    By changing the voltage at grid
    steering current at anode
  Limitations
    Parasitic capacitor from anode to control grid (g1)
    Tendency to oscillate
Basics of grid tube
From diode to tetrode amplifier
E. Montesinos

## Slide 69
Cathode and filament
e-
e-
e-
Ua
anode
Ug1 Control grid
e-
e-
Basics of grid tube
Ug2 Screen grid
Tetrode
  To avoid oscillation, add a screen grid (g2)
    Positive (lower anode)
    decouples anode from control grid g1
    Higher gain
  Limitations
    Secondary electrons due to anode bombardement
    To avoid this the anode is treated to reduce secondary emission
e-
e-
e-
e-
From diode to tetrode amplifier
E. Montesinos

## Slide 70
Tetrode based power amplifier
Ua
Anode
Grounded screen grid
RF in
RF out
Cathode and filament
Example of SPS 200 MHz amplifier, tetrode RS2004
Very simplified block diagram small signal RF going in and amplified RF coming out
Ug1 Control grid
Ug2 Screen grid
E. Montesinos

## Slide 71
Example: Tetrode amplifier driving SPS RF
Two transmitters, 2  1 MW at 200 MHz (almost continuous)
Eight tetrodes per amplifier
RS2004 tetrode
Amplifier trolley
Complete transmitter
E. Montesinos
In operation since 1976
Consists of 8 individual amplifiers.

## Slide 72
Amplifiers of the 200 MHz travelling wave system in the CERN SPS and their coaxial power lines leading to the underground installation (feeder lines)
Example: Tetrode amplifier driving SPS RF
and transfer to the cavity
Having the amplifiers on the surface and the cavity underground is only possible because no strict matching from amplifier to cavity is needed.

## Slide 73
Tetrode amplifier driving PS RF
Frequency range 2.8…10 MHz, ~60 kW per cavity, 11 units
Space constraints to have amplifier installed below cavity
Tetrode is obvious choice
  High power in small volume is needed
  Operates in radioactive environment (consists of ceramics and metal parts)
Amplifier trolley underneath cavity

## Slide 74
In a push-pull circuit the RF signal is applied to two devices
  One of the devices is acting on the positive voltage swing and off during the negative voltage swing
  The other device works in the opposite manner so that the two devices conduct half the time
  The full RF signal is then amplified and need to be recombined.
Needs two different type of devices that work as “ matched pairs” - and this cannot be obtained in RF.
Basics of RF solid state amplifiers
NPN BJT
PNP BJT
Vin
VDC
Vout
E. Montesinos
BJT: Bipolar Junction Transistor

## Slide 75
Another push-pull configuration is to use two identical transistors and a balun (balanced-unbalanced “transformer” )
  Power splitter, equally dividing the input power between the two transistors
  Balun keeps one port in phase and inverts the second port in phase (sign flip!)
Since the signals are out of phase only one device is on at a time
This configuration is easier to manufacture since only one type of BJT is required
Basics of RF solid state amplifiers
Vdc
Input balun
(Unbalanced-Balanced)
Output balun
(Balanced-Unbalanced)
0 ⁰
0 ⁰
180 ⁰
180 ⁰
NPN BJT
NPN BJT
Vin
Vout
E. Montesinos
NXP Semi- conductors AN11325 2-way Doherty amplifier with BLF888A
BJT: Bipolar Junction Transistor
Two semincoductor BJTs on one ceramic.

## Slide 76
Example: Soleil 45 kW (1st Generation)
For the electron storage ring running at 352 MHz
600 W, 300 VDC/30 VDC converter
330 W for one amplifier module
Set of splitters and combiners.
Modules are mounted into towers.
Problem: Solid state amplifiers has high current requirement → heating and high losses.
Converters need to be near by to avoid transport of high currents over long distance.

## Slide 77
Example: Soleil for 352 MHz
Large scale solid state amplifier installations
45 kW per tower (2004 and 2007)
150 kW per tower (2012)
E. Montesinos
Requires a series of power combiners to moderate power per amplifier module to several tens of kilowatts

## Slide 78
Example: BESSY II (more tranditional looks…)
500 MHz solid state amplifiers: 4  80 kW for storage ring, 40 kW for booster synchrotron
B. Schriefer
Power per module limited by RF transistors
Increasing with modern semiconductor devices
Amplifier modules
80 kW unit
Combiner

## Slide 79
1.6 MW at cavity input
Example: SPS
200 MHz solid state amplifiers: 2 amplifiers with 1.6 MW peak power, 16 towers per amplifier
E. Montesinos
80 modules per tower, 1280 modules with 5120 transistors per amplifier
Presently the largest RF installation in a particle accelerator
From LLRF
1/16 splitter

## Slide 80: All these slides were from Eric Montesinos – BIG thanks! AND to Heiko Damerau for giving additional explanations.

## Slide 81
RF power amplifier
E. Jensen
Power capability of commercially available amplifier types

## Slide 82
How to choose the right RF amplifier?
Prefer tube amplifier, when | Prefer solid-state amplifier, when
Amplifier must be installed in the accelerator tunnel Expecting important spikes from beam induced voltage Large output power of a single device is required, without combiners Not much space is available High peak power in pulsed mode Amplifier must be compact and/or close to cavity | Amplifier can be located in non-radioactive environment Circulator can be installed to protect the amplifier Delay due to unavoidable combiner stages is little issue Sufficient space can be made available Continuous operation Amplifier can be separate from the cavity
Mostly no hard criteria  decide on case by case basis

## Slide 83
Summary
RF system parameters
  Choose frequency and voltage wisely
Parameters of RF cavities
  R, R/Q
  No ‘one-size fits’ all
Power amplifier
  Ideal amplifier does not (yet) exist
  Tube or solid-state based

## Slide 84
[1] A. Grudiev, S. Calatroni, W. Wuensch: New local field quantity describing the high gradient limit of accelerating cavities, Physical Review Special Topics – Accelerators and Beams, vol. 12, no. 102001, 2009.
[2] W. Wuensch: High Gradient Breakdown in Normal-Conducting RF Cavities, CERN/PS 2002-028 (RF), http://cds.cern.ch/record/2833138/files/CERN-PS-2002-028-RF.pdf
[3] Smythe: Reducing Ferrite Tuner Loss by Bias-Field Rotation, IEEE, Trans Nuclear Science, Vol 30, no. 4, 1983.
J. W. Wang, G. A. Loew, Field Emission and RF Breakdown in High-Gradient Room-Temperature Linac Structures, SLAC-PUB-7684, 1997, http://www.slac.stanford.edu/cgi-wrap/getdoc/slac-pub-7684.pdf
W. D. Kilpatrick, Criterion for vacuum sparking designed to include both rf and dc, Rev. Sci. Instrum. 28 (1957), 1957, http://inspirehep.net/record/44645
References and Recommended Literature
Books:
POZAR, David M., “Microwave Engineering”, 4th edition, Wiley and sons.
ZHANG, Keqian, “Electromagnetic Theory for Microwaves and Optoelectronics”, 2nd edition, Springer.

## Slide 85
Walk through the CERN acceleratos by using Google street view!
PS machine
https://home.cern/science/accelerators/proton-synchrotron
Use an electronic Smith-chart!
References and Recommended Literature
Smith-Chart Software “Dellsperger”
https://www.fritz.dellsperger.net/smith.html

## Slide 86
Thank you very much for your attention!

## Slide 87: Dispersion Diagram
general dispersion relation
From origin to point on the dispersion curve
Tangent at point on the dispersion curve
vg is zero at cut-off frequency
vg is smaller than c0
vp can be larger than c0
Source: Zhang, Electromagnetic Theory for Microwaves and Optoelectronics, Springer
dispersion relation
of waveguide
From waveguide to slow wave structure…
NOTE that “we”, the RF engineers often use BETA for the imaginary part of the propagation constant (formerly “k”).

## Slide 88
RF systems
Single gap cavity
“Pillbox type”
Multiple cell cavities
Travelling wave cavities
Standing wave cavities
Multiple cell cavities
Typically used in applications with low beam loading, e.g. ring accelerators (storage rings)
Typically used in applications with high beam loading, e.g. linear accelerators (linacs)
RF-systems
RF load
source: F. Caspers et al., JUAS 2021
Notes: There are MANY ways to implement an RF system..it first good to know what we have in our toolbox and then select the best tool for the job to be done..what is beam loading? in short: how much energy stored in the cavity is taken out by the beam..per passage..

## Slide 89: Disc-loaded circular waveguide (1/2)
Disc-loaded waveguide is a circular metallic waveguide with periodically added metallic discs and holes for particle passage and for coupling of the cells.
We speak of a coupled-cavity chain structure.
EM-fields need to fulfill boundary conditions on the metallic discs.
Disc-loaded waveguide can operate in travelling-wave as slow wave structure or in standing-wave mode.
In standing wave mode, the cells present a “concatenation” of TM010-mode “pillbox”-type cavities.

## Slide 90: Disc-loaded circular waveguide (2/2)
The name of the resonant mode is given by the phase advance between two consecutive cells.
Example: Pi-mode structure in standing wave (SW) … can be derived from pillbox TM010-mode.
Source: Kramer, Studies of HOM-couplers for the Upgrades Travelling Wave Acceleration System in the CERN SPS, PhD, CERN-THESIS-2019-371
Different coupling mechanisms between the individual cells exits, either on the side or in the center.
We speak of iris-coupled-structure and slot-coupled-structure.
For slot-coupled-structures, the center opening for the beam can be very small and is often ignored in the EM-calculations.

## Slide 91: Example of Pi-mode Cavities (SW, 1/3)
0-mode structure
source: F. Gerigk, CAS Ebeltoft, Cavity Types, 2010
Alvarez-type linac (= drift-tube-linac)
How does this work?
Remember: The name of the resonant mode is given by the phase advance between two consecutive cells.
Pi-mode structure
Wideroe-type linac (= drift-tube-linac)

## Slide 92: Example of Pi-mode Cavities (SW, 2/3)
How does this look in reality?
Slot-coupled-structure (PIMS) at CERN
Picture of Linac1, CERN
sources: P. Bourquin et al., Development Status of the Pi-mode Accelerating Structure (PIMS) for LINAC4, Proc. Of LINAC08, Canada.
C. Plostinar (ed.), Comparative Assessment of HIPPI Normal Conducting Structures, CARE-report-2002-0771
Drift tube structure, CERN
Note that a ‘cell’ is not necessarily a pillbox-type shape. In drift tube structures, a cell is the area between two drifttubes and looks in principle like a pillbox with nose cones.

## Slide 93: Example of Pi-mode Cavities (SW, 3/3)
Slot-coupled-structure (PIMS) at CERN
Picture sources: CERN cds
R. Wegner et al., Linac4 PIMS Construction and First Operation, IPAC2017, Copenhagen.
P. Bourquin et al., Development Status of the Pi-mode Accelerating Structure (PIMS) for LINAC4, Proc. Of LINAC08, Canada
PIMS cell
PIMS test set-up
Completed LINAC4, CERN

## Slide 94: Waveguide becomes Slow Wave Structure
To get power transferred to the beam, the accelerating field needs to be kept in phase with the charged particle.
For single gap cavities, this means that the resonance needs to be synchronous with the particle phase. We can then concatenate many “pillbox cavities” to one multi-cell pattern.
Another way to reduce phase velocity is to build the disc-loaded waveguide where discs are added in a periodic pattern (schematic pictures look the same).
As for the concatenated “pillbox cavities”, a multi-cell pattern builds up. The addition of discs inside the cylindrical waveguide induces multiple reflections between the discs and results in a change of the dispersion curve. The structure can then be used in travelling wave mode.
If the wave is travelling with speed-of-light, and we slow down this wave (=reduce phase velocity), we obtain so-called slow wave structures (SWS).
Slow wave structures are known from dielectrics (where the EM-wave slows down due to permittivity ), but here we will discuss slow-wave structures with metallic boundaries used for particle acceleration.

## Slide 95: Slow wave structure (1/7)
source: G. Dome, RF Systems: Waveguides and Cavities, aip-conf-proc.153-1296
Slow wave structures work in the range of vp< c0.
The addition of discs inside the cylindrical waveguide induces multiple reflections between the discs and results in a change of the dispersion curve.
The disc-loaded structure can then be used in travelling wave mode. The dispersion curve changes from continuous to splitting up into different modes which are slowed down. We speak of pass-bands. These modes are separated by stopbands.

## Slide 96: Slow wave structure (2/7)
Dispersion Curves, phase- and group velocity for FW and BW wave in periodic structure.
Forward wave (FW) vg and vp point in the same direction.
Backward wave (BW)
vg and vp point in the opposite direction.
Source: Zhang, Electromagnetic Theory for Microwaves and Optoelectronics, Springer
For the advanced RF-fans: 1. All guides modes in common transmission lines, metallic and dielectric waveguides are forward waves.
2. For transmission lines of “high-pass filter” type, the phase constant β decreases with increasing frequency.
3. “High-pass filter” type lines are modelled with a distributed series capacitance and a shunt inductance (i.e., opposite of what is usually done in the transmission line modelling!).
4. Forward and backward type of waves – this makes no difference for the direction of the beam.

## Slide 97: Slow wave structure (3/7)
Dispersion diagram of periodic structure (uniform waveguide is shown for orientation)
source: M. Weiss, Introduction to RF Linear Accelerators.
Dispersion diagram shows the periodicity of the structure.
For a given mode, there is a limited pass band of possible frequencies.
The passbands are separated by stopbands where the specific mode cannot propagate.
At both ends of the passband, the group velocity is zero and wave propagation stops.
When group velocity and phase velocity are in the same direction, we speak about forward waves, if they are in different direction, we speak about backward waves. This has nothing to do with the direction of the particle travelling.

## Slide 98: Slow wave structure (4/7)
Source: Zhang, Electromagnetic Theory for Microwaves and Optoelectronics, Springer
The Floquet Theorem describes the relation between the phase constant of the n-th space harmonic and is a fundamental theorem of periodic structures.
The request to fulfill the periodic boundary conditions leads to the concept of space harmonics (instead of wave modes).
Space harmonics are closely connected the so-called Floquet Theorem (we will not cover this here).

## Slide 99: Slow wave structure (5/7)
As was shown before, drift tubes can be used instead of separating discs to slow down the EM-field. The theory for drift tubes is very similar to calculating a slot-coupled structure. Just imagine that the slot is very large.
In travelling wave (TW) mode, the field propagates through each cell.
The phase advance per cell (distance between the discs, or periodic spacing of drift tubes) determines the length of the cell:
Remember? Is distance that a particle travels during one RF-period.
Inside view of the SPS travelling wave structure © CERN.

## Slide 100: Slow wave structure (6/7)
The only missing component for our travelling wave system are the input and output couplers.
These have to be matching the structure to avoid that standing waves are building up inside the periodic structure.
Often, higher order modes (HOMs) are building up in the structure due to the finite length (end covers are put there). Note that a matching network is used to obtain the travelling state. This network is only matching the fundamental mode and not the HOMs! I.e. the fundamental mode is travelling, others might be travelling, partially travelling or standing modes.

## Slide 101: Slow wave structure (7/7)
Backward wave structure
SPS 200 MHz travelling wave cavity (16m long).
beam direction
RF IN side
RF OUT side
Water cooled coaxial load
Drift tube
with water cooling
© CERN

## Slide 102: 200 MHz TWC of SPS (1/2)
courtesy: E. Montesinos, CERN
Cavity is part of the LHC injector chain and was upgraded recently and equipped with new power amplifiers to reach a higher accelerating voltage.
The cavity was entirely modelled in CST, so that we could well see the fields of the fundamental and the HOMs.
Single cell CST model with symmetries (no HOM coupler)
Electric field of fundamental mode in the
Cross-section
Surface currents on the
Drift tube
E-field in a cell with HOM-coupler (22π/33 mode)
Modelling in CST
(P. Kramer, CERN)

## Slide 103: 200 MHz TWC of SPS (2/2)
courtesy: E. Montesinos, CERN
Cavity is part of the LHC injector chain and was upgraded recently and equipped with new power amplifiers to reach a higher accelerating voltage.
A number of HOMs are developing, mostly as standing wave and these were taken out by HOM-couplers. Most harmful was the mode at 630 MHz, each section of the cavity has a number of these Hom couplers installed:
E-field pick-up probe
Schematic illustration
Modelling in CST
(P. Kramer, CERN)