## Slide 1: Injection and Extraction (+Kickers, Septa)
Introduction: Kickers, septa and normalised phase-space
Injection methods
  Single-turn hadron injection
  Injection errors, filamentation and blow-up
  Multi-turn hadron injection
  Charge-exchange H- injection
  Lepton injection
Extraction methods
  Single-turn (fast) extraction
  Non-resonant and resonant multi-turn (fast) extraction
  Resonant multi-turn (slow) extraction
Linking machines
Frank Tecker, CERN (ATS-DO)
based on lectures by Matthew Fraser and M.J. Barnes, W. Bartmann, J. Borburgh, V. Forte, B. Goddard, V. Kain and M. Meddahi
Many THANKS!!

## Slide 2: Injection and extraction
An accelerator has limited dynamic range
Chain of stages needed to reach high energy
Periodic re-filling of storage rings, like LHC
External facilities and experiments:
  e.g. ISOLDE, HIRADMAT, AWAKE…
Beam transfer (into, out of, and between machines) is necessary.
CERN Accelerator Complex

## Slide 3: Basics: injection, septum and kicker
Septum magnet
Kicker magnet
Kickers produce fast pulses, rising their field within the particle-free gap in the circulating beam (temporal separation)
Septa compensate for the relatively low kicker strength, and approach closely the circulating beam (spatial separation)
F-quad
t
kicker field
intensity
injected
beam
Injected beam
Circulating beam
D-quad

## Slide 4: Google
Kicker
Septum
…so we also call them “Fast Pulsed Magnets”

## Slide 5
Kickers - Magnetic parameters
B
HV conductor
Vertical aperture, Vap
Ferrite
HV
Return conductor
Horizontal
aperture, Hap
Magnetic field
Derivation: remember Ampère’s Law:
Magnet inductance
[per unit length]
Derivation: remember Faraday’s Law:
and
Dimensions Hap and Vap specified by beam parameters at kicker location
Ferrite (permeability μr ≈ 1000) reinforces magnetic circuit and field uniformity in the gap
For fast rise-times the inductance must be minimised: typically the number of turns, N = 1
Kickers are often split into several magnet units, powered independently
μr
μ0
A C-core geometry,
commonly used at CERN
Pulsed magnet with very fast rise time (<100 ns – few μs)

## Slide 6: Magnetic and electrostatic septum
Magnetic
Septum coil: 2 – 20 mm
Electrostatic
Thin wire or coil: ~0.1 mm
E = V / g
Typically V = 200 kV
E = 100 kV/cm
E0
E=0
High voltage
electrode
Hollow earth
electrode
Thin wire or
foil
g
circulating
beam
circulating
beam
Bo = μ0I / g
Typically I 5 - 25 kA
Septum coil
return coil
B=0
B0

## Slide 7: Single-turn injection – same plane
Septum deflects the beam onto the closed orbit at the centre of the kicker
Kicker compensates for the remaining angle
Septum and kicker either side of D quad to minimise kicker strength
Septum magnet
Kicker magnet
F-quad
t
kicker field
intensity
injected
beam
‘boxcar’ stacking
Injected beam
Circulating beam
D-quad

## Slide 8: Normalised phase space
Transform real transverse coordinates (x, x’, s) to normalised co-ordinates ( , , ) where the independent variable becomes the phase advance μ:

## Slide 9: Normalised phase space
x(s)
x’(s)
Area = pe
Area = pe

Real phase space
Normalised phase space

## Slide 10: Single-turn injection
Septum magnet
Kicker magnet
Injected beam
Circulating beam
D-quad
Normalised phase space at centre of idealised septum

## Slide 11: Single-turn injection
septum
Septum magnet
Kicker magnet
Injected beam
Circulating beam
D-quad
Normalised phase space at centre of idealised septum

## Slide 12: Single-turn injection
90o betatron phase advance to kicker location
Septum magnet
Injected beam
Circulating beam
D-quad
Kicker magnet

## Slide 13: Single-turn injection
Kicker deflection places beam on central orbit:
Normalised phase space at centre of idealised kicker
kicker
Septum magnet
Injected beam
Circulating beam
D-quad
Kicker magnet

## Slide 14: Injection oscillations
kicker - Δ
For imperfect injection the beam oscillates around the central orbit,
e.g. kick error, Δ:

## Slide 15: Injection oscillations
After 1 turn…
For imperfect injection the beam oscillates around the central orbit,
e.g. kick error, Δ:

## Slide 16: Injection oscillations
After 2 turns…
For imperfect injection the beam oscillates around the central orbit,
e.g. kick error, Δ:

## Slide 17: Injection oscillations
After 3 turns etc…
For imperfect injection the beam oscillates around the central orbit,
e.g. kick error, Δ:

## Slide 18: Injection oscillations
Betatron oscillations with respect to the Closed Orbit:
Transfer line
LHC (first turn)
Horizontal
Vertical
Angular errors from septa and kicker have different orbit pattern
Correct the difference between injected beam and closed orbit or 1st and 2nd turn

## Slide 19: Filamentation

## Slide 20: Filamentation

## Slide 21: Filamentation

## Slide 22: Filamentation

## Slide 23: Filamentation

## Slide 24: Filamentation

## Slide 25: Filamentation

## Slide 26: Filamentation

## Slide 27: Filamentation

## Slide 28: Filamentation

## Slide 29: Filamentation
Non-linear effects (e.g. higher-order field components) introduce amplitude-dependent effects into particle motion
Over many turns, a phase-space oscillation is transformed into an emittance increase
So any residual transverse oscillation will lead to an emittance blow-up through filamentation
  “Transverse damper” systems are used to damp injection oscillations - bunch position measured by a pick-up, which is linked to a kicker
  Chromaticity coupled with a non-zero momentum spread at injection can also cause filmentation, often termed chromatic decoherence
See appendix for derivation of the emittance increase

## Slide 30: Filamentation - Decoherence
Residual transverse oscillations lead to an effective emittance blow-up through filamentation.
Due to tune spread and energy spread, the oscillation will not be seen for long on a BPM signal:
Injection oscillation
Reference closed orbit

## Slide 31: Multi-turn injection
For hadrons the beam density at injection can be limited either by space charge effects or by the injector capacity
If we cannot increase charge density, we can sometimes fill the horizontal phase space to increase overall injected intensity.
  Cannot inject into same phase space area, as we would kick out the beam located there
  If the acceptance of the receiving machine is larger than the delivered beam emittance we can accumulate intensity

## Slide 32: Multi-turn injection for hadrons
Septum magnet
No kicker but fast programmable bumpers
Bump amplitude decreases and a new batch injected turn-by-turn
Phase-space “painting”
Programmable closed orbit bump
Varying amplitude bump
Injected beam
(usually from a linac)
Circulating beam

## Slide 33: Multi-turn injection for hadrons
Turn 1
Septum
Example: CERN PSB injection from Linac 2, fractional tune Qh ≈ 0.25 Beam rotates π/2 per turn in phase space
On each turn inject a new batch and reduce the bump amplitude

## Slide 34: Multi-turn injection for hadrons
Turn 2
Septum
Example: CERN PSB injection, high intensity beams, fractional tune Qh ≈ 0.25 Beam rotates π/2 per turn in phase space

## Slide 35: Multi-turn injection for hadrons
Turn 3
Septum
Example: CERN PSB injection, high intensity beams, fractional tune Qh ≈ 0.25 Beam rotates π/2 per turn in phase space

## Slide 36: Multi-turn injection for hadrons
Turn 4
Septum
Example: CERN PSB injection, high intensity beams, fractional tune Qh ≈ 0.25 Beam rotates π/2 per turn in phase space

## Slide 37: Multi-turn injection for hadrons
Turn 5
Septum
Example: CERN PSB injection, high intensity beams, fractional tune Qh ≈ 0.25 Beam rotates π/2 per turn in phase space

## Slide 38: Multi-turn injection for hadrons
Turn 6
Septum
Example: CERN PSB injection, high intensity beams, fractional tune Qh ≈ 0.25 Beam rotates π/2 per turn in phase space

## Slide 39: Multi-turn injection for hadrons
Turn 7
Septum
Example: CERN PSB injection, high intensity beams, fractional tune Qh ≈ 0.25 Beam rotates π/2 per turn in phase space

## Slide 40: Multi-turn injection for hadrons
Turn 8
Septum
Example: CERN PSB injection, high intensity beams, fractional tune Qh ≈ 0.25 Beam rotates π/2 per turn in phase space

## Slide 41: Multi-turn injection for hadrons
Turn 9
Septum
Example: CERN PSB injection, high intensity beams, fractional tune Qh ≈ 0.25 Beam rotates π/2 per turn in phase space

## Slide 42: Multi-turn injection for hadrons
Turn 10
Septum
Example: CERN PSB injection, high intensity beams, fractional tune Qh ≈ 0.25 Beam rotates π/2 per turn in phase space

## Slide 43: Multi-turn injection for hadrons
Turn 11
Septum
Example: CERN PSB injection, high intensity beams, fractional tune Qh ≈ 0.25 Beam rotates π/2 per turn in phase space

## Slide 44: Multi-turn injection for hadrons
Turn 12
Septum
Example: CERN PSB injection, high intensity beams, fractional tune Qh ≈ 0.25 Beam rotates π/2 per turn in phase space

## Slide 45: Multi-turn injection for hadrons
Turn 13
Septum
Example: CERN PSB injection, high intensity beams, fractional tune Qh ≈ 0.25 Beam rotates π/2 per turn in phase space

## Slide 46: Multi-turn injection for hadrons
Turn 14
Septum
Example: CERN PSB injection, high intensity beams, fractional tune Qh ≈ 0.25 Beam rotates π/2 per turn in phase space

## Slide 47: Multi-turn injection for hadrons
Turn 15
In reality, filamentation (often space-charge driven) occurs to produce a quasi-uniform beam
Phase space has been “painted”

## Slide 48: Charge exchange H- injection
Multi-turn injection is essential to accumulate high intensity
Disadvantages inherent in using an injection septum:
  Width of several mm reduces aperture
  Beam losses from circulating beam hitting septum:
    typically 30 – 40 % for the CERN PSB injection at 50 MeV
  Limits number of injected turns to 10 – 20
Charge-exchange injection provides elegant alternative
  Possible to “cheat” Liouville’s theorem, which says that emittance is conserved….
  Convert H- to p+ using a thin stripping foil, allowing injection into the same phase space area

## Slide 49: Charge exchange H- injection
H- beam
Injection chicane dipoles
Circulating p+
p+
Stripping foil
H0
H-
Circulating p+
Start of injection process

## Slide 50: Charge exchange H- injection
Circulating p+
Stripping foil
End of injection process with painting
H- beam
p+
H0
H-
Injection chicane dipoles
Displace orbit
Circulating p+

## Slide 51: Accumulation process on foil
V. Forte, Performance of the CERN PSB at 160 MeV with H- charge exchange injection, PhD thesis – CERN and Université Blaise Pascal
Linac4 connection to the PS booster at 160 MeV:
  H- stripped to p+ with an estimated efficiency ≈98 % with C foil 200 μg.cm-2

## Slide 52: Charge exchange H- injection
Paint uniform transverse phase space density by modifying closed orbit bump and steering injected beam
Foil thickness calculated to double-strip most ions (≈99%)
  50 MeV – 50 μg.cm-2
  800 MeV – 200 μg.cm-2 (≈ 1 μm of C!)
Carbon foils generally used – very fragile
Injection chicane reduced or switched off after injection, to avoid excessive foil heating and beam blow-up
Longitudinal phase space can also be painted turn-by-turn:
  Variation of the injected beam energy turn-by-turn (linac voltage scaled)
  Chopper system in linac to match length of injected batch to bucket

## Slide 53: H- injection - painting
Time
x’ vs x
y’ vs y
y vs x
Note injection into same phase space area as circulating beam
≈100 turns

## Slide 54: Lepton injection
Single-turn injection can be used as for hadrons; however, lepton motion is strongly damped (different with respect to proton or ion injection).
  Synchrotron radiation
    see Electron Beam Dynamics lectures by L. Rivkin
Can use transverse or longitudinal damping:
  Transverse - Betatron accumulation
  Longitudinal - Synchrotron accumulation (2 x faster than transverse)
Can be used for top-up injection (keeping constant current)
  need full-energy injector

## Slide 55: Betatron lepton injection
Beam is injected with an angle with respect to the closed orbit
Injected beam performs damped betatron oscillations about the closed orbit
Septum magnet
Closed orbit bumpers or kickers
Injected beam
Circulating
beam

## Slide 56: Betatron lepton injection
Injected bunch performs damped betatron oscillations
In LEP at 20 GeV, the damping time was about 6’000 turns (0.6 seconds)

## Slide 57: Synchrotron lepton injection
Septum magnet
Beam injected parallel to circulating beam, onto dispersion orbit of a particle having the same momentum offset Δp/p
Injected beam makes damped synchrotron oscillations at Qs but does not perform betatron oscillations
Closed orbit bumpers or kickers
Bumped circulating beam
xs = Dx · Δp/p0
xs
p = p0
p = p0 + Δp
Inject an off-momentum beam at a location with dispersion
Injected beam

## Slide 58: Synchrotron lepton injection
F
E
Double batch injection possible….
Longitudinal damping time in LEP was ~3’000 turns (2x faster than transverse)
Injection 1 (turn N)
Injection 2 (turn N + Qs/2)
Stored beam
RF bucket

## Slide 59: Synchrotron lepton injection in LEP
Synchrotron injection in LEP gave improved background for LEP experiments due to small orbit offsets in zero dispersion straight sections

## Slide 60: Injection - summary
Several different techniques using kickers, septa and bumpers:
  Single-turn injection for hadrons
    Boxcar stacking: transfer between machines in accelerator chain
    Angle / position errors  injection oscillations
    Uncorrected errors  filamentation  emittance increase
  Multi-turn injection for hadrons
    Phase space painting to increase intensity
    H- injection allows injection into same phase space area
  Lepton injection: take advantage of damping
    Less concerned about injection precision and matching

## Slide 61: Extraction
Different extraction techniques exist, depending on requirements
  Fast extraction: ≤1 turn
  Non-resonant (fast) multi-turn extraction: few turns
  Resonant low-loss (fast) multi-turn extraction: few turns
  Resonant multi-turn extraction: many thousands of turns
Usually higher energy than injection  stronger elements (∫B.dl)
  At high energies many kicker and septum modules may be required
  To reduce kicker and septum strength, beam can be moved near to septum by closed orbit bump
  Beam size scales with => smaller than injection

## Slide 62: Fast single turn extraction
Septum magnet
Kicker magnet
Bumpers move circulating beam close to septum to reduce kicker strength
Kicker deflects the entire beam into the septum in a single turn
Most efficient (lowest deflection angles required) for π/2 phase advance between kicker and septum
Closed orbit bumpers
    Entire beam kicked into septum gap and extracted over a single turn
Extracted beam
F-quad
D-quad
Circulating
beam
t
kicker field
intensity

## Slide 63: Fast single turn extraction
For transfer of beams between accelerators in an injector chain
For secondary particle production
  e.g. neutrinos, radioactive beams
Losses from transverse scraping or from particles in extraction gap:
  Fast extraction from SPS to CNGS:
Particles in SPS extraction kicker rise- and fall-time gaps

## Slide 64: Multi-turn extraction
Some filling schemes require a beam to be injected in several turns to a larger machine…
And very commonly Fixed Target physics experiments and medical accelerators often need a quasi-continuous flux of particles…
Multi-turn extraction…
  Fast: Non-resonant and resonant multi-turn ejection (few turns) for filling
    e.g. PS to SPS at CERN for high intensity proton beams (>2.5 1013 protons)
  Slow: Resonant extraction (ms to hours) for experiments

## Slide 65: Non-resonant multi-turn extraction
Extracted beam
Bumped circulating beam
Magnetic
septum
Fast bumper deflects the whole beam onto the septum
Beam extracted in a few turns, with the machine tune rotating the beam
Intrinsically a high-loss process: thin septum essential
Often combine thin electrostatic septa with magnetic septa
Fast closed orbit bumpers
    Beam bumped to septum; part of beam ‘shaved’ off each turn
Electrostatic septum

## Slide 66: Non-resonant multi-turn extraction
Example system: CERN PS to SPS Fixed-Target ‘continuous transfer’.
  Accelerate beam in PS to 14 GeV/c
  Empty PS machine (2.1 μs long) in 5 turns into SPS
  Do it again
  Fill SPS machine (11 x CPS, 23 μs long)
  Quasi-continuous beam in SPS (2 x 1 μs gaps)
  Total intensity per PS extraction ≈ 2.5  1013 p+
  Total intensity in SPS ≈ 5  1013 p+
Extracted beam
beam
To the SPS
The PS

## Slide 67: Non-resonant multi-turn extraction
CERN PS to SPS: 5-turn continuous transfer – 1st turn
Qh = 0.25
1 2 3 4 5
Bump vs. turn
1
2
3
4
5
septum

## Slide 68: Non-resonant multi-turn extraction
CERN PS to SPS: 5-turn continuous transfer – 2nd turn
Qh = 0.25
1 2 3 4 5
Bump vs. turn
1
2
3
4
5
septum

## Slide 69: Non-resonant multi-turn extraction
CERN PS to SPS: 5-turn continuous transfer – 3rd turn
Qh = 0.25
1 2 3 4 5
Bump vs. turn
septum
1
2
3
4
5

## Slide 70: Non-resonant multi-turn extraction
CERN PS to SPS: 5-turn continuous transfer – 4th turn
Qh = 0.25
1 2 3 4 5
Bump vs. turn
septum
1
2
3
4
5

## Slide 71: Non-resonant multi-turn extraction
CERN PS to SPS: 5-turn continuous transfer – 5th turn
Qh = 0.25
5
1 2 3 4 5
Bump vs. turn

## Slide 72: Non-resonant multi-turn extraction
CERN PS to SPS: 5-turn continuous transfer
  Losses impose thin septum…
  … an electrostatic septum is needed in addition to the magnetic septum
  Still about 15 % of beam lost in PS-SPS CT
  Difficult to get equal intensities per turn
  Different trajectories for each turn
  Different emittances for each turn
1
2
3
4
5
I
1
2
3
4
5

## Slide 73: Resonant multi-turn (fast) extraction
Adiabatic capture of beam in stable “islands”
  Use non-linear fields (sextupoles and octupoles) to create islands of stability in phase space
  A slow (adiabatic) tune variation to cross a resonance and to drive particles into the islands (capture) with the help of transverse excitation (using damper)
  Variation of field strengths to separate the islands in phase space
Several big advantages:
  Losses reduced significantly (no particles at the septum in transverse plane)
  Phase space matching improved with respect to existing non-resonant multi-turn extraction - ‘beamlets’ have similar emittance and optical parameters

## Slide 74: Resonant multi-turn (fast) extraction
Unperturbed beam
Increasing non-linear fields
Beam captured in stable islands
Islands separated and beam bumped across septum – extracted in 5 turns
(see Non-Linear Beam Dynamics lectures by Hannes Bartosik)
Courtesy M. Giovannozzi: MTE Design Report, CERN-2006-011, 2006

## Slide 75: Resonant multi-turn (fast) extraction
Septum wire
1 2 3 4 5
Bump vs. turn
Qh = 0.25
Unperturbed beam
Increasing non-linear fields
Beam captured in stable islands
Islands separated and beam bumped across septum – extracted in 5 turns
Courtesy M. Giovannozzi: MTE Design Report, CERN-2006-011, 2006

## Slide 76: Resonant multi-turn (slow) extraction
Extracted beam
Bumped circulating beam -
particles moved across
septum by resonance
Slow bumpers move the beam near the septum
Tune adjusted close to nth order betatron resonance
Multipole magnets excited to define stable area in phase space, size depends on ΔQ = Q - Qr
Closed orbit bumpers
    Non-linear fields excite resonances that drive the beam slowly across the septum
Magnetic
septum
Electrostatic septum

## Slide 77: Resonant multi-turn (slow) extraction
3rd order resonances – see lectures by Hannes Bartosik
  Sextupole fields distort the circular normalised phase space particle trajectories.
  Stable area defined, delimited by unstable Fixed Points.
  Sextupole magnets arranged to produce suitable phase space orientation of the stable triangle at thin electrostatic septum
  Stable area can be reduced by…
    Increasing the sextupole strength, or…
    Fixing the sextupole strength and scanning the machine tune Qh (and therefore the resonance) through the tune spread of the beam
    Large tune spread created with RF gymnastics (large momentum spread) and large chromaticity
Rfp

## Slide 78: Third-order resonant extraction
Particles distributed on emittance contours
ΔQ large – no phase space distortion
Septum wire

## Slide 79: Third-order resonant extraction
Sextupole magnets produce a triangular stable area in phase space
ΔQ decreasing – phase space distortion for largest amplitudes
Septum wire

## Slide 80: Third-order resonant extraction
Septum wire
Sextupole magnets produce a triangular stable area in phase space
ΔQ decreasing – phase space distortion for largest amplitudes

## Slide 81: Third-order resonant extraction
Septum wire
Sextupole magnets produce a triangular stable area in phase space
ΔQ decreasing – phase space distortion for largest amplitudes

## Slide 82: Third-order resonant extraction
Septum wire
Sextupole magnets produce a triangular stable area in phase space
ΔQ decreasing – phase space distortion for largest amplitudes

## Slide 83: Third-order resonant extraction
Largest amplitude particle trajectories are significantly distorted
Locations of fixed points noticeable at extremities of phase space triangle
Septum wire

## Slide 84: Third-order resonant extraction
Septum wire
ΔQ small enough that largest amplitude particle trajectories are unstable
Unstable particles follow separatrix branches as they increase in amplitude

## Slide 85: Third-order resonant extraction
Septum wire
Stable area shrinks as ΔQ becomes smaller

## Slide 86: Third-order resonant extraction
Septum wire
Separatrix position in phase space shifts as the stable area shrinks

## Slide 87: Third-order resonant extraction
As the stable area shrinks, the circulating beam intensity drops since particles are being continuously extracted
Septum wire

## Slide 88: Third-order resonant extraction
Septum wire
As the stable area shrinks, the circulating beam intensity drops since particles are being continuously extracted

## Slide 89: Third-order resonant extraction
Septum wire
As the stable area shrinks, the circulating beam intensity drops since particles are being continuously extracted

## Slide 90: Third-order resonant extraction
Septum wire
As the stable area shrinks, the circulating beam intensity drops since particles are being continuously extracted

## Slide 91: Third-order resonant extraction
Septum wire
As ΔQ approaches zero, the particles with very small amplitude are extracted

## Slide 92: Slow extracted spill quality
  Reducing DQ with main machine quadrupoles can be augmented with a ‘servo’ quadrupole, which can modulate DQ in a servo loop, acting on a measurement of the spill intensity
50 Hz
10 Hz
  An example of a spill at SPS to the North Area with large n x 50 Hz components and another noise source at 10 Hz
  The slow-extraction is a resonant process and it amplifies the smallest imperfections in the machine:
    e.g. spill intensity variations can be explained by ripples in the current of the quads (mains: n x 50 Hz) at the level of a few ppm!
    Injection of n x 50 Hz signals in counter-phase on dedicated quads can be used to compensate

## Slide 93: Extraction - summary
Several different techniques:
  Single-turn fast extraction:
    for transfer between machines in accelerator chain, beam abort, etc.
  Non-resonant (fast) multi-turn extraction
    slice beam into equal parts for transfer between machine over a few turns.
  Resonant low-loss (fast) multi-turn extraction
    create stable islands in phase space: slice off over a few turns.
  Resonant (slow) multi-turn extraction
    create stable area in phase space  slowly drive particles into resonance  long spill over many thousand turns.

## Slide 94: Linking Machines
Extract a beam out of one machine  initial beam parameters
Transport this beam towards the following machine (or experiment)
Inject this beam into a following machine with a predefined optics
   Transfer line optics has to produce required beam parameters for matching
Extraction
Transfer
Injection
s
(αx, βx, Dx, D’x αy, βy, Dy, D’y)1
M12
(αx, βx, Dx, D’x αy, βy, Dy, D’y)2

## Slide 95: Linking Machines
Beams have to be transported from extraction of one machine to injection of the next machine:
  Trajectory must be matched in all 6 geometric degrees of freedom (x,y,z,θ,Φ,ψ)
Linking the optics is a complicated process:
  Parameters at start of line have to be propagated to matched parameters at the end of the line (injection to another machine, fixed target etc. )
  Need to “match” 8 variables (αx, βx, Dx, D’x and αy, βy, Dy, D’y)
  Done with number of independently power (“matching”) quadrupoles
  Maximum β and D values are imposed by magnetic apertures
  Other constraints exist:
    Phase conditions for collimators
    Insertions for special equipment like stripping foils
    …
Matching with computer codes and relying on mixture of theory, experience, intuition, trial and error.

## Slide 96: Optics Matching example
SPS
LHC
Regular lattice (FODO)
(elements all powered in series
with same strengths)
Final
matching
section
SPS to LHC Transfer Line (3 km)
Extraction
point
Injection
point
Initial
matching
section
Independently powered (tuneable) quadrupoles
Independently powered (tuneable) quadrupoles and (in this case) passive protection devices
  Need to match 8 variables (TWISS parameters) for propagation from start to end of a transfer

## Slide 97: Optical Mismatch at Injection
Filamentation fills larger ellipse with same shape as matched ellipse
x
x’
Turn 0
Turn N
Time
Dispersion mismatch at injection will also cause emittance blow-up

## Slide 98: Further reading and references
Lots of resources presented at the specialised CAS School:
Beam Injection, Extraction and Transfer, 10-19 March 2017, Erice, Italy
https://cas.web.cern.ch/schools/erice-2017

## Slide 99: Appendix

## Slide 100: Injection errors
kicker
bpm1
bpm2
phase m
~p/2
~p/2
~p/2
septum
Angle errors
Dqs,k
Measured
Displacements
d1,2
Dqs,
Dqk,
d1
d2
At kicker location

## Slide 101: Injection errors
kicker
bpm1
bpm2
phase m
~p/2
~p/2
~p/2
septum
Angle errors
Dqs,k
Measured
Displacements
d1,2
d1 = Dqs (bsb1) sin (m1 – ms) + Dqk (bkb1) sin (m1 – mk)
≈ Dqk (bkb1)
Dqs,
Dqk,
d1
d2
At BPM1 location
d2 = Dqs (bsb2) sin (m2 – ms) + Dqk (bkb2) sin (m2 – mk)
≈ -Dqs (bsb2)

## Slide 102: Blow-up from steering error
Misinjected
beam
Matched
particles
L
A0
The new particle coordinates in normalised phase space are:
For a general particle distribution, where Ai denotes amplitude in normalised phase of particle i:
The emittance of the distribution is:
q

## Slide 103: Blow-up from steering error
So we plug in the new coordinates:
Taking the average over distribution:
Giving the diluted emittance as:
0
Effect of steering error on a given particle
Matched
particles
A
L
q
0

## Slide 104: Blow-up from steering error
Consider a collection of particles with max. amplitudes A
The beam can be injected with an error in angle and position
For an injection error Δa, in units of σ = (βε), the mis-injected beam is offset in normalised phase space by an amplitude L = Δaε
Misinjected
beam
Matched
particles
L
A

## Slide 105: Blow-up from steering error
Consider a collection of particles with max. amplitudes A
The beam can be injected with an error in angle and position.
For an injection error Δa, in units of σ = (βε), the mis-injected beam is offset in normalised phase space by an amplitude L = Δaε
Misinjected
beam
Matched
particles
L
A

## Slide 106: Blow-up from steering error
Consider a collection of particles with max. amplitudes A
The beam can be injected with an error in angle and position.
For an injection error Δa, in units of σ = (βε), the mis-injected beam is offset in normalised phase space by an amplitude L = Δaε
Misinjected
beam
Matched
particles
L
A

## Slide 107: Blow-up from steering error
Consider a collection of particles with max. amplitudes A
The beam can be injected with an error in angle and position.
For an injection error Δa, in units of σ = (βε), the mis-injected beam is offset in normalised phase space by an amplitude L = Δaε
Matched
particles
A
L
Any given point on the matched ellipse is randomised over all phases after filamentation due to the steering error:
q
Effect of steering error on a given particle

## Slide 108: Blow-up from steering error
Consider a collection of particles with max. amplitudes A
The beam can be injected with an error in angle and position.
For an injection error Δa, in units of σ = (βε), the mis-injected beam is offset in normalised phase space by an amplitude L = Δaε
Matched
particles
A
L
Any given point on the matched ellipse is randomised over all phases after filamentation due to the steering error
For a general particle distribution, where Ai denotes amplitude in normalised phase of particle i:
q
Effect of steering error on a given particle

## Slide 109: Blow-up from steering error
Consider a collection of particles with max. amplitudes A
The beam can be injected with an error in angle and position.
For an injection error Δa, in units of σ = (βε), the mis-injected beam is offset in normalised phase space by an amplitude L = Δaε
Effect of steering error on a given particle
Matched
particles
A
L
Any given point on the matched ellipse is randomised over all phases after filamentation due to the steering error
For a general particle distribution, where Ai denotes amplitude in normalised phase of particle i:
After filamentation:
q
See appendix for derivation

## Slide 110: Blow-up from steering error
A numerical example….
Consider an offset Δa = 0.5σ for injected beam:
For nominal LHC beam:
…allowed growth through LHC cycle ~10 %
Misinjected beam
Matched
Beam
0.5e
e

## Slide 111: Third-order resonant extraction
Particle at turn 0
On resonance, sextupole kicks add-up driving particles over septum

## Slide 112: Third-order resonant extraction
Particle at turn 1
On resonance, sextupole kicks add-up driving particles over septum

## Slide 113: Third-order resonant extraction
Particle at turn 2
On resonance, sextupole kicks add-up driving particles over septum

## Slide 114: Third-order resonant extraction
Particle at turn 3
On resonance, sextupole kicks add-up driving particles over septum

## Slide 115: Third-order resonant extraction
On resonance, sextupole kicks add-up driving particles over septum
  Distance travelled in these final three turns is termed the “spiral step,” ΔXES
  Extraction bump trimmed in the machine to adjust the spiral step
Extracted beam
q

## Slide 116: Third-order resonant extraction
On resonance, sextupole kicks add-up driving particles over septum
  Distance travelled in these final three turns is termed the “spiral step,” ΔXES
  Extraction bump trimmed in the machine to adjust the spiral step
RF gymnastics before extraction:
Extracted beam
q
momentum spread, tune
  Spill = 4.8 s
time
Schottky measurement during spill, courtesy of T. Bohl
Δϕ = π
Δϕ = -π
small Δp
rotation: large Δp
RF off
RF gymn.

## Slide 117: Slow extraction channel: SPS
electrostatic septum (ES)
QFA
QDA
magnetic
septum (MST)
magnetic septum (MSE)
QFA
TPST
mask
extraction
bumper
To TT20
and NA
ES
circulating beam
extracted beam

## Slide 118: Second-order resonant extraction
An extraction can also be made over a few hundred turns
2nd and 4th order resonances
  Octupole fields distort the regular phase space particle trajectories
  Stable area defined, delimited by two unstable Fixed Points
  Beam tune brought across a 2nd order resonance (Q → 0.5)
  Particle amplitudes quickly grow and beam is extracted in a few hundred turns

## Slide 119: Resonant extraction separatrices
Amplitude growth for 2nd order resonance much faster than 3rd – shorter spills (≈milliseconds vs. seconds)
Used where intense pulses are required on target – e.g. neutrino production
3rd order resonant extraction
2nd order resonant extraction