## Slide 1
Discussion on Conceptual Design HTS magnet (M3)
20/01/2022
Thibault Lécrevisse (thibault.lecrevisse@cea.fr)

## Slide 2: January 13th meeting feedback
5 Participants : Ernesto De Matteis (INFN), Eugen Shabagin (BNG), Fernando Toral (CIEMAT), Daniel Barna (WIGNER)
Start to converge on the magnet parameters to be completed (see next slide)
Timing is very short now and we have to focus on what is specific to HTS (and what can be handle in a short time) : possibilities of delaying the milestone?
Set-up the documents in the sharepoints environment : allow work in parallel to fill the report by involved peoples on each aspects.

## Slide 3: Parameter list of HTS magnet
Parameters | Values | unit | Comments
Magnet type | CCT | - | 
Geometry | Straight | - | Combined function (no constrains on Quadrupole strength)
Central magnetic field B0 | 4 | T | as HITRI+ and SIGRUM demostrators No specific field quality at this stage?
Magnetic and physical length | 0.8, 1 | m | 
Bore diameter | 80 | mm | as HITRI+ and SIGRUM demostrators
dB/dt | 0.4 | T/s | as HITRI+ and SIGRUM demostrators
Operation temperature | 4.7, 10, 20 | K | Helium gas + Cryocoolers ? Conduction cooled + cryocoolers ?
Loadline margin (@4.7 K, 10 K, 20 K) static | 20-25 ? | % | Design at 20 K with lower margin ? Keep the margin at lower temperature?
Superconductor | ReBCO | - | Strategy with the cable? Stack / complex cable, delay/cost ?

## Slide 4: CDR content ?
Focus on what is specific to the REBCO HTS conductor :
High AC losses (current redistribution in the tapes)
No hardway bending  specific designs / former / grooves
High stability but complex protection : only hotspot study ?
Include what is similar to LTS ?
AC losses in the former
Mechanics
Cable choice : too early (maybe a short list?)
What can not be addressed in this report :
Cryogenics design : require the losses study
AC losses /transient: require cable geometry and dedicated modelling

## Slide 5: CDR plan (tentative)
Introduction
HTS magnet set of parameters
Magnetic design
  Conductor assumptions (performances, geometry…)
  Design assumptions (saturated tapes, no hardway bending, margin vs temperature…)
  Proposed design with and without quadrupole function
HTS REBCO specificities in the design
  Cable possibilities and short list
  Protection : Adiabatic hotspot
Cable possibilities and short list (twisted stack, CORC, Roebel…)
Mechanics : (similar to LTS work)
Former (similar to LTS work with specific grooves?)
Missing elements ?

## Slide 6: Work to do and participants list
Aspect | Who? | When?
Magnetic design |  | 
Cable |  | 
Protection |  | 
Mechanics |  | 
Former |  | 
… |  | 
… |  |