## Slide 1: First tracks and initial timing results with Timepix4 detectors
Martin van Beuzekom
27 June 2022
Riva del Garda

## Slide 2: Introduction & Motivation
Beam telescopes will be used for characterization
of novel sensors, in view of LHC upgrades
After successful Timepix3 beam telescope, upgrade based on Timepix4
Main improvement (and challenge) is a better track time resolution
  Timepix3 telescope achieved 236 ps after long and careful tuning
Aim for (about) 20 ps track time resolution
  If using fast sensors and reference timing layer
Maintain excellent pointing resolution of (about) 2 mm
Operation at ‘high’ rate (> 1 Mtracks/s)
Timepix4 is an excellent candidate chip for a beam telescope
  Large area, high resolution time stamping, large design team and user community
This work shows the first testbeam results; step-1 on the way to a full telescope
DUT

## Slide 3: Timepix4 main specifications
Pixel electronics
Peripheral circuits
Wire bond extenders
(can be diced off)
24.64 mm
28.16 mm
65 nm CMOS
Matrix of 512 x 448 pixels
55 x 55 um2 pixels
  Electronics in 55 x 51.4 um2
Active area 6.94 cm2
4-side buttable, using redistribution layer
Many modes, for telescope: simultaneous Time-Of-Arrival and Time-Over-Threshold
195 ps TDC bins
Data driven readout: 16 x 10.24 Gbps
Min. threshold: ~500 e-
X. Llopart et al. 2022 JINST 17 C01044

## Slide 4: Timepix4 time measurement
Base clock of 40 MHz
Hit starts 640 MHz oscillator
  1.56 ns bins
  Count #clock cycles (like in Tpx3)
  Oscillator shared by 8 pixels in superpixel
Oscillator is stopped by first rising edge of 40 MHz clock
In addition the internal state of ring oscillator (VCO) is captured –> 195 ps bins
Back edge of Time-over-Threshold signal is measured with a high time resolution
  Improved ToT measurement

## Slide 5: Timepix4 versions
Version1 with sensor used in testbeam
  Voltage Controlled Oscillator running 25% too fast
  And not properly locked to its reference oscillator
Version2 (still) without sensor used for lab measurements
More Timepix4 info in Xavi Llopart’s seminar: https://indico.cern.ch/event/1121147/

## Slide 6: SPIDR4 readout
Readout specifically for Timepix4
Default: 10 Gbits/s readout
  More than sufficient for typical testbeam
Supports full bandwidth of chip (160 Gbit/s) with optional DAQ server
Timepix4 chipboard
Control board
Optional DAQ server
Off–the-shelf
computer
External clock/timing
(optional)
gRPC, 1 Gb Ethernet
Data
10 Gb Ethernet
Raw data (64b/66b)
160 Gbit/s
Config. / Control
Pixel data
Config. / status
Clock / Timing
Data access
Config. / Control

## Slide 7: Configuration
SPIDR4
CFD
CFD
CFD
TLU
DAQ
SPIDR4
SPIDR4
SPIDR4
100 mm sensors
300 mm sensors
downstream
scintillator
upstream
scintillators
N30
N29
N23
N28
10 GbE
40 MHz
t0-sync
Particle beam
180 GeV/c (p,p,K)
RunCtrl
All sensors are n-on-p (e- collecting)
SlowCtrl
1 GbE

## Slide 8
Timepix4-v1
SPIDR4
Detector Box
scintillators

## Slide 9: Cooling
Power consumption of few Watts per Timepix4
All chips/PCBs attached to 3D printed titanium cooling block
Glycol used to cool chips to about room temperature
Ready to go colder
Current
cooling
Ti
Silicon
Envisioned
cooling
Ti
PCB
Silicon
PCB

## Slide 10: First beam on Timepix4
Hitmap of associated clusters to a track on a single plane
✔️ DAQ and synchronization works
✔️ Online monitoring works
✔️ Offline analysis using the LHCb’s Kepler framework works
-> ToT and hitmap look as expected
10
TOT/Charge distribution for the two sensor variants
100 mm
300 mm

## Slide 11: Efficiencies
”Out of the box” efficiencies
Not yet optimized (but anyhow, >> 90% sufficient for telescope)

## Slide 12: Spatial residual distributions
Unbiased residuals, measured by extrapolating tracks made with the other 3 detectors
The pointing resolution is not subtracted from these values, hence the huge variation between similar planes
Results in line with expectation
Beam direction

## Slide 13: Optimizing for spatial resolution
The 300 mm sensors are placed at a 9° pitch and yaw angle w.r.t. beam
Improves spatial resolution to ~ 6 mm
  Binary resolution 55 mm / sqrt(12) = 15.9 mm
Low threshold operation is beneficial for spatial resolution
  ~600 e- seems feasible with careful tuning
Find balance between optimization for spatial resolution and for timing

## Slide 14: Optimization for timing
Time offset per pixel determined via time-to-threshold measurement
Planned for final telescope: per-TDC-bin offset correction
  Requires substantial statistics
Time offset per pixel
‘Standard’ time-walk correction for thin perpendicular sensors
Currently using Time-over-Threshold, accurate charge calibration not yet available

## Slide 15: Timewalk correction for thick tilted planes
Tilting sensors is beneficial for spatial resolution, but affects time resolution
Timewalk plot for tilted thick sensor shows multi-band structure
Requires timewalk correction based on track topology, currently limited by statistics
More details: K. Heijhoff https://doi.org/10.1088/1748-0221/15/09/P09035
4

## Slide 16: Temporal resolution of individual planes
Limited by bias voltage on sensor
Lower threshold for 300 mm sensors might improve time resolution

## Slide 17: Track time resolution
Current track time resolution is (‘only’) 340 ps
Improvements expected from:
  More layers: at least 8, maybe 10 or 12
  Operation at higher bias voltage
  Timepix4v2, with locked TDC oscillators
  Higher preamplifier current
  Cluster time instead of hit time
  Better track topology based timewalk correction (suffering from limited statistics)
Major improvement will come from faster sensors: LGAD, (trench) 3D
Time resolution of TPX4 analog front-end,
with testpulse
K. Heijhoff: arXiv:2203.15912 (accepted by JINST)

## Slide 18: Summary and outlook
Reconstructed first tracks through Timepix4 !
Successful first testbeam, many things tested/learnt:
  Mechanics and cooling
  Slow control and online monitoring
  Synchronisation
  Track reconstruction
  Experience with Timepix4, SPIDR4 etc.
Performance in line with expectation
Track time resolution so far: 340 ps
Many ‘knobs’ we can turn to improve time resolution
  Tuning, corrections, and more corrections
Next testbeam in about 3 weeks from now
  8 layers: 4 x Timepix4v2, 4 x Timepix4v1

## Slide 19: Thank you