## Slide 1: Imaging and time-stamping single optical photons with nanosecond resolution for quantum applications Andrei Nomerotski, Brookhaven National Lab, Upton NY, USA

## Slide 2: Will talk about
Fast, data driven approach to optical imaging
Quantum applications
Quantum assisted telescopes

## Slide 3: Optical cameras: normally signal is integrated in a slice of time and whole frame is read out
0.2 msec
Quite far from 1 nanosecond!
5 kframe per second camera

## Slide 4: Imaging with photon counting
Low occupancy
Integrated image
Photons appear as standalone objects  data driven readout
Has parallels with x-ray imaging and particle detection in HEP

## Slide 5: Alternative Approach to Optical Imaging
Detect and time stamp photons, one by one, using intelligent pixels with data-driven readout
Accumulate statistics for images, also for more complex analysis (coincidences, correlations etc)
Frame-by-frame imaging 
continuous stream of time stamped single photons
Tpx3Cam: time-stamp 10 MHz flux of photons with 1 ns precision
A.Nomerotski, Imaging and time stamping of photons with nanosecond resolution in Timepix based optical cameras, Nuclear Instruments and Methods Sec A, Volume 937 (2019) pp 26-30
Also: PImMS1 & PImMS2 – monolithic version with different architecture
PImMS, a fast event-triggered monolithic pixel detector with storage of multiple timestamps,
JJ John et al, Journal of Instrumentation 7 (08), C08001 (2012)

## Slide 6: Timepix Optical Cameras

## Slide 7: Hybrid pixel detectors
Lukas Tlustos and Erik H. M. Heijne, Performance and limitations of high granularity single photon processing X-ray imaging detectors, in CERN proceedings (2005)
Decouple readout chip and sensor
Optimize technologies for chip and sensor separately
Use different sensors with same readout, versatile approach for x-rays (Si, CZT)
 we will use OPTICAL sensors
credit: IZM
Have roots in R&D for LEP/LHC vertex detectors

## Slide 8: Thin window optical sensors
Developed at BNL, first produced at CNM (Barcelona, Spain) in 2015
Surface preparation is very important, inspired by astronomical CCDs (LSST)
High QE
Nomerotski et al, Characterization of TimepixCam, a fast imager for the time- stamping of optical photons,
Journal of Instrumentation 12 (01) (2017) C01017.
M. Fisher-Levine, A. Nomerotski, Timepixcam: a fast optical imager with time-stamping,
Journal of Instrumentation 11 (03) (2016) C03016.
Backside illuminated optical sensors
Anti-reflective coating, thickness 300 um

## Slide 9: Timepix3 Camera  Tpx3Cam
Camera = sensor + ASIC + readout
Timepix3 ASIC:
256 x 256 array, 55 x 55 micron pixel
  14 mm x 14 mm active area
1.56 ns timing resolution
Data-driven readout, 600 e min threshold, 80 Mpix/sec, no deadtime
each pixel measures time and flux, ~1ms pixel deadtime when hit
Sensor is bump-bonded to chip
Use existing x-ray readouts:
SPIDR (Nikhef & ASI)
www.amscins.com
Zhao et al, Coincidence velocity map imaging using Tpx3Cam, a time stamping optical camera with 1.5 ns timing resolution,
Review of Scientific Instruments 88 (11) (2017) 113104.
T. Poikela et al, Timepix3: a 65k channel hybrid pixel readout chip with simultaneous ToA/ToT and sparse readout,
Journal of Instrumentation 9 (05) (2014) C05013.

## Slide 10
TPX3Cam @ ASI
SPIDR readout for Timepix3 (Nikhef, ASI)
eX readout for Timepix2 (Imatek)
Use existing readouts of x-ray detectors:
J. Visser et al, SPIDR: a readout system for Medipix3 and Timepix3, Journal of Instrumentation 10 (12) (2015) C12028.

## Slide 11: Single (optical) photons

## Slide 12: Intensified camera: use off-the-shelf image intensifier
Image intensifier (Photonis PP0360EG)
Cricket@
Intensifier
Intensified cameras are common:
  iCCD
  iCMOS cameras

## Slide 13: Choice of photocathodes
Photonis photocathodes

## Slide 14: Single Photons in Tpx3Cam
Tpx3Cam + intensifier by Photonis
data taken by J. Long (ASI)
1 ms slice of data
1.5 ns time-stamping
TOA
TOT
TOT

## Slide 15
TOA
TOT
Each photon is a cluster of pixels
3D (x,y,t) centoiding
Spatial resolution: 0.1 pixel / photon
Time resolution: < 1 ns / photon

## Slide 16: Applications & Results
Quantum imaging
High Energy Physics applications
Neutron imaging
Lifetime imaging
Ion imaging

## Slide 17: Quantum Applications

## Slide 18: Quantum Astrometry
Idea: employ quantum entanglement to improve precision of optical interferometers

## Slide 19: Astronomy picture of the decade
2019 ApJL 875
Black hole in the center of M87 imaged at 1.3mm
Achieved by radio interferometry with ~10000 km baselines
sensitive to features
on angular scale

## Slide 20
Radio
Optical
Can literally record entire waveform, over some band, separately at each receiver station and interfere later offline
One photon at a time! Need to bring paths to common point in real time
Need path length compensated to better than c/bandwidth
Need path length stabilized to better than
Accuracy ~ 1 mas
Max baselines to ~ 100 m

## Slide 21: Two-photon techniques

## Slide 22
Measure photon wave function phase difference performing Bell State Measurement at one station so teleporting the sky photon to the other station
Enables long baselines and could improve astrometric precision by orders of magnitude
Major impact on astrophysics and cosmology
Quantum (two-photon) interferometer
Second photon for quantum assist

## Slide 23: Quantum Astrometry
Idea: use another star as source of entangled states for the interference
Relative path phase difference d1 - d2 can be extracted from the coincidence rates of four single photon counters: c, d, g and f
Can provide 10 microarcsec resolution for bright stars
Allows to start exploring this approach experimentally
Stankus, Nomerotski, Slosar, Vintskevich, Two-photon amplitude interferometry for precision astrometry
arxiv.org/abs/2010.09100
Rates
HBT
New oscillatory term!
Full QFT calculation

## Slide 24: Requirements for detectors
Photons must be indistinguishable = close enough in frequency and time to interfere  temporal & spectral binning: need ~ 20 ps * 0.1 nm for 800 nm
Fast imaging techniques are the key: target 1-100 ps resolution
Spectral binning: diffraction gratings, Echelle spectrometers
Photon detection efficiency: high
Quantum-Assisted Optical Interferometers: Instrument Requirements; Andrei Nomerotski et al, Proceedings Volume 11446, Optical and Infrared Interferometry and Imaging VII; 1144617 (2020) SPIE Astronomical Telescopes +Instrumentation, https://doi.org/10.1117/12.2560272; arxiv:2012.02812

## Slide 25: Experiments in progress
Bench-top model of two-photon interferometry
Ar vapor lamps with ultra-narrow band filters
Superconducting nanowire single-photon detectors
See correlations of counters as expected
Strong HBT peak
8 ch. SNSPD
photon phase shifting
A.Nomerotski et al, arxiv.org/abs/2107.09229

## Slide 26: On-sky experiments in progress
Chen, Stankus, Nomerotski, Slosar, Vintskevich, Astrometry in two-photon interferometry using Earth rotation fringe scan, arxiv.org/abs/2205.09091
Arcturus, PSF ~ 1 arcsec

## Slide 27: Spectroscopic binning
In collaboration with NRC (Ottawa) D.England, Y.Zhang et al
Y Zhang, D England, A Nomerotski, P Svihra et al, Multidimensional quantum-enhanced target detection via spectrotemporal-correlation measurements, Physical Review A 101 (5), 053808
P Svihra et al, Multivariate Discrimination in Quantum Target Detection, Appl. Phys. Lett. 117, 044001 (2020)
Pump photon wavelength vs time difference
dl*dt ~ 5 ns * 0.5 nm

## Slide 28
Current setup at BNL: SPDC source as spectrometer characterization tool

## Slide 29: Argon lamp spectrum
better magnification:
0.1 nm resolution

## Slide 30: Next steps: spectrometer based on LinoSPAD2
Diffracted photon stripes projected on to single linear array
Spectrometer time resolution: ns  100 ps
Collaboration with E.Charbon EPFL
LinoSPAD2

## Slide 31: More Quantum Imaging
Take home message: two-photon interference requires fast imaging ~10-100 ps

## Slide 32: Hong-Ou-Mandel effect
time
credit: Wikipedia HOM article
50/50 beam splitter
HOM dip for coincidences of two fibers
Bunched photons in single fibers

## Slide 33: HOM Setup
qutools.com

## Slide 34: Examples of bunched HOM photons
TOA
TOT
Distance between two photons, pix

## Slide 35: Hong-Ou-Mandel effect
Coincidence of photons in two fibers
Coincidence of photons in single fibers

## Slide 36: HOM effect with post-selection
10, 5, 3 nm post-selection filters
2 nm filters at 805 nm and 817 nm.
In collaboration with NRC (Ottawa) D.England, Y.Zhang et al

## Slide 37: More quantum imaging
other recent publications on quantum optics which used Tpx3Cam
High-speed imaging of spatiotemporal correlations in Hong-Ou-Mandel interface Xiaoqin Gao et al. Optics Express, 30(11) 19456 (2022)
Observation of Nonclassical Photon Statistics in Single-Bubble Sonoluminescence M. Rezaee et al. Arvix (2022)
Ray-tracing with quantum correlated photons to image a 3D scene Y. Zhang et al. Phys. Rev. A (2022)
Tera-mode of Spatiotemporal N00N States X. Gao et al. Optics Express, 30(11) 19456 (2022)

## Slide 38: Imaging of trapped ions
Time resolved qubit manipulation (Blinov group, UWash)
Register 493 nm photons to probe dark/bright state of ion = state of qubit register
Fast Simultaneous Detection of Trapped Ion Qubit Register with Low Crosstalk, M.Zhukas, P.Svihra, A.Nomerotski, B.Blinov, arxiv.org/abs/2006.12801
RF 18 MHz
Paul trap
Ba ions

## Slide 39: Time resolved ion oscillations
Emission rate oscillations due to Doppler shift of laser light wrt moving ion
Simultaneous time & position information allows to monitor ion micro-motions
Powerful technique to characterize traps
54 ns  18 MHz
L.Zhukas, M.Millican, P.Svihra, A.Nomerotski, B.Blinov, Direct observation of ion micromotion in a linear Paul trap, https://arxiv.org/abs/2010.00159, Phys. Rev. A 103, 023105 (2021)

## Slide 40: Ion micromotion
Emission rate oscillations due to Doppler shift of laser light wrt moving ion
Simultaneous time & position information allows to monitor ion micro-motions
  Period 54 ns
  Amplitude 0.4 micron
L.Zhukas, M.Millican, P.Svihra, A.Nomerotski, B.Blinov, Direct observation of ion micromotion in a linear Paul trap, https://arxiv.org/abs/2010.00159, Phys. Rev. A 103, 023105 (2021)

## Slide 41: Ion micromotion in 2D
2D ion crystals, RF period 92 ns
A.Kato et al, Two-tone Doppler cooling of radial two-dimensional crystals in a radiofrequency ion trap, arxiv.org/abs/2111.05829; Phys. Rev. A 105, 023101

## Slide 42: HEP applications

## Slide 43
TPX3Cam on ARIADNE 1-ton dual phase Liquid argon TPC
LAr Cosmic Muons (10msec slice)
A. Roberts et al., 2019 First demonstration of 3D optical readout of a TPC using a single photon sensitive Timepix3 based camera JINST 14 P06001
D. Hollywood et al, 2020 ARIADNE—A novel optical LArTPC: technical design report and initial characterisation using a secondary beam from the CERN PS and cosmic muons JINST 15 P03003
Image light from avalanches in gas phase in THGEM
hep.ph.liv.ac.uk/ariadne/index.html
Kostas Mavrokoridis et al

## Slide 44
5.5 MeV alphas in CF4 gas
in Tpx3Cam
Color = TOA
Color = TOT
First demonstration of 3D optical readout of a TPC using a single photon sensitive Timepix3 based camera, A Roberts, P Svihra, A Al-Refaie, H Graafsma, J Küpper, K Majumdar, ... K. Mavrokoridis, A.Nomerotski … Journal of Instrumentation 14 (06), P06001 (2019)

## Slide 45: More ideas
Flashes in scintillator are imaged by intensified Tpx3Cam
Alphas, hard x–rays, neutrons, …
Thin fast scintillator
Difficulty: light collection efficiency (but it’s single photon sensitive)
Advantage: outside of the beam, around the corner (with mirrors)

## Slide 46: Alphas in LYSO in Tpx3Cam
Am241 5.5 MeV alphas
LYSO 0.5 mm thickness
Alpha hits in Tpx3Cam
TOT
TOA
G. D'Amen et al 2021 JINST 16 P02006
Neutron detection paper submitted to NIM

## Slide 47: Neutron detection with Tpx3Cam
6Li-based scintillator
Neutrons produce alphas
Time resolved
Material characterization with Bragg edges
J.Yang et al, arxiv.org/abs/2102.13386
A.Losko et al, DOI:10.21203/rs.3.rs-257513/v1
Tpx3Cam neutron event display

## Slide 48: Future directions

## Slide 49
X. Llopart
by Medipix4 collaboration
WISH LIST:
ASIC with optimized timing for clusters and with triggering capabilities,
Readout with several 10 ps TDCs in synch with Tpx
X. Llopart et al., Timepix4, a large area pixel detector readout chip which can be tiled on 4 sides providing sub-200 ps timestamp binning, JINST 17 (2022) C01044

## Slide 50: Direct MCP  Timepix detection

## Slide 51: Single Photon Sensitivity without intensifier?
So far needed outside amplification (MCP) to have a detectable signal
Limitation: QE ~ 35% (for 800nm)
GaAs
Photonis photocathodes

## Slide 52: Single Photon Sensitivity without intensifier?
Can the amplification be integrated into the sensor? Silicon QE can be >90%
SPADs
Currently PDE (photon detection eff) ~30-50% but there is no fundamental limit
Can we build a hybrid (SPAD + Timepix4.1) camera?

## Slide 53: Summary
  Time stamping of optical photons with data-driven readout is attractive alternative to frame readout
  Works well for sparse data
  Needs intelligent pixels with complex functionality
  Timing resolution: 10 nsec  0.1 nsec
  Photon sensitivity: 1000 photons  single photon
  New technologies for fast single photon detection  hot topic in quantum applications

## Slide 54: Acknowledgements
Eden Figueroa
Paul Stankus
Tom Tsang
Justine Haupt
Mael Flament
Guodong Cui
Sonali Gera
Michael Keach
Steven Paci
Alex Parsells
Jonathan Schiff
Denis Dolzhenko
Stepan Vintskevich
Anze Slosar
Zhi Chen
Jesse Crawford
Rom Simovitch
Jingming Long
Martin van Beuzekom
Bram Bouwens
Erik Maddox
Jord Prangsma
Duncan England
Yingwen Zhang
Boris Blinov
Mila Zhukas
Maverick Millican
Alex Kato
Peter Svihra
Michal Marcisovsky
Sergei Kulkov
BNL team
SBU team

## Slide 55: spares

## Slide 56: Photon absorption in silicon
Blue photons are absorbed near the surface (~0.25 um for 430 nm, P47 max emission)
~1 um for 500 nm, ~10 um for 800 nm
d, m
l, nm

## Slide 57: Ion Imaging

## Slide 58
Ions in TimepixCam

## Slide 59
FLASH data, paper submitted to Journal of Synchrotron Radiation

## Slide 60: Quantum Network
Attenuation in fibers  need quantum repeater to reproduce qubits
  Simple amplification will not conserve the quantum state
Qubit teleportation: produce entangled photons and send them to two locations
Bell State Measurement (BSM) on one photon will collapse the wave function of the other one (or swap entanglement, or teleport photon)
A.Zeilinger

## Slide 62: Characterization of Single Photon Down-Conversion Source
Figueroa lab
qubit: use H, V photon polarization states

## Slide 63
Find coincidences, plot as function of two polarizations
Figure of merit: S-value
  If > 2: photons are entangled
  max value: 2
Measurement:
S-value = 2.720.02
Time resolution: 2ns
Time difference between photons

## Slide 64: Spatial characterization of entanglement
Imaging enables scalability
Measure S-value
for 81 combinations of subareas

## Slide 65: Scalability
Tpx3Cam supports 10MHz single photon rate :
= 10 x 10 x 100kHz beams
Time, ns
Photon router:
Used acousto-optical modulators to create 8x8 grid
Arbitrary routing between spots
10 ns time resolution, 1 ms switching
AOM: x & y
laser

## Slide 66: Scalability
Goal: storage of multiple qubits in single 87Rb cell

## Slide 67: Hanbury Brown – Twiss Interferometry

## Slide 68: Possible impact on astrophysics and cosmology
offers orders of magnitude better astrometry with major impact
Parallax: improved distance ladder (DE)
Proper star motions (DM)
Microlensing, see shape changes (DM)
Black hole imaging
Gravitational waves, coherent motions of stars
Exoplanets
https://arxiv.org/abs/2010.09100

## Slide 69: Qubit detection error
Fast Simultaneous Detection of Trapped Ion Qubit Register with Low Crosstalk, M.Zhukas, P.Svihra, A.Nomerotski, B.Blinov, arxiv.org/abs/2006.12801
single qubit detection error: ~ 5 ppm

## Slide 70: Lifetime Imaging

## Slide 71: Lifetime imaging with ns timing

## Slide 72: Lifetime imaging with oxygen sensors
Sensor lifetime depends on oxygen concentration  in-vivo monitoring of oxygen in tissues
Oxygenation
De-oxygenation
Polystyrene
PVC
PVDC
PMMA
Hydrogel
Polystyrene
PVC
PVDC
PMMA
Hydrogel
49.4 µs
44.9 µs
51.05 µs
56.2 µs
48.9 µs
48.9 µs
35.5 µs
13.4 µs
34.8 µs
37.3 µs
Oxygenation and Deoxygenation of PtBp Solid State sensors
New luminescence lifetime macro-imager based on a Tpx3Cam optical camera, R Sen et al, Biomedical optics express 11 (1), 77-88 (2020)
Papkovski group, University College Cork (Ireland)

## Slide 73: Measurements with biosamples
Intraluminal application (Mice2)
Large Intestine
Inhibitor
Inhibitor
Inhibitor
Inhibitor
Small Intestine
Inhibitor
Inhibitor
35.5
33.9
22.8
32.2
33.6
30.2
35.3
38
35
28.6
33
35
30.1
31.3
35.4
23.1
30.9
27.7
36.3
32.8
31
38.2
44.5
43.1
23.5
30.1
32.7
21.5
22.4
20.3
22.1
24.4
27
19.7
23.7
21.1
Large Intestine
Time Lapse
2 hr
4 hr
3 hr
1 hr
43.9
40.3
40.99
43.6
43.6
43.65
43.1
46.8
47.3
45.1
43.2
46.6
35.3
38
35
0 hr
Inhibitor
Papkovski group, University College Cork (Ireland)
Mapping O2 concentration in ex-vivo tissue samples on a fast PLIM macro-imager, R Sen et al, Scientific reports 10 (1), 1-11 (2020)