## Slide 1: Propagating in a Magnetic Field in AdePT
AdePT developers
May 4th, 2022

## Slide 2: Propagation in a magnetic field
AdePT breaks each physics step into segments to decrease chance to miss a volume
deflection from momentum direction smaller than pre-set ‘miss distance’
this allows to precalculate this distance - simpler than G4’s which uses test step’s sagitta.
An integration substep charged particle tracks the minimum of
The remaining distance to achieve the physics step
The estimated length that produces the deflection
The initial version implements a helix for constant magnetic field (e.g. Bz in example13)
The field and integration method are selected in electron kernel using a ‘fieldPropagation’ interface
p
s
deflection

## Slide 3: Challenges and approximations
Each integration segment must be checked against the geometry
Except if the chord length is smaller than the isotropic safety
So substantially different code paths are involved (independent of integration method):
whether (or not) a volume boundary is encountered by the chord, but also
a variable number of ‘chord’ segments.
Currently the results of the boundary crossing are approximated
the location is that of the first attempted chord-boundary intersection;
the momentum direction is estimated using the initial and final momentum.
p
s
chord

## Slide 4: Improvements
Overcame issues with particles stuck at boundaries
The geometric (isotropic) safety is reused or recalculated
- reduced the number of navigator calls and improved performance.
Tackled tracks that need large number of ‘chord’ substeps
A maximum number (default=100) is imposed (to limit divergence)
Reducing it to 10 yielded 10% performance improvement - but involves more approximate msc length conversions.
Investigating how to benefit with minimal or no extra such approximation.
A global step limit ensures that charged particles looping in a low-density medium do not live ‘forever’
Count the global steps without a change in number of electrons, if only electrons are left in event,
After a maximum number (200) of these in a row, the simulation is ended.
p
s
Notes: Varying this parameter does have an effect on performance: a test CMS simulation with 1 T B-field ran for 25.6 s (for 1000), 24.6 s (for 100) and 22.1 s (for 10). Runs by Jonas on RTX 2070 equipped PC.

## Slide 5: Outlook
Integration using Runge-Kutta (5th order Dormand Prince) for non-uniform fields
is under development
Reducing divergence remains a challenge - and it’s coupled with need for some tracks to interrogate the navigator (potentially repeatedly)
Methods with interpolation (recently used in Geant4) offer intermediate points
But ‘ordinary’ 7 stage methods (DoPri5) need 60 FP values!
Evaluating alternative RK methods with reduced storage (will require fewer registers)
but no interpolation is possible - intermediate values are overwritten!