## Slide 1
High-Gradient Accelerator Development and Applications
Part 2

## Slide 2
Vacuum breakdown
You saw in Flyura’s lectures an in-depth introduction to vacuum breakdown. Narrative recap:
On the microscopic scale:
High surface electric fields cause field emission of electrons from a cathode surface and transfer of electrode atoms to vacuum. The electrons ionize some of the (copper) atoms, now positively charged, which are accelerated back to the electrode surface. On impact, they eject more copper, that gets ionized, a plasma forms, with it a plasma sheath, more electrons are emitted – avalanche! This all occurs on small surface, something of the order of a few tens of microns across, and it happens quickly, in a few nanoseconds.
On the macroscopic scale:
A high voltage, or high field in the case of rf, system starts with a lot of electromagnetic energy stored in the fields and power supply of the system. It stays where it is because the vacuum is insulating. A breakdown generates a conducting zone in the vacuum, the high currents that drain the stored energy of the system and cause a sudden and substantial modification of the electromagnetic fields in the system.
Accelerator scale:
The currents and collapsing fields mean that our accelerating structures don’t. The collapsed fields give less acceleration and transverse breakdown currents distort and kick the beam.

## Slide 3
Microscopic scale

## Slide 5
What’s going on inside.
ArcPIC simulation of the onset of breakdown, starting from field emission and going through the formation of a plasma, a plasma sheath and dramatically rising emitted current.
The code is ArcPIC and simulates a 20 micron wide dc gap.
https://doi.org/10.1002/ctpp.201400069

## Slide 6
Looking afterwards with an electron microscope

## Slide 7
Macroscopic and rf system scale

## Slide 8
Vacuum arc in an accelerating structure

## Slide 9
The basic layout of an rf system
Transmitted
Incident
Reflected
splitter
load
directional coupler
klystron
accelerating structure

## Slide 10
incident power
transmitted
power
reflected power
incident
transmitted
reflected
Envelope of rf pulse
From CLIC XBoxes
rf signals

## Slide 11
incident power
transmitted
power
reflected power
incident
transmitted
reflected
Suppression of transmission and reflection due to breakdown
rf signals

## Slide 12
Accelerating Structure Diagnostics
Faraday Cup
Directional coupler
Ion Gauge
Structure output couplers
RF Load
Structure input couplers
Temperature probe
RF hybrid splitter
(behind metal support)
Ion Pump
Vacuum valve
Ion Gauge

## Slide 13
Current in Faraday cup
Current of the level of amps

## Slide 14
Back to CLIC
BDR (BreakDown Rate) is the fraction of pulses which have a vacuum arc. Arc currents and lost acceleration result in lost luminosity on that pulse.
CLIC specification:
3x10-7 1/pulse/m
At 50 Hz, per structure:
1 BD every 3 days
Per 380 GeV facility:
1 BD someplace every 12 seconds

## Slide 15
CLIC 12 GHz prototypes – what is possible
Peak surface electric fields about x 2.5 higher
Much of the progress has been in quantifying dependence of gradient on RF design.
https://doi.org/10.1103/PhysRevAccelBeams.21.061001,
https://doi.org/10.1103/PhysRevAccelBeams.20.052001 etc.

## Slide 16
A very brief look at some accelerator-specific critical questions in breakdown theory

## Slide 17
How does structure geometry affect achievable gradient?
global power flow
local complex power flow
Hs/Ea
Es/Ea
Sc/Ea2
A. Grudiev, S. Calatroni, and W. Wuensch,
New local field quantity describing the high gradient limit of accelerating structures,
Phys. Rev. ST Accel. Beams 12, 102001 (2009)
Sc is typically the quantity which dominates the design of high-gradient travelling wave structures.
https://doi.org/10.1103/PhysRevSTAB.12.102001

## Slide 18
What drives the statistics of breakdown?
Describing mobile dislocation population evolution:
Leads to an exponential decay:
Eliyahu Zvi Engelberg, Yinon Ashkenazy, and Michael Assaf Phys. Rev. Lett. 120, 124801 (2018) https://doi.org/10.1103/PhysRevLett.120.124801
Physical model based on defect formation
K. Nordlund, F. Djurabekova, Defect model for the dependence of breakdown rate on external electric fields, Phys. Rev. ST Accel. Beams 15, 071002 (2012) https://doi.org/10.1103/PhysRevSTAB.15.071002

## Slide 19
Applications of high gradient accelerators
Having made a significant step in practical accelerating gradient for CLIC, we looked more broadly to see if there are applications that could benefit, or become realistic, due to this step in performance.

## Slide 20
X-band and high-gradient applications overview
Linear collider
Light source - XFEL
Light source - Inverse Compton Scattering Source
Medical applications
Beam manipulation
GeV-range research linacs
eSPS

## Slide 21
X-band and high-gradient infrastructure worldwide

## Slide 22
Focusing on one application – FLASH radiation therapy

## Slide 23
Introduction
A very hot topic in radiation oncology is so-called FLASH therapy which involves delivering an entire radiation treatment in a few hundred ms or less, as opposed to minutes, and in one or few fractions.
This fast delivery can reduce toxicity to healthy tissue while maintaining tumor control expanding the parameter space for treatment – more in a moment.
Another trend in radiation oncology is a renewed interest in VHEE (Very High Energy Electron) therapy.
In a parallel universe, major developments in accelerator technology have occurred in linear collider projects, relevant for this story, CLIC…

## Slide 24
FLASH goes way back

## Slide 25
What oncology data can look like

## Slide 26
Visually
First human patient – skin cancer treated with 10 MeV-range electrons
Vozenin et al
Clin Cancer Res
2018
Illustration of the Flash-RT effect in pig :
A major decrease of radiation side effects

## Slide 27
First clinical translation with low energy electrons

## Slide 29
What a high-energy electron beam can do
Estelle Brierre
2.5 Gycm2/nC
cm
cm
200 MeV electrons in water

## Slide 30
The CHUV-CERN collaboration
From a few coincidences then follow up discussions (a story for another day) CHUV and CERN realized that electron linac technology developed for CLIC could be the basis for a facility for treating large, deep-seated tumors in FLASH timescales – extending CHUV’s clinical translation program.
An extremely dynamic collaboration started in early 2019 to make a conceptual design of such a facility. This design is now done, feasibility OK and we have a good idea of the critical areas.
CHUV succeeded in finding a donor to fund the construction of the facility.
The project officially started on 1 September 2022, and ramp-up – as a collaboration, at CHUV and at CERN – is now underway.
Participation of an industrial partner is planned and investigation and discussions are underway.

## Slide 31
Layout
S-band laser driven photoinjector
X-band linac
Patient
Beam delivery system
≈ 10 m
Electron beam
S-band is 3 GHz
X-band is 12 GHz

## Slide 32
Basic parameters
S-band laser driven photoinjector
X-band linac
Patient
Beam delivery system
Maximum energy of beam > 100 MeV – Depth of tumor
Treatment time < 500 ms – FLASH effect
Largest field > 10 cm – Clinical scope
Current average over treatment > 100 µA – Field size over time capability
Electron beam

## Slide 33
Starting in the middle – the X-band linac
S-band laser driven photoinjector
X-band linac
Patient
Beam delivery system
Critical issues:
Give energy to the beam of > 100 MeV in a short distance – X-band technology
High current beam – High beam loading and challenging beam stability
Electron beam

## Slide 34
X-band linac hardware
Based on CLIC accelerating structures and XBox test stands.
CPI 50 MW klystron
Scandinova solid state modulator
Prototype CLIC accelerating structure

## Slide 35
The S-band photoinjector
S-band laser driven photoinjector
X-band linac
Patient
Beam delivery system
Critical issues:
Generate a high-current beam
Stability
Precise beam characteristics
Electron beam

## Slide 36
Laser-driven RF photoinjectors
Laser-driven RF photoinjectors are a commonly used device to provide well controlled electron bunches in a wide variety of linacs including XFELS, Inverse Compton Sources, ERLs, linear collider related test facilities etc.
From J.E. Clendenin, LINAC96
2021 - New CLEAR gun from INFN Frascati

## Slide 37
The beam delivery system
X-band linac
Patient
Beam delivery system
XRay therapy system
from https://www.varian.com/en-ch
(not same scale)

## Slide 38
The beam delivery system
S-band laser driven photoinjector
X-band linac
Patient
Beam delivery system
Critical issues:
Provide multiple irradiation angles in FLASH sub-100 ms – no time for mechanical gantry movement so use energy switching and spectrometer magnet
Expand beam to target cross section >10 cm
Specially designed combined function separator magnet.
Electron beam

## Slide 39
Pulsing and energy modulation
LINAC2
XBox-3 high-gradient test stand. Klystrons operate at 400 Hz, alternatively powering two test slots at 200 Hz.

## Slide 40
Spectrometer magnet
Energy E1
Isocenter
Pulsed linac

## Slide 41
Spectrometer magnet
Energy E2
Isocenter
Pulsed linac

## Slide 42
The overview again
S-band laser driven photoinjector
X-band linac
Patient
Beam delivery system
≈ 10 m
Electron beam

## Slide 43
More information

## Slide 44
Fundamental processes of high-fields
Dynamic and growing community of university, laboratory and industrial groups.
Fields include accelerators, fusion devices, satellites, vacuum interrupters, electron sources, photo-switching nano-devices, high-voltage systems etc.
Next meeting https://indico.cern.ch/event/1099613/ in person hosted by the University of Tartu!

## Slide 45
The High-Gradient RF Workshop Series
Our last in-person meeting, Chamonix, summer 2019
https://indico.cern.ch/event/1080222/
Last meeting, remote, hosted by Tsinghua University.

## Slide 46
https://indico.cern.ch/event/1131207/
More on FLASH therapy

## Slide 47
Animation
https://www.youtube.com/watch?v=87JLhcsuIao