## Slide 2: ELENA lines instrumnetaion
Y. Dutheil (SY-ABT)

## Slide 3: Immediate concern, ABT view
Grid 0181 (vertical one to STEP) is essential
0611 misses many wires, but worked as-is until now. Replacement is not critical
0533 has 2H planes, repair/change is favored
0546 is missing, installation is strongly favored since only 1 other grid before hand-over
One grid from sector 01 (0141 to 0312) could be removed with minimal risk on beam transport

## Slide 4
issues
2 H grids
No monitor
5125
5143
Few working wires
Could be replaced by position only measurement

## Slide 5: Medium-term, ABT view
Currently 41 grids
Need to maintain position & beam size measurement
  at 2 monitors before each experiment hand-over point for beam characterization
  At monitors around injection and extraction
  Below vertical lines, as it is very close to experiments (possible stray field effect on optics)
  Total of 26 monitors
  Non-destructive
    Much better for measurements
    Beam position at the end of lines used continuously by some experiments
Other monitors could be restricted to beam position measurement
Comprehensive coverage of beam position showed necessary when AEGIS turned their solenoid
Intensity monitoring along the lines would be relevant as well as transparent trajectory measurement
First considerations, will need more precise look

## Slide 6
Thank you