## Slide 1
Updates on β* for 2011
R. Bruce, R.W. Assmann
Acknowledgment: T. Baer, W. Bartmann, C. Bracco, S. Fartoukh, M. Giovannozzi, B. Goddard, W. Herr, S. Redaelli, R. Tomas, G. Vanbavinckhove, J. Wenninger, S. White, D. Wollmann

## Slide 2: Introduction
Hierarchy between cleaning stages must be preserved to guarantee protection (should account for β-beat and orbit variation)
To optimize β*, we have to review
  Triplet aperture
  Margins in cleaning hierarchy
Primary
Secondary
Triplet Aperture
Dump Protection
Tertiary
Absorbers
9.3 σ
15.0 σ
beam
17.5 σ ?
17.7 σ
8.5 σ
5.7 σ
6.0 σ
8.8 σ
17.2 σ
10.2 σ
12.8 σ
13.9 σ ?
6.0 σ
7.0 σ
10.0 σ
7.5 σ
8.3 σ
8.4 σ ?
2010
Intermediate
nominal
Only limits from aperture considered

## Slide 3: Aperture calculations (review)
Using 2 methods:
n1
scaling of measured injection aperture
  Assume pessimistically injection aperture=global limit+2 σ
  Only one plane matters with good approximation - reduce to 1D
  Scale beam size to pre-collision (larger βx and γ), add orbit offsets in relevant plane
  Solve for top energy aperture
Additional assumption: reduce separation to nominal value 0.7 mm
MQXB.B2L1
s= -40.8 m
2mm separation

## Slide 4: Parameters in aperture calculation
Scaling
  All mechanical and alignment errors already included in measurement – nothing changes between injection and top energy
  2mm orbit uncertainty (difference between orbit during measurement and top energy)
    More detailed analysis done, all runs from sept 18 to nov 30, data sampled every 2 minutes in stable beams, excluding points from van der Meer scan
  β-beat must be accounted for
    Assuming 5% reproducibility and measured β-beat
n1
  2.3 mm orbit variation (BPMs in triplets, difference to ideal MAD-X orbit)
  10% β-beat

## Slide 5: New β* without changing margins

## Slide 6: Margins in cleaning hierarchy
Orbit: separate analysis on following slides
10% β-beating. Bias in correction at TCT-triplet wanted
40 μm positioning error
10 μm setup error
Small lumi scans can be included in the margin

## Slide 7: Orbit movements TCT-triplet
TCT
Triplet
Correlated orbit movement at TCT and triplet considered
Because of phase advance, orbit movements in the same direction will cancel at the first triplet and add up at the second
Reduction in margin calculated in both planes for each triplet separately over full data set
1.6 σ covers all triplets 99% of the time in stable beams for IR1, IR5, IR8
2.4 σ needed in IR2 (large static orbit offsets)
IP
Reduction in margin
Triplet

## Slide 8: Example: IR1 B1 V

## Slide 9: Margins between collimators
A similar analysis (but more pessimistic, without phase considerations) shows
  99% of the time in stable beams, all horizontal TCTs are shadowed by the dump protection with a 1.1σ margin (presently 5.7σ total margin)
  We should not reduce the margin between IR7 and dump protection
  We should not reduce the margin between primary and secondary collimators in IR7 (possible loss in cleaning efficiency)

## Slide 10: Damage risks
What does a 99% coverage mean in terms of damage risks?
  Assume 1 asynchronous dump per year
  Assume 1% of the time the margin dump-TCT is violated (uncorrelated to async. dump)
  Assume 1/3 of the time spent in stable beams => 1 event in 300 years could be dangerous for the TCTs
  Assume 1% of the time the margin TCT-triplet is violated => 1 event in 30000 years could be dangerous for the triplets
  This considers only orbit. Simultaneously all other errors have to add up pessimistically at both locations. => The real risk is much lower!
  In case of the TCT being hit by a bunch there is no catastrophic damage, most likely it will be scratched and we can use a spare surface (see talk A. Bertarelli in Chamonix)
To further reduce the risk we propose interlocks or warnings before the orbit runs out of limit

## Slide 11: Proposed margins and settings
Summing linearly we get the margins
and the settings
Assuming IP2 remains at larger margins. Proposed settings very similar to what was used in 2010 run with β*=2.0m

## Slide 12: Operational proposals
Reduce the separation at the IPs to its nominal value of 0.7 mm
Measure the triplet aperture locally
β-beating below 10%, reproducibility 5%, bias at TCTs/triplets
Interlocks or warnings to reduce damage risk further
New settings to be qualified with loss maps and async. dump tests. Problems => margins and β* to be increased
cleaning hierarchy to be verified on a regular basis
Detailed study to correlate n1 calculation and measurements

## Slide 13: Reach in β*
Minimum β* calculated for three options, using n1 and scaling method:
  2010 margins
  2011 margins (as calculated on previous slide)
  Nominal collimator settings with increased beam-beam separation
Assumptions in calculations:
  Always taking min margin over all IPs, planes and beams
  Minimum β* given by intersection between interpolation and desired margin (see slide 9)
  Using nominal 0.7 mm separation and nominal emittance
  Using measured β-beat at injection and top energy with 5% reproducibility, 10% β-beat in n1 calculation
  Assuming max 2 mm orbit shift in pessimistic direction between measurement at injection and top energy , 2.3 mm orbit in n1
  Assuming 12 σ beam-beam separation (larger than nominal)
  Triplet aperture at injection assumed 2 σ larger than global limit

## Slide 14: Results n1

## Slide 15: Results with aperture scaling

## Slide 16: Conclusions
Reviewed both aperture estimate and margins
  Measurements show larger aperture, orbit and β-beat better than traditionally used in n1-model
  TCTs can be moved in closer to dump protection
Choice of β* should maximize performance without risking safety
Proposal: start at 4 TeV, β*=1.5m, 2011 margins
  Measure local triplet aperture
  Collimator settings to be qualified through provoked losses before being used during runs

## Slide 18: Backup – orbit during fill IR2

## Slide 19: Backup – orbit IR1