## Slide 1: What if the dump does not work ?
Aim to define a procedure in case a programmed or manual (OP switch) dump does not work.
Define a sequence of actions to be executed one after the other until we reach the last resort of scraping the beam.
  Step1: in case of programmed dump, use the switch and vice-versa. Note that both programmed dump & switch enter the CCC BIC
  Step2: Try to trigger the BIS without doing harm to the beam.
    Activate the AC dipole.
    If in STABLE BEAMS, go to ADJUST without handshake.
    Trigger a SIS interlock.
  Step3: Try to trigger the LBDS ‘internally’.
  Step4: Move the beam to 1/3 resonance to lower the lifetime and scrape the beam out slowly.

## Slide 2: LBDS triggering without BIS
If for some reason the problem is ‘between BIS and LBDS’, we could try to provoke an internal trigger of the LBDS.
Question: how?
  Can we re-use the inject-dump trigger mechanism via external timing event (not with the injection events as they difficult to generate)?
  Define a trigger on another reserved event?
  Can we trigger a internal failure through some of the internal monitoring?
  ?