## Slide 1: Overview of single bunch asynchronous dump failures on collimators
Luisella LARI
For the collimator team
Special thanks to R.W.Assmann, R.Bruce, A.Rossi
BE/ABP
9th March 2012
MPP meeting

## Slide 2: Summary of what was done
Scan over the MKD pre-fire pulse form to find the angle for which the TCDQAs are by-passed for possible misalignment  for each MKD failure mode (each 1 MKD studied separately)
Once find the angles  scan all over the LHC machine to find the elements that are touched by the beam 1 or 2 kicked, playing with the location of the faulty MKD:
  Results for impacts with beam center
  Results for impact with 1/2/3 sigma x
Particular attention was done for possible interactions with TCTs and/or TCLAs.
1 jaw
1 jaw
1 sx
2 sx

## Slide 3: Reference case
”Configuration for 2012”
Collision energy = 4TeV,
Crossing and Spectrometers switched ON [4TeV145 mrad half crossing angle in IP1 and IP5]
Physics run with 0.6 m beta* in IP1/5 & 3.0 m beta* in IP2/IP8 (i.e. SEP OFF),
Ref. optics “as-built” thin V6.503
Transverse normalized emittance 3.5 mm rad
7TeV
ON
2.5

## Slide 4: Collimator Aperture  4 TeV
TCP.IP7 | 4.3
TCSG.IP7 | 6.3
TCLA.IP7 | 8.3
TCP.IP3 | 12
TCSG.IP3 | 15.6
TCLA.IP3 | 17.6
TCT.IP1.IP2.IP5.IP8 | 9.0
TCL.IP1.IP5 | 10
TCLI/TDI.IP2 | Tot opened
TCDQ.IP6 | 7.6
TCSG.IP6 | 7.1
Beam 1
Beam 2
&
Ref: Evian 2011 – R.Bruce

## Slide 5: Scan over the MKD pre-fire pulse form (1)

## Slide 6: Scan over the MKD pre-fire pulse form (2)
Around 7mrad TCDQAs by passed TCSG@IP6
by considering B1 or B2 and
by the location of the MKD with problem
But if we are looking for the effects on the downstream elements (TCT, TCLA) the worst is to consider an error in the alignment of the TCDQAs position (i.e. max 1.5 mm)  means GO TO ANGLE > 7 mrad

## Slide 7: Point 7!
Beam 2
Beam 1
In MADX to select the “worst” scenario for further studies

## Slide 8: Beam1
Chart: 
| TCDQA.A4R6.B1 | TCDQA.B4R6.B1 | TCSG.4R6.B1 | TCP.C6L7.B1 | TCP.B6L7.B1 | TCSG.6R7.B1 | TCLA.B6R7.B1 | TCLA.D6R7.B1 | TCTH.4L1.B1 | TCTH.4L2.B1 | TCTH.4L5.B1
 | 34.3683 | 34.2761 | 53.6604 | 39.6584 | 1.7181 | 81.3971 | 12.4601 | 2.5338 | 0.67169 | 3.7513 | 3.1742
% of intercepted beam, Gaussian distribution (error function)
Failure MKD.A5L6.B1
1.95 [ms]; +12.39910241 [mrad]

## Slide 9: Beam1
Failure MKD.A5L6.B1
1.95 [ms]; +12.39910241 [mrad]
Chart: 
| TCDQA.A4R6.B1 | TCDQA.B4R6.B1 | TCSG.4R6.B1 | TCP.C6L7.B1 | TCP.B6L7.B1 | TCSG.6R7.B1 | TCLA.B6R7.B1 | TCLA.D6R7.B1 | TCTH.4L1.B1 | TCTH.4L2.B1 | TCTH.4L5.B1
 | 1.5756 | 1.5919 | 1.9202 | 0.95081 | 0.29833 | 1.9519 | 0.64486 | 0.24075 | 0.57133 | 0.52253 | 1.3001
mm [abs] inside the jaw

## Slide 10: Beam1
Failure MKD.A5L6.B1
1.95 [ms]; +12.39910241 [mrad]
Chart: 
| TCDQA.A4R6.B1 | TCDQA.B4R6.B1 | TCSG.4R6.B1 | TCP.C6L7.B1 | TCP.B6L7.B1 | TCSG.6R7.B1 | TCLA.B6R7.B1 | TCLA.D6R7.B1 | TCTH.4L1.B1 | TCTH.4L2.B1 | TCTH.4L5.B1
 | 2.5976 | 2.5951 | 3.0919 | 2.7378 | 0.8842 | 3.8926 | 1.8477 | 1.0458 | 0.52794 | 1.2197 | 1.1442
Sigma (x) inside one jaw

## Slide 11: Beam2
Same failure situation for the different MKD locations
Chart: 
| TCDQA.A4L6.B2 | TCDQA.B4L6.B2 | TCSG.4L6.B2 | TCTH.4R5.B2 | TCTH.4R1.B2 | TCP.C6R7.B2 | TCP.B6R7.B2 | TCSG.A5R7.B2 | TCSG.B4R7.B2 | TCSG.A4R7.B2
 | 32.4864 | 32.2302 | 51.224 | 0.1831 | 0.35507 | 91.3368 | 53.2944 | 6.9825 | 80.2794 | 0.24718
% of intercepted beam, Gaussian distribution (error function)

## Slide 12: Beam2
mm [abs] inside the jaw
Same failure situation for the different MKD locations
Chart: 
| TCDQA.A4L6.B2 | TCDQA.B4L6.B2 | TCSG.4L6.B2 | TCTH.4R5.B2 | TCTH.4R1.B2 | TCP.C6R7.B2 | TCP.B6R7.B2 | TCSG.A5R7.B2 | TCSG.B4R7.B2 | TCSG.A4R7.B2
 | 1.6475 | 1.662 | 2.0094 | 0.097272 | 0.37157 | 1.6527 | 1.1358 | 0.5699 | 1.3696 | 0.064916

## Slide 13: Beam2
Same failure situation for the different MKD locations
Sigma (x) inside one jaw
Chart: 
| TCDQA.A4L6.B2 | TCDQA.B4L6.B2 | TCSG.4L6.B2 | TCTH.4R5.B2 | TCTH.4R1.B2 | TCP.C6R7.B2 | TCP.B6R7.B2 | TCSG.A5R7.B2 | TCSG.B4R7.B2 | TCSG.A4R7.B2
 | 2.5459 | 2.5387 | 3.0307 | 0.094099 | 0.30795 | 4.3618 | 3.0827 | 1.5229 | 3.8516 | 0.18931

## Slide 14: Conclusion  Next steps
First selection of cases for B1 and B2 using this preliminary studies with tight collimation settings.
Following SixTrack simulations using realistic beam distribution.
Consider magnet errors could change the hierarchies of the impacted collimators.
Changing the aperture of collimators  change the pattern of the loads on downstream collimators/beam elements (needed FLUKA simulations).
Courtesy F. BURKART

## Slide 15: Additional slides
Luisella LARI
BE/ABP
9th March 2012
MPP meeting

## Slide 16: Collimator Aperture  7 TeV
TCP.IP7 | 6  4.3
TCSG.IP7 | 7  6.3
TCLA.IP7 | 10  8.3
TCP.IP3 | 15  12
TCSG.IP3 | 18  15.6
TCLA.IP3 | 20  17.6
TCT.IP1.IP2.IP5.IP8 | 8.3  9.0
TCL.IP1.IP5 | 10
TCLI/TDI.IP2 | Tot opened
TCDQ.IP6 | 8  7.6
TCSG.IP6 | 7.5  7.1
Beam 1
Beam 2
&

## Slide 17: Optics IP6
&
Beam 1
Beam 2