## Slide 2: MPP Workshop 2013 Executive summary Acknowledgements: B.Dehning, S.Redaelli, J. Uythoven, J.Wenninger, D.Wollmann, M.Zerlauth in the name of all Workshop particpants

## Slide 3: Mandate
Discuss mid-and longer-term improvements of the MP systems for the LHC + injector complex:
  review of the current operational experience with MP systems during the first running period (2009-2013).
  understanding the planned changes of MP equipment during LS1 and the consequences/potential limitations for operation after LS1.
  identify areas where improvements are required.
  ensuring coherence between the different MP systems.
  identify misses.

## Slide 4: Program
Indico Page
6 sessions, 2 ½ days, ~ 85 participants
  MPS experience (2008-2012) and outlook (D.Wollmann)
  Injection and LHC beam dumping system (J.Uythoven)
  Beam Diagnostics (B.Dehning)
  Collimation and movable devices (S.Redaelli)
  Electrical circuit related protection (M.Zerlauth)
  Operation after LS1 (J.Wenninger)
  Summary and discussion (R.Schmidt)
Executive summary @ CERN in special LMC (today)
More detailed session summary in ATS Seminar (tbd)

## Slide 5: Goal today…
Agree on a common MP view of issues
Complete the list if needed
Agree/define responsibilities for follow-up
Definition of priorities to be completed for LMC
More detailed session review in ATS seminar (tbc)
Follow up of issues already started and will be coordinated in different WGs and MPP meetings

## Slide 6: Material Damage / failure scenarios
Review/Update Setup Beam Flag parameters/functions (SMP) in view of updated damage limits, commissioning procedures, collimation setup, MDs etc. (MPP with Coll, FLUKA, MPE, ABT)
  Onset of damage? Dependency on emittance (BCMS beams); 7TeV
  Conclusion by beginning 2014
Use of collimators with new materials (molybdenum, copper-diamond?). (ABP, EN-MME/STI, ABT, MPE) [replacing winter stop 2015/16?]
  Mini-WG to analyse results of material tests and feedback into Coll upgrade strategy (CWG).
  Update failure cases for asynch beam dump (worst case phase advance / realistic phase advance). (later 2013; Coll [Roderik, Luisella], ABT)
  Study ion beam damage. (ABP [Luisella, Maria])
  Planning of new tests with beam in HiRadMat.

## Slide 7: Material Damage / failure scenarios
Review / update LHC failure scenarios and expected damage (single/two kickers firing).  Expected beam offset/kick.
  Estimate damage in case of one kicker firing (25ns, BCMS, new TCDQ, … ). (MPE, ABT)
  (Disposable) absorbers, redundant kickers.
New working group to discuss beam induced heating issues &validate new designs (ABP [Elias, Benoit, et al.], Equipment teams, MPP)
Review operational scenarios in the view of MP (D1 failure, etc.) and collimation. (OP, Coll, ABP  LBOC / Evian like workshop in 2014 ?!):
  combined ramp +squeeze.
  beta* leveling.
  lower beta* at injection.
  Optics changes in IR2 + IR8 for 7TeV.

## Slide 8: Injection / LBDS
BIS-LBDS retriggering: high reliability required. Reliability run planned for beginning of 2014 (04.2013  ABT, MPE [Stephane]).
Scan of MKD waveform with beam and direct BLM dump  Test @ injection during commissioning 2015? (LIBD [Jan])
TDE block: pressure rise may reach venting level, when repeated dumps occur 6.5/7TeV. What is the criticality? (LIBD [Jan])
TCDQ in BETS (masking for set-up). Review failure cases. (04.2013  LIBD [Jan], MPP).
MSI current and TDI gap (how measured?) into BETS. Re-do failure analysis. How tight need the tolerances to be? (04.2013  LIBD [Jan], Coll [Stefano], MPP)

## Slide 9: Injection / LBDS
TCDIs: virtual beta* and interlocking in SIS via SMP timing.  Specifications (OP [Jorg, Verena], LIBD [Jan], Coll [Stefano]).
SPS extraction interlocking. (OP [M. Interlock])
TDI gap supervision from SIS to BIS. Redundant gap measurement? (EN-STI, MPP)
Beam position in TCSG (IR6) interlock from SIS to BIS. (MPP)
  Keep for start-up as is, then interlock with buttons implemented in jaws.
  Functional spec on how to use buttons ([COLL])

## Slide 10: Commissioning / Revalidation of MP systems / Powering tests
Review / update commissioning procedures: (All teams, MPP)
  Update existing commissioning procedures. (Coll [Belen], Powering Interlocks [Ivan], ABT [Yan et al?], …)
  ACCTEST framework for commissioning and revalidation.
  Define (non-negotiable) re-validation tests for MP systems in case of system changes (Asynch dump, Loss maps, PC tests, QPS tests, … ).  Risk analysis (600A, main bends, … ).  Define procedures accordingly.
  Tracking of Changes (see also software tools).
Powering tests: efficient execution tools, but analysis bottle neck. More automatic analysis tools needed/possible? (MP3, MPE)

## Slide 11: Powering Interlocks / QPS / Electrical distribution
QPS and BLM systems will be completely removed from the tunnel and re-installed during LS1 (ECR [BLM team])
QPS: Change of strategy for implementation of critical upgrades when running at 6.5TeV/7TeV? Currently: firmware improvements can only be implemented in long shutdowns? (MPE)
FMCM: improve performance, dependability analysis. (MPE)
UPS consolidation + new switching frequency: 4kHz, 7kHz … discuss frequency change (tune, … )? (EN-EL, ADT-Team)
COD current checks from SIS to PC-Interlock. (OP, MPE)
Extend PC interlocks (Kajetan) to other PCs. (OP, MPE)
Interlocking fast power aborts for CMS / LHCb / 60A corrector states in BIS. Redundancy to BLM system. (MPP)

## Slide 12: Software tools / Operation
Tracking of changes in MP systems (HW exchange, expert masking, … )  Software tool, procedures (MPP with input from equipment teams?).
XPOC: improve/reduce number of false latching (warning level / latching). (ABT, OP, MPP)
IQC: improve to require fewer resets (warning level / latching). (ABT, OP, MPP)
Additional PM modules. (OP, ABT, Coll, MPE) [after powering tests, during 2015?]
Review Alarms in LASER, Review / Improve fixed displays, Review SIS GUI. (LBOC, OP with Equipment teams)
Aperture meter for ring and transfer lines. (LBOC, OP, ABP, ABT)
Online model for ring and transfer lines. (ABP)

## Slide 13: Software tools / Operation
Applications for BLM system: Internal parameters app, system status app, system management app, monitor factor app. Additional RS and higher resolution of BLMs in PM. (BI, MPP)
Facilitating loss-map checks. (Coll, OP)
Masks /SFB consistency check before beginning of ramp to avoid false dumps. (Sequencer task [OP])
Testing of BIS inputs: automatically (Acctest), manually?
  Regular re-check of BIS-channels (once per year?).
  Review BIS-channel triggering from TIMBER after dumps, during ramp-down, access, … .

## Slide 14: MPP / rMPP / MDs / Fault tracking
Maintain rMPP after LS1:
  Update membership.
  rMPP piquet: dump analysis, follow-up on operational issues, contact to coordinators and operational crews.
MPP <-> MP3 improved interplay for magnet powering systems.
MD documents: Prepare / propose table of required information. (LSWG, MPP)
Review / Update MP procedures for OP. (MPP)
Availability Matrix for all LHC systems with use case for ~2 weeks with examples for the different equipment. (AWG)
Implementation of a fault tracker. (AWG)

## Slide 15: Moveable Devices
TCDQ upgrade: new interlocking strategy as other ring collimators? (ABT, MPP)
How to use Collimators with buttons? (Coll [Stefano, Gianluca], BI, MPP)
  Interlocking (TCSG-IR6, TCT, OFB, … )
  How to link LVDT-gap measurements and button measurements?
Momentum loss maps with reduced RF frequency change? (Coll)
Verification of settings. (Coll)
Collimator (TCT) position limits as function of separation. (Coll) [04.2013]

## Slide 16: Beam Instrumentation (high priority)
BPMS (IR6) improved dynamic range and PM buffers (to XPOC). (MPP)
DIDT ?!
LICs in injection region. Thresholds / protection / energy level 0? (MPP, BI, ABT)
Inhibit BLMs in injection region? Which BLMs? What discrimination time? Which signal? (MPP, BI, ABT)
Reliable/redundant abort Gap Monitoring: System which can also dump?! (MPP, BI, MPE, ABT, Alice, ADT-team)
Improved reliability of OFB. (Review in May 2013, BI)

## Slide 17: Beam Instrumentation
BLM thresholds for 7TeV (QP3 extrapolation, Quench test analysis). (TWG, QTAWG, MPP)
BLM threshold generation via LSA. (BI, MPP)
BI follow-up on BLM thresholds after Eduardo? Two people follow-up?
BLM displacement  ECR. (BI)

## Slide 18: Internal Reviews
Direct link from BIS to LBDS retriggering line.
LBDS retriggering (kicker testing, two kicker firing, … ).
QPS: Quench loop of RBs.
Collimation (May 2013).
HL-LHC
Crab cavities studies: quench behavior of sc. Cavities. (MPP)
Beam-beam kick in case of HL-LHC beam parameters. (MPP)
Protection of beams with depleted beam halos (Movable devices, Vacuum valves, … ) (Coll, MPP)
Prototype crab cavity in SPS: interlocking?

## Slide 19
End