## Slide 1: Testing with Beams: WP11 report on TNA
5 Accelerator Test Facilities for ARIES Trans National Access
WP11.1 KARA at KIT: Karlsruhe Research Accelerator, a synchrotron storage ring up to 2,5 GeV electron energy
WP11.2 FLUTE at KIT: Ferninfrarot Linac- und Test-Experiment accelerates ultra-short e-bunches 5 to 50 MeV
WP11.3 IPHI at CEA: Injector of Proton for High Intensity accelerates a 100 mA continuous p-beam up to 3 MeV
WP11.4 ARES at DESY: Accelerator Research Experim. at SINBAD accelerates ultra-short e-bunches up to 155 MeV
WP11.5 VELA at STFC: Versatile Electron Linear Accelerator ultra-high-performance injector up to 50 MeV, 250 pC Robert Ruprecht, Florian Burkart, Anthony Gleeson, Michael Nasse, Marcel Schuh, Jerome Schwindling et al.
Contact: Robert Ruprecht@kit.edu

## Slide 2: ARIES-TNA-WP11.1 KARA, KIT
Beam dynamics studies in the negative momentum compaction factor αc regime in an e- storage ring
Joint measurement campaign with SOLEIL and PSI
  negative alpha optics at 500 MeV
  Operation with different tunes, chromaticity and alpha
Collaboration with ARIES - WP7
P. Schreiber et al, DOI:10.23732/CYRCP-2020-009.297
Contact: Marcel.Schuh@kit.edu
    Courtesy: P. Schreiber, M. Brosi, A. Papash et al.
Large orbit deviations necessary for injection
Measurement of bunch length @ beam current
Notes: Studied the injection orbit at low and negative alpha condition, the bunch length with a streak camera and the THz emission dynamics as function of alpha. Beam characterization, dynamics studies, and the study of collective effects

## Slide 3: ARIES-TNA-WP11.1 KARA, KIT
BESTEX at KARA
  FCC-hh Beam Screen prototypes including the baseline design tested at CERN’s BESTEX beamline at KARA
  test under cryogenic conditions (liquid Nitrogen cooling)
L. A. González et al,DOI: 10.1103/PhysRevAccelBeams.22.083201
TNA [h] | P3 | overall
KARA | 558 | 2746
Contact: Marcel.Schuh@kit.edu
    Courtesy: R. Kersevan et al.
Notes: Partners CERN, INFN (I), Ciemat (ES), KIT (D)

## Slide 4: ARIES-TNA-WP11.2 FLUTE, KIT
Split Ring Resonator (SRR) experiment
Goal: single shot longitudinal diagnostics based on THz-driven streaking using a SRR amplifier
International collaboration with the University of Bern and PSI
Priniciple:
    Courtesy M. Nabinger
20 µm
1 mm
    Photos M.J. Nasse
4
TNA [h] | P3 | overall
FLUTE | 320 | 456
Contact: Michael.Nasse@kit.edu

## Slide 5: ARIES-TNA-WP11.2 FLUTE, KIT
Status of SRR experiment
THz generation adjusted in photoinjector optical setup in experimental hall reaching a conversion efficiency of 0.027% [5]
[1] J. Fabiańska et. al., Sci. Rep. 4, 5645 (2014) [2]V. Schlott et al, IBIC 2017, TUPCC16 (2017) [3] M. Yan et al, IPAC 2018, WEPAL029 (2018) [4] M.J.Nasse et al., IPAC2019, MOPTS018 (2019) [5] M. Nabinger, master thesis KIT (2021) [6] C. Sax, master thesis KIT (2021)
  Many experiment done, no streaking observed yet
Uncompressed IR pulses from laser lab
Cu cathode
SRR chamber
Electrons
Compressor
gun
Compressor
THz gen. SRR
THG
Pulse picker
TPF THz generation
  Done: control transversal and longitudinal laser beam shape with spatial light modulators [6]
    Courtesy: M. Nabinger, C. Sax, M.J. Nasse
Contact: Michael.Nasse@kit.edu

## Slide 6: ARIES-WP11.3 IHPI, CEA
ESS BILBAO Beam Position Monitor
Profile monitors for ESS
Emittance meter for MYRTE / MYRRHA
The accelerator IPHI was running during 4 weeks in September – October 2018 to accommodate experiments including tests of the BPM + electronics from Bilbao + ESS (TNA)
3 MeV protons

## Slide 7: ARIES-TNA-WP11.3 IHPI, CEA Saclay
Beryllium target + cooling inside ½ moderator + shielding
Since then, most time devoted to tests of neutron production using Beryllium targets in view of the French compact neutron source project SONATE
1st version of the target operated during ~ 100 hours at ~ 3.5 kW (500 W/cm2)
A 50 kW version has been developed and tested in 2021
Because of this program and lack of TNA users, IPHI was not involved in TNA extension
Work financed by a grant from the Ile – de – France region
TNA [h] | 2020 | Overall
IPHI | 0 | 72

## Slide 8
First successful external user experiments at SINBAD/ARES: S band linac
PSI wirescanner tests to characterize electron bunches with micron precision
ARIES-TNA-WP11.4 ARES, DESY
Contact: florian.burkart@desy.de
Wirescanner with 1 micron thick gold wires.
Installed in the ARES UHV experimental chamber
Measured loss signal
Reconstructed beam
Project Leader: Dr. Pavle Juranić
“Successful test of the wirescanner at ARES and successful characterization of the electron bunch for both a 2D and 4D scan with extremely high resolution.”
TNA [h] | 2021 | overall
ARES | 77 | 210
    Courtesy: F. Burkart
Notes: Before/to Dot3: Shutdowns heavily delayed due to Corona restrictions / shutdowns at external companies.
Therefore full completion of ARES in mid 2021. first internal users
To Dot4_ Internal users = Accelerator on a Chip collaboration with limited numbers of people allowed in the control room, results to be published.

## Slide 9: ARIES-TNA-WP11.4 ARES, DESY
Contact: florian.burkart@desy.de
TNA [h] | P3 | overall
ARES | 242 | 242
2nd TNA at ARES: normal conducting S-band electron linac
High energy & high dose irradiation of diamond samples
3 mm x 3 mm x 0.3 mm
thick diamond plate
Exploring the physics of high energy electron irradiation of diamond for increasing the yield of nitrogen vacancy (NV) center creation, with potential benefits for quantum sensing.
Project Leader: Prof. Dr. Christophe Galland, Dr. Elena Losero
beam irradiation finished,
analysis ongoing
    Courtesy: F. Burkart
Notes: 1 mol% holmium-doped yttrium lithium fluoride (YLiF4)
Unclear, if possible TNA users can come to ARES in 2021.
210h units expected until the end of TNA in 2022.

## Slide 10: VELA: Status
TNA units delivered in this period: 104
The final period saw successful delivery of TNA for DESY (Knetsch et al) following-up on their previous work on plasma afterglow metrology and for PSI (Frojdh et al) evaluating the Jungfrau hybrid pixel detector for electron diffraction at MeV energies.
A VELA/CLARA user meeting will be held on 5th July 2022 at Daresbury Laboratory to celebrate completion of the latest exploitation run (including TNA) and provide information on forthcoming machine updates and schedules.
ARIES-TNA-Experiments within WP11.5
Contact: Anthony.Gleeson@stfc.ac.uk

## Slide 11: VELA: Status
The VELA/CLARA facility will now undergo further developments to complete CLARA Phase 2, including commissioning of the 250 MeV Full Energy Beam for Exploitation (FEBE) facility
The next round of beam exploitation is anticipated in 2024, with the intention to offer TNA access to VELA/CLARA under the Horizon Europe EURO-LABS project.
ARIES-TNA-Experiments within WP11.5
TNA [h] | P3 | overall
VELA | 104 | 184
Contact: Anthony.Gleeson@stfc.ac.uk

## Slide 12: ARIES-TNA-Experiments within WP11
ARIES-TNA WP 11 | TA in P3 for remote [h] | TA for users in 5 years, all [h]
KARA (ANKA) | 558 | 2746
FLUTE | 320 | 456
IPHI | - | 72
ARES (SINBAD) | 242 | 242
VELA | 104 | 184
Overview, Boundary Conditions, and Outlook:
Corona Virus Covid 19: lock-downs, no travelling in EU, worldwide
Only remote users in 2020 to 2022
KARA and FLUTE delivered more TNA as planned in Annex 1
SINBAD operation in P3, two proposals in 2021/22
VELA with technical delay, start-up in Q3-2021
IPHI closed ARIES-TNA after 4 years
Contact: Robert Ruprecht@kit.edu
Robert Ruprecht, Florian Burkart, Anthony Gleeson, Michael Nasse, Marcel Schuh, Jerome Schwindling et al.

## Slide 13: ARIES-TNA-WP11.1 KARA, KIT in P1
Optics characterisation at KARA including the high wiggler field
Tune and chromaticity measurements based on turn by turn orbit data using NAFF
Presented at the 1st ARIES Annual Meeting by P. Zisopoulos
NAFF = Numerical Analysis of Fundamental
Frequencies allows a fast convergence to the tunes in the order of 1/N4
P. Zisopoulos et al., https://indico.cern.ch/event/699219/contributions/2929063/ attachments/1654466/2647866/ARIES18_Zisopoulos.pdf
Contact: Marcel.Schuh@kit.edu
Notes: The Numerical Analysis of Fundamental Frequencies (NAFF) allows a fast convergence to the tunes in the order of 1/N4