## Slide 1: IST SEM systems PS YETS 2021-2022 @ BI PS meeting - 23-02-2022 Aurélie Goldblatt , Jean Tassan, Michel Duraffourg, FR Description of the tests: - Test of the movement where applicable -connectivity tests in situ where needed - Use of LabView app and/or FESA to inj test signals and check acquisition - When possible, injection of a test signal with LabView app inside vacuum and on amplifiers Few details on next slides, especially about open issues
More Details (for all SEMs in PS complex): EDMS 2694859 v.1

## Slide 2: PS Inj - SEMs
PI.BSGF42: 42_2 (2d amplifier) ch15 very weak
PI.BSGF48, 52, 54: (TxT)
  Ana Guerrero and Jean Tassan-Viol found that when the FESA setting “integration time” is set to maximum, the acquisition is realised only every second trigger, not all of them.
    If this setting is set just a bit below the max, everything is fine.
  There is the need to send 2-3 times the command in order the grid moves. Ana had a look and found that the FESA layer doesn’t send systematically the command to PLC layer. Correction to be tested during hardware commissioning.
Ready for operation, need to double check:
SEM – RAL interlock (?)
SEM 48-52-54 in-out

## Slide 3: TT2 BSGs
F16.BSGF257 H: Pressure leak in IN position, Christophe Vuitton made an adjustment on 21st January, should be fine.
F16.BSGF267 H: small pressure leak in OUT position, Christophe Vuitton made an adjustment on 21st January, should be fine.
F16.BSG268 HV: ch26 no signal
F16.BSG277 HV: ch15 weak signal
Ready for operation, few channels faulty