## Slide 1: Pulsed and continuous neutron beams at the CNA HISPANOS facility
Carlos GUERRERO
Universidad de Sevilla, 41012 Seville, Spain
Centro Nacional de Aceleradores (CNA), 41092 Seville, Spain
41st RD50 Workshop on Radiation hard semiconductor devices for very high luminosity colliders

## Slide 2
Some general considerations

## Slide 3: Neutron moderation process
Continuous neutron scattering end up with the neutrons in thermal equilibrium with the medium:
MB distrib. with characteristic kT

## Slide 4: Neutron energy ranges
Colonna et al., PPNP 2018

## Slide 5: Continuous vs. pulsed beams: time-of-flight
neutron start
neutron stop
neutron time-of-flight experiment
Time-of-Flight to En relation (non-rel.):
=> En resolution increases with L
time
Continuous: Neutrons of all energies “together”:
=> integral effects (not a problem if spectrum adequate)
Examples:
- Irradiation (thermal, atmospheric, etc.)
- Production of radioisotopes
- Activation for a given spectrum
Pulsed: allows for time-of-flight
  => time of arrival provides neutron kinetic energy
  => differential experiments => X(En)

## Slide 6
Neutron production

## Slide 7: Neutrons produced by fission

## Slide 8: ILL (France): 1015 n/cm2/s @core (~meV)

## Slide 9: Neutron producing nuclear reactions (I)
In two-body reactions monoenergetic neutrons can be produced, e.g. DT-reaction: T(D,n)4He, Q = 17.16 MeV
Kinematics determines the angular distribution and energy spectrum
The yield (neutrons /primary particles) is determined by the differential cross section
Realistic yield determination by integration over the target thickness and angular range (slowing down of the beam in the target material)

## Slide 10: Neutron producing nuclear reactions (II)

## Slide 11: Monoenergetic (& quasi) neutron beams
dashed lines: quasimonoenergetic range indicated, due to breakup T(p,n), D(d,n) 7Li(p,n)7Be*
(7.7 – 13.2 MeV)
Reaction | 7Be* Exc. Energy (MeV) | Q-value (MeV) | Threshold (MeV)
7Li(p,n)7Be | 0 | -1.644 | 1.881 forward 1.920 backward
7Li(p,n)7Be* | 0.429 | -2.073 | 2.371 forward 2.421 backward
7Li(p,n3He)4He | break-up | -3.229 | 3.692
7Li(p,n)7Be** | 4.57 | -6.214 | 7.110 forward 7.260 backward

## Slide 12: Nuclear reactions with high energy ions
GANIL’s SPIRAL-2, a Superconducting Linear Accelerator:
40 MeV deuteron and 33 MeV protons
Beam current 5 mA, i.e. rotating target
Flight path 5 to 10 meters
Frequency=0.25-1 MHz
Flight path: 5 – 30 m
Energy range: 0.1- 40 MeV
Low -flash background
Low instantaneous flux
High repetition rates

## Slide 13: Neutron production by spallation
Nucleon-Nucleus collisions at relativistic energies
Tcoll < 10-22s : Collisions of the projectile nucleon with nucleons in the target (Intranuclear Cascade, emission of fast particles ,n,p,…)
Tequil> 10-21s – 10-16s Reorganisation of the residual nuclei, thermalization, particle evaporation (n,p,d,,…), gamma ray emission
Relativistic protons
impinging on heavy
target nuclei
Fast neutrons emitted
during collision
and afterwards from
excited residual nuclei
-flash from pion decay

## Slide 14
n_TOF at CERN

## Slide 15: The n_TOF facility at CERN (I)

## Slide 16
The n_TOF Facility at CERN (II)
PS 20 GeV
Linac
50 MeV
Booster
1.4 GeV
Proton Beam
20 GeV/c
7x1012 ppp
Pb Spallation Target
Neutron Beam
10o prod. angle
n_TOF-EAR1 200 meters
n_TOF-EAR2
20 meters
n_TOF-NEAR
3 meters

## Slide 17: The n_TOF Facility at CERN (III)
MeV to GeV range
Three pulsed beams available:
- EAR1 (185 m): ~ 106 -107 neutrons/pulse
- EAR2 (20 m): ~108 neutrons/pulse
- NEAR (3 m): expected 109 neutrons/pulse
ENERGY RESOLUTION

## Slide 18
HISPANOS at CNA

## Slide 19
HiSPANoS is the first Accelerator-based neutron source in Spain and it is installed at the the 3 MV Tandem Accelerator.
Continuous & Pulsed
HiSPANoS at the 3 MV Tandem Accelerator

## Slide 20
Chopper
Buncher
Wien Filter
Neutron Time-Of-Flight line
Pick up
target
HiSPANoS at the 3 MV Tandem Accelerator
HiSPANoS is the first Accelerator-based neutron source in Spain and it is installed at the the 3 MV Tandem Accelerator.
Continuous & Pulsed

## Slide 21
Chopper:
Variable width: 40 ns-250 ns
RR: 31.25 kHz-2MHz
Switcher Voltage: 650 V
250 kHz
250 ns
RR verification
4µs (250 kHz)
Pulse width verification
Chopper
Buncher
Beam
B. Fernández XIII CPAN Days 21-23 Marzo 2022
Pulsing system: p,d & α

## Slide 22
Chopper
Buncher
Beam
Buncher:
Needs tuning (delay & power) for synchronization
1.5 ns
Capacitive pickup signal
B. Fernández XIII CPAN Days 21-23 Marzo 2022
g-flash
Pulsing system: p,d & α

## Slide 23
Target | Geometry | Reaction [Q value] | E beam (MeV) | Neutron spectra
Li (metallic) | Ø 10 mm Thickness < 1mm | 7Li(p,n) [-1.7 MeV] | Ep=1.912 | quasi-Maxwellian@kT=30keV Thermal by means of moderation
LiF (Evaporated on Cu) | Ø 30 mm Thickness: 16 µm |  |  | 
D:Ti >1.5 | Ø 30 mm D/Ti (500 µg/cm2) | D(d,n) [3.3 MeV] | Ed=0.5-6 | Quasi-monoenergetic between 3-9 MeV
Be | Square: 25 mm Thickness: 3 mm | 9Be(p,n) [-1.9 MeV] | Ep=2.1-6 | Continium from keV to En~Ed-2.1MeV
 |  | 9Be(d,n) [4.4 MeV] | Ed=0.5-6 | Fast between 4 and 10 MeV
Neutron production targets/mechanism
EJ301 @0o
EJ301 @30o
Be target
100 cm
PickUp
HiSPANoS
monoenergetic

## Slide 24
Medical Physics applications PULSED
7Li(p,n)7Be @1912 keV
7Li(p,n) 7Be@ 1950 keV for BNCT evaluation
Neutron field and activation measurements for…
10uA protons on a water cooled Li target
Astrophysics applications PULSED & CONTINUOUS

## Slide 25
  @HISPANOS: Be(d,n) + time-of-flight
  H2020-ARIEL TA => January 2022
Neutron sensitivity of i-TED for neutron capture at CERN n_TOF (with CSIC-IFIC) PULSED
Characterization of C7LYC for fast (2,5 MeV) neutron diagnostic in fusion (with INFN-MIB) PULSED
Development of the ANTILOPE detector
(with CIEMAT & n_TOF) CONTINUOUS
+ CERN n_TOF: s(n,g) measurements by ToF
+ Scattered neutrons: main background
Carachterization of detector response to epitermal neutrons => 7Li(p,n) + time-of-flight
Detector characterization

## Slide 26
Neutron production from (a,n) reactions for dark matter searches and astrophysics PULSED
(The MANY Collaboration: CNA, CMAM, CIEMAT, UPC, IFIC, UPM)
Development of the capabilities to measure (n,cp) reactions by ToF PULSED
Measurements at CNA (cont.& pulsed) and CMAM (cont. only) with the detectors:
miniBELEN
MONSTER
MONSTER module@HISPANOS
6Li(n,a)3H
3H
a
MONSTER@JYFL
Cross sections measurements

## Slide 27
Identification of elements in large samples by PGA (with UPV & IDOM) CONTINUOUS
Neutron Imaging
X-ray imaging
Neutron, gammas and x-ray imaging
CONTINUOUS
Gammagraphy (60Co irradiator)
B. Fernández XIII CPAN Days 21-23 Marzo 2022
Imaging and material inspection

## Slide 28
Dosimetric mapping & dosimeter intercomp. with fast (MeV) neutrons (with UPM) CONTINUOUS
Buds irradiation with fast (MeV) neutrons
(Colab. ANECOOP & RadLab@CNA) CONTINUOUS
  @100 cm & 0o:
  + LUPIN (UPM): 77(1) mSv/h/µA
  + BIOREM (CNA): 88(1) mSv/h/µA
13% agreement
Electronic damage (soft error rate) by irradiation with protons and fast (MeV) neutrons CONTINUOUS
B. Fernández XIII CPAN Days 21-23 Marzo 2022
Fast neutron irradiations & dosimetry

## Slide 29: HISPANOS for RD50?
A few examples found:
Kaska et al., Study on 150 um thick n- and p-type epitaxial silicon sensors irradiated with 24 GeV/c protons and 1 MeV neutrons, NIM-A 612 (2010)
Pacifico et al., Characterization of proton and neutron irradiated low resistivity p-on-n magnetic Czochralski ministrip sensors and diodes, NIM-A 658 (2011)
Kramberger et al, Modeling of electric field in silicon micro-strip detectors irradiated with neutrons and pions, JINS 9 (2014)
Gurimskaya et al., Radiation damage in p-type EPI silicon pad diodes irradiated with protons and neutrons, NIM-A 958 (2020)
Reactor neutrons (meV) from JSI in Slovenia, then normalized to 1 MeV neutron-equivalent values
Reminder: According to https://rd50.web.cern.ch/niel/, equivalent “Displacement Damage in Silicon” compared to 1 MeV neutrons is 0.001 for thermal neutrons and 2 for 5 MeV neutrons.
Fasts neutrons @HISPANOS => @ 10 cm with 10 uA
p+Li => 7x106 n/cm/s
p+Be => 5x106 n/cm/s
d+Be => 107 n/cm/s
Transnational Access via H2020-EuroLABS & H2020-ARIEL
(see Palomo’s talk tomorrow)

## Slide 30
THANK YOU