## Slide 1
FCC
PS
SPS
LHC
Status Report on FCC Accelerator Science and Technology
Frank Zimmermann, CERN
Estonia, Engagement Meeting,
2 March 2022
photo: J. Wenninger
Work supported by the European Commission under the HORIZON 2020 projects EuroCirCol, grant agreement 654305; EASITrain, grant agreement no. 764879; ARIES, grant agreement 730871, FCCIS, grant agreement 951754, and I.FAST, grant agreement 101004730.
http://cern.ch/fcc

## Slide 2
Double ring e+ e- collider
Common footprint with FCC-hh, except around IPs
Asymmetric IR layout and optics to limit synchrotron radiation towards the detector
2 IPs, large horizontal crossing angle 30 mrad, crab-waist collision optics (alternative layouts with 4 IPs under study now)
Synchrotron radiation power 50 MW/beam at all beam energies
Top-up injection scheme for high luminosity Requires booster synchrotron in collider tunnel
ee design choices & new “lowest risk” layout

## Slide 3
Parameter [4 IPs, 91.2 km circumference] | Z | WW | H (ZH) | ttbar
beam energy [GeV] | 45 | 80 | 120 | 182.5
beam current [mA] | 1400 | 135 | 26.7 | 5.0
no. bunches/beam | 8800 | 1120 | 336 | 42
bunch intensity [1011] | 2.76 | 2.29 | 1.51 | 2.26
SR energy loss / turn [GeV] | 0.0391 | 0.37 | 1.869 | 10.0
total RF voltage 400/800 MHz [GV] | 0.120/0 | 1.0/0 | 2.48/0 | 4.0/7.67
long. damping time [turns] | 1170 | 216 | 64.5 | 18.5
horizontal beta* [m] | 0.15 | 0.2 | 0.3 | 1
vertical beta* [mm] | 0.8 | 1 | 1 | 1.6
horiz. geometric emittance [nm] | 0.71 | 0.28 | 0.64 | 1.49
vert. geom. emittance [pm] | 1.42 | 4.34 | 1.29 | 2.98
bunch length with SR / BS [mm] | 4.32 / 15.2 | 3.55 / 7.02 | 2.5 / 4.45 | 1.67 / 2.54
luminosity per IP [1034 cm-2s-1] | 181 | 17.3 | 7.2 | 1.25
beam lifetime rad Bhabha / BS [min] | 19 / - | 20 / - | 10 / 19 | 12 / 46
FCC-ee collider parameters (stage 1)
preliminary - for new layout & with 4 IPs

## Slide 4
Marica Biagini
B-factories: KEKB & PEP-II:
double-ring lepton colliders,
high beam currents,
top-up injection
DAFNE: crab waist, double ring
S-KEKB: low by*, crab waist
LEP: high energy, SR effects
VEPP-4M, LEP: precision E calibration
KEKB: e+ source
HERA, LEP, RHIC: spin gymnastics
combining successful ingredients of several recent colliders → highest luminosities & energies
FCC-ee design concept
based on lessons and techniques from past colliders (last 40 years)
Marica Biagini

## Slide 5
new: FCC-ee asymmetric crab-waist IR optics
ttbar 182.5 GeV
Novel asymmetric IR optics to suppress synchrotron radiation toward the IP, Ecritical <100 keV from 450 m from IP (e) – lesson from LEP
4 sextupoles (a – d) for local vertical chromaticity correction combined with crab waist, optimized for each working point – novel “virtual crab waist”, standard crab waist demonstrated at DAFNE
yellow boxes:
dipole magnets
K. Oide et al., Design of beam optics for the future circular collider e+e- collider rings, Phys. Rev. Accel. Beams 19, 111005 (2016).
H. Burkhardt, K. Oide, et al.
low incident SR,
minimum nonlinearities

## Slide 6
new: “bootstrapping” & top-up injection
D. Shatilov
S. Ogur
injection from zero, alternating between beams to avoid beam-beam flip-flop effect
alternating replenishment of the two colliding beams, keeping beam currents stable within a few per cent
average luminosity ~ peak luminosity

## Slide 7
by* = 0.8 mm achieved in both rings – using the
FCC-ee-style “virtual” crab-waist collision scheme
Design: double ring e+e- collider as B-factory at 7(e-) & 4(e+) GeV; design luminosity 8 x 1035 cm-2s-1; by* 0.3 mm; nano-beam – large crossing angle collision scheme (crab waist w/o sextupoles); beam lifetime5 minutes; top-up injection; e+ rate up to 2.5 1012 /s ; under commissioning
Y. Funakoshi, Y. Ohnishi, K. Oide
SuperKEKB is demonstrating FCC-ee key concepts
M. Tobiyama, K. Oide
SuperKEKB – pushing luminosity and b*
new world record L = 3.81 x 1034 cm-2s-1 on 23 December ‘21

## Slide 8
FCC-ee RF staging scenario
three sets of RF cavities to cover all options for FCC-ee & booster:
high intensity (Z, FCC-hh): 400 MHz mono-cell cavities (4/cryom.)
higher energy (W, H, t): 400 MHz four-cell cavities (4/cryomodule)
ttbar machine complement: 800 MHz five-cell cavities (4/cryom.)
installation sequence comparable to LEP ( ≈ 30 CM/shutdown)
WP | Vrf [GV] | #bunches | Ibeam [mA]
Z | 0.1 | 16640 | 1390
W | 0.44 | 2000 | 147
H | 2.0 | 393 | 29
ttbar | 10.9 | 48 | 5.4
“Ampere-class” machine
“high-gradient” machine
RF development: SC cavities, SRF material & coating techniques, cavity fabrication,
cryomodules, FPC & HOM couplers, RF power sources, …

## Slide 9
prototypes of FCC-ee low-power magnets
Twin-dipole design with 2× power saving
16 MW (at 175 GeV), with Al busbars
Twin F/D arc quad design with 2× power saving
25 MW (at 175 GeV), with Cu conductor
prototype
prototype
A. Milanese
Phys. Rev. Accel. Beams 19, 112401 (2016)
even more efficient alternative magnet designs are being explored

## Slide 10
FCC-ee complete arc half-cell mock up
including girder, vacuum system with antechamber + pumps, dipole, quadrupole + sext. magnets, BPMs, cooling + alignment systems, technical infrastructure interfaces.
key beam diagnostics elements
bunch-by-bunch turn-by-turn longitudinal charge density profiles based on electro-optical spectral decoding (beam tests at KIT/KARA) ; ultra-low emittance measurement (X-ray interferometer tests at SuperKEKB, ALBA) ; beam-loss monitors (IJCLab/KEK?) ;
beamstrahlung monitor (KEK); polarimeter ; luminometer
FCC-ee R&D: prototypes by 2025
bunch electric field at the crystal
changes the laser pulse polarization
A.-S. Müller et al, KIT
R. Kersevan et al

## Slide 11
high-yield positron source
target with DC SC solenoid or flux
concentrator
400 MHz SRF cryomodule,
+ prototype multi-cell cavities for FCC ZH operation
High-efficiency RF power sources
positron capture linac
large aperture S-band linac
beam test of e+ source & capture linac at SwissFEL – yield measurement
SwissFEL linac
strong support from Switzerland via CHART II program 2019 – 2024 for FCC-ee injector, HFM, beam optics developments, geology and geodesy activities.
FCC-ee R&D: prototypes by 2025
P. Craievich, H. Braun,
A. Grudiev, I. Chaikovska

## Slide 12
FCC hh basic design choices
dual aperture superconducting magnets
two high-luminosity experiments (A & G)
two other experiments (D & J) combined with injection upstream of experiments
two collimation insertions
  betatron cleaning (F)
  momentum cleaning (H)
extraction/dump insertion (B)
RF insertion (L)
Injection from LHC (3 TeV) or scSPS (1.2 TeV)

## Slide 13
parameter | FCC-hh |  | HL-LHC | LHC
collision energy cms [TeV] | 100 |  | 14 | 14
dipole field [T] | 16-17 |  | 8.33 | 8.33
circumference [km] | 91.2 |  | 26.7 | 26.7
beam current [A] | 0.5 |  | 1.1 | 0.58
bunch intensity [1011] | 1 | 1 | 2.2 | 1.15
bunch spacing [ns] | 25 | 25 | 25 | 25
synchr. rad. power / ring [kW] | 2700 |  | 7.3 | 3.6
SR power / length [W/m/ap.] | 32.1 |  | 0.33 | 0.17
long. emit. damping time [h] | 0.45 |  | 12.9 | 12.9
beta* [m] | 1.1 | 0.3 | 0.15 (min.) | 0.55
normalized emittance [mm] | 2.2 |  | 2.5 | 3.75
peak luminosity [1034 cm-2s-1] | 5 | 30 | 5 (lev.) | 1
events/bunch crossing | 170 | 1000 | 132 | 27
stored energy/beam [GJ] | 7.8 |  | 0.7 | 0.36
FCC-hh (pp) collider parameters (stage 2)
preliminary - for new layout

## Slide 14
worldwide FCC Nb3Sn program
Main development goal is wire performance increase:
Jc (16T, 4.2K) > 1500 A/mm2 50% increase wrt HL-LHC wire
Reduction of coil & magnet cross-section
3150 mm2
~1.7 times less SC
~10% margin
HL-LHC
~10% margin
FCC ultimate
5400 mm2
After 1-2 years development, prototype Nb3Sn wires from several new industrial FCC partners already achieve HL-LHC Jc performance
FCC conductor development collaboration:
Bochvar Institute (production at TVEL), Russia
Bruker, Germany, Luvata Pori, Finland
KEK (Jastec and Furukawa), Japan
KAT, Korea, Columbus, Italy
University of Geneva, Switzerland
Technical University of Vienna, Austria
SPIN, Italy, University of Freiberg, Germany
2019/20 results from US, meeting FCC Jc specs:
Florida State University: high-Jc Nb3Sn via Hf addition
Hyper Tech /Ohio SU/FNAL: high-Jc Nb3Sn via artificial pinning centres based on Zr oxide.

## Slide 15
16 T dipole design activities and options
Cos-theta
Blocks
Common coils
Short model magnets (1.5 m lengths) will be built until 2025
Swiss contribution
Canted
Cos-theta
H2020
INFN
CEA
CIEMAT
PSI
LBNL
FNAL

## Slide 16
US – MDP: 14.5 T magnet tested at FNAL
15 T dipole demonstrator
Staged approach: In first step pre-stressed for 14 T
Second test in June 2020 with additional pre-stress reached 14.5 T
60-mm aperture
4-layer graded coil
84% on the laodline at 1.9 K
92% on the loadline at 4.2 K

## Slide 17
FCC-ee is first stage of FCC integrated programme; 1st physics ~2045
FCC-ee design incorporates many lessons from recent & present e+e- colliders, and goes further! SuperKEKB demonstrates key concepts
FCC-ee = efficient and sustainable collider at the e+e- energy frontier: highest luminosity per input power, highest luminosity per construction cost, most precise energy calibration, and ultimate upgrade potentials (100 TeV FCC-hh, FCC based muon collider …)
Prototypes of FCC-ee key components by 2025
Superconducting cable & high-field magnet programme prepares for 100 TeV proton-proton collider, FCC-hh, in the same tunnel, to begin operation around ~2065/70
Take home messages