## Slide 1: BGC Planning for v3 and v4
Gerhard Schneider

## Slide 2: Content
v3 in the Laboratory building 8 and on EBTS
v3 tunnel operation with distributed gas
v3 Phase 2 with gas curtain
V4 timeline: Collaboration Contract basis

## Slide 3: v3 in the Laboratory Building 8 and on EBTS
Change from CI vacuum system to LHC compatible vacuum system
  Objective: September 2022.
Operate BGC with gas curtain on EBTS
  Objective: September 2022.
Open question: Operation of BGC on EBTS with CI or LHC compatible vacuum system

## Slide 4: v3 Tunnel operation with distributed gas
Ready
Operation in 2022 (and 2023?)

## Slide 5: v3 Phase 2 tunnel operation with gas curtain
Objective: Installation in CERN Year End Technical Stop (YETS) 2022/23
  A lot of work on the way
  Stay optimistic

## Slide 6: v4 Timeline
2022: Mechanical and vacuum engineering
2023: Design and preparation of manufacture
2024: Manufacture and test
2025: Ready for LHC installation

## Slide 7: Thank you ! Questions?

## Slide 8: Extra Slides
Signal is defined as the total intensity in the highest amplitude region of the background subtracted final image corresponding to an area of 0.1 mm2 in the source plane. Noise is defined as the standard deviation of the intensity in regions without signal in the final image corresponding an area of 0.1 mm2 in the source plane.
This value is calculated by scaling the intensity and beam size of the electron beam used to qualify the performance at the Cockcroft Institute, and taking into account the relative difference in expected proton/ electron fluorescence cross section.

## Slide 9: Collaboration Contract is the Basis
Delivery of Gas-Curtain Beam Profile Monitors (BGC) for HL-LHC (Task 2); Collaboration contract between CERN, the Cockcroft Institute and Liverpool University
  CERN EDMS document No. 2369616 LHC-BGC-ES-0001

## Slide 10: Design Performance criteria V4
The instrument shall be designed to:
determine the beam centroid of a nominal intensity and emittance HL-LHC proton beam at 7 TeV to better than 100 m within a fixed, 2D image plane in less than 10 seconds
simultaneously produce the 2D image of a hollow electron beam, with the nominal operating parameters of 15keV, 5A an inner/outer beam diameter of 4/9 mm, in the same frame of reference as the proton beam image, within 1 second.
cope with an orbit variation of  4 mm in either transverse dimension away from the central axis of the device.

## Slide 11: Reference Parameters V4
Particle Type | Energy (eV) | Current (A) | Size (mm) | Distribution
Electron | 15×103 | 5 | ID: 4 OD: 9 | Quasi - uniform
Proton | 7×1012 | 1.1 | s : 0.37 | Gaussian
Reference parameters for nominal HL-LHC proton and electron beams

## Slide 12: Key Performance Criteria V4
Criterion | Units | Value
Minimum gas density in the curtain | mol.m-3 | 2x1016
Minimum transverse curtain dimension | mm | 20
Variation in transverse density over the central 10mm of the gas curtain | % | 20
Maximum deviation from the central transverse density at  10mm from the gas curtain centre | % | 50
Maximum through-thickness curtain dimension | mm | 1.5
Maximum residual gas pressure in the interaction chamber, 24h after a 24h bakeout at 250 °C and pumping with nominal system and beam aperture blanked-off. | mbar | 1x10-9
Signal to noise ratio* of the image area corresponding to 0.1 mm2 at the source plane for the highest intensity signal region of a nominal proton beam as measured at the imaging plane in 10 seconds*. | Ratio | 10
* See Extra Slides for detailed definition

## Slide 13: Target Performance Criteria V4
* See Extra Slides for detailed definition
Criterion | Units | Value
Gas density in the curtain | mol.m-3 | 1x1017
Transverse curtain dimension | mm | 40
Variation in transverse density over the central 20mm of the gas curtain | % | 10
Maximum deviation from the central transverse density at  20mm from the gas curtain centre | % | 30
Through-thickness curtain dimension | mm | 0.5
Maximum residual gas pressure in the interaction chamber, 24h after a 24h bakeout at 250 °C and pumping with nominal system and beam aperture blanked-off. | mbar | 1x10-9
Signal to noise ratio of the image area corresponding to 0.1 mm2 at the source plane for the highest intensity signal region of a nominal proton beam as measured at the imaging plane in 10 seconds. | Ratio | 100

## Slide 14: Timeline V4: UK Deliverables
Deliverable Number | Deliverable Description | Type
D3.2.1 | Get-jet monitor engineering design: report that shows proposed design fits specification and can be built | Document
D3.2.2 | Final design: report with final drawing, integration, costs production and commissioning plan | Document
D3.2.3 | Delivery of interaction chambers for integration in Hollow Electron Lens build-up | Hardware
D3.2.4 | Delivery of gas-curtain monitor unit 1, pre-tested at the Cockcroft Institute, for integration in Hollow Electron Lens and testing, participation in commissioning tests | Hardware
D3.2.5 | Delivery of gas-curtain monitor unit 2 for integration at CERN, pre-tested at the Cockcroft Institute | Hardware

## Slide 15: Timeline V4: CERN Deliverables
Deliverable Number | Deliverable Description | Type
DC.1 | Integration Drawings | Document
DC.2 | Nozzle manufacturing Flat-divergent nozzles for units 1 and 2 | Hardware
DC.3 | Compliance of the Cockcroft Institute design to 2 T stray magnetic fields | Document
DC.4 | Vacuum valves required for HL-LHC operation | Hardware
DC.5 | HL-LHC Infrastructure: Off-instrument cabling Any electronics not forming part of the instrument Gas lines and bottles for LHC integration LHC vacuum control hardware and software LHC operational software | Hardware