## Slide 1: Analysis of Earthquake Effects on Belle II Detector and SuperKEKB Accelerator
KEK
Hiroshi Yamaoka
yamaokah@post.kek.jp

## Slide 2
Distribution of earthquake in Japan
https://earthquake.tenki.jp/bousai/earthquake/seismicity-map/100days/
In 30 days,
129 times
In 100 days,
493 times
 In Japan, we experience a lot of earthquakes!
Each color: Depth
Circle size: Magnitude
KEK
KEK

## Slide 3
Nov. 1st, 2021
Motivation
KEK
Intensity: 3.50
Tokyo
Superconducting quadrupole magnet (QCS) for SuperKEKB was quenched.
This was second time quench from the earthquake on Mar. 20, 2021.
Induced voltage exceeded the trigger level which was 1.5V.
Why this was happend??
gal = 1 cm/s2 = 1/100 m/s2

## Slide 4
SuperKEKB Interaction Region
Superconducting quadrupole magnet (QCS)
 There are three superconducting magnets.
Belle II Detector(1400ton)
QCS
QCS
QCS
Belle solenoid

## Slide 5
Iron yoke
Air
Coil2
Coil3
Coil1
Distribution of combined magnetic field
Disturb magnetic field
Generate induced voltage
Quench!
How much is the relative displacement when shaking?
Large relative displacement causes damage to B.P, etc.
Process to the magnet quench
Earthquake!
Exceed trigger level
Power shutdown

## Slide 6
Investigation of relative displacement of QCS
Data is input to the constraint points
Get relative displacement
(Input data)
Response Spectrum
Conversion
Time history
Extrapolate until 100Hz
Response Spectrum analysis (RSA/FEM)
Damping
z = 5%

## Slide 7
Modal analysis is done before spectrum analysis
Result(QCS)
(Result)
Relative displacement = 14mm
- Displacement of QCS is the same as that of floor until reaching 1st mode.
 No relative displacement
- After Passing 1st mode, generates the relative displacement.
Response Spectrum Analysis (RSA/FEM)
Modal analysis
(Summary of RSA/FEM of QCS)
QCS shakes with floor with the same phase  Very small relative displacement.
- First mode of natural frequency is out of the earthquake effect.
- Displacement is decreasing according to increase frequency.

- How much is the relative displacement of Belle II detector?
f1= 31Hz

## Slide 8
Mode shape of the Belle II detector.
 Rigid body mode at 4- 5Hz. Because,
- Belle II detector is not fixed on the floor.
- Belle II detector is placed on the Teflon sheet.
 Make a FEM model for Belle II detector.
Natural frequencies in the horizontal direction was measured around 4Hz.
Here
Natural frequency of Belle II detector

## Slide 9
Belle II detector FEM model
(Assumptions)
- Make columns around the Belle II.
- Connect springs between column and the Belle II.
- Adjusted spring constant which to be around 4 - 5Hz.
Belle II can move horizontal direction freely.
But it fixed to the vertical direction.
4.6Hz
Results of modal analysis
4.7Hz
8e5 N/mm
4e5 N/mm

## Slide 10
~1.0mm
Nov. 1st, 2021
Displacement
(Input data)
Response spectrum
Response Spectrum Analysis (RSA/FEM)
Date | Intensity | QCS | BelleII
Apr. 12th, 2020 | 3.5 | 0.065mm | 2.1mm
Mar. 20th, 2021 | 3.5 | 0.017mm | 0.7mm
Mar. 16th, 2022 | 4.3 | 0.023mm | 3.4mm
If these calculations are true, we need to take account;
- Damage of bellows of beam pipe.
- Disappearing gap btwn. sub-detectors.
(Results)
 Displacement = 14mm (QCS), 1.0mm (Belle II)
As the cause of magnet quench, Belle II would be shaken not QCS.
Other comparison of RSA/FEM
Damping
z = 5%

## Slide 11
Specifications (Gap sensors) | 
Type | Capacitive
Company | Digi-tex lab
Scale | 0.1 – 8.5mm
Precision | < 0.6mm
Range | DC -100Hz
Size | f30 x 35 (D) mm
Comparisons |  |  | 
Date | Intensity | FEM | Gap sensor
Apr. 19, 22 | 2.5 | 0.52mm | 0.3mm
May 3rd, 22 | 1.3 | 0.13mm | 0.035mm
May 5th, 22 | 2.4 | 0.40mm | 0.10mm
May 8th, 22 | 0.8 | 0.05mm | 0.019mm
May 9th, 22 | 1.0 | 0.05mm | 0.03mm
May 22, 22 | 2.4 | 0.12mm | 0.10mm
Comparison of RSA/FEM and measurement
Gap sensor
Difference between FEM and measurement might be difference of response spectrum at ground level and underground (GL-16m).

## Slide 12
Specifications of each sensor |  | 
Detection | Acc. | Disp.
Type | Piezo | Laser
I.D. | 356B18 | LK-80
Range | 0.5 - 3kHz | DC – 10kHz
Sensitivity | 1mV/gal | 0.5mm/V
Precision | 0.05 gal | 0.2 mm
Earthquake measurement system
Accelerometer (Belle TOP)
Accelerometer (Floor: GL-16m)
Laser distance sensors
Trigger level: 5 gal

## Slide 13
Earthquake on May 29, 2022
KEK
Tokyo
KEK
We have caught an earthquake!
Intensity: 3

## Slide 14
Time history
Response Spectrum
Smaller
Smaller
Same
Same
Getting larger
Same
Getting larger
Same

## Slide 15
Earthquake on Jun. 12, 2022
Time data
Response Spectrum
 Similar situation as that of May 29.
NS
EW
UD

## Slide 16
RSA/FEM with GL-16m data of earthquake on May 29.
Response spectrum (GL-16m)
Displacement= 0.15mm
Displacement= 0.17mm
Good agreement!
FEM
Gap sensor
Damping= 5%

## Slide 17
Correlation between QCS-L and QCS-R
Summary of displacement measured by the gap sensors at several earthquakes |  |  |  | 
Date | Intensity | L-side (mm) | R-side (mm) | Difference (mm)
May 3rd, 22 | 1.3 | 0.0359 | 0.0364 | 0.0005
May 5, 22 | 2.4 | 0.099 | 0.104 | 0.0053
May 8th, 22 | 0.8 | 0.0189 | 0.0194 | 0.0005
May 9th, 22 | 1.0 | 0.0371 | 0.0353 | 0.0017
May 22, 22 | 2.4 | 0.091 | 0.083 | 0.0084
Gap sensor
QCS-R(24Hz)
Gap sensor
QCS-L(31Hz)
If two QCS’s don’t recieve earthquake effect, displacement of both sensors must be almost same and small.
Evidence:
 Belle II shakes not QCS
Quench:
 Belle II shakes not QCS
Result:
- Small displacement. - Almost same value.

## Slide 18
Measurement of relative displacement
Detect. | Acceleration
Type | Servo
Company | Tokkyo-kiki
Range | 0.1 – 400Hz
Sensitivity | 32.6gal/1V
Precision | 10-6 gal
High precision acceleration sensors are set.
Displacement can be get from two times integration of acceleration time history.

## Slide 19
Earthquake on Sep. 30th, 2022
Intensity:
2.1
KEK
Tokyo

## Slide 20
Displacement
Relative displacement is larger than that of Belle II top!
EW
NS
NS
EW
Resonance
Data is still insufficient...

## Slide 21
Summary
- QCS was quenched due to an earthquake.
Response spectrum analysis (RSA/FEM) has been done.
QCS was shaken? Belle II was shaken?
Answer: Belle II, not QCS.
True?
- We decided to confirm FEM results.
- We have to think about other effects. Bellows, Gap, etc.
Let’s measure earthquake at Belle II and QCS!
From compare gap sensors  Belle was shaken.
Results of RSA/FEM is consistent with measurement.
Earthquakes is not damped at underground (GL-16m) until 2Hz.
Relative displacement becomes larger than absolute displacement.
Rel. disp. < Abs. disp.  Rel. disp. > Abs. disp.

## Slide 22: Thank you!

## Slide 23
JMA (Japan Meteorological Agency) |  |  |  | http://www.jma.go.jp/jma/kishou/know/shindo/explane.html | 
Scale: I | JMA | Acc.(cm/s2): acc=0.45x10^(0.5I) | People | Indoor Situations | Outdoor Situations
0 |  |  | Imperceptible to people. |  | 
1 | 0.8 | 1.4 | Felt by only some people in the building. |  | 
2 | 2.5 | 4.5 | Felt by most people in the building. Some people awake. | Hanging objects such as lamps swing slightly. | 
3 | 25 | 14 | Felt by most people in the building. Some people are frightened. | Dishes in a cupboard rattle occasionally. | Electric wires swing slightly.
4 | 80 | 45 | Many people are frightened. Some people try to escape from danger. Most sleeping people awake. | Hanging objects swing considerably and dishes in a cupboard rattle. Unstable ornaments fall occasionally. | Electric wires swing considerably. People walking on a street and some people driving automobiles notice the tremor.
5-Lower | 250 | 142 | Most people try to escape from a danger. Some people find it difficult to move. | Hanging objects swing violently. Most Unstable ornaments fall. Occasionally, dishes in a cupboard and books on a bookshelf fall and furniture moves. | People notice electric-light poles swing. occasionally, windowpanes are broken and fall, un-reinforced concrete-block walls collapse, and roads suffer damage.
5-Upper |  | 253 | Many people are considerably frightened and find it difficult to move. | Most dishes in a cupboard and most books on a bookshelf fall. Occasionally, a TV set on a rack falls, heavy furniture such as a chest of drawers falls, sliding doors slip out of their groove and the deformation of a door frame makes it impossible to open the door. | In many cases , un-reinforced concrete-block walls collapse and tombstones overturn. Many automobiles stop because it becomes difficult to drive. Occasionally, poorly-installed vending machines fall.
6-Lower | 400 | 450 | Difficult to keep standing. | A lot of heavy and unfixed furniture moves and falls. It is impossible to open the door in many cases. | In some buildings, wall tiles and windowpanes are damaged and fall.
6-Upper |  | 800 | Impossible to keep standing and to move without crawling. | Most heavy and unfixed furniture moves and falls. Occasionally, sliding doors are thrown from their groove. | In many buildings, wall tiles and windowpanes are damaged and fall. Most un-reinforced concrete-block walls collapse.
7 |  | 1423 | Thrown by the shaking and impossible to move at will. | Most furniture moves to a large extent and some jumps up. | In most buildings, wall tiles and windowpanes are damaged and fall. In some cases, reinforced concrete-block walls collapse.

## Slide 24
A response spectrum is a function of frequency or period, showing the peak response of a simple harmonic oscillator that is subjected to a transient event. The response spectrum is a function of the natural frequency of the oscillator and of its damping. Thus, it is not a direct representation of the frequency content of the excitation (as in a Fourier transform), but rather of the effect that the signal has on a postulated system with a single degree of freedom (SDOF).
Response Spectrum
Response
Output
Input
Response Spectrum

## Slide 25
 If a big earthquake is struck such as intensity of 5 or 6, the Belle II would be shaken 10mm or 20mm??
Maybe no??
There are four anchors.
But those have to be have enough rigidness.
以上

## Slide 26
Displacement on Sep. 30. 2022
Ground (GL)
Belle-Top
Floor(GL-16m)

## Slide 27
EW
NS
UD
1st mode natural frequency : 4 – 5 Hz
Natural frequency of Belle when the magnet is excited.
EW
NS
UD