## Slide 1
From Engineering to Alignment How functional geometrical requirements on equipment are handled and transferred into installation drawings
Dr Bertrand Nicquevert
Fabien Rey

## Slide 2
A use case: the ESS Target Monolith Systems assembly
    An Integration challenge
    What space do we need?
    A communication problem
Systematic approach through Technical Drawings and ISO GPS language
    Deployment at ESS
    Acceptance and Verification
Developing tools applicable from Design to Commissioning
    Positioning requirements = Tolerance zones?
    Introduction to Datum System
    Datum System vs Coordinate System
    A generic tool
Geodetic application with installation drawings
    Multiples Target Coordinate Systems
    Geodetical Network and [TCSsam]
    Examples
Conclusion

## Slide 3
European Spallation Source
Build and operate the world’s most powerful neutron source
European Research Infrastructure Consortium (ERIC)
Host countries: Sweden & Denmark
+11 partner countries
In – Kind Contribution
15 instruments under construction
User Operation starting 2027
22 instruments complete after 2030

## Slide 4
Ion Source
Proton Beam
Target
Neutrons
Instruments
Process in which a heavy nucleus emits a large number of nucleons as a result of being hit by a high-energy particle.
Neutrons with Spallation at ESS
Wheel
Moderator Reflector
Neutron Optics
Linear proton accelerator
Energy: 2 GeV
Rep. Rate: 14 Hz Current: 62.5 mA PeakPulse length: 2.86 ms
Neutrons

## Slide 5
250 m
750m
LINAC Tunnel
Gallery Building
Cryo Compressor Building
Target Building
Experimental Halls
ESS Technical Buildings

## Slide 6
A use case: the ESS Target Monolith Systems assembly
    An integration challenge
SECTION VIEW OF TARGET BUILDING
ESS TECHNICAL BUILDINGS
ESS MACHINE
Proton Beam

## Slide 7
Target Coordinate System
Proton Beam
Neutron Beam
Beam Port Coordinate System
North Sector
East Sector
West Sector
South Sector
NEUTRON OPTICS
A use case: the ESS Target Monolith Systems assembly
    An integration challenge
Instrument Source Coordinate System
Focal Points
TCS
4 Upper
4 Lower
X
Y
Z

## Slide 8
A use case: the ESS Target Monolith Systems assembly
    An integration challenge
BASE PLATES
NEUTRON OPTICS
TARGET MONITORING
TARGET DRIVE UNIT
MODERATOR REFLECTOR
PROTON BEAM INSTRUMENTATION
PROTON BEAM
WINDOW
WHEEL
PROTON BEAM
NEUTRON BEAM

## Slide 9
A use case: the ESS Target Monolith Systems assembly
    An integration challenge
NEUTRON BEAM PORT INSERT
NEUTRON BEAM PORT INSERT WITH OPTICS
PORT TUBES

## Slide 10
A use case: the ESS Target Monolith Systems assembly
    An integration challenge
Monolith Vessels
Welding Vessel – Port Tubes
LIGHT SHUTTERS
OUTER SHIELDING
INNER SHIELDING
PORT TUBES

## Slide 11
Numerous meetings and workshops to talk about geometrical tolerances
Additional constraints:
  Vacuum vessel - pressurized equipment
  Thermal effects
  Radiation
  Differential settlement
Many systems designed by ESS teams and In-Kind partners
Nominal CAD model with tight nominal clearances
Mobility of systems : wheel, plugs and insert , installation, operation and maintenance
Section view of the
Target Monolith Systems
A use case: the ESS Target Monolith Systems assembly
    An integration challenge
Each teams try to express their needs as they can:
Interface documents
Technical Drawings
Excels files
PowerPoints
Whiteboards sketch
Clash analysis
Assembly simulations
Try to establish:
Manufacturing Tolerances
Installation Tolerances
Operation Tolerances
2019

## Slide 12
A use case: the ESS Target Monolith Systems assembly
    What space do we need?
ESS Engineering Handbook
All good !!!! until we have a problem :
    large geometrical deviations observed during manufacturing of the monolith vessel
Can we accept this component apparently out of manufacturing tolerances?
Are we sure that we expressed without ambiguity our needs?
Manufacturing
drawings
Interface documents
Geometrical requirements
Verification
and Acceptance ?
March 2020

## Slide 13
A use case: the ESS Target Monolith Systems assembly
    An communication problem
During Verification , ESS teams and in-kind partners realize :
too much ambiguities in the way of expressing geometrical requirements
various teams were not using all the same “ language “ to express their needs
Our functional analysis was not consistent and reliable
We must change our way of working !
We have a communication problem

## Slide 14
Systematic approach through technical drawings and ISO GPS language
    Deployment at ESS
Strategy: rely on International Standards (ISO)
Technical Drawings
ISO GPS language
Geometrical Product Specification
(ISO GPS) is the system used to define the geometrical requirements of workpieces in engineering specifications, and the requirements for their verification.
ISO 14638:2015
Technical Product Documentation - ISO 128
Type of documents with GPS- ISO/TS 21619:2018
Make distinction between three types of specifications
Functional specification: FUN-SPEC
Manufacturing specification: MAN-SPEC
Verification specification: VERI-SPEC (F) ou (M)
WHAT
HOW
WHETHER
Convince Top management!
ISO-GPS Training organized for many teams
Not only designers but also mechanical workshop , Installation teams, managers …
GPS- ISO 8015:2011

## Slide 15
Systematic approach through technical drawings and ISO GPS language
    Acceptance and Verification
All teams started talking the same language ISO GPS
Functional analysis fully revisited
3D tolerance stack-up analysis carried out
Functionals and Verifications Drawings – ISO GPS compliant
Immediate benefit :
we can express the geometrical needs of each stakeholders in an unambiguous and common way
Better understanding of 3D interfaces between systems
Clarification of objectives for :
Manufacturing
Installation
Operation

## Slide 16
Systematic approach through technical drawings and ISO GPS language
    Acceptance and Verification
We go from :
TO

## Slide 17
Systematic approach through technical drawings and ISO GPS language
    Acceptance and Verification
Raw measurement data
(extracted integral features)
Verification Report
VERI-Spec derived from FUN-Spec

## Slide 18
Developing tools applicable from Design to Commissioning
    Positioning requirements = Tolerance zones ?
Identify functional surfaces and
express geometrical specifications
ESS Engineering Handbook
Functional
drawings
Manufacturing
drawings
Verification
drawings
Installation
drawings
What is an installation drawing?
Provide information for positioning and orientation of a part or assembly with respect to a local or global reference frame
Translation in
ISO GPS language:
Frame usage not normalized
Express geometrical specifications on functional features of the part with respect to situation features of type :
point
Line
plane
[PL]
[SL]
[PT]
Or a combination of them
Positioning requirements
“I want this component to be within ± 1 mm
with respect to this reference frame”
X
Y
Z
X
Y
Z
4x
A
A
TED
In this case not locking all degrees of freedoms !
ISO 1101:2017
Geometrical product specifications (GPS)
Geometrical tolerancing – Tolerances of form, orientation, location and run- out
TED: Theoretical Exact Dimension (can be a distance or an angle)

## Slide 19
Developing tools applicable from Design to Commissioning
    Introduction to Datum System
A datum system can always be reduced to a resulting minimal set, made of :
ISO 5459:2011 Geometrical product specifications (GPS) – Geometrical tolerancing – Datums and datum systems
or a subset of those (locking three to five degrees of freedom)
- A theoretically exact plane [PL]
- A straight line [SL] in this plane
- A point [PT] on this straight line
locking all degrees of freedom !
with respect to which geometrical specifications are referenced.
This is the “resulting datum system”.
This resulting datum system may be called a “ToLiP”: PoinT On Line In Plane.
We have now the tools to fully express positioning requirements using tolerances zones with respect to ToLiP’s
X
Y
Z
DS1
4x
DS1
TED
TED
TED
Example of geometrical specification

## Slide 20
Developing tools applicable from Design to Commissioning
    Datum System vs Coordinate System
Y
Z
X
(CS)
[DS]
The idea came to specifically declare Datums Systems and attach them to Coordinate Systems contained in our CAD skeleton
To help designers to reference their design, we defined some specific
ESS Datums Systems
attached to
ESS main Coordinates Systems
and also to instruct designers on how to use them and establish their own ones.
Note: Not fully equivalent (no direction)
Rarely an issue.
Example of association DS to CS

## Slide 21
Developing tools applicable from Design to Commissioning
    Datum System vs Coordinate System
Examples of ESS Datum Systems
Establishing a real functional definition of the neutron source
For a generic beam skeleton

## Slide 22
Developing tools applicable from Design to Commissioning
    A generic tool
A generic tool applicable to express geometrical specifications for positioning different concepts
Theoretical beam physic lattice DS
Mechanical DS
Multi physic DS
(magnetic axis-optical axis- electrical axis…)
DS Nominal
DS Magnetic
DS Mechanical
Fiducialization DS
Geodetic DS
Spatial Integration Envelope DS
DS Fiducialization
DS Geodetic
DS Integration
External envelope and 3D interfaces
Final position in Global Reference
Multi physic properties to external references
Mechanical references
Multi Physic properties
Nominal definition

## Slide 23
Geodetical applications with installation drawings
    Multiples Target Coordinate Systems
The passage from CAD to Reality imposes some geodetical considerations:
Another definition of TCS
X
Y
Z
Absolute orientation of the TCS axis is defined as follow:
Z-axis: Collinear to local gravity in opposite direction
X-axis: Oriented positive in East direction, making an angle of 28.5 degrees with the East SWEREF 99 13 30 grid
Y-axis: right hand rule.

## Slide 24
Geodetical applications with installation drawings
    Multiples Target Coordinate Systems
2013
2019
2023
Civil Engineering - Building Construction
3D Laser Scanning
Machine Installation
Geodetic Network
External pillars
Accuracy : mm
Alignment Network
Dense SAM references
Accuracy - bellow ±0.1 mm close to TCS
- network error propagation
- Environmental conditions
- Differential settlement
Target and NSS systems installation
Functioning position of TCS
Neutron source defined by moderator position
Not directly accessible once installed
TCS Geod
TCS Funct
???

## Slide 25
Geodetical applications with installation drawings
    Geodetical Network and [TCSSAM]
Generally , our daily geodetical positioning problem could be expressed as follow:
Global Reference
X
Y
Z
Geodetical network – true value expressed in global reference CS
Geodetical network – Measured and calculated -
Local Positioning of an Measuring Instrument (Laser Tracker)
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
Local Accuracy and Precision
quantify and describe our capacity to repeatedly position ourselves with respect to the local network
Global Accuracy and Precision
quantify and describe our capacity to repeatedly position ourselves with respect to the global reference
Local Uncertainty
Global Uncertainty

## Slide 26
Geodetical applications with installation drawings
    Geodetical Network and [TCSSAM]
Global accuracy toward TCS
TCS
< ± 100 microns at 3 sigma
< ± 200 microns at 3 sigma
< ± 300 microns at 3 sigma
Local Positioning at ESS
Global Positioning at ESS
Estimated Local Accuracy
Inside all technical buildings
within a spherical volume R=10m
Less than ± 100 microns at 3 sigma
< ± 500 microns at 3 sigma

## Slide 27
Geodetical applications with installation drawings
    Geodetical Network and [TCSSAM]
[TCSSAM]
Express our capability to define the Global Reference (TCS) using a local geodetic network
TCSSAM
n x CF
+
Network reference
CF: Contacting Feature
Very dependent on the quality of geodetic network !

## Slide 28
Geodetical applications with installation drawings
    Examples
Reference to skeleton CS number
CAD number
illustration and association CS to DS
Geometrical Specifications
Expression
of a
Local Positioning
Installation drawing
Explicit representation of the nominal position of the situation features

## Slide 29
Geodetical applications with installation drawings
    Examples
Installation drawing
Same local positioning requirements over multiple similar systems using skeleton CS .
one unique drawing !

## Slide 30
CONCLUSION
Benefit of relying on international standard : Technical Drawings and ISO GPS
Introduction of TOLIP as fully constrained datum system
Versality of the tool to address different concepts and remove ambiguities
Traceability of requirements from Engineering to Alignment
Functional
drawings
Manufacturing
drawings
Verification
drawings
Installation
drawings
Verification
drawings

## Slide 31
Thank you
Dr Bertrand Nicquevert
Fabien Rey