## Slide 1: Engineering survey and alignment network design for Siam Photon Source II
S. Srichan, M. Phanak, K. Sittisard, K. Rittaprom,
S. Suphachiaraphan, O. Utke
Synchrotron Light Research Institute
THAILAND
16th International Workshop on Accelerator Alignment, CERN, Geneva 31 Oct-4 Nov 2022

## Slide 2: Outline
Introduction to Siam Photon Source
New Synchrotron Facility in Thailand-Siam Photon Source II Project
Siam Photon Source II reference network design (Conceptual)
Conclusion and future work

## Slide 3: Siam Photon Source

## Slide 4: Siam Photon Source: Nakhon Ratchasima, Thailand
Things to do in Nakhon Ratchasima
PIMAI Historical Park
KHAO YAI National Park

## Slide 5: Siam Photon Source

## Slide 6: Siam Photon Source

## Slide 7: Time to go Forward

## Slide 8: Siam Photon Source II (SPS-II)
Parameters SPS-I and SPS-II
Parameters | SPS | SPS-II
Circumference (m) | 81.3 | 327.502
Energy (GeV) | 1.2 | 3.0
Relativistic factor γ | 2348.34 | 5870.85
Emittance εx0 (nm·rad) | 41.0 | 0.96
Beam current (mA) | 150 | 300
Nat. energy spread σE (%) | 0.066 | 0.077
Nat. chromaticity ξx/ξy | -8.7/-6.4 | -65.6/-76.7
Tune Qx/ Qy | 4.75/ 2.82 | 34.24/12.31
Momentum compaction αc | 1.70e-2 | 3.33e-4
Damping times hor./ver./long. (ms) | 10.7/9.8/4.7 | 9.7/11.3/6.2
Straight/circumference | 0.33 | 0.35
Energy loss per turn U0 (MeV) | 0.066 | 0.577
RF frequency (MHz) | 118.00 | 119.00
RF voltage (MV) | 0.3 | 1.5
Harmonic number | 32 | 130
Overvoltage V/U0 | 4.5 | 2.6
Synchronous phase (degree) | 167.29 | 157.34
Synchrotron tune | 0.00460 | 0.00178
Nat. bunch length (mm) | 29.03 | 7.48
Nat. bunch duration (ps) | 96.8 | 24.9
Higher beam energy -> Higher photon energy
Larger ring -> More Beamlines
Lower emittance
Higher current
More space availability -> More Beamlines
-> Higher flux, brightness

## Slide 9: Siam Photon Source II: Rayong, Thailand
Rayong Province
160 km (99 mi) from Bangkok 90 km (55 mi) from U-tapao International Airport 90 km(55 mi) from Pattaya
Eastern Economic Corridor of Innovation (EECi)

## Slide 10: SPS-II Machine
SPS-II Main Components
Electron gun
150 MeV linear accelerator
3.0 GeV booster synchrotron - (Circumference 304.8 m)
Low and high energy transfer line
3.0 GeV storage ring - (Circumference 327.1 m)
Beamlines*
21 Insertion Device (ID) beamlines
2 infrared beamlines
2 diagnostic beamlines
1. Electron gun
4. Low-energy beam transfer line
4. High-energy beam transfer line
3. Booster synchrotron
5. Storage ring
Insertion device
Front-end
Double Triple Bend Achromat (DTBA) cell
with insertion device & front-end
DTBA Cell
6. Beamline
2. Linear accelerator

## Slide 11: Beam Dynamics: Storage Ring
14 Cell -> RING
28 straights in total
DTBA (Double Triple Bend Achromat )
Originated from Diamond Light Source upgrade study
Performance --> MBA cell, low emittance (<1nmrad)
Feasibility --> Moderate magnets requirement
Productivity --> Space usage (>35%)
Design concept:
Circumference (m) : 327.5
Emittance (nm.rad): 0.96

## Slide 12: Beam Dynamics: Booster
Booster
Storage ring
Circumference (m) : 304.8288
Emittance (nm.rad) 5.87
Distance between BS and STR: 3.64 m
Concentric booster
low emittance for providing a clean injection into the storage ring
Minimize the building construction cost (substantial saving of building space and shielding)
Minimize magnet manufacturing cost (small lattice elements, low power consumption)
Simple transfer line between booster and ring
8 Cell -> RING

## Slide 13: 150-MeV Linear Accelerator
Design considerations:
Target beam energy of 150 MeV
Total linac length < 25 m
Compatible with 119-MHz RF system of booster and storage ring
Proposed Components:
Triode gun with 119-MHz voltage modulation at the grid level to produce a chopped beam
Subharmonic pre-buncher operating at 476 MHz
S-band buncher operating at 2856 MHz
S-band accelerating structures
Parameter | Value
Beam energy | 150 MeV
Normalized emittance | ≤ 50 mm∙mrad
RMS energy spread | ≤ 0.5 %
Bunch train charge (MBM) | > 6 nC
Bunch charge (SBM) | ≥ 1.5 nC
Bunch train duration (MBM) | 150-600 ns
Bunch duration (SBM) | < 1 ns
Repetition rate range | 1-5 Hz
Nominal repetition rate | 2 Hz
Main Parameters of the SPS-II Linac
Subharmonic
prebuncher
Buncher
S-band accelerating structure
S-band accelerating structure
The last
S-band accelerating structure
Triode
gun

## Slide 14: Magnet System
Moderate requirements
Offset quadrupole design (ESRF) for combined dipole-quadrupole magnet
Manufacturing tolerance ± 0.02 mm
Static deformation of magnet structure < 0.005 mm
Pulsed multipole magnet (nonlinear kicker) for injection into storage ring
Magnets for storage ring (solid steel) and booster synchrotron (laminated steel) to be manufactured in Thailand
Pulsed magnets (septum, kicker) to be purchased as a turnkey system
Half-cell of SPS-II storage ring DTBA lattice

## Slide 15: Vacuum System
Fabrication tolerances | < 1 mm/m
Taper inclination | < 1/10
The step height | < 1 mm
Photon absorbers have been designed to tolerate SR power with the beam current up to 500mA + 20% margin
High power tolerance absorber
Vacuum chamber
Considering local manufacture technology (especially welding technology) and a limitation of the chamber thickness located between the magnet poles, stainless steel has been selected as chamber material due to its excellent strength
Domestical manufacturing
To enhance production potential of Thai industrial sector, the knowledge of vacuum part fabrication has been transferred to Thai local company for producing chamber parts with ultrahigh vacuum and high precision requirements.

## Slide 16: Photon Beamlines
High resolution soft X-ray spectroscopy (HRSXS)
Tender X-ray absorption spectroscopy (TXAS)
Hard X-ray absorption spectroscopy (HXAS)
Small and wide angles X-ray scattering (SWAXS)
High-resolution X-ray diffraction (HRXRD)
X-ray micro computed tomography (XMCT)
Macromolecular X-ray crystallography (MX)
1 eV
10 eV
100 keV
far IR and IR
VIS
UV
10 keV
hard X-ray
1 keV
100 eV
VUV/soft X-ray
1. HRSXS: 0.08 – 2.5 keV
2. TXAS: 1.0 – 1.3 keV
3. HXAS: 4.0 – 35 keV
4. SWAXS: 4.0 – 23 keV
5. HRXRD: 8.0 – 25 keV
6. XMCT: 8.0 – 60 keV
7. MX: 5.0 – 20 keV
Beamline | Techniques
HRSXS | PES, ARPES, XPS, PEEM, NEXAFS, XMCD
TXAS | XANES, EXAFS, XRF
HXAS | XANES and QEXAFS, XRF, XES
SWAXS | SAXS, WAXS USAXS, GISAXS
HRXRD | XRD, High Resolution XRD, XRD imaging
XMCT | micro-tomography
MX | micro-focused MX MAD and SAD
1st phase beamlines

## Slide 17: Project Schedule
Building Construction
2025
Procurement and Construction of SPS-II
2023
Prototype R&D
2022
Development of Prototypes
2021
Design of the 3 GeV Synchrotron Light Source
2020
Installation and Commissioning
2029
Installation and Commissioning
2028
Operational SPS-II
User beam service (phase 1).
2030
Completion of SPS-II buildings

## Slide 18: Buildings and Facilities

## Slide 19: The budget tolerance
According to beam dynamic requirements, the accelerator physicist give the maximum alignment error as described:
Table: Storage ring magnet alignment tolerance
Error type | RMS
Element misalignment | 
Horizontal for quad,sext,dipole | 100 µm
Vertical for quad,sext,dipole | 100 µm
Longitudinal for dipole | 100 µm
Tilt for all | 200 µrad

## Slide 20: Reference network design
Area 140,493 sq.m
GNSS
GNSS
GNSS
GNSS

## Slide 21: Primary survey network
We classify our control network to two steps;
The primary survey network is used as the global control of the whole synchrotron that consists of 14 primary control points for accelerator part included M0. These are a central monument (M0), for M13 and M14 located in Linac tunnel and M1-M12 located around the storage ring tunnel. M0 or central control point will be established on the concrete pile embedded in bedrock. It will be used for an absolute displacement measurement.
The secondary survey network or alignment network

## Slide 22: Conclusion and future work
The survey network of SPS-II will be constructed by using GPS, total station, digital level, laser tracker and the metrology software. Our existing instruments are FARO laser tracker and CAM2 software, theodolite and optical level. We will assemble the team for surveying, focused on development of survey and alignment strategy for SPS-II installation. We are planning to visit and participate in alignment activities on accelerator laboratory around the world while we are also getting a good cooperation. In the future, we have to do a lot of work.

## Slide 23: Instrumentation

## Slide 24: Survey and Alignment Group
The organization of our Synchrotron Light Research Institute currently consists of 200 staffs which are 100 researchers, 30 engineers and 70 administrative officers.
Currently, we do not have survey and alignment group. We have supporting team consists of 1 civil engineer and 4 mechanical engineers.

## Slide 25
Thank you for your attention
Welcome to Thailand
Welcome all suggestions and recommendations.