## Slide 1: Status CTF3 committee 9/2010
DL only beam sent through – no combination
out of 12A in CR (x4), 10A get to TBL/TBTS PETS
up to 70MW with recirculation in TBTS PETS
3 MeV acceleration of probe beam
since then
focus on x8 combination (DL+CR)
maximize power production
maximize probe beam acceleration
1 week stop during International Linear Collider Workshop

## Slide 2: Factor 8 combination (DL+CR)
Combination well optimized in operation
  transmission
  closure
  path length
=> record current this year (MKS13 off)

## Slide 3: 12 GHz bunch phase studies
20 deg
100 deg
12 GHz RF phase
Erik Adli, Reidar Lillestøl
=>
=>
For 12 GHz power production, bunch phase along the pulse crucial
  => need stable beam energy, klystron phases, beam current
  DL, CR ring length, orbit, closure carefully optimized
  used RF pulse compression to minimize ∆E/E after the linac =>
  D0608=0.61m => 13mm = ~2% to ~3mm = ~0.5% ∆E/E
detailed studies of bunch phase, variation understood and minimized

## Slide 4: Emittance
measured in H and V for various stages of combination
emittance increase more from CR than from DL
Simona Bettoni
horizontal | CR 1st | DL+CR 1st | CR 4th combined | DL+CR 4th combined
emittance [mm mrad] | 148 | 262 | 532 | 682
beta [m] | 4.8 | 5.0 | 3.7 | 3.6
alpha | 0.9 | 0.9 | 1.0 | 1.2
vertical | CR 1st | DL+CR 1st | CR 4th combined | DL+CR 4th combined
emittance [mm mrad] | 88 | 129 | 152 | 170
beta [m] | 17.2 | 11.0 | 7.3 | 9.9
alpha | -8.1 | -5.1 | -3.1 | -4.3

## Slide 5: TL2 - TBTS
x8 recombination in CR
good transmission also for x8 combined beam from CR
>17A get to TBTS PETS

## Slide 6: TBTS - PETS
up to >250MW in PETS structure (?)
>100MW to structure (?)
RF calibration verified/corrected
signals internally consistent
deceleration studies suggest overestimation of power measurement

## Slide 7: Probe beam acceleration
probe beam acceleration optimized
  in time
  in phase
up to 18 MeV => gradient ~90 MV/m
Andrea Palaia

## Slide 8: Probe beam acceleration
acceleration less than expected
power calibration, structure frequency, other modes?
Simona Bettoni
connection to 30˚C water

## Slide 9: Probe beam acceleration
probe beam changes shape when accelerated (measured on straight screen for different focusing)
without with acceleration

## Slide 10: Schedule – restart 31/1/2011
Optics improvements (DL dispersion)
Full transport to CLEX
Bunch length control (first tests)
TBTS initial PETS tests
CALIFES setup
new setup when MKS13 available?
PETS conditioned to nominal power/pulse length TBL PETS tests
Accelerating structure conditioned to nominal power/pulse length
PETS breakdown rate measurements???
Test of new PETS on-off scheme
  Two-Beam test
  power & energy gain, 100MV/m
  Beam Loading compensation experiment
  Measurement of breakdown kicks
    Measurement of effect of beam loading on breakdown rate
  installTBL PETS ??
  <---->
  2nd TBL PETS installation
  6 weeks PHIN
  phase-coding
  Laser preparation
  TBL studies (limited)
    Stability studies & improvements
    PETS no recirculation
    Phase stability
    Operation at 5 Hz (or more)
    Control of beam losses
    Coherent Diffraction Radiation …
  TBL studies 30% deceleration ?
1
1
2
2
3
3
4
5
6
8
7
4
5
6
7
8
1
4
2
3
6
5
7
8
Beam