## Slide 1: IT-4738 Specifications Committee
Ll. Miralles

## Slide 2: Outlook
Introduction
Design
Project contract breakdown
MS-4738 results

## Slide 3
Introduction
The Long-Baseline Neutrino Facility (LBNF) supporting the international Deep Underground Neutrino Experiment (DUNE)
“The LBNF/DUNE project will be the first internationally conceived, constructed, and operated mega-science project hosted by the Department of Energy in the United States” - DOE

## Slide 4
DUNE Far detectors initial configuration
Single Phase horizontal drift
Single Phase vertical drift
1.5 Km
Introduction

## Slide 5
LAr TPC : large cryostat vessels
Cold cryostat volume ~ 13’000 m3, an industrial type of building
Liquid argon ~18 ktons / cryostat
Passive insulation to minimize long-term operation risks (no vacuum insulation)
Location : deep underground with limited elevator access : very modular assembly, minimal welding, …
LNG technology adopted
Design

## Slide 6
Far Detectors
6
FS det # 1
FS det # 2
High precision tracking (TPC charge collection)
High precision calorimetry
(charge and scintillation light)
17.5 ktons of LAr/det
>10 ktons active/det
3700 tons cryostat weight
LAr TPC : LBNF membrane cryostats
65’840 mm x 18’940 mm x 17’840 mm
(L x W x H)
Design

## Slide 7
Warm structure

## Slide 8
Warm structure

## Slide 9
The membrane of the LBNF have some ribs oriented vertically and horizontally;
Some clamps are used in order to fix and support the weight of the plate during installation and provide stability during the vacuum load case;
Analytical computations and simulations to verify the ribs pitch and the clamp capacity where performed.
Ribs
Clamp
M14
M16
Note: M14 bolts simulated with As – for more conservative results.
In addition, frictionless contacts were used for the clamp.
M14 and M16 bolts of class 8.8.
Tertiary membrane

## Slide 10
LAr TPC : large membrane cryostats
Warm steel structure (equivalent to the LNG ship)
Cold structure (protected by industrial IP)
80 cm PU reinforces foam
corrugated primary membrane
additional secondary membrane
+ many details
Cold structure

## Slide 11
Project contract breakdown
Warm structure material
Warm structure components manufacturing
Warm structure membrane manufacturing
Warm structure underground assembly
Cold structure material procurement
Cold structure underground assembly

## Slide 12
Budget breakdown
CONCEPT | ESTIMATION (MCHF)(*) | DR
Warm structure material | 2.4 | YES
Warm structure components manufacturing | 6.3 | YES
Warm structure membrane manufacturing | 1.0 | YES
Small components procurement | 1.3 | NO
Warm structure underground assembly | 4.0 | YES
Cold structure material procurement | 11.1 | YES
Cold structure underground assembly | 8.2 | YES
Transport | 1.2 | NO
TOTAL | 35.5 | 
(*) 1 Cryostat

## Slide 13
Schedule

## Slide 14
Schedule

## Slide 15
Schedule

## Slide 16
Schedule

## Slide 17
Schedule

## Slide 18
Schedule

## Slide 19
Schedule

## Slide 20
Schedule

## Slide 21
MS-4738 results

## Slide 22
MS-4738 Results

## Slide 23
MS-4738 Results

## Slide 24
MS-4738 Results
1 firm qualified from an European non member state