## Slide 1: Beam instrumentation status, studies and upgrades for Run 2a
E. Senes for the BI AWAKE team
AWAKE collaboration meeting, 12-13 April 2022
…. with many thanks to the colleagues from CERN, TRIUMF, CLEAR, MPP, UCL, Liverpool …

## Slide 2: Where do we start ?
More or less the same talk was given at the last Collaboration Meeting. Very diverse activities and dramatic improvement (and a lot of work) on:
Digital cameras systems
New current transformer
High Frequency button BPM
Cherenkov Diffraction BPMs
Spectrometer camera array
DMD halo monitor
… plus filling the laser holes in the screens, motors, etc …

## Slide 3: Digital cameras – systems
CERN to abandon analog cameras due to end of production and inferior performance
Two systems to replace the PXIs, up to 24 cameras each

## Slide 4: Digital cameras – systems
CERN to abandon analog cameras due to end of production and inferior performance
Beamline cameras (TSG41 + cs-ccr-awakecam)
Two systems to replace the PXIs, up to 24 cameras each
10 devices: 6 BTVs + BTV54 + Exp. Volume + 2 Halos
8 non-standard: 2 DMD halos + 4 spectrometer cams + 2 streak monitoring cams
Laser cameras (TSG40 + cs-ccr-awakecam1)
8 devices: 5 Virtual line + UV laser room + IR laser room + UV cathode
6 free
16 free

## Slide 5: Digital cameras – status
All the hardware currently installed
Support for Basler Ace Classic cameras, up to 1920x1200
Intense software development in 2022 – in parallel with testing
CAM1
CAM24
GiGE PoE SWITCH
64 CORE
SERVER
10G
FIBRE LINK
CCR
AWAKE

## Slide 6: Digital cameras – testing
Many test campaigns in 2021 and 2022
Continuous improvement since the FESA deployment:
10 cameras constantly installed
18 cameras for large scale tests (today!)
New features added
Support for non-BI cameras under development
To launch camera diagnostic:
/user/esenes/bin/AWAKE-camera-monitor/launch_camera_monitor.sh

## Slide 7: Digital cameras – testing
Many test campaigns in 2021 and 2022
Continuous improvement since the FESA deployment:
10 cameras constantly installed
18 cameras for large scale tests (now !)
New features added
Support for non-BI cameras under development
THE BEST STRESS TEST IS YOU
… we are dangerously close to when …

## Slide 8: Streak camera line
1 inch angular difference after 6m of optical line
Collaboration with the MPP team to improve the upstream streak camera optical line
Upcoming developments:
Motorization of a second mirror on the optical line
Check on screen flatness
Check on screen position repeatability
Work in progress …

## Slide 9: BCT downstream the plasma cell
Goals:
Measure charge after the plasma
Calibrate the spectrometer scintillator
Bergoz commercial BCT installed upstream the spectrometer
Installed in March with CERN readout electronics, currently under commissioning
Spectrometer
BCT
Quadrupole
For details AWK-BCTIA-EC-0001
https://edms.cern.ch/document/2714008/0.1

## Slide 10: High-frequency BPM studies
In the common line, the protons blind conventional electron BPM systems
eBPM working frequency
STRONGER PROTONS
STRONGER ELECTRONS
Need for a system performing the detection at sufficiently high frequency
It’s extremely difficult to build a well-behaved device that works at 10s of GHz
1
High frequency button BPMs
2
Cherenkov Diffraction Radiation BPMs

## Slide 11: High-frequency button BPM
HF BPM
Commercial 40 GHz conical buttons by OMC on an adapted DESY design
Installed yesterday
HF button vs traditional pBPM button
Upcoming tests with electrons (dedicated) and protons (parasitic)
Initial setup:
- Bandpass filters and diode detectors
- Investigating bands at 11 and 26 GHz
See A. Angelovski et al., Phys. Rev. ST Accel. Beams 15, 112803 (2012)
For details AWK-BPM-EC-0003 https://edms.cern.ch/document/2713307/0.1

## Slide 12: High-frequency button BPM
HF BPM
Commercial 40 GHz conical buttons by OMC on an adapted DESY design
Installed yesterday
HF button vs traditional pBPM button
Upcoming tests with electrons (dedicated) and protons (parasitic)
Initial setup:
- Bandpass filters and diode detectors
- Investigating bands at 11 and 26 GHz
See A. Angelovski et al., Phys. Rev. ST Accel. Beams 15, 112803 (2012)
For details AWK-BPM-EC-0003 https://edms.cern.ch/document/2713307/0.1

## Slide 13: ChDR BPMs
ChDR button vs traditional pBPM button
High operating frequency of 30 GHz
Successful in-air test campaign at CLEAR in 2021
Brazed ceramic inserts ø6 mm
Body #1 installed yesterday
Detection electronics under production by TRIUMF
For details AWK-BPM-EC-0002 https://edms.cern.ch/document/2667362/0.1
See Collette’s presentation on Wednesday

## Slide 14: ChDR BPMs
ChDR button vs traditional pBPM button
High operating frequency of 30 GHz
Successful in-air test campaign at CLEAR in 2021
Brazed ceramic inserts ø6 mm
Body #1 installed yesterday
Detection electronics under production by TRIUMF
For details AWK-BPM-EC-0002 https://edms.cern.ch/document/2667362/0.1

## Slide 15: Spectrometer camera array
Digital camera array at 150 cm
D. Cooke, F. Pannell, M. Wing (UCL)
Scintillator tile
Camera array
Spectrometer mirror
Permanently on the BI DAQ
New setup for the upcoming run with 4x 75mm f/2.8 lenses and 525 ± 46 nm filters
Goal: electron beam emittance measurement.
Factor x10 improvement on the existing spectrometer resolution
See David’s presentation tomorrow

## Slide 16: DMD halo monitor test
Screen
Core camera
Halo camera
DMD
Lens
Lens
Lens
Test of a Micro Mirror Device (DMD) to dynamically create masks for halo monitors
J. Wolfenden, C. Welsch (Liverpool U.)
DMD
CAMERA
LENS
PERISCOPE
EXISTING HALO
Low installation to limit radiation damage
Successful test run in November 2021

## Slide 17: DMD halo monitor test
Limited test beamtime as the September run was problematic & no plasma in November
J. Wolfenden, C. Welsch (Liverpool U.)
CORE
HALO
PROTONS ONLY
PLASMA ON
Exciting prospects for measurements now that the system is installed and the technical issues are solved !

## Slide 18
Comments (12-Apr-2022 12:00:00)
Thanks for your attention !
16-09-21 11:15:00