## Slide 1: High power RF system
Kévin Pepitone, Dragos Dancila, Alireza M. Kasai, Kristiaan Pelckmans
13 April 2022

## Slide 2: Outline
Layout of the RF line
Solid state power amplifier
Low level RF mTCA

## Slide 3: Layout of the RF line

## Slide 4: Modulators and klystrons – 1st line
2 Scandinova K100
2 Canon E37349 6 MW or E3779B 7.5 MW
CLERC Vincent BE-EA-DC

## Slide 5: Modulators and klystrons – 2nd line
CLERC Vincent BE-EA-DC
1 Scandinova K100 - Canon E37349 6 MW or E3779B 7.5 MW
1 Scandinova K200 - Canon E37118 10 MW
1 Scandinova K400 - CPI VKX-8311 50 MW

## Slide 6: RF components
SPECIFICATIONS: Model 2520-07 Vacuum Circulator
Frequency Range: 2998 MHz +/- 10 MHz
Peak Power: 10 MW maximum
Pulse Width: 5 uS
PRF: 10 Hz
Average Power: 500 Watts
Input VSWR: 1.15:1 maximum
Insertion Loss: 0.4 dB maximum
Isolation: 20 dB minimum
Waveguide Size: WR284
Waveguide Flanges: LIL
Waveguide Atmosphere: < 1 x 10-6 Torr
Cooling: Ambient Air
Materials: OFHC Copper waveguide (0.173” wall)
Stainless Steel, Alloy 316L, Ferrite
SF6-free
UHV circulator !!!
Pulse compressor BOC (CTF3)
The design is with waveguides without SF6

## Slide 7: HV stability
50 Hz, 4.5 us
250 Hz, 4.0 us
10 Hz, 3.0 us
K100 with 10 MW klystron

## Slide 8: Future developments and tests
R&D on oil for the modulator August-November 2022
HV tests and RF tests of 15 different samples
Test of the UHV circulator with high power RF
RF stability measurement:
Pulse to pulse
Repeatability
Temperature
Compression
…

## Slide 9: Solid state amplifiers

## Slide 10: Development of SSPA as driver for the klystrons
SSPA
Specifications
@3 GHz
1) 200W at the input of the 6 or 7.5 MW S-band klystron
@12 GHz
2) 200 W at the input of the 6 MW X-band klystron
3) 1000 W at the input of the 50 MW X-band klystron

## Slide 11: SSPA development at 3 GHz and 12 GHz
The development is planned to be incremental, starting with the high-power amplifiers, continuing with the integration of interlocks and finally with more advanced control.

## Slide 12: State of the art transistors
S-Band
X-Band
100 W transistor chip are quite expensive -> alternative combining many at lower power levels
GaN transistor will be chosen for the design

## Slide 13: Design in progress

## Slide 14: 12 GHz – 100 W is the max power available per transistor
Low loss power combiners development is key.
Price tag of this 500 W amplifier is prohibitive, i.e. 50 k$ and we would need to combine 2 of them for the klystron needs, i.e. 1000 W.
Thus, we plan to develop our own power amplifier at X band, based on combining 40+ transistors of 25 W each.
MMICs (monolithic microwave/millimeter-wave IC) combine transistors and passive devices

## Slide 15: Low level RF - mTCA

## Slide 16: mTCA crate at FREIA
DWC8VM1
SIS8300ku
Zone 3

## Slide 17: Specifications
Board Support Packages (BSPs):
CERN (SPS upgrade, 2019)
STRUCK demo (running, 2016)
DESY development (beta, 2022)

## Slide 18: Current CERNs development for SPS
+
All open source + inhouse (e.g. wishbone module + LM32 soft core processor)
-
Large latency
Tight integration with eRTM/White Rabbit
SISO control loops
(Simple loops, not considering interactions between the channels)
Ad-hoc architecture
(subjective: we found it challenging to modify the code to our needs)

## Slide 19: Current measurements at FREIA
STRUCK Board Support Package (BSP), 2016.
+ Operating
  Direct support
  ACQ (testing)
- No closed loop
  Outdated IP-cores.
  Inflexibly organised
  Unbounded latencies
+
Operating
Direct support from STRUCK
ACQ
(reading/writing module, used for testing)
-
No closed loop.
Outdated IP-cores
(e.g. use of the microBlaze module, instead LM32).
Inflexibly organised
(not meant to be modified)
Unbounded latencies

## Slide 20: Open source mTCA software
DESY BSP, 2022 (beta)
+
Mostly Open Source.
Support from DESY/MTCA.
Flexibly implemented.
(easy to extend)
Allows for extremely low latencies.
(DESY reports 72 clock cycles)
-
Some Closed IP-cores.
(e.g. Xilinx xDMA)
No closed loop open sourced yet
(codebase will be used for FLASHFORWARD)
TODO:
8x1 MIMO Closed Loop (Controlling interactions between channels)
Control design + latency optimization
Timing/interlocks
Measuring performance

## Slide 21: Planning
Working LLRF system
Implementation/
testing/simulation/
documentation
LLRF system
… preparation since oct 2021

## Slide 22: Conclusions

## Slide 23: Conclusions
RF lines well defined
Choice of the transistor is done
Work ongoing on the LLRF
The choice of the components is well advanced
R&D ongoing on different topics
Many material bought for the Xband and Sband SSPAs
Test of the Sband SSPA very soon
Material at FREIA
Good contact with Struck and DESY

## Slide 24: Thank you for your attention