## Slide 1: 60 GHz ECR source status
T. Lamy
M. Marie-Jeanne, P. Sortais, T. Thuillier
Laboratoire de Physique Subatomique et de Cosmologie, Grenoble – France
I.V. Izotov, A. V. Sidorov, V. A. Skalyga, V. G. Zorin
Институт Прикладной Физики - RAS, Nizhny Novgorod – Russia
F. Debray, C. Trophime, N. Vidal
Laboratoire National des Champs Magnétiques Intenses, Grenoble – France
* Sixty GHz ECR Ion Source using Megawatt Magnets

## Slide 2: 60 GHz ECR ion source for the Beta Beams
Euro-nu Beta Beams
High ionization efficiency ion source required, delivering high intensity
  Radiation hard ECR ion source
  low volume, high plasma density (high ECR frequency)
  10 Hz operation
LPSC long term strategy in ECR ion sources development
  To take advantage of this project to develop the ECR ion source operating
    At the highest present ECR frequency
    For a reasonable cost (warm technology for the magnet)
Decay ring
Based on CERN accelerators
251.33 m
10 Hz
50 µs
For a 100 % ionization efficiency
I(He2+) = 32 mA + all other species
I extracted  several 100 mA
6He  6Li + e- + e-
  6He (t1/2 = 807 ms), 18Ne, 8B , 8Li
  Continuous production
  5 . 1013 pps
e-
Superconducting
Proton LINAC

## Slide 3
Classical ‘Minimum B’ ECRIS
Electron Cyclotron Resonance Ion Sources (Basics)
Vacuum chamber
Magnetic field
(axial + radial)
Gas injection (typically 2) or vapor + gas
Microwaves (ECR)
Electron heating
Confinement of the plasma (hot e-, cold ions)
Step by step ionization
Extraction (High Voltage)
Microwaves
Gas
or
vapor
ECR
Brad ≈ 2*BECR
Binj ≈ 4 * BECR
Bmed ≈ 0.6 BECR
Bext ≈ 0.9 Brad
Ion
Extraction
Gas
Injection
Binj = 4 T
@ ECR 28 GHz
Iextracted  ni =
Electronic cyclotronic Resonance
Cutoff density pe = ce
To increase I, increase ne so ce and consequently B
I ∝ ωce2

## Slide 4: First 60 GHz ECRIS ‘SEISM’ prototype specifications
‘simple’ magnetic structure, pulsed Microwave
CUSP magnetic structure
  Compact source (l = 100 mm)
  Spherical ECR zone at center
ECR
Specifications
  60 GHz ECR, 10 Hz duty factor
  Cw magnetic field (future cw source)
    Injection 6 T
    Extraction 3 T
    Radial 4T
    2.14 T Spherical ECR zone
4 T
3 T
6 T
4 T
Injection
Extraction
Magnetic field lines crossing the ECR zone don’t touch the walls
60 mm
100 mm between the Bmax
ECR
zone 2.14 T
Presently no ECRIS with such a (high) magnetic field (and high gradient)
Conceptual design undergoing for superconducting 56 GHz minimum B ECRIS in US and China

## Slide 5: 60 GHz ECRIS prototype simulation
R&D towards high ECR frequency for future ECRIS
  Low cost and fast development
  No superconductors, high field techniques (copper and water)
  Collaboration with CNRS intense magnetic fields laboratory (LNCMI)
    Choice : Polyhelix technique (high currents in copper helices)
Magnetic field lines
2.14 T
> 7 T injection (spec. 6T)
> 3.5 T ion extraction (spec. 3T)
> 4.6 T radial mirror (spec. 4T)
  30000A, J~650 A/mm2
  P ~ 6 MW
  TMax loc. ~ 330 °C (H1)
  TMean ~ 80°C to 180°C (H1)
Injection
Extraction
H1
H2
H3
H4
Getdp
Plasma
Chamber
Extraction helices
H4
H2
injection
helices
H3
H1

## Slide 6
Helices construction
Helical slit cut by spark erosion
Chemical treatment
Positioning the prepreg insulators
H1
H3
2 current leads per helix
Ring with recess
on the internal coils
Keys on the external coils
Oven
Final machining
pitches from 2 to 5 mm
Cleaning
to prevent shortcuts

## Slide 7: Prototype mechanical design
2 sub-assemblies
helices and current leads
The basic part: ‘exchanger’
CAD
Extraction Flange
Characteristics
  Diameter 620 mm
  Length 480 mm
  600 kg
  30 tons Repel force

## Slide 8: Radial cooling of the helices
Water cooling
(deionized water )
  Water cooling flow ~ 30 l/s
  Pin = 27 bars ; Pout = 4 bars
  Tinlet = 20 °C, Toutlet = 40 °C
Water
Inlet
Water
distribution
part
Outlet
Insulators
Worth case (thinner pitch of H1)
  I = 30000 A
  Empty space : 1.7 mm
  Copper thickness : 2 mm
  Tmean = 180 °C, Tmax = 330 °C
About 700
insulators
10 % of the total surface

## Slide 9: SEISM prototype assembly

## Slide 10
LNCMI : a place to perform experiments
19 T /160 mm
34 T /34 mm
Cooling
1000 m3/h
deionized water
4 Power supplies
15 000 A, 400 V
(24 mW)
28 GHz 15000 A
2.5 MW
60 GHz 30000 A
6 MW
M5
M7

## Slide 11: SEISM prototype setup on the M5 site
M5 site adaptation for SEISM
  Parallel hydraulic circuit ( 50 l/s from 150 l/s)
  Serial electrical connexion with M5 (impedance matching)
M5 site

## Slide 12: SEISM magnetic field measurements principles
Helices temperature monitoring
  Resistance variation with T, R=R0(1+*T), Copper (= 0.0036)
    R0 = 3 m at 10 °C (SSI Hall temperature in winter...)
  R=U/I = R0(1+*T)  T
    Voltage measured during operation
    Intensity given by LNCMI supplies
Automated magnetic induction measurements
  Tesla meters, axial and radial Hall probes on specific stands (calibrated on M5)
  probes movements with jacks – steppers 1 mm / 300 mm
  Labview control
Voltage
measurement
Jack
Hall probe
Hall probes

## Slide 13: Magnetic field measurements results
Axial magnetic field induction from 1500 up to 15000 A
  Axial and radial measurements three axis of the prototype (0, 15 and 30 mm)
Magnetic field induction norm
Expected results (and obtained)
  Axial symetry of the magnetic field
  Linear increase of B with intensity
Unexpected results
  10 mm shift of the maxima
  Lower amplitude on the extraction side
  No impact on the plasma characteristics
15000 A measurements

## Slide 14
28 GHz
14 GHz
Iso-B for resonance zones
Plasma experiments are already ‘magnetically’ possible at 28 GHz
using two LNCMI current supplies
Phase 1 of this project is a success
28 GHz (1T) ECR zone closed at about 12000 A
The 60 GHz closed ECR zone should be obtained at 26000 A

## Slide 15: Application for magnet time
Characterization of ion beams extracted from a 28 GHz ECR plasma in a split magnet
To progress towards 60 GHz ECR operation of the ECRIS
  Simple beam line : magnetic spectrometer and beam characterization devices
  10 kW 28 GHz gyrotron available from LPSC
  A lot of safety issues (Microwaves, X rays, High voltage...)
After beam measurements (a few weeks)
  Terminate magnetic field measurements from 15000 up to 30000 A
  If gyrotron available : 60 GHz experiments
  Accepted for 20 days
28 GHz
waveguide
High voltage
ring
Plasma
chamber
Plasma
electrode
Extraction
insulator
Puller
electrode
Inside ECRIS 28 GHz prototype design

## Slide 16: Efficiencies and currents expected ...?
Fast ionization, efficient ionization
  High density necessary
  High ECR frequency (60 GHz) and high power density
  60 GHz : cut-off density 4.46x1013 ions/cm3 to be compared with
  2x1010 ions/cm3 He ...(5 x 1012 in a 0.25 l (plasma): 2x1010 ions/cm3
  (ratio  4.5 10-4)
  Multi-Ampères source !!!! Certainly avoid multi charged ions...
    High intensity beam line will be required (mandatory...)
    But good news from Russia
8th International Workshop ‘Strong Microwaves and Terahertz Waves Sources and Applications’
July 9 - 16, 2011 Nizhny Novgorod, Russia
    1.6 mm extraction hole leads to 80% efficiency for He+ and only 300 mA total current
    “Gas utilization efficiency optimization for short-pulsed ECR ion source”
    I. V. Izotov, V. A. Skalyga, V. G. Zorin (IAP Nizhny Novgorod)

## Slide 17: LNCMI site preparation for future experiments
Design of the High intensity beam line
  Vacuum components (turbo pumps, chambers, tubes...) ordered
  Stands ordered
  Magnetic spectrometer current supply operational
  LNCMI installation in M3 rather problematic...
      Concrete foundation slab resistance ... (Magnet > 2 tons)...
      Layout
      Magnetic fringing fields from other magnets and prototype (for gyrotron)
      A lot of safety issues (HV, MW, X rays...)

## Slide 18: 60 GHz gyrotron
Pulsed 60 GHz 300 kW gyrotron manufactured by GYCOM
Supplies Institute of Applied Physics - RAS (Nizhny Novgorod – Russia)
  Frequency 60 GHz, MW power 10 - 300 kW
  Pulse duration from 50 ms to 1 ms, pulse repetition rate up to 5 Hz
Tube
Gyrotron in the
cryomagnet
Matching Optics Unit
Delivery at Grenoble spring 2012
Project #3965
Design, Manufacturing and Tests of Short Pulse ECR Multi-Charged Ion Source Prototype with High Ionization Efficiency

## Slide 19: Eqipex 2011 under preparation
40 T HIGH FIELD
MAGNETS
HIGH FIELDS MAGNETS
25 MW POWER SUPPLIES
ION SOURCES
PLASMAS
Superconducting bus from LNCMI to LPSC (4*15000 A) allowing future ECRIS R&D
28 and 60 GHz ion sources for SPIRAL2

## Slide 20
Thank you !
We acknowledge the financial support of the European Community under the European Commission Framework Programme 7 Design Study: EUROnu, Project Number 212372. The EC is not liable for any use that may be made of the information contained herein.