## Slide 1: 8th Internationally Participated Congress On Particle Accelerators And Applications (UPHUK VIII)
RF powering for accelerators
eric.montesinos@cern.ch
September 05 - 07 2022, The Turkish Physical Society, Bodrum, Turkey

## Slide 2: RF Powering
(Very important for all projects)
W → kW → MW
€ → k€ → M€

## Slide 3: Outlook
RF power amplifiers for accelerators
  Grid Tubes
  Klystrons
  Inductive Output Tubes (IOT)
  Transistors (LDMOS)
  Combiners
RF power lines
  Wave Guides
  Coaxial lines
  Circulators
FPC
Efficiency

## Slide 4: RF Power Amplifier
DUT
(Device Under Test)

## Slide 5: RF power source classification
Vacuum Tubes
Grid Tubes
Triodes
Tetrodes
Pentodes
Diacrodes
Linear Beam Tubes
Klystrons
Travelling Wave Tubes (TWT)
Gyrotrons
Inductive Output Tube (IOT)
Crossed-field Tubes
Magnetrons
Transistors
Bipolar Junction Transistor (BJT)
Field Effect Transistor (FET)
Junction Gate FET (JFET)
Metal Oxide Semiconductor FET (MOSFET)
power MOSFET
Vertically Diffused Metal Oxide Semiconductor (VDMOS)
Laterally Diffused Metal Oxide Semiconductor (LDMOS)
Gallium Nitride (GaN)
Silicon Carbide MOSFET (SiC)

## Slide 6: RF power source classification
Vacuum Tubes
Grid Tubes
Triodes
Tetrodes
Pentodes
Diacrodes
Linear Beam Tubes
Klystrons
Travelling Wave Tubes (TWT)
Gyrotrons
Inductive Output Tube (IOT)
Crossed-field Tubes
Magnetrons
Transistors
Bipolar Junction Transistor (BJT)
Field Effect Transistor (FET)
Junction Gate FET (JFET)
Metal Oxide Semiconductor FET (MOSFET)
power MOSFET
Vertically Diffused Metal Oxide Semiconductor (VDMOS)
Laterally Diffused Metal Oxide Semiconductor (LDMOS)
Gallium Nitride (GaN)
Silicon Carbide MOSFET (SiC)

## Slide 7: Grid tubes
Diode, John Ambrose Fleming
Audion (first triode), Lee de Forest
Triode as amplifier, Fritz Lowenstein
Triode ‘higher vacuum’, Harold Arnold
first transcontinental telephone line, Bell
1916 Tetrode, Walter Schottky
Pentode, Bernardus Tellegen
1994 Diacrode, Thales Electron Devices
The first diode prototype Fleming Diode, 1904
Thales TH 628 diacrode, 1998

## Slide 8: Essentials of grid tube
Vacuum tube
Heater + Cathode
  Heated cathode
    Coated metal, carbides, borides,…
  thermionic emission
  Electron cloud
Anode
Diode
Cathode & Filament
e-
e-
e-
e-
e-
Ua
Anode
e-
e-
e-
e-
Icurrent
e-
e-

## Slide 9: Essentials of grid tube
Vacuum tube
Heater + Cathode
  Heated cathode
    Coated metal, carbides, borides,…
  thermionic emission
  Electron cloud
Anode
Diode
Ua
Anode
e-
e-
e-
Icurrent
Cathode & Filament

## Slide 10: Essentials of grid tube
Triode
  Modulating the grid voltage proportionally modulates the anode current
  Transconductance
    Voltage at the grid
    Current at the anode
  Limitations
    Parasitic capacitor Anode/g1
    Tendency to oscillate
Ug1
Control Grid
Ua
Anode
e-
e-
e-
e-
e-
e-
e-
e-
e-
Cathode & Filament

## Slide 11: Essentials of grid tube
Tetrode
  Screen grid
    Positive (lower anode)
    Decouple anode and g1
    Higher gain
  Limitations
    Secondary electron
    Anode treated to reduce secondary emission
e-
Ug1
Control Grid
Ug2
Screen Grid
Ua
Anode
e-
e-
e-
e-
e-
e-
e-
e-
Cathode & Filament

## Slide 12: Tetrode RS 2004 CERN SPS example
Ug1
Control Grid
Ug2
Screen Grid
Ua
Anode
Grounded Screen Grid
RF in
RF out
CERN SPS, RS 2004 Tetrode (very) simplified bloc diagram
Cathode & Filament

## Slide 13: Tetrode RS 2004 CERN SPS amplifier @ 200 MHz
CERN SPS, RS 2004 Tetrode, Trolley (single amplifier), and transmitter (combination of amplifiers)
Two transmitters of eight tubes delivering 2 x 1 MW @ 200 MHz, into operation since 1976

## Slide 14: Tetrodes & Diacrodes available from industry
Chart: Frequency MHz
| 30 | 30 | 30 | 30 | 30 | 30 | 50 | 50 | 60 | 80 | 80 | 110 | 110 | 110 | 120 | 120 | 130 | 200 | 200 | 200 | 200 | 200 | 200 | 210 | 220 | 352 | 352 | 400 | 400 | 450 | 450
peak < 1 ms | 1000 | 700 | 500 | 1500 | 500 | 4000 | 600 | 1000 | 1000 | 120 | 2500 | 500 | 3000 | 120 | 200 | 30 | 100 | 15 | 200
CW | 750 | 700 | 400 | 300 | 150 | 1500 | 2000 | 1500 | 2000 | 100 | 100 | 1700 | 60 | 200 | 60 | 450 | 40 | 20 | 60
#REF! | 1

## Slide 15: RF power source classification
Vacuum Tubes
Grid Tubes
Triodes
Tetrodes
Pentodes
Diacrodes
Linear Beam Tubes
Klystrons
Travelling Wave Tubes (TWT)
Gyrotrons
Inductive Output Tube (IOT)
Crossed-field Tubes
Magnetrons
Transistors
Bipolar Junction Transistor (BJT)
Field Effect Transistor (FET)
Junction Gate FET (JFET)
Metal Oxide Semiconductor FET (MOSFET)
power MOSFET
Vertically Diffused Metal Oxide Semiconductor (VDMOS)
Laterally Diffused Metal Oxide Semiconductor (LDMOS)
Gallium Nitride (GaN)
Silicon Carbide MOSFET (SiC)

## Slide 16: Linear beam tubes
1937 Klystron, Russell & Sigurd Variant
1938 IOT, Andrew V. Haeff
1939 Reflex klystron, Robert Sutton
1940 Few commercial IOT
1941 Magnetron, Randall & Boot
1945 Helix Travelling Wave Tube (TWT), Kompfner
1948 Multi MW klystron
1959 Gyrotron, Twiss & Schneider
1963 Multi Beam Klystron, Zusmanovsky and Korolyov
1980 High efficiency IOT
Thales TH 1802, 2002
Russell & Sigurd Varian klystron, 1937

## Slide 17: Essentials of klystron
Klystrons velocity modulation
  converts the kinetic energy into radio frequency power
Vacuum tube
Electron gun
  Thermionic cathode
  Anode
Electron beam
Drift space
Collector
e- constant speed until the collector
Cathode & Filament
Ubeam
Uanode
Electron Gun
Drift Space
Collector

## Slide 18: Essentials of klystron
Cavity resonators
RF input cavity (Buncher)
  modulates e- velocity
  Some are accelerated
  Some are neutral
  Some are decelerated
  Bunching the e-
RF output cavity (Catcher)
  Resonating at the same frequency as the input cavity
  At the place with the numerous number of e-
  Kinetic energy converted into voltage and extracted
Ubeam
Cathode & Filament
Uanode
Cavity
Coupling
loop
Accelerating
gap
Beam
line

## Slide 19: Essentials of klystron
Cavity resonators
RF input cavity (Buncher)
  modulates e- velocity
  Some are accelerated
  Some are neutral
  Some are decelerated
  Bunching the e-
RF output cavity (Catcher)
  Resonating at the same frequency as the input cavity
  At the place with the numerous number of e-
  Kinetic energy converted into voltage and extracted
+
-
+
-
→
→

## Slide 20: Essentials of klystron
Cavity resonators
RF input cavity (Buncher)
  modulates e- velocity
  Some are accelerated
  Some are neutral
  Some are decelerated
  Bunching the e-
RF output cavity (Catcher)
  Resonating at the same frequency as the input cavity
  At the place with the numerous number of e-
  Kinetic energy converted into voltage and extracted
+
-
+
-
→
→

## Slide 21: Essentials of klystron
Cavity resonators
RF input cavity (Buncher)
  modulates e- velocity
  Some are accelerated
  Some are neutral
  Some are decelerated
  Bunching the e-
RF output cavity (Catcher)
  Resonating at the same frequency as the input cavity
  At the place with the numerous number of e-
  Kinetic energy converted into voltage and extracted

## Slide 22: Essentials of klystron
Cavity resonators
RF input cavity (Buncher)
  modulates e- velocity
  Some are accelerated
  Some are neutral
  Some are decelerated
  Bunching the e-
RF output cavity (Catcher)
  Resonating at the same frequency as the input cavity
  At the place with the numerous number of e-
  Kinetic energy converted into voltage and extracted
-
+
Voltage in cavities
vs time
time
decelerated
neutral
accelerated
Distance (drift space)
e- density at input cavity
e- density at output cavity
Bunching of e- beam in a klystron

## Slide 23: Essentials of klystron
Additional bunching cavities
  Resonate with the pre-bunched electrons beam
  Generate an additional accelerating/decelerating field
  Better bunching
  Gain 10 dB per cavity
Focusing magnets
  To maintain the e- beam as expected and where expected
Collector
Anode
Cathode & Filament

## Slide 24: Klystron TH 2167 CERN LHC @ 400 MHz
CERN LHC, TH 2167 klystron in lab and in UX45 cavern
16 klystrons delivering 330 kW @ 400 MHz, into operation since 2008

## Slide 25: Klystrons available from industry
Chart: Frequency MHz
| 350 | 352 | 401 | 500 | 500 | 500 | 500 | 2450 | 4900 | 1300 | 1500 | 2856 | 2998 | 2998 | 352 | 402 | 805 | 1300 | 700 | 500 | 915 | 1497 | 1300 | 2450 | 5000 | 7145 | 7900 | 10000 | 14000 | 16700 | 17300 | 21000 | 805 | 352 | 1300 | 2856 | 2998 | 5400 | 11994
peak < 50 µs | 30000 | 20000 | 60000 | 60000 | 45000 | 2800 | 2500 | 5000 | 10000 | 2500 | 2800 | 10400 | 5500 | 7500 | 3000 | 50000
CW | 1100 | 1300 | 300 | 180 | 250 | 310 | 800 | 50 | 50 | 1000 | 800 | 100 | 110 | 300 | 500 | 20 | 25 | 14.5 | 10 | 13 | 2.5 | 2.4 | 2

## Slide 26: RF power source classification
Vacuum Tubes
Grid Tubes
Triodes
Tetrodes
Pentodes
Diacrodes
Linear Beam Tubes
Klystrons
Travelling Wave Tubes (TWT)
Gyrotrons
Inductive Output Tube (IOT)
Crossed-field Tubes
Magnetrons
Transistors
Bipolar Junction Transistor (BJT)
Field Effect Transistor (FET)
Junction Gate FET (JFET)
Metal Oxide Semiconductor FET (MOSFET)
power MOSFET
Vertically Diffused Metal Oxide Semiconductor (VDMOS)
Laterally Diffused Metal Oxide Semiconductor (LDMOS)
Gallium Nitride (GaN)
Silicon Carbide MOSFET (SiC)

## Slide 27: Essentials of IOT
IOT density modulation
  converts the kinetic energy into radio frequency power
Vacuum tube
Triode input
  Thermionic cathode
  Grid modulates e- emission
Klystron output
  Anode accelerates e- buckets
  Short drift tube & magnets
  Catcher cavity
  Collector
Ugrid
e-
e-
e-
Cathode & Filament
e-
e-
Uanode

## Slide 28: IOT TH 795 CERN SPS @ 800 MHz
CERN SPS, TH 795 IOT, Trolley (single amplifier), and transmitter (combination of amplifiers)
Two transmitters of four tubes delivering 2 x 240 kW @ 801 MHz, into operation since 2014

## Slide 29: IOT available from industry
Chart: Frequency MHz
| 815 | 1300 | 500 | 605 | 400 | 503 | 805
peak < 10 ms | 130 | 90 | 110 | 100
CW | 30 | 30 | 90 | 80 | 60 | 85 | 60
#REF! | 1
Possible even if
never requested yet

## Slide 30: RF power source classification
Vacuum Tubes
Grid Tubes
Triodes
Tetrodes
Pentodes
Diacrodes
Linear Beam Tubes
Klystrons
Travelling Wave Tubes (TWT)
Gyrotrons
Inductive Output Tube (IOT)
Crossed-field Tubes
Magnetrons
Transistors
Bipolar Junction Transistor (BJT)
Field Effect Transistor (FET)
Junction Gate FET (JFET)
Metal Oxide Semiconductor FET (MOSFET)
power MOSFET
Vertically Diffused Metal Oxide Semiconductor (VDMOS)
Laterally Diffused Metal Oxide Semiconductor (LDMOS)
Gallium Nitride (GaN)
Silicon Carbide MOSFET (SiC)

## Slide 31: Transistor for RF power
1925 theory, Julius Edgar Lilienfeld
1947 Germanium US first transistor, John Bardeen, Walter Brattain, William Shockley
1948 Germanium European first transistor, Herbert Mataré and Heinrich Welker
1953 first high-frequency transistor, Philco
1954 Silicon transistor, Morris Tanenbaum
1960 MOS, Kahng and Atalla
1966 Gallium arsenide (GaAs)
1980 VDMOS
Silicon-Germanium (SiGe)
Gallium Nitrade (GaN)
1997 Silicon carbide (SiC)
Graphene (GFET)
20xx …
First transistor invented at BELL labs in 1947
XXI century LDMOS

## Slide 32: Essentials of RF transistor
In a push-pull circuit the RF signal is applied to two devices
  One of the devices is active on the positive voltage swing and off during the negative voltage swing
  The other device works in the opposite manner so that the two devices conduct half the time
  The full RF signal is then amplified
Two different type of devices
NPN BJT
PNP BJT
Vout
Vin
Vdc

## Slide 33: Essentials of RF transistor
Another push-pull configuration is to use a balun (balanced-unbalanced)
  it acts as a power splitter, equally dividing the input power between the two transistors
  the balun keeps one port in phase and inverts the second port in phase
Since the signals are out of phase only one device is on at a time
This configuration is easier to manufacture since only one type of device is required
Vout
Vin
Vdc
NPN BJT
NPN BJT
Input balun
(Unbalanced-Balanced)
Output balun
(Balanced-Unbalanced)
0 ⁰
0 ⁰
180 ⁰
180 ⁰

## Slide 34: Essentials of RF transistor
NXP Semiconductors AN11325
2-way Doherty amplifier with BLF888A

## Slide 35: Transistors available from industry
Chart: Frequency MHz
| 470 | 1500 | 860 | 128 | 600 | 500 | 2200 | 1500 | 1300 | 1400 | 2500 | 1500 | 1000 | 860 | 2000
peak < 50 µs
CW | 600 | 160 | 300 | 1400 | 1400 | 1200 | 10 | 200 | 70 | 100 | 10 | 500 | 600 | 450 | 100
#REF! | 1

## Slide 36: Combiners & Splitters
RF power combiners and RF power splitters are the same items
Resistive power splitters & Combiners
  Cheap and easy to build
  Use of resistor to maintain the impedance
  Power limitation and losses induces by the resistors (→ not used in high power)
Hybrid power splitters & Combiners
  Use RF lines
  Low levels of loss
  Limitation by the size of the lines
P
P
2P
P
P/2
P/2

## Slide 37: Combiners & Splitters
3 dB phase combiner
With correct input phases
P1
P2
Δ
Correctly adjusting the phase and the gain, P1 = P2 = P

## Slide 38: Combiners & Splitters
CERN SPS 64 to 1 combiner @ 200 MHz

## Slide 39: Combiners & Splitters
Low loss T-Junction
With
We have a N-ways splitter
Zc
Zc
Zc
Zc
Zc
160 to 1 @ 352 MHz
T-junction combiner

## Slide 40: Transistors SOLEIL @ 352 MHz and ESRF @ 352 MHz
ESRF four 150 kW @ 352 MHz
solid state amplifiers (2012)
SOLEIL 45 kW @ 352 MHz
solid state amplifier towers (2004 & 2007)

## Slide 41: Combining system
3 dB combiner
32 x 35 kW to 1 x 1 MW
(~ 50 m2)
VHPCC (Very High Power Cavity Combiner)
16 x 70 kW to 1 x 1 MW
(~ 3 m2)
CC (Cavity Combiner)
144 x 1 kW to 1 x 144 kW

## Slide 42: Combining system
In order to ensure 100 % availability, your combining system will define the number ‘Base units’
Base unit = 1
Nominal Output = 16
Wish to have full performance with 2 ‘Off Line’
Degraded Output = 12.25
So, in order to be 100 % available, this system composed of 16 x Base Units, is in fact a 12 x Base Unit
In order to perform the same 12 x Base Unit, with the same 2 Base unit tolerance, with a cavity combiner, you need only 14 x Base Unit instead of 16

## Slide 43: Combining system granularity
Nominal Output = 16
If because of your ‘pre-grouping’, several transistors are not available, granularity is then not enough
Degraded Output = 9
So, in order to be 100 % available, this system composed of 16 x Base Units, is in fact a 9 x Base Unit
In order to perform the same 9 x Base Unit, with the same 1 Module unit tolerance, with a cavity combiner and keeping the Base unit granularity, you need only 10 x Base Unit instead of 16
1 Module =
4 x Base unit
In order to ensure 100 % availability, your Granularity will define the number ‘Module units’ and ‘Base units’

## Slide 44: ‘Young’ technology for HPRF in 100 kW to MW range
CERN SPS Thales Solid State Power Amplifiers,
32 towers x 144 kW @ 200 MHz, combined into 2 x 2 MW amplifiers,
into operation since 2021

## Slide 45: Transistors available from industry
Chart: Frequency MHz
| 470 | 1500 | 860 | 128 | 600 | 500 | 2200 | 1500 | 1300 | 1400 | 2500 | 1500 | 1000 | 860 | 2000
#REF! | 1
CW | 60 | 16 | 30 | 140 | 140 | 120 | 1 | 20 | 7 | 10 | 1 | 50 | 60 | 45 | 10
#REF! | 1

## Slide 46: Power density
SOLEIL 45 kW @ 352 MHz
2004
Power density
3.5 kW m-3
ESRF 150 kW @ 352 MHz
2012
Power density
6.5 kW m-3
CERN 160 kW @ 200 MHz
2021
Power density
15 kW m-3
Chart: including power supplies and combining systems AND granularity providing 100 % availability !
| 2004 | 2012 | 2021 | 2030
200 MHz | 5 | 8 | 15 | 60
400 MHz | 3.5 | 5.5 | 11 | 42
800 MHz | 2.5 | 4 | 7.5 | 30
FCC 1 MW @ 400 MHz
Power density
43 kW m-3
FCC 200 kW @ 800 MHz
Power density
10 kW m-3
Approximation, given the fact that transistors deliver less with respect to frequency, and taking into account a smaller combining system size

## Slide 47: Overhead comparison
Chart: Tetrodes, Klystrons, SSPA
| 0 | 0.14857142857142858 | 0.29428571428571426 | 0.45 | 0.61428571428571432 | 0.79285714285714282 | 1 | 1.3142857142857143 | 1.8871428571428572 | 3.2142857142857144 | 6.4285714285714288 | 0.54545454545454541 | 0.61818181818181817 | 0.72727272727272729 | 0.83636363636363631 | 0.98181818181818181 | 1 | 1.1272727272727272 | 1.3090909090909091 | 1.509090909090909 | 1.7636363636363637 | 2.0363636363636362 | 2.3636363636363638 | 2.4727272727272727 | 3.676408537275877E-2 | 0.16810482465774959 | 0.30804216967959258 | 0.44534997545593652 | 0.59379996727458195 | 0.75953918166077616 | 0.999381782168974 | 1.2091871815897948
Tetrode & IOT | 0 | 0.16667 | 0.33333 | 0.5 | 0.66667 | 0.83333 | 1 | 1.1667 | 1.3333 | 1.5 | 1.6667
Klystron | 0.593 | 0.67 | 0.763 | 0.876 | 0.979 | 1 | 1.092 | 1.219 | 1.284 | 1.312 | 1.311 | 1.282 | 1.275
SSPA | 0.025333 | 0.16667 | 0.33333 | 0.5 | 0.66667 | 0.83333 | 1 | 1.0833

## Slide 48: High Power options
Final stage | DC Voltage | Driver | Gain | Power per unit | Combiner (for 1 MW)
Tetrode | 15 kV | 6.2 kW | 13 dB | 135 kW | 8:1
Klystron | 100 kV | 10 W | 50 dB | 1 MW | -
IOT | 40 kV | 320 W | 23 dB | 65 kW | 16:1
SSPA | 50 V | 5 W | 23 dB | 1100 W | 1024:1
mW
Driver
Final
Combiner
(0.05 dB losses per flange level)
MW

## Slide 49: RF Power Lines
DUT
(Device Under Test)

## Slide 50: Rectangular waveguides
The main advantage of waveguides is that waveguides support propagation with low loss
Wavelength | 
Cutoff frequency dominant mode | 
Cutoff frequency next higher mode | 
Usable frequency range | 1.3 to 0.9
Wavelength | 
Cutoff frequency dominant mode | 
Cutoff frequency next higher mode | 
Usable frequency range | 
b
a

## Slide 51: Rectangular waveguides
Waveguides are usable over certain frequency ranges
  For very lower frequencies the waveguide dimensions become impractically large
  For very high frequencies the dimensions become impractically small & the manufacturing tolerance becomes a significant portion of the waveguide size
b
a
Waveguide name |  |  | Recommended frequency band of operation (GHz) | Cutoff frequency of lowest order mode (GHz) | Cutoff frequency of next mode (GHz) | Inner dimensions of waveguide opening (inch)
EIA | RCSC | IEC |  |  |  | 
WR2300 | WG0.0 | R3 | 0.32 — 0.45 | 0.257 | 0.513 | 23.000 × 11.500
WR1150 | WG3 | R8 | 0.63 — 0.97 | 0.513 | 1.026 | 11.500 × 5.750
WR340 | WG9A | R26 | 2.20 — 3.30 | 1.736 | 3.471 | 3.400 × 1.700
WR75 | WG17 | R120 | 10.00 — 15.00 | 7.869 | 15.737 | 0.750 × 0.375
WR10 | WG27 | R900 | 75.00 — 110.00 | 59.015 | 118.03 | 0.100 × 0.050
WR3 | WG32 | R2600 | 220.00 — 330.00 | 173.571 | 347.143 | 0.0340 × 0.0170

## Slide 52: Rectangular waveguides Maximum Power handling
With
P = Power in watts
a = width of waveguide in cm
b = height of waveguide in cm
λ = free space wavelength in cm
Emax = breakdown voltage gradient of the dielectric filling the waveguide in Volt/cm (for dry air 30 kV/cm, for ambient air 10 kV/cm)
Chart: Peak Power vs Frequency
| 200 | 250 | 300 | 350 | 400 | 450 | 500 | 550 | 600 | 650 | 700 | 750 | 800 | 850 | 900 | 950 | 1000
WR2300 | 526.6212 | 691.9711 | 780.7698 | 836.2189 | 873.7253
WR2100 | 505.359 | 603.6639 | 662.6881 | 701.8693 | 729.5056
WR1800 | 356.7648 | 426.8444 | 470.6129 | 500.5393 | 522.1536
WR1500 | 266.9728 | 302.4189 | 326.8145 | 344.6071 | 358.0966 | 368.6196
WR1150 | 156.0606 | 172.9928 | 185.53 | 195.1925 | 202.852 | 209.0547
WR975 | 107.9109 | 119.5368 | 128.3767 | 135.3407 | 140.9658 | 145.5965
WR2300
WR2100
WR1800
WR1500
WR1150
WR975

## Slide 53: Rectangular waveguides Attenuation
With
a0 = 3 10-7 [dB/m] for copper
a = width of waveguide in m
b = height of waveguide in m
λ = free space wavelength in m
Attenuation factors of waveguides made from different material normalized to a waveguide of same size made of copper | 
Copper | 1.00
Silver | 0.98
Aluminium | 1.30
Brass | 2.05
Chart: Peak Power vs Frequency
| 200 | 250 | 300 | 350 | 400 | 450 | 500 | 550 | 600 | 650 | 700 | 750 | 800 | 850 | 900 | 950 | 1000
WR2300 | 0.11918 | 0.08698 | 0.075652 | 0.070332 | 0.067643
WR2100 | 0.11633 | 0.094541 | 0.085004 | 0.080085 | 0.077442
WR1800 | 0.15349 | 0.12459 | 0.11126 | 0.10398 | 0.099747
WR1500 | 0.18508 | 0.15998 | 0.14626 | 0.13794 | 0.13266 | 0.12927
WR1150 | 0.27748 | 0.24602 | 0.22674 | 0.21398 | 0.20516 | 0.19893
WR975 | 0.37177 | 0.33005 | 0.3036 | 0.28555 | 0.27267 | 0.26322
WR2300
WR2100
WR1500
WR1150
WR975

## Slide 54: Coaxial Lines
Characteristic impedance is
With
D = inner dimension of the outer conductor
d = outer dimension of the inner conductor
εr = dielectric characteristic of the medium
Size | Outer conductor |  | Inner conductor | 
 | Outer diameter | Inner diameter | Outer diameter | Inner diameter
7/8" | 22.2 mm | 20 mm | 8.7 mm | 7.4 mm
1 5/8" | 41.3 mm | 38.8 mm | 16.9 mm | 15.0 mm
3 1/8" | 79.4 mm | 76.9 mm | 33.4 mm | 31.3 mm
4 1/2" | 106 mm | 103 mm | 44.8 mm | 42.8 mm
6 1/8" | 155.6 mm | 151.9 mm | 66.0 mm | 64.0 mm
Coaxial cables are often with PTFE foam to keep concentricity
Flexible lines have spacer helicoidally placed all along the line
Rigid lines are made of two rigid tubes maintained concentric with supports

## Slide 55: Coaxial lines Maximum Power handling
Power handling of an air coaxial line is related to breakdown field E
With
E = breakdown strength of air (‘dry air’ E = 3 kV/mm, commonly used value is E = 1 kV/mm for ambient air)
D = inside electrical diameter of outer conductor in mm
d = outside electrical diameter of inner conductor in mm
Zc= characteristic impedance in Ω
εr = relative permittivity of dielectric
f = frequency in MHz
d
D

## Slide 56: Coaxial lines Attenuation
The attenuation of a coaxial line is expressed as
where
α = attenuation constant, dB/m
Zc= characteristic impedance in Ω
f = frequency in MHz
D = inside electrical diameter of outer conductor in mm
d = outside electrical diameter of inner conductor in mm
εr = relative permittivity of dielectric
tan δ = loss factor of dielectric
Material | εr | tan δ | Breakdown MV/m
Air | 1.00006 | 0 | 3
Alumina 99.5% | 9.5 | 0.00033 | 12
PTFE | 2.1 | 0.00028 | 100

## Slide 57: Reflection from Load
0 | when the line is perfectly matched, no reflection
 | when the line is perfectly matched, no reflection
-1 | when the line is short-circuited complete negative reflection
0 | when the line is perfectly matched, no reflection
1 | when the line is open-circuited complete positive reflection
 | when the line is short-circuited complete negative reflection
 | when the line is perfectly matched, no reflection
 | when the line is open-circuited complete positive reflection
DUT
(Device Under Test)
Zc
DUT
(Device Under Test)
Z Zc
Standing Wave Ration SWR is a measure of impedance matching of DUT
A wave is partly reflected when a transmission line is terminated with other than a pure resistance equal to its characteristic impedance
The reflection coefficient is defined by
Zc
Vf
Vr
Line = Zc

## Slide 58: Reflection from Load
At some points along the line the forward and reflected waves are exactly in phase
full reflection
At other points they are 180° out of phase
full reflection
The Voltage Standing Wave Ratio is equal to
DUT
(Device Under Test)
Full reflection
Zc
Vf
Vr
Line = Zc

## Slide 59: Reflection from Load
In case of full reflection Vmax = 2 Vf (Pmax equivalent to 4 Pf)
RF power amplifiers will not like this reflected wave
  Klystron output cavity disturbed
  Grid tube, IOT and Transistor voltage capability
Swift protection if Pr > Prmax
  system NOT operational (not always possible)
DUT
Pf
Pr
Swift protection if Pr

## Slide 60: Circulator
In order to protect our lines and our amplifiers from this reflected power: Circulator
  passive non-reciprocal three-port device
  signal entering any port is transmitted only to the next port in rotation
The best place to insert it is close to the reflection source
  Lines between circulator and DUT shall sustain 4 Pf if full reflection
  A load of Pf is needed on port 3 to absorb Pr
1
2
3
Full reflection
2 Vf
(4 Pf)
Vr
↓
Load
Vf →
← Vr
Vf →

## Slide 61: Circulator
Even in case of full reflection Vmax = 2 Vf (Pmax equivalent to 4 Pf)
  RF power amplifiers will not see reflected power and will not be affected
  Lines between circulator and DUT MUST at least be designed for 4 Pf
  Loads must be designed for Pf
System remains always operational at any time
DUT
Pf
4 Pf
Pf

## Slide 62: Fundamental Power Coupler FPC
The Fundamental Power Coupler is the connecting part between the RF transmission line and the RF cavity
It is a specific piece of transmission line that also has to provide the vacuum barrier for the beam vacuum
FPC are one of the most critical parts of the RF cavity system in an accelerator
A good RF design, a good mechanical design and a high quality fabrication are essential for an efficient and reliable operation
LHC FPC
SPL FPC
HL-LHC FPC
L4 FPC window
Various FPC at CERN

## Slide 63: Overall Efficiency = Electrical bill
Building HVAC (Heating, Ventilation, Air Conditioning)
RF power in
DC power in
Heat out
RF power out
AC/DC
AC power in
Amplifier Cooler
Building Cooler
DUT
(Device Under Test)
45 %

## Slide 64: Efficiency
Cavity = 1 MW
150 m coaxial line = + 0.2 dB = + 5 % = 1.050 MW
Circulator = + 0.2 dB = + 5 % = 1.103 MW
Hybrid combiner 16:1 = + 0.3 dB = + 7 % = 1.175 MW
DC to RF (efficiency ~ 60 %) = 1.960 MW
Air cooling station (10 % of 1’000 kW = 100 kW) ~ + 50 kW = 2.225 MW
Water cooling station (90 % of 1’000 kW = 900 kW) ~ + 45 kW = 2,270 MW
Electrical distribution (5 % of 2.270 MW) ~ + 50 kW = 2,4 MW taken from the grid
AC to DC (efficiency ~ 90 %) = 2.175 MW (1’000 kW to be dissipated)
Overall efficiency 41,9 %
Thales design report: ‘Le rendement des blocs RF avec les MRFE6VP61K25N est de l’ordre de 66 % (valeur conservative)’
This was before linearity and bandwidth adjustments, I reduced it to 60 % for this exercise

## Slide 65: Efficiency
Cavity = 1 MW
20 m coaxial line = + 5 % + 1 % = 1.010 MW
Circulator = + 0.2 dB = + 5 % = 1.060 MW
Hybrid combiner 16:1 = + 0.3 dB = + 7 % = 1.130 MW
DC to RF (efficiency ~ 60 %) = 1.890 MW
Air cooling station (10 % of 970 kW = 97 kW) ~ + 49 kW = 2,149 MW
Water cooling station (90 % of 970 kW = 873 kW) ~ + 44 kW = 2,190 MW
Electrical distribution (5 % of 2,190 MW) ~ + 99 kW = 2,3 MW taken from the grid
AC to DC (efficiency ~ 90 %) = 2,100 MW (970 kW to be dissipated)
Having the amplifiers very close to the cavity, will reduce all other losses
A gallery is very expensive, as an acquisition cost, but can help to reduce acquisition cost of transmission lines and to reduce cost of operation
150 m
20 m
LIU-SPS
HL-LHC
Overall efficiency 43,5 %
41,9 %

## Slide 66: Efficiency
41,9 %
Cavity = 1 MW
20 m coaxial line = + 1 % = 1.010 MW
NO Circulator = + 5 % + 0 % = 1.010 MW
Hybrid combiner 16:1 = + 0.3 dB = + 7 % = 1.080 MW
DC to RF (efficiency ~ 60 %) = 1.800 MW
Air cooling station (10 % of 920 kW = 92 kW) ~ + 46 kW = 2,046 MW
Water cooling station (90 % of 920 kW = 828 kW) ~ + 42 kW = 2,088 MW
Electrical distribution (5 % of 2,088 MW) ~ + 104 kW = 2,2 MW taken from the grid
AC to DC (efficiency ~ 90 %) = 2,000 MW (920 kW to be dissipated)
As said, we are now able to build Power Amplifiers without circulator (Tetrodes and IOT can also do it)
The ‘cost’ is a (very) good protection system on the LLRF side
Overall efficiency 45,5 %
41,9 %

## Slide 67: Efficiency
41,9 %
Cavity = 1 MW
20 m coaxial line = + 1 % = 1.010 MW
NO Circulator = 1.010 MW
VHPCC 16:1 = + 0.1 dB = + 7 % + 2,5 % = 1.035 MW
DC to RF (efficiency ~ 60 %) = 1.725 MW
Air cooling station (10 % of 882 kW ~ 88 kW) ~ + 44 kW = 1,964 MW
Water cooling station (90 % of 882 kW ~ 794 kW) ~ + 39 kW = 2,003 MW
Electrical distribution (5 % of 2,003 MW) ~ + 100 kW = 2,1 MW taken from the grid
AC to DC (efficiency ~ 90 %) = 1,920 MW (882 kW to be dissipated)
Using cavity combiners instead of 3 dB combiners will also reduce maintenance cost as no more power loads to maintain
Overall efficiency 47,6 %

## Slide 68: Efficiency
41,9 %
Cavity = 1 MW
20 m coaxial line = + 1 % = 1.010 MW
NO Circulator = 1.010 MW
VHPCC 16:1 = + 0.1 dB = + 2,5 % = 1.035 MW
DC to RF (efficiency ~ 60 % ~ 66 %) = 1.570 MW
Air cooling station (10 % of 615 kW ~ 62 kW) ~ + 31 kW = 1,681 MW
Water cooling station (90 % of 615 kW ~ 553 kW) ~ + 28 kW = 1,709 MW
El. distribution (5 % of 1,709 MW) ~ + 86 kW = 1,8 MW taken from the grid
AC to DC (efficiency ~ 90 % ~ 95 %) = 1,650 MW (615 kW to be dissipated)
Granularity of the SSPA solution also allows to switch ON the exact correct number of modules such that we operate as close as possible to the nominal point
Overall efficiency 55,5 %

## Slide 69: Efficiency
41,9 %
Cavity = 1 MW
20 m coaxial line = + 1 % = 1.010 MW
NO Circulator = 1.010 MW
VHPCC 16:1 = + 0.1 dB = + 2,5 % = 1.035 MW
DC to RF (efficiency ~ 66 %) = 1.590 MW
Air cooling station (10 % of 615 kW 590 kW ~ 60 kW) ~ + 27 kW = 1,652 MW
Water cooling station (90 % of 615 kW 590 kW ~ 530 kW) ~ + 24 kW = 1,676 MW
El. distribution (5 % of 1,709 MW 3 % 1,676 MW) ~ + 50 kW = 1,7 MW taken from the grid
AC to DC (efficiency ~ 95 %) = 1,625 MW (590 kW to be dissipated)
Taking advantage of the natural chimney effect of the tower, having a well defined water station (variable speed), and shortening the LV cables will help reducing the remaining losses
5 m from HV to LV
Overall efficiency 58,8 %

## Slide 70: Acquisition & operation costs
Technology * Including SSPA driver | Very rough estimates for a 100 kW CW 352 MHz RF system including RF power + Power Supplies + circulators + cooling + controls (lines not included) | Lifetime ** x 1000 hours | 20 years Maintenance Tubes, HVPS, workshop | 20 years Electrical bill 3000 hours / year 10 hours/day 6/7 days 50 weeks/year 0.15 € / kWh η = 45 % | Total 20 years
Tetrode | 500 k€ | 20 | 350 k€ | 200 k€ | 1050 k€
IOT | 600 k€ | 50 | 200 k€ | 200 k€ | 1000 k€
Klystron | 750 k€ | 100 | 100 k€ | 200 k€ | 1050 k€
SSPA | 850 k€ | 200 | 50 k€ | 200 k€ | 1100 k€
Circulator | 75 k€ | - | - |  | 75 k€
Lines | 1 k€/m | - | - |  | 1 k€/m
** Tubes need highly qualified HV specialists for maintenance
* Construction of the infrastructure not included
SSPA option requires more volume

## Slide 71: Conclusion
We plan to launch (or we even already launched) R&D on
  Combining systems, this will reduce foot print and increase power density; plenty of ideas, cavity combiners, waveguide progressive combiners, RF transmission combiners, Gysel combiners, multi layers waveguides combiners)
  Availability, including granularity, hot swappable modules, embedded spares
  Efficiency, next key parameter, must be grid AC to RF for fair comparison
  Low cost circulators, at small power level ~kW and high power level ~MW
  Cost optimization, asking the correct architecture
  Mass production optimization, asking for the correct parameters
  Close follow-up of new technologies available in large series production (SiC, GaN, 2D transistors…).

## Slide 72: RF powering
DUT
(Device Under Test)
This was a quick overview of the RF powering, for detailed explanations, please refer to specialized CAS on RF
  2010 (468 pages) https://cas.web.cern.ch/schools/ebeltoft-2010
  2000 (486 pages) CERN-2005-003
  1992 (596 pages) http://cds.cern.ch/record/211448/files/CERN-92-03-V-2.pdf

## Slide 73: References
Reference Data for Radio Engineers (ISBN 0-672-22753-3)
HÜTTE des ingenieurs taschenbuch (Berlin 1955 edition)
Taschenbuch der Hochfrequenz-technik (Berlin-Heidelberg-New York 1968 edition)
Online
Thales, e2v, CPI, L-3 communications, Toshiba
NXP, Freescale

## Slide 74
They did not know it was impossible, so they did it !
Mark Twain