## Slide 1: The n_TOF EAR1 beam line
S. Amaducci, M. Bacak, A. Casanovas, F. Garcia-Infantes, J. Lerendegui-Marco, A. Manna, E. Musacchio, N. Patronis, J. Pavon-Rodriguez, M. Sabate-Gilarte, E. M. Stamati, R. Zarrella
30.05.2022 – n_TOF Collaboration Meeting

## Slide 2: n_TOF @ CERN
Neutron Time Of Flight facility: n_TOF
Operation since 2001
CERN: European Organization
for Nuclear Research (Geneva, Switzerland)
2022:
37 institutes
131 researchers

## Slide 3: n_TOF overview
pulsed
0.8 Hz
20 GeV/c
11 ns RMS
850·1010 ppp
~ 300 n/p
< 2020: water cooled uncladded lead block
>2020: Nitrogen-gas cooled uncladded lead slabs
clean charged particles
Experimental ARea 2
@ 18.5 m
~106 cm-2pulse-1
E/E ~ 4·10-3 @ 1 eV
Experimental ARea 1
@ 185 m
~104 cm-2pulse-1
E/E ~ 5·10-4 @ 1 eV

## Slide 4: Facility upgrades – spallation target
150 mm
50 mm
Al-6082-T6 supporting structure
(anti-creep and N2 cooling channels)
N2 gas cooling to avoid Pb corrosion and contamination of the cooling circuit
See O. Aberle’s talk Phys. Rev. Accel. Beams 24, 093001 (2021)

## Slide 5: Facility upgrades – neutron line
Sweeping magnet from electro magnet to
Cobalt-Samarium permanent magnet
Carbon steel sheets, laser cut
Borated PE
Ø 20 mm
Ø 80 mm
Movement
Vacuum chambers
See O. Aberle‘s talk
2nd collimator
(reproducibility & faster)

## Slide 6: Flux setup
SiMon 6Li
PPACMon1 235U
MeGas 235U & 10B
PTB 235U
Neutrons
+ Gold foil activation
 | Reaction(s) | Mass (g/cm2) | Energy RoI (eV)
SiMon | 6Li(n,)3H | 600 (95% 6LiF) (± 20%) | 2510-3 – 106
PPACMon1 | 2x 235U(n,f) | 278.5 (± 1%) 298.4 (± 1%) | 2510-3 0.15106 – 109
MeGas | 10B(n,)7Li 235U(n,f) | 24.5 (80% 10B4C) (± 20%) 281.4 (± 1.1 g/cm2) | 2510-3 – 106 2510-3 0.15106 – 109
PTB | 10x 235U(n,f) | 10x 444.3 (± 2%) | 2510-3 0.15106 – 109
Gold | 2x 197Au(n,) | 50 m (upstream) 100 m (downstream) | 4.9

## Slide 7: Extracted preliminary flux
Gold foil activation analysis pending
Data: transmission correction pending
Good detector agreement
Simulations under investigation
simulation vs. data:
collimator alignment
Geometry / B content
 | SiMon | PPACMon1 | MeGas | PTB | Gold
PSA |  |  |  |  | n/a
Gain drifts |  | n/a |  |  | n/a
Pile-Up |  |  |  |  | n/a
Efficiency |  |  |  |  | 
High Energy | n/a |  |  |  | n/a
Transmission | n/a |  |  |  | 






## Slide 8: Resolution function – setup
4x C6D6 detectors

## Slide 9: Resolution function – measurements

## Slide 10: Resolution function – results
Analysis ongoing
  Gain calibrations done
  Flight path calibration ongoing
  Careful subtraction ongoing
  Preparation for SAMMY potentially before ND2022
First impression: comparable with previous target

## Slide 11: Profile – setup
Timepix Quad
  ~ 30x30 mm2 active area  not covering full beam
  Sensitive to neutrons (> 1 MeV) and gammas
  TOF integrated (time delay/gating possible)
  Excellent for alignment
PPACMon1:
  Covering full beam
  Sensitive to neutrons only
  TOF/En selective
  Detector rotated with respect to world-axes
X

## Slide 12: Profile – PPACMon1 235U (target2)
*I am a GIF

## Slide 13: Summary & outlook
Successful restart after long shutdown at CERN with
  New N2 gas-cooled spallation target
  New permanent sweeping magnet and 2nd collimator for the neutron beam line
(A lot of) Commissioning data under analysis by several groups:
  Neutron flux: 4 detectors & 6 samples (Q4/2022*) + evaluation
  Resolution function: 4 detectors & 5 samples + SAMMY (Q4/2022*)
  Profile: 1 detector (2 samples) (Q4/2022*)
  + simulations (Q4/2022*)
Final results in dedicated publication ~Q2/2023*
*estimated

## Slide 16: Profile – PPACMon1 235U (target2)

## Slide 17: Profile – PPACMon1 235U (target2)

## Slide 18: Profile – PPACMon1 235U (target2)

## Slide 19: Profile – Timepix results
~184 m
~188 m
Sensitive to neutrons and gammas
TOF integrated

## Slide 21: Flux analysis - corrections
 | SiMon | PPACMon1 | MeGas | PTB | Gold
PSA |  |  |  |  | n/a
Gain drifts |  | n/a |  |  | n/a
Pile-Up |  |  |  |  | n/a
Efficiency |  |  |  |  | 
High Energy | n/a |  |  |  | n/a
Transmission | n/a |  |  |  | 




