## Slide 1: Update on the NEAR neutron flux measurement with ANTILoPE
Pablo Pérez-Maroto, Carlos Guerrero and José M. Quesada
on behalf of Universidad de Sevilla, CIEMAT and the n_TOF Local Team.
The n_TOF Collaboration meeting. 30/05/2022
A NeuTron multi-foIL sPEctometer

## Slide 2: A neutron multi-foil spectrometer for NEAR
Pablo Pérez Maroto || nTOF Collaboration Meeting || 30/05/2022
Neutrons
Neutrons
Gold foils
Fast-neutron Pb converter

## Slide 3: ANTILoPE response matrix with Geant4
  ANTILoPE irradiated at n_TOF-NEAR in October 2021
  Gold sample’s activities measured with USevilla’s LaBr3 + CAEN digitizer
  Analyis ongoing with CERN’s RooUnfold
Pablo Pérez Maroto || nTOF Collaboration Meeting || 30/05/2022

## Slide 4: We have investigated the effect on the results of several issues/inputs/choices
  How critical is the dependence with
    Neutron scattering background
    New FLUKA simulations
    Number of iterations
    Number of foils
    Initial guess
    Binning
    Deconvolution code
Pablo Pérez Maroto || nTOF Collaboration Meeting || 30/05/2022

## Slide 5: We have investigated the effect on the results of several issues/inputs/choices
  How critical is the dependence with
    Neutron scattering background
    New FLUKA simulations
    Number of iterations
    Number of foils
    Initial guess
    Binning
    Deconvolution code
FLUKA simulations by J.A. Pavón & M. Sabaté
Pablo Pérez Maroto || nTOF Collaboration Meeting || 30/05/2022

## Slide 6: FLUKA simulations: J.A. Pavón & M. Sabaté
Pablo Pérez Maroto || nTOF Collaboration Meeting || 30/05/2022
NEAR real geom.
Vacuum
NEAR real geom.
Vacuum
NEAR real geom.
Vacuum
NEAR real geom.
Vacuum

## Slide 7
Pablo Pérez Maroto || nTOF Collaboration Meeting || 30/05/2022
Difference in Au activation by scattered neutrons
Ratio between 2.5 & 9

## Slide 8
Pablo Pérez Maroto || nTOF Collaboration Meeting || 30/05/2022
Difference in Au activation by scattered neutrons
Correction by the contribution of scattered neutrons
Ratio between 2.5 & 9
Ratio between 2 & 4.5

## Slide 9: We have investigated the effect on the results of several issues/inputs/choices
  How critical is the dependence with
    Neutron scattering background
    New FLUKA simulations
    Number of iterations
    Number of foils
    Initial guess
    Binning
    Deconvolution code
Nº of captures higher than expected
Pablo Pérez Maroto || nTOF Collaboration Meeting || 30/05/2022
Succesfully corrected

## Slide 10: Then: updated FLUKA simulations by M. Cecchetto
Pablo Pérez Maroto || nTOF Collaboration Meeting || 30/05/2022
New FLUKA simulations by M. Cecchetto available
With the updated expected flux together with the background correction the measured values match with the expected ones: better than 5% in the first 14 samples!
±5%

## Slide 11: We have investigated the effect on the results of several issues/inputs/choices
  How critical is the dependence with
    Neutron scattering background
    New FLUKA simulations
    Number of iterations
    Number of foils
    Initial guess
    Binning
    Deconvolution code
Effects in the unfolding
Pablo Pérez Maroto || nTOF Collaboration Meeting || 30/05/2022
Succesfully corrected
Succesfully corrected

## Slide 12: Effect of # iterations
Pablo Pérez Maroto || nTOF Collaboration Meeting || 30/05/2022
Stabilization of the eV-MeV range after 100 iterations
Large fluctuations in the above 1 MeV, optimum choice?

## Slide 13: We have investigated the effect on the results of several issues/inputs/choices
  How critical is the dependence with
    Neutron scattering background
    New FLUKA simulations
    Number of iterations
    Number of foils
    Initial guess
    Binning
    Deconvolution code
Effects in the unfolding
Pablo Pérez Maroto || nTOF Collaboration Meeting || 30/05/2022
Studied, not clear conclusions
Succesfully corrected
Succesfully corrected

## Slide 14: Effect of # foils
Pablo Pérez Maroto || nTOF Collaboration Meeting || 30/05/2022
Removal of up to 10 downtream foils affects only above 5 MeV, and very significantly above 20 MeV

## Slide 15: We have investigated the effect on the results of several issues/inputs/choices
  How critical is the dependence with
    Neutron scattering background
    New FLUKA simulations
    Number of iterations
    Number of foils
    Initial guess
    Binning
    Deconvolution code
Pablo Pérez Maroto || nTOF Collaboration Meeting || 30/05/2022
No effects in the unfolding
Stable results below ~5-10 MeV
Studied, not clear conclusions
Succesfully corrected
Succesfully corrected

## Slide 16: We have investigated the effect on the results of several issues/inputs/choices
  How critical is the dependence with
    Neutron scattering background
    New FLUKA simulations
    Number of iterations
    Number of foils
    Initial guess
    Binning
    Deconvolution code
Pablo Pérez Maroto || nTOF Collaboration Meeting || 30/05/2022
Ongoing
Does not affect the results
Stable results below ~5-10 MeV
Studied, not clear conclusions
Succesfully corrected
Succesfully corrected

## Slide 17: We have investigated the effect on the results of several issues/inputs/choices
  How critical is the dependence with
    Neutron scattering background
    New FLUKA simulations
    Number of iterations
    Number of foils
    Initial guess
    Binning
    Deconvolution code
Pablo Pérez Maroto || nTOF Collaboration Meeting || 30/05/2022
Succesfully corrected
Studied, not clear conclusions
Stable results below ~5-10 MeV
Does not affect the results
Ongoing
Others to be tested
Succesfully corrected

## Slide 18: NEAR flux with ANTILoPE
Pablo Pérez Maroto || nTOF Collaboration Meeting || 30/05/2022

## Slide 19: CEIDEN Grupo de Usuarios Neutrónicos meeting @CNA, 8-9 June 2022
Pablo Pérez Maroto || nTOF Collaboration Meeting || 30/05/2022
  The meeting will connect basic nuclear physics groups with others working on neutron dosimetry, medical physics, engineering and other applications.
  Several groups use deconvolution codes for dosimetry and use Bonner Spheres, we hope to share our experience and doubts to get some defintive answer to (some of) the open questions just discussed.

## Slide 20: Simplified design test at HiSPANoS@CNA
  Changes in the set-up
  No need for the Pb converter
  Removal of the first 2 foils and the last 8
  Test of target material: the strong 5 eV 197Au resonance may make gold a not optimal choice => test of Cu for producing 64Cu(b+; 12,7h)
  Goals:
  Irradiate with epithermal (1-100 keV) and mono-energetic fast (4,6 MeV) fluxes to test the sensibility of ANTILoPE.
  Irradiation at HiSPANoS last week: results soon!
Pablo Pérez Maroto || nTOF Collaboration Meeting || 30/05/2022
20 um Au foils
1 mm Cu foils

## Slide 21: Simplified design test at HiSPANoS@CNA
  Changes in the set-up
  No need for the Pb converter
  Removal of the first 2 foils and the last 8
  Test of target material: the strong 5 eV 197Au resonance may make gold a not optimal choice => test of Cu for producing 64Cu(b+; 12,7h)
  Goals:
  Irradiate with epithermal (1-100 keV) and mono-energetic fast (4,6 MeV) fluxes to test the sensibility of ANTILoPE.
  Irradiation at HiSPANoS last week: results soon!
Pablo Pérez Maroto || nTOF Collaboration Meeting || 30/05/2022

## Slide 22
Summary & Conclusions
ANTILoPE: designed in 2021 for measuring the neutron flux at NEAR
Measurements were succesfully perfomed at both NEAR and EAR-2 in 2021
New FLUKA simulations of NEAR flux => estim./meas. # captures agree within ±5%
Effect of the scattered neutrons with FLUKA => affects the En>10 MeV mainly
Effect of the choice of # iterations and # foils: reasonable results
Study of binning dependence: ongoing
Test others unfolding codes pending: coming soon
Meanwhile, simplified design and irradiation at HiSPANoS@CNA
  Epithermal neutrons (1912 keV proton on LiF target): quasimaxwellian of ~ 30 keV
  Mono-energetic fast neutrons (d-D producing 4,6 MeV neutrons)
  Analysis ongoing
RooUnfold is a “black box” for us. Looking forward to CEIDEN-GUN meeting in June to improve our understanding
Pablo Pérez Maroto || nTOF Collaboration Meeting || 30/05/2022

## Slide 23: Thank you!
Pablo Pérez Maroto || nTOF Collaboration Meeting || 30/05/2022

## Slide 24: Sensitivity according to the position inside the block
Simulated with Geant4 & G4NeutronHPThermal physics
The first two samples respond mainly to the 5 eV resonance
No peaks in the keV region, but the response is different enough for unfolding
Well defined response peaks around the MeV region
Pablo Pérez Maroto || nTOF Collaboration Meeting || 30/05/2022
Notes: We simulate the activation with the equation seen earlier, and we can see very well the different response of the foils
What we see in the keV region is the same that happens with Bonner Sphere
Simulations benchmarked with MCNP

## Slide 25: Sensitivity according to the position inside the block
Some limitations around the 100 MeV region
Thanks to the Pb we improve a lot the last bins
Pablo Pérez Maroto || nTOF Collaboration Meeting || 30/05/2022

## Slide 26: Irradiation at NEAR during 12 days (20/10 -> 01/11)
Pablo Pérez Maroto || nTOF Collaboration Meeting || 30/05/2022

## Slide 27: Measurement of the decay of the samples
During 9 days, in the “old Control Room”
Almost one sample per day, every day
Two LaBr3 detectors and one CAEN-720 digitizer (from Universidad de Sevilla)
Pablo Pérez Maroto || nTOF Collaboration Meeting || 30/05/2022

## Slide 28: Unfolding with and without Pb
Pablo Pérez Maroto || nTOF Collaboration Meeting || 30/05/2022