## Slide 1: STEAM framework for simulations of transients in superconducting magnet circuits
Emmanuele Ravaioli and Mariusz Wozniak
on behalf of the STEAM team:
Lennard Bender, Bernardo Bordini, Marvin Janitschke, Tim Mulder, Emmanuele Ravaioli,
Erik Schnaubelt, Arjan Verweij, Andrea Vitrano, Mariusz Wozniak
with thanks to all the past STEAM members
TE-MPE-PE section meeting 08 June 2022
https://espace.cern.ch/steam

## Slide 2: STEAM
Vision
Achieve specialized, trusted, consistent, repeatable and sustainable software tools and models for rapid Simulation of Transient Effects in Accelerator superconducting Magnet circuits.
Mission
Develop capability and know-how for simulation with an appropriate utilization of established and modern technology. Engage community in framework adaptation and validation by sharing well documented tools and models. Support tools that are part of STEAM and welcome integration with externally developed code.
Values
continuity, readiness, simplicity, recognition, completeness, maintainability

## Slide 3: STEAM Simulation of Transient Effects in Accelerator Magnets
LHC
Challenges / Opportunities:
Multi-domain – need to include thermal, magnetic and electrical domains
Multi-physics – need to couple above domains and between models
Multi-rate – need to include fast effects in long time scale models
Multi-scale – need to account for local effects in large models
STEAM is used daily for several flagship projects at CERN:

## Slide 4
Note: All figures are only meant to give a rough estimation
STEAM project in the last few years and future trends
STEAM
30%
LHC
50%
HL-LHC
5%
HFM
15%
Other
10%
Physics
10%
Matlab
5%
Java
35%
Python
60%
Applications
Develop circuit or magnet models, validate them, perform simulations,…
40%
Development
Develop new program features, code maintenance, enhance automation…
5%
COMSOL
35%
Gmsh
GetDP

## Slide 5
STEAM users
→ We support users in various labs and universities across the world [most revolve around HL-LHC projects]
→ However, most STEAM models/applications are CERN-based as the main driver is CERN circuit simulations

## Slide 6
2nd STEAM workshop [October 2021, indico]
UPDATES ON STEAM DEVELOPMENT
PRESENTATIONS FROM STEAM USERS
HANDS-ON SESSIONS ON ALL THE TOOLS
Figures from the presentations at the workshop by D. Davis, D. Delkov, V. Ferrentino,
M. Janitschke, V. Marinozzi, M. Mentink, X. Sarasola, O. Tranum Arnegaard, M. Wozniak

## Slide 7
DIFFERENT TRANSIENTS
Energy extraction and quench-back
Quench heater induced quench
CLIQ induced quench
Powering
Electrical arc
Frequency transfer measurement
No-Insulation coils
DIFFERENT MAGNET TYPES
Cos-theta
Block-coil
Common coil
Canted Cos-Theta (CCT)
Solenoid, pancake coils
DIFFERENT CONDUCTOR TYPES
Nb-Ti
Nb3Sn
Bi-2212
YBCO
DIFFERENT CIRCUIT TYPES
Stand-alone magnets
Nested circuits
Series-connected magnets
…many combinations of those
DIFFERENT LEVEL OF DETAIL
Circuit → Magnet → Cable → Wire → Filament
→ We develop, validate, and use different simulation tools for solving different problems
Scope of STEAM framework

## Slide 8: Which physics is included in the STEAM models – and which isn’t
Main takeaways: 1. Transients in superconducting circuits are complex. 2. We try to include as much relevant physics as it is practical in each tool, but each includes simplifications. 3. Nope, we can’t simulate everything :-/
ELECTRICAL CIRCUITS
Electrodynamics
Non-linear components (Diodes, thyristors)
Empirical model of magnet eddy-currents
Parasitic capacitance to ground
Cold Diode heating effect
Busbar self-inductance
Power converter control
Dependence of inductance on current
Heating effect in EE resistor
Mutual coupling between busbars of different circuits
…
MAGNETS
Non-linear material properties
Quench development and ohmic loss
1D, 2D and 3D thermal diffusion
Inter-filament coupling loss
Inter-strand coupling loss
Iron-yoke saturation effect on self-inductance
Cooling to thermal sink (collars, bore, wedges)
Persistent-currents loss
Eddy currents in metal elements
Accurate helium cooling
3D magnetic field
Hysteresis in iron yoke
Mechanics
…

## Slide 9
STEAM tools - 2021
BBQ
SIGMA
LEDET
PROTECCT
SING
COSIM
Conductor
Magnet
Circuit

## Slide 10
STEAM tools - 2022
BBQ(Comsol)  PyBBQ BBQ(GetDP)
SIGMA
LEDET
PROTECCT
SING  PySING
COSIM
FiQuS
Conductor
Magnet
Circuit

## Slide 11
BBQ (BusBar Quench)
vQ
Temperature [K]
x [m]
Temperature-development along
length of conductor
→ To simulate 1D+1D quench propagation in superconducting busbars
→ New development: PyBBQ (Python program, finite difference solver)
→ Future development: BBQ based on GetDP
Comsol (FE) based BBQ tool drawbacks (mainly commercial licence and lack of input file) are being addressed.
Finite difference BBQ coded in python (PyBBQ) is being developed
Finite difference LEDET can be used for BBQ simulation
Finite element tool based on GetDP is planned to be developed

## Slide 12
SIGMA (STEAM Integrated Generator of Magnets for Accelerators)
→ To simulate electro-magnetic and thermal transients in superconducting magnets in a 2D geometry using a finite-elements (FE) model

## Slide 13
LEDET (Lumped-Element Dynamic Electro-Thermal)
→ To simulate electro-magnetic and thermal transients in superconducting magnets in 2D and 3D geometry using finite-differences method

## Slide 14
ProteCCT (Protection of Canted-Cosine-Theta) type magnets
→ To simulate electro-magnetic and thermal transients in canted-cosine-theta (CCT) using finite-differences method

## Slide 15
SING (STEAM Integrated Network Generator)
Circuit.cir file
Generalized
notebook code
Circuit schematic
→ To automatically generate PSPICE and LTSPICE circuit models relying on shared sub-components
→ In 2022 it was completely re-written in Python (ParserPSPICE):
+ less Java code to maintain
+ inputs are yaml based (as the rest of the framework)
+ automatic writing of yaml circuit file from existing .cir netlist file

## Slide 16
COSIM (Co-operative Simulation)
Waveform relaxation (Gauss-Seidel Method) coupling :
Field
→ To run co-operative simulations of models developed in different programs (and possibly by different people)

## Slide 17: Finite Elements Quench Simulator (FiQuS)
2D Example for quadrupole MQXA
3D Example of a CCT magnet
3D Example of a NI HTS coil
B and M calculation for LEDET
Stand-alone quench simulations
Thermal transient and steady state sim.
HTS coils ramp up and down simulations
HTS coils quench simulations
Coils with insulation, no-insulation, partial- insulation.
B and M calculation for LEDET
Eddy currents in the formers
Temperature of the formers
No plans for a stand alone quench simulation
Induced currents in all metal parts.
Joule heating due to induced currents.
IFCC and ISCC to be introduced.
<- 2D coupled Th-EM for E-CLIQ
GMSH for E-CLIQ
Gmsh used to create 3d models of small demonstrator formers that can be 3d printed.
GetDP
Gmsh

## Slide 18
Library of Material Properties
STEAM website: https://espace.cern.ch/steam/_layouts/15/start.aspx#/SitePages/Material%20Properties.aspx
https://gitlab.cern.ch/steam/steam-material-library
https://gitlab.cern.ch/steam/steam-ledet-material-library
→ We share our material property database with users to support a community of users across different labs/universities and to help model cross-checking
Work has been done to allow to use the same material properties (coded in C) across tools written in Python, MATLAB and FE solvers (Comsol, GetDP i.e. FiQuS).
MEX
DLL
C++
C
GetDP

## Slide 19
STEAM model library: how the models are generated and versioned
Software | 2021 | 2022
BBQ | Manual in COMSOL | Manual in COMSOL
PyBBQ | - | Yaml + Python API
FiQuS | - | Yaml + Python API
SIGMA | Notebook + Java .jar | Notebook + Java .jar
LEDET | Notebook + Python API | Yaml + Python API
ProteCCT | Manual in Excel | Yaml + Python API
SING | Notebook + Java .jar | Yaml + Python API
COSIM | Notebook + Java .jar + Python API | Yaml + Python API (foreseen for the end of 2022)

## Slide 20
STEAM model library: Input files [items in red: TO DO]
Conductor file
PyBBQ
LEDET
BBQ [GetDP]
Magnet file
LEDET
ProteCCT
SIGMA
FiQuS
Circuit file
PSPICE
Co-simulation file
COSIM

## Slide 21: Why STEAM could be useful to YOU
We can offer help to
Obtain reference cases for transients in LHC and HL-LHC circuits (quenches, ELQA high-voltage tests, power-converter switching-off, energy-extraction switch opening, transfer function measurements,…)
Understand the behaviour of non-trivial circuits (magnet chains, parallel paths, nested magnets, etc)
Assess the impact of proposed changes to circuit hardware or operation modes
Study failure scenarios
Identify worst-case scenarios for circuit components
Attempt to reproduce unexpected events or observations
Develop simulations for R&D quench detection and protection techniques
Provide boundary conditions for analyses of other systems
Obtain material properties in various forms

## Slide 22: Examples of what STEAM models were used for in 2021
LHC
Frequency
domain
Quench
Heaters
Short
circuits
SC effects
Simulate an internal short-circuit in an MB magnet (in RB, main dipole circuit)
Analyse earth current in RB circuits during quenches and FPA
Simulate powering transients of an MCBY magnet with an internal short-circuit
Assess the consequences of raising MB quench detection thresholds (worst-case analysis)
Analyse quench protection of Q1 magnet in RQX.R1 with non-conform quench heater discharge unit
Calculate the effect of quench-heater field on the beam, including the effects of beam-screen shielding and inter-filament coupling currents in the magnet coil
Simulate quench-heater protection of MQY magnet at T=1.9 K
Reproduce the measured frequency-domain impedance of MB magnets measured in the tunnel, including the effect of neighbouring magnets
Assess when quench-back is expected in 600 A circuits
Simulate the effects of persistent-currents on the powering transients in LHC circuits

## Slide 23: Examples of what STEAM models were used for in 2021
HL-LHC
Frequency
domain
Baseline verification
Validation and Predictions
Systematic measurement/simulation comparison during events in various test campaigns SM18
Simulation of transients in CCT-type magnet, and validation with MCBRD prototype magnet data
Simulate proposed MQXF special trimmed powering tests
Explain the observed extra ohmic loss in coils made of conductor with non-uniform RRR
Estimate the effect of QH discharge on voltages across coils and quench-antenna coils
Verification of baseline quench protection for various HL-LHC circuits
Parametric analyses and worst-cases for all circuit components in HL-LHC Inner Triplet circuit
Analyse quench protection of HEL larger solenoids
Uncertainty quantification by automatically performing hundreds of parametric simulations
Simulate of the effects of additional insulation layers between quench heaters and coil
Propose MQXF coil electrical order that minimizes the expected peak voltage to ground
Frequency transfer function analysis of one MQXF coil

## Slide 24: Some highlights from 2022

## Slide 25: Some topics worked on in 2022
M. Wozniak, E. Ravaioli, A. Verweij, "Co-Simulation of Quench Behaviour of HL-LHC Dipole Canted Cos-Theta Orbit Corrector Prototypes"
A. Vitrano, M. Wozniak, E. Schnaubelt, T. Mulder, E. Ravaioli, A. Verweij, "An open-source finite element quench simulation tool for superconducting magnets"
T. Mulder, E. Schnaubelt, M. Wozniak, E. Ravaioli and A. Verweij, "External Coil Coupled Loss Induced Quench (E-CLIQ) System for Protection of LTS Magnets"
E. Ravaioli, A. Verweij, M. Wozniak, "Analysis of an internal electrical short in an LHC orbit-corrector magnet with a 3D multiphysics simulation"
E. Schnaubelt, M. Wozniak, S. Schöps, "Quench Simulation of No-Insulation HTS Coils With 3D FEM Using a Thin Shell Approximation"
B. Caiffi, L. Bender, A. Bersani, S. Farinon, A. Foussat, F. Levi, F. Mangiarotti, D.Novelli, A. Pampaloni, E. Ravaioli, E. Todesco, G. Willering, "Protection Scheme Effectiveness Study for the Hi Luminosity LHC MBRD magnet"
S. Yammine,..., E. Ravaioli,..., et al., "Experimental Program of the HL-LHC Inner Triplet String Test at CERN"
… as a list of abstracts accepted for ASC2022
CCT
HTS
Fusillo
E-CLIQ
LHC

## Slide 26: Main takeaways – What is the STEAM team doing?
We develop and use STEAM software tools to simulate transients in superconducting magnets and circuits
We maintain and provide a set of tools that have different strengths and limitations
We continuously improve our tools to address the expanding needs of the superconducting community
We ensure that STEAM can be used every day for several CERN flagship projects (LHC, HL-LHC, FCC)
We offer the simulation tools and material library in order to build a community [aka gather up superconductivity geeks] and to facilitate model cross-checking
We aim at making the model generation and running processes as easy and intuitive as possible so that newcomers and external users can learn quickly
We try to include as much relevant physics as it is practical... but nope, we can’t simulate everything :-/
We can offer help in simulating powering transients, quenches, ELQA high-voltage tests, power-converter switching-off, energy-extraction switch opening, transfer function measurements, R&D quench protection systems… and we like exotic transients
Don’t hesitate to contact the STEAM team: the first coffee is on us! → steam-team@cern.ch

## Slide 27
The future of STEAM
The following slides are copied from 2021 STEAM Workshop
We’ll go through them now and discuss the 2022 progress

## Slide 28: What this session is about?
We would like this session to be very interactive
Please let us know your thoughts on each topic that we present
For each slide we would like to know:
What are your thoughts?
Would you use this feature / benefit from development?
Could we do it a different way?
Do you have experience in this topic you could share?
Do you know a colleague who would be interested or could help?
Thoughts?
Benefits for you?
Different way?
Your experience?
Contact person?
These are abbreviated on each slide as a reminder

## Slide 29: STEAM strategic priorities
reinforcing
upgrading
evolving
short term
mid-term
mid-term and beyond
Mission
Develop capability and know-how for simulation with an appropriate utilization of established and modern technology. Engage community in framework adaptation and validation by sharing well documented tools and models. Support tools that are part of STEAM and welcome integration with externally developed code.
Values
continuity, readiness, simplicity, recognition, completeness, maintainability
Vision
Achieve specialized, trusted, consistent, repeatable and sustainable software tools and models for rapid Simulation of Transient Events in Accelerator superconducting Magnet circuits.

## Slide 30: STEAM strategic priorities
reinforcing
Broaden capability to simulate all LHC and HL-LHC superconducting magnet circuits
Increase reliance on the same input files
for generating models across the STEAM framework
Continue to maintain and version control our models
Improve capability for scripted model validation
Increase number of codes covered with software testing
Keep simulation tools and circuit/magnet models ready to analyze transients occurring in LHC/HL-LHC
short term
Thoughts?
Benefits for you?
Different way?
Your experience?
Contact person?

## Slide 31: STEAM strategic priorities
reinforcing
short term
Broaden capability to simulate all LHC and HL-LHC superconducting magnet circuits
Increase reliance on the same input files for generating models in across the STEAM framework
Continue to maintain and version control our models
Improve capability for scripted model validation
Increase number of codes covered with software testing
Keep simulation tools and circuit/magnet models ready to analyze transients occurring in LHC/HL-LHC
LHC
Thoughts?
Benefits for you?
Different way?
Your experience?
Contact person?

## Slide 32: STEAM strategic priorities
reinforcing
short term
Broaden capability to simulate all LHC and HL-LHC superconducting magnet circuits
Increase reliance on the same input files for generating models in across the STEAM framework
Continue to maintain and version control our models
Improve capability for scripted model validation
Increase number of codes covered with software testing
Keep simulation tools and circuit/magnet models ready to analyze transients occurring in LHC/HL-LHC
Thoughts?
Benefits for you?
Different way?
Your experience?
Contact person?

## Slide 33: STEAM strategic priorities
reinforcing
short term
Broaden capability to simulate all LHC and HL-LHC superconducting magnet circuits
Increase reliance on the same input files for generating models in across the STEAM framework
Continue to maintain and version control our models
Improve capability for scripted model validation
Increase number of codes covered with software testing
Keep simulation tools and circuit/magnet models ready to analyze transients occurring in LHC/HL-LHC
Thoughts?
Benefits for you?
Different way?
Your experience?
Contact person?

## Slide 34: STEAM strategic priorities
reinforcing
short term
Broaden capability to simulate all LHC and HL-LHC superconducting magnet circuits
Increase reliance on the same input files for generating models in across the STEAM framework
Continue to maintain and version control our models
Improve capability for scripted model validation
Increase number of codes covered with software testing
Keep simulation tools and circuit/magnet models ready to analyze transients occurring in LHC/HL-LHC
Thoughts?
Benefits for you?
Different way?
Your experience?
Contact person?

## Slide 35: STEAM strategic priorities
Keep simulation tools and circuit/magnet models
ready to analyze transients occurring in LHC/HL-LHC
reinforcing
short term
Broaden capability to simulate all LHC and HL-LHC superconducting magnet circuits
Increase reliance on the same input files for generating models in across the STEAM framework
Continue to maintain and version control our models
Improve capability for scripted model validation
Increase number of codes covered with software testing
Thoughts?
Benefits for you?
Different way?
Your experience?
Contact person?

## Slide 36: STEAM strategic priorities
upgrading
mid-term
Review and improve High Performance Computing* capabilities
Decrease dependency on commercial software
Improve scripting capabilities for model building, solving and postprocessing
Improve capabilities and provide examples for interfacing with advanced parametric analyses **
*Both shared and distributed memory clusters, with focus on machines available at CERN
Further streamline validation of models with measurements
** and design exploration, model calibration, risk analysis, and uncertainty quantification
Thoughts?
Benefits for you?
Different way?
Your experience?
Contact person?

## Slide 37: STEAM strategic priorities
upgrading
mid-term
Review and improve HPC* (High Performance Computing) capabilities
Decrease dependency on commercial software
Improve scripting capabilities for model building, solving and postprocessing
Improve capabilities and provide examples for interfacing with advanced parametric analyses **
*Both shared and distributed memory clusters
Further streamline validation of models with measurements
** and design exploration, model calibration, risk analysis, and uncertainty quantification
ONELAB, GetDP, Gmsh
What are your thoughts on GetDP replacing Comsol ?
What do you think of free FE solvers ?
Would you recommend other FE tools ?
Thoughts?
Benefits for you?
Different way?
Your experience?
Contact person?

## Slide 38: STEAM strategic priorities
upgrading
mid-term
Review and improve HPC* (High Performance Computing) capabilities
Decrease dependency on commercial software
Improve scripting capabilities for model building, solving and postprocessing
Improve capabilities and provide examples for interfacing with advanced parametric analyses **
*Both shared and distributed memory clusters
Further streamline validation of models with measurements
** and design exploration, model calibration, risk analysis, and uncertainty quantification
TDMS
Thoughts?
Benefits for you?
Different way?
Your experience?
Contact person?

## Slide 39: STEAM strategic priorities
upgrading
mid-term
Review and improve HPC* (High Performance Computing) capabilities
Decrease dependency on commercial software
Improve scripting capabilities for model building, solving and postprocessing
Improve capabilities and provide examples for interfacing with advanced parametric analyses **
*Both shared and distributed memory clusters
Further streamline validation of models with measurements
** and design exploration, model calibration, risk analysis, and uncertainty quantification
Thoughts?
Benefits for you?
Different way?
Your experience?
Contact person?

## Slide 40: STEAM strategic priorities
upgrading
mid-term
Review and improve HPC* (High Performance Computing) capabilities
Decrease dependency on commercial software
Improve scripting capabilities for model building, solving and postprocessing
Improve capabilities and provide examples
for interfacing with advanced parametric analyses **
*Both shared and distributed memory clusters
Further streamline validation of models with measurements
** and design exploration, model calibration, risk analysis, and uncertainty quantification
Thoughts?
Benefits for you?
Different way?
Your experience?
Contact person?

## Slide 41: STEAM strategic priorities
evolving
mid-term and beyond
For the above, include all physics relevant for quench protection and powering transients
Adapt tools to the needs of new magnets,
in particular High Field Magnet (HFM) programme at CERN
Review and consider improving capabilities to interface with structural analysis software, with a consideration of quench in magnets with brittle superconductors
Thoughts?
Benefits for you?
Different way?
Your experience?
Contact person?

## Slide 42: STEAM strategic priorities
evolving
mid-term and beyond
Adapt tools to the needs of new magnets,
in particular HFM (High Field Magnet) programme at CERN
For the above, include all physics relevant
for quench protection and powering transients
Review and consider improving capabilities to interface with structural analysis software, with a consideration of quench in magnets with brittle superconductors
Thoughts?
Benefits for you?
Different way?
Your experience?
Contact person?

## Slide 43: STEAM strategic priorities
evolving
mid-term and beyond
For the above, include all physics relevant for quench protection and powering transients
Review* and consider improving capabilities to interface
with structural analysis software, with a consideration of quench
in magnets with brittle superconductors
Adapt tools to the needs of new magnets,
in particular HFM (High Field Magnet) programme at CERN
* Some previous work: https://indico.cern.ch/event/712782/contributions/2928119/attachments/1616581/2569496/MechanicalStressDuringQuench.pdf
Thoughts?
Benefits for you?
Different way?
Your experience?
Contact person?
or free FE tool

## Slide 44: Discussion time !!!
What are we missing in our strategic priorities?
Features, tools (inc. FE), magnets, languages, materials?
What stops you from using STEAM tools?
Are any long-term topics more urgent than we think?
Anything else related to STEAM we should know?

## Slide 45: Annex

## Slide 46: STEAM Circuit Library structure
INPUT: Circuit + Magnet info
LHC Design Report
LHC magnet diagrams
ROXIE magnetic models*
Experimentally deduced values of unknown parameters
OUTPUT: STEAM models
*We don’t develop ROXIE models, we only use them. ROXIE LHC magnet repository:
https://roxie-lhc-magnets.web.cern.ch/roxie-LHC-magnets/
PSPICE electrical models of circuits in the time domain
STEAM-LEDET electro-magnetic and thermal models of magnets
STEAM-SIGMA FEM magnet models
PSPICE magnet/circuit models in the frequency domain
STEAM-COSIM models [coupled PSPICE circuit model + LEDET magnet model]
Model validation with existing experimental data plus additional ad-hoc experiments
Python-based SWAN notebooks
Python steam-nb-api
PSPICE electrical element library

## Slide 47: Superconducting Accelerator Circuits – Numerical Challenges
PI
Iref
-
+
Network model of a circuit
Differential-algebraic equations
Varying time constants ~1 ms (switch) - ~10 min (circuit discharge)
Varying geometric scales ~10 cm (diode) - ~10 km (circuit)
~10 k elements
Non-linear behaviour
Field/network model of a magnet
Controller Model
Differential-algebraic equations
Fixed frequency of operation
10-100 elements
Non-linear behaviour
Partial differential equations
Varying time constants ~10us (quench) - ~10ms (losses)
Varying geometric scales ~10 um (filaments) - ~10 m (magnet)
~10 k degrees of freedom
Highly non-linear material properties and equations
R
U
A
M2
M154
Multi-Domain, Multi-Physics, Multi-Rate and Multi-Scale Simulation
Busbar Model
Partial differential equations
Varying time constants
Adaptive mesh refinement
~1k elements
Non-linear behaviour

## Slide 48: STEAM tools application (over) simplification
Supercon busbar quench simulation:
Supercon magnet / circuit quench simulation:
  Unless, it is a CCT magnet, in that case:
  If it is a more complex circuit, benefit from above and / or:
  If any of above need to be used in ‘one’ simulation, use:
  In most cases, it is best to start with:
  And most tools have behind exact (or equivalent) :
LEDET
SIGMA
BBQ
ProteCCT
COSIM
SING and PSPICE
Jupyter notebooks
Material properties
BBQ
ProteCCT
COSIM
SING and PSPICE
Jupyter notebooks
Material properties
LEDET
SIGMA
and / or
STEAM has more tools, but only ones covered in the hands-on sessions are shown

## Slide 49: STEAM tools, solvers, languages, input files
Package | Recommended model generation/editing | Software needed for input generation/editing | Physics engine / logic | Files and software needed for final solve
BBQ | Manual edit of Comsol model | - Comsol Multiphysics | Provided in Comsol model | - Comsol model - Material properties - COMSOL Multiphysics
COSIM | Jupyter notebook with Java and Python API | - Jupyter kernel - Python - Java Runtime Environment | Coded in compiled COSIM.exe file | - COSIM.exe - json files - Models to couple - Java Runtime Environnent
LEDET | - Jupyter notebook with Python API - Roxie or PySoleno or Comsol model for field map and inductance matrix calc. | - Jupyter kernel - Python - Excel - ROXIE/PySoleno*/COMSOL | Coded in compiled LEDET.exe file | - Excel file - LEDET.exe - Field map files - MATLAB Runtime
ProteCCT | - Manual edit of Excel file - Comsol model for field and ind. calc. | - Excel - Comsol Multiphysics | Coded in compiled ProteCCT.exe file | - Excel file - ProteCCT.exe - MATLAB Runtime
SIGMA | Jupyter notebook with Java and Python API | - Jupyter kernel - Python - Java Runtime Environment | Generated and saved in Comsol model by SIGMA.jar | - Comsol model - Material properties - COMSOL Multiphysics
SING and PSPICE | Jupyter notebook with Java API | - Jupyter kernel - Java Runtime Environment | PSPICE circuit solver | - Circuit definition netlist - STEAM PSPICE component library (.cir, .stl) - Cadence Pspice
 |  | License fee for file / software: | License fee for file / software | Paid Free Free at CERN, Paid outside
* https://gitlab.com/mawoznia/PySoleno
STEAM has more tools, but only ones covered in the hands-on sessions are shown

## Slide 50: STEAM tools, solvers, languages, input files
LEDET
SIGMA
BBQ
text files
Excel files
ProteCCT
COSIM
SING and PSPICE
Jupyter notebooks
STEAM has more tools, but only ones covered in the hands-on sessions are shown
Material properties
Use COMSOL solver
Use MATLAB solver
Use EXCEL input files
Are written in JAVA
Use PSPICE solver
Use text input files
Inputs files can be generated by Jupyter notebooks
Could be (are) used in co-simulation
Use material properties
Inputs in the model

## Slide 51
STEAM components
In-house model development: We develop circuit and magnet models that include physical phenomena and assumptions tailored to our applications
In-house physics solver: For finite-difference models, we write the code to solve the physical problem in-house
In-house numerical solver: We rely on available low-level solvers: PSPICE for circuits, COMSOL for finite-element models, Matlab for finite-difference models.
Automated model generation: Models can be generated automatically using Java or Python API’s
Versioned library of models: Models are routinely versioned on Gitlab
Library of sub-components: We share circuit sub-components and material properties to facilitate model cross-checking
TASKS | CIRCUIT MODELS | FINITE-ELEMENT MAGNET MODELS | FINITE-DIFFERENCE MAGNET MODELS | FREQUENCY-DOMAIN MODELS
In-house model development | + | + | + | +
In-house physics solver |  |  | + | 
In-house numerical solver |  |  |  | 
Automated model generation | + | + | + | +
Versioned library of models | + | + | + | +
Library of sub-components | + | + | + | +

## Slide 52: BBQ (BusBar Quench)
FEM-based Comsol simulation model for superconducting busbars.
Calculations of:
  Quench propagation velocity
  Development of voltage after quench origination for quench detection calc.
  Hotspot temperature as a function of quench integral (adiabatic and with heat exchange)
Ability to simulate circuits with known discharge characteristics (time constant)
Compatible with STEAM co-simulation framework
More:
STEAM website: https://espace.cern.ch/steam/_layouts/15/start.aspx#/SitePages/BBQ.aspx
1st STEAM workshop (2019): https://indico.cern.ch/event/808547/timetable/

## Slide 53: LEDET (Lumped-Element Dynamic Electro-Thermal)
2D, 2D+1D, 3D magnet model + simplified circuit
Field maps and inductance dependence on iron yoke saturation calculated externally (ROXIE, COMSOL, PySoleno)
Inter-filament and inter-strand coupling currents
Turn-to-turn heat exchange, simplified helium cooling
Energy-extraction, quench heaters, CLIQ transients
Can be used in co-simulation, benefiting from COSIM
Computationally efficient, stand-alone exe, so LEDET is fast!
Some new features, as covered in Emmanuele’s talk
Currently LEDET is a workhorse of our quench simulations
Tool to simulate electro-magnetic and thermal transients in superconducting magnets
More:
STEAM website: https://espace.cern.ch/steam/_layouts/15/start.aspx#/SitePages/BBQ.aspx
1st STEAM workshop (2019): https://indico.cern.ch/event/808547/timetable/

## Slide 54: SIGMA (STEAM Integrated Generator of Magnets for Accelerators)
Automatic COMSOL model generation via Jupyter notebook
COMSOL models generated with SIGMA implement strongly coupled magnetoquasistatic, thermal and network equations
These equations (physics engine) are visible and editable in the model and could be expanded to suit user needs (double-edged sword)
Models provide an interface for co-simulation in a current- and voltage-driven modes, benefiting from COSIM
The iron yoke and copper wedges could be easily included
This is fully fledged FE model, expansion and addition of physics and features is virtually limitless (within COMSOL capabilities)
Material properties library files can be changed in the model, it is possible to use your own (like HTS or high-Cp materials)
More:
STEAM website: https://espace.cern.ch/steam/_layouts/15/start.aspx#/SIGMA/
1st STEAM workshop (2019): https://indico.cern.ch/event/808547/timetable/

## Slide 55: Magnet / Circuit quench simulation
LEDET
SIGMA
Why have both?
Increased confidence in quench simulation results (mitigate risk of error in simulations). This is especially important for novel magnets / conductors / circuits configurations when it is more difficult to know what to expect.
On detail level, they have different capabilities, limitations, setup and computational effort, like:
  Finite differences vs finite elements
  Simplifying assumptions, strengths and weaknesses
  Hardcoded vs. user editable equations / logic
  Ways to deal with iron and conducting structures
  Efficiency, solvers, input and output (matrix vs mesh)
  Extendibility and flexibility for extension

## Slide 56: ProteCCT (Protection of Canted-Cosine-Theta) type magnets
Accounts for quench-back from conductive formers
User-interface: Input and output to / from Excel
Relies on accompanying COMSOL model for field and inductance calculation when geometry is changed
High degree of consistency between simulations and experimental observations (for MCBRD magnet)
Two fixed global correction parameters fLoopFactor and addedHeCpFrac for all cases
Computationally efficient, standalone executable, ProteCCT is fast!
Simulation tool for evaluating quench of CCT-type magnets
More:
STEAM website: https://espace.cern.ch/steam/_layouts/15/start.aspx#/SitePages/ProteCCT.aspx
1st STEAM workshop (2019): https://indico.cern.ch/event/808547/timetable/

## Slide 57: SING (STEAM Integrated Network Generator) & PSPICE (Personal Simulation Program with Integrated Circuit Emphasis)
Semi-automatic generation of netlists, useful for large circuits
Circuit components can be added in programmatic and iterative way, effectively allowing (‘for’) loops for circuit generation
Models could be generated more quickly and with fewer bugs and less expert knowledge needed
Can be used for turns in magnet or magnets in circuit
Models can be used for frequency domain and transient analysis, like quench and/or short circuits
Tools for automated generation of complex circuits + circuit solver
More:
STEAM website: https://espace.cern.ch/steam/_layouts/15/start.aspx#/SING/
1st STEAM workshop (2019): https://indico.cern.ch/event/808547/timetable/

## Slide 58: COSIM (Cooperative Simulation)
Most commonly: field model is solved with Lumped Element (LEDET) and/or Finite Element (COMSOL) tool and circuit model is solved with circuit solver (PSPICE)
Iteration of field and circuit models until consistent solution (convergence of results) is reached
Relies on data exchange of Input and Output (IO) ports in tools compatible with COSIM (all covered so far)
Capable of hierarchical co-simulation allows for switching of models and coupling schemes
Simulations provide consistent results with measurements for several complex cases
Tool to couple different software simulating interdependent phenomena occurring in various domains, with different time-scales.
Waveform relaxation (Gauss-Seidel Method) coupling :
Field

## Slide 59: Library of Material Properties
Material properties functions coded in:
  C (compiled files also available)
  MATLAB
Properties: cp, k, ρ, Jc (not: E, σy , ν)
Functions are used by STEAM tools, very useful for cross-checking results
These materials properties used in many quench models give consistent results with measurements
We welcome contributions of material properties we do not cover. These need to haver reference
C
More:
STEAM website: https://espace.cern.ch/steam/_layouts/15/start.aspx#/SitePages/Material%20Properties.aspx
1st STEAM workshop (2019): https://indico.cern.ch/event/808547/timetable/
https://gitlab.cern.ch/steam/steam-material-library
https://gitlab.cern.ch/steam/steam-ledet-material-library