## Slide 1: Urgent Instrumentation Requests for P42
Johannes Bernhard (BE-EA)
EABI WG, 10.05.2022

## Slide 2: Beam Instrumentation – Existing and Needed
One SEMgrid existing at s = 511 m. Request: Three additional SEMgrids would be needed relatively urgently and would allow to make a link to TT20. They should be located at s = 397 m, 654 m, 832 m (T10 target). Pitch etc. to be defined together with ECN3TF. Alternative locations at s = 107 m, 261 m, 717 m were originally proposed, having SEMgrids with 1 mm pitch.
There are two BSIs that are regularly used.  Request: Check calibration (relative between BSIs, e.g. T4, but ideally absolute value).
At least two BBS scanners exist (e.g. miniscans on T10 are done during the commissioning).  Request: Check and commission all BBS.
There are some detectors which have not been used (might be working) since at least 20 years (BSM, BSP) and there are no BLMs.
There are several FISCs for operating P42 in electron / secondary beam mode.
We use three 4-jaw collimators during the commissioning with low intensity beams to adjust beam position and angle in the line, scanning on the T10 BSI and NA62 muon signals.
Note: The vacuum level of P42 is not comparable to the other transfer lines, typically at 1e-3 mbar to 1e-2 mbar. For best performance, SEMs should be pumped, ideally P42 vacuum consolidated.