## Slide 1
Reference point
DFHX  YRP_DFHX = 1517 mm without wheel spacer
BusBar  YRP_BB = 1611 mm
1 – DFHX positioning to horizontally match Busburs
1611
Y
1517

## Slide 2
38mm
2 – Horizontal displacement
Horizontal displacement to compensate the one caused by the rotation (see Phase 7)

## Slide 3
3 – Jack system installation

## Slide 4
35mm
35mm
4 –Jack system brought to contact with the frame

## Slide 5
68mm
68mm
5 – Cryostat lifted up

## Slide 6
6 – Wheels removal

## Slide 7
mm
mm
1.7°
7 – Cryostat tilted
Rotation Point

## Slide 8
8 – Cryostat secured to the floor
Feet installation
Fixation system installation

## Slide 9
Fixation Bracket Model

## Slide 10
Equipment
Hydraulic cylinder  Enerpac RC55, 4.9-ton Capacity, 5.00’’ Stroke + Tilt saddle to absorb the inclination
Wheel  Blickle LS-GTH 202K-RI4, Ø = 200mm, Height = 255, Capacity (static) = 4-ton
Feet  elesa+Ganter GN 23 Stainless Steel-Levelling feet
Blickle LS-GTH 202K-RI4
Enerpac RC55 + Tilt Saddle
GN 23 Stainless Steel-Levelling feet