## Slide 2: Crystal Collimation MDs with Proton Beams
M. D’Andrea, R. Bruce, R. Cai, D. Mirarchi, S. Redaelli
LSWG Meeting: Floating MD preparation

## Slide 3: Motivation and scope of crystal MDs
Aim of tests with proton beams: validation of new devices, consolidation of strategies and previous findings, verify implementation of interlock functions
Early feedback on these aspects is crucial in preparation of deployment with Pb ion beams - could have implications for choice of beam energy in Pb ion run (to be made summer 2022)
Following results obtained in Run 2, crystal collimation planned to be used already during 2022 Pb ion run to mitigate losses in IR7-DS
B1H STD
B1H CRY
  Vertical crystal collimators on both beams replaced with new devices in LS2

## Slide 4: Present schedule and readiness
In present schedule, two slots (12h+12h) assigned to crystal collimation tests during commissioning
Extensive interlock and control checks without beam carried out in past weeks by D. Mirarchi and CEM team
Possible conflicting schedule of floating MDs for some participants due to superimposition with IPAC22
All proposed measurements based on tests performed during Run 2: procedure well established and refined
  Quorum of experts anyway available to cover MD slots
  MD requests as “backup” in case measurements cannot be completed or additional tests are required

## Slide 5: Beam setup and collimator settings
Both beams at injection and flat top
Up to 30 pilot bunches, respecting intensity limit of 31011 total protons per beam
Operational collimator settings
Optimized collimator settings
“Adiabatic” insertion of crystals in standard system (0.25 σ tighter)
Proposed settings for use in operation with ion beams
Settings used for validation studies and potential further cleaning improvement
Different settings of downstream TCSGs and TCLAs
TCP
TCSG
TCSG
TCLA
CRY
TCP
TCSG
TCSG
TCLA
CRY

## Slide 6: MD #7006 Validation of Crystal Collimators with Proton Beams
Estimated time: 10 hours
Beam-based linear alignment of crystal collimators
Typical characterization measurements with upstream collimators open and ADT excitation
Loss maps at flat top for cleaning efficiency measurements using operational settings, optimized settings, possibly more configurations
Angular scan of crystal
Linear scan with secondary collimator

## Slide 7: MD #7007 Operation of Crystal Collimators during Energy Ramp
Estimated time: 10 hours
Generation of linear and rotational ramp functions and interlocks using optimal alignment position and orientation previously found
Multiple ramp attempts with all 4 crystals in channeling: monitoring of channeling conditions via loss maps every ~500 GeV
Any leftover measurements at flat top if time allows

## Slide 8: Thank you for your attention!