## Slide 1: MD plan for the 2023 configuration
S. Fartoukh
Recap on the 2023 configuration
Breakdown of main activities with time estimate
Possible alternative (after discussion with GI, MS, SR, and JW)
MD readiness status

## Slide 2
450 GeV: Run 2 injection optics
(BCMS preferred with 2748 bunches)
Ramp: standard ramp & squeeze b*= 1.33 m & rTele = 1.0 EoR
b*= 2 m @ IP1/5/8 reached at 4.5 TeV
Then 2 additional matched points (b*=1.55 m and 1.33 m) added in the ramp
Adjust (b*[m]= 1/10/1/2 at IP1/2/5/8 - X/2 = 160 mrad in IR1/5, 200 mrad in IR2/8 )
Telescopic b* levelling at IP1/5: b*= 60 cm 0.30 m (2 m @ IP8)
Constant X-angle of 160 mrad
Squeeze: b*= 60 cm & rTele = 1.0 EoS
Adjust (b*[m]= 1.2/10.0/1.2/2.0 at IP1/2/5/8 - X/2 = 160 mrad in IR1/5, 200 mrad in IR2/8 )
Telescopic b* levelling at IP1/5: b*= 1.2 m 0.30 m (2 m @ IP8)
First period of X-angle anti-levelling at constant b* (to reach the BBLR limit of 135 mrad @ 1.2 m)
Ramp: combined with telesqueeze: b*= 2.0 m & rTele = 0.5 EoR
b*= 2.0 m @ IP1/5/8 reached at 4.5 TeV
Then telescopic gymnastics at constant
Mini-squeeze in IR1/5 (4 min.): b*= 1.2 m & rTele = 0.5 EoS
Scenario 1 (Run2-like) for 2022
Scenario 2 for 2023/2024/2025
Several optics synergies
Q-change (after the squeeze)
[ LHCb rotation assessed in MD ] (H V ext. crossing @ b*= 2.0 m at IP8)
Q-change (after the squeeze)
LHCb rotation (H V ext. crossing @ b*= 2.0 m at IP8)
Recap on the 2023 configuration (1/2)

## Slide 3
Recap on the 2023 configuration (2/2)
What is different w.r.t. 2022?
The second part of the ramp (E> 4.5 TeV) with the deployment of
the anti-telescope
The mini-squeeze (2 m 1.2 m)
The LHCb rotation
The b* levelling BP
  Doubled dynamic range (1.2 m  30 cm), but the 2nd part (60  30 cm) is the same as in 2022
  Concomitant variations of the crossing angle (135160 mrad)
  TCT setting management (center & mm-gap varying with b*)

## Slide 4
Breakdown of main activities & beam time estimates
(based on MD3270 experience: combined ramp and tele-squeeze)
Validation of the mechanics (except collimator set to coarse settings) with probes, OMC activities @ 1.2 m, and optics measurement all along the cycle
 1 shift with 2 fills: 10 h (+2 h recovery time)  MD1 (or floating MD?)
Machine validation & MO threshold measurement with set-up beams
  LMs in the ramp with new TCT functions, @ FT before/after the LHCb rotation
  optimize the collisions at 1.2 m
  Full orchestration of X-angle & TCT (embedded MD, i.e. additional MD time not counted)
  series of LMs in collision + ASD test
  Validation of the new MO ramp function
  1 shift with 3 fills: 12 h (+2 h) recovery time MD1
Machine re-validation & intensity ramp up to 600-700 bunches for full assessment (beam stability, e-cloud, lifetime, lumi,..)
  Benchmark the BBLR (X-angle) limit and Q-function during b*-levelling with at least 1 train/beam
  Validate the LHCb rotation at high intensity (600-700 bunches)
 2 shifts of 3 h (1 fill) & 13 h (3 fills): 16 h (+2*2 h)  MD2 (or MD1 to save the revalidation?)

## Slide 5
Alternative
1. Activities with probes  kept and scheduled for MD1
 But mechanics of LHCb rotation (EoR) removed from the program (see later)
2. Activities with set up beams  kept and scheduled for MD1
But validation of the LHCb rotation removed from the program (see later),
TCT full orchestration tested in the nom. cycle (including “some” X-angle variations during b*-levelling)
3. The Intensity ramp up cancelled and replaced by
4. A dedicated MD for “X-angle and tunes vs. b*” using the nominal cycle
LM’s needed in collision to validate the 120-160 mrad X-angle range for several b*
To be anticipated during commissioning (or machine revalidation after a TS)
Not clear whether there is a real gain?
5. A dedicated MD for the validation at high intensity of the LHCb rotation, inserted EoS in the
nominal cycle, to be used later on at the end the 2022 pp run
 Certainly a very good idea !
  1 shift with 3 fills: 12 h (+2 h) recovery time MD1
Machine re-validation & intensity ramp up to 600-700 bunches for full assessment (beam stability, e-cloud, lifetime, lumi,..)
  Benchmark the BBLR (X-angle) limit and Q-function during b*-levelling with 1 train/beam
  Assess the LHCb rotation with 600-700 bunches
 2 shifts of 3 h (1 fill) & 13 h (3 fills): 16 h (+2*2 h)  MD2 (or MD1 to save the revalidation?)

## Slide 6
MD readiness
Optics available
/afs/cern.ch/eng/lhc/optics/runIII/RunIII_dev/2022_V5/PROTON
What is missing?
  - MO ramp functions & “matched points” for the LHCb rotation
  LSA settings & BPs (including LHCb rotation) & sequence
  TCT functions (& nrj and b* interlock)
Detailed procedures (a big part of MD3270 can be recycled)