## Slide 1
Optics measurements & correction in the old ESRF storage ring (2010-2018)
Andrea Franchi (ESRF, Grenoble)
mini-workshop on FCC-ee optics tuning and alignment, 11-12 May 2022

## Slide 2: Outlines
Understanding & correcting linear coupling (2009-2010)
Nonlinear optics & magnet calibration via turn-by-turn (TbT) BPM data (2010-2013)
Error analysis of linear optics measurements via orbit & TbT analysis (2016-2017)
Applications of AC Orbit data (2016-2019)
Experience of AC dipole & TbT BPM data (2016-2018)

## Slide 3: Outlines
Understanding & correcting linear coupling (2009-2010)
Nonlinear optics & magnet calibration via turn-by-turn (TbT) BPM data (2010-2013)
Error analysis of linear optics measurements via orbit & TbT analysis (2016-2017)
Applications of AC Orbit data (2016-2019)
Experience of AC dipole & TbT BPM data (2016-2018)

## Slide 4: Understanding & correcting linear coupling
Misconception #1: In the presence of coupling we deal with vertical emittances (plural is not a typo)
Misconception #2: Coupling correction is a linear problem not needing CPU-intense random/genetic/non-linear optimizers
Misconception #3: Guignard formulas don’t apply to modern synchrotron light sources & damping rings (integer part of tunes Qx>>Qy)
Misconception #4: “indirect measurements” of vertical emittance should be avoided

## Slide 5: Understanding & correcting linear coupling
Misconception #1: In the presence of coupling we deal with vertical emittances (plural is not a typo)
Misconception #2: Coupling correction is a linear problem not needing CPU-intense random/genetic/non-linear optimizers
Misconception #3: Guignard formulas don’t apply to modern synchrotron light sources & damping rings (integer part of tunes Qx>>Qy)
Misconception #4: “indirect measurements” of vertical emittance should be avoided

## Slide 6: Understanding & correcting linear coupling
Vertical emittance in the absence of coupling
Eigen-emittance E: constant along the ring, with Ev≅0
Non measurable RMS emittance:
Measurable emittance from RMS beam size:
Ev=εy=Ey=const.
With zero vertical dispersion, Ev=εy=Ey≅0

## Slide 7: Understanding & correcting linear coupling
Vertical emittances in the presence of coupling
Eigen-emittance E: constant along the ring, but Ev≠0
Non measurable projected s-dependent RMS emittance:
Measurable apparent s-dependent emittance from RMS beam size:
Ev=const ≠ εy(s) ≠ Ey(s)

## Slide 8: Understanding & correcting linear coupling
Vertical emittances in the presence of coupling
Measurable apparent emittance:
Non measurable projected emittance:
eigen-emittance
Ev= 9 pm
Lattice errors from Orbit Response Matrix measurement + Accel. Toolbox

## Slide 9: Understanding & correcting linear coupling
Vertical emittances in the presence of coupling
Measurable apparent emittance:
Non measurable projected emittance:
Lattice errors from Orbit Response Matrix measurement + Accel. Toolbox

## Slide 10: Understanding & correcting linear coupling
all skew quad correctors OFF ey/ex ~ 5%
C*, D*: emittance monitors
Coupling correction is a linear problem not needing CPU-intense random/genetic/non-linear optimizers

## Slide 11: Understanding & correcting linear coupling
after correction ey/ex ~ 1‰
C*, D*: emittance monitors
Coupling correction is a linear problem not needing CPU-intense random/genetic/non-linear optimizers
~20 min. for ORM
a few seconds for RDT correction

## Slide 12: Understanding & correcting linear coupling
after correction ey/ex ~ 1‰
C*, D*: emittance monitors
Coupling correction is a linear problem not needing CPU-intense random/genetic/non-linear optimizers
~20 min. for ORM
a few seconds for RDT correction

## Slide 13: Outlines
Understanding & correcting linear coupling (2009-2010)
Nonlinear optics & magnet calibration via turn-by-turn (TbT) BPM data (2010-2013)
Error analysis of linear optics measurements via orbit & TbT analysis (2016-2017)
Applications of AC Orbit data (2016-2019)
Experience of AC dipole & TbT BPM data (2016-2018)

## Slide 14: Nonlinear optics & magnet calibration
Get synchronized and decent(*) TbT BPM data in both planes
(*) from nonlinear optics with zero chromaticity and zero (linear) amplitude-dependent detuning

## Slide 15: Nonlinear optics & magnet calibration
Perform a suitable FFT of the TbT data & look at the lines popping up in the spectra

## Slide 16: Nonlinear optics & magnet calibration
RDTs require
CRDTs require
less information, but no systematic error from px,y
from the spectral lines infer the combined resonance driving terms (CRTDs) @ all BPMs

## Slide 17: Nonlinear optics & magnet calibration
Compare & fit measured & model CRDTs

## Slide 18: Nonlinear optics & magnet calibration
Compute your sextupole error model or calibrate individual magnets

## Slide 19: Nonlinear optics & magnet calibration
(optionally) correct your sextupole error model & check beam lifetime
@ Diamond light source

## Slide 20: Nonlinear optics & magnet calibration
(optionally) correct your sextupole error model & check beam lifetime
Not @ESRF: minor lifetime increase in low-intensity-per-bunch mode, detrimental for Touschek-dominated modes
@ Diamond light source

## Slide 21: Nonlinear optics & magnet calibration
(for fun) measure second-order terms
skew sextupole CRDTs
normal octupole CRDTs

## Slide 22: Nonlinear optics & magnet calibration
Digression: a similar beam-based sextupole calibration performed via measurement & fit of off-energy ORM (chromatic functions db/dd, D’, Q’)
momentum compaction
collaboration with Laura Torino & Nicola Carmignani

## Slide 23: Outlines
Understanding & correcting linear coupling (2009-2010)
Nonlinear optics & magnet calibration via turn-by-turn (TbT) BPM data (2010-2013)
Error analysis of linear optics measurements via orbit & TbT analysis (2016-2017)
Applications of AC Orbit data (2016-2019)
Experience of AC dipole & TbT BPM data (2016-2018)

## Slide 24: Error analysis of linear optics measurements
L. Malina et. al. PRAB 20, 082802 (2017)
R. Tomás et. al. PRAB 20, 054801 (2017)

## Slide 25: Error analysis of linear optics measurements
low beam excitation incompatible with ultra-low coupling
large beam excitation incompatible with strong chromatic sextupoles
https://arxiv.org/abs/1603.00281

## Slide 26: Error analysis of linear optics measurements
L. Malina et. al. PRAB 20, 082802 (2017)
large beam excitation incompatible with strong chromatic sextupoles

## Slide 27: Error analysis of linear optics measurements
measured β-functions
best precision TbT: 0.4%
best precision ORM: 0.5%
best accuracy ORM-TbT: ~1%
L. Malina et. al. PRAB 20, 082802 (2017)
 | TbT & tune ampli | TbT & tune phase | orbit & ORM
BPM calibration |  |  | 
BPM synchro. |  |  | 
Nonlinear. & chroma |  |  | 
time consuming |  |  | 
model dependent |  |  | 
DC
AC

## Slide 28: Error analysis of linear optics measurements
 | TbT & tune ampli | TbT & tune phase | orbit & ORM
BPM calibration |  |  | 
BPM synchro. |  |  | 
Nonlinear. & chroma |  |  | 
time consuming |  |  | 
model dependent |  |  | 
DC
AC

## Slide 29: Error analysis of linear optics measurements
 | TbT & tune ampli | TbT & tune phase | orbit & ORM
BPM calibration |  |  | 
BPM synchro. |  |  | 
Nonlinear. & chroma |  |  | 
time consuming |  |  | 
model dependent |  |  | 
DC
AC
Castro’s formula (no error dk1 between BPMs, model needed)

## Slide 30: Error analysis of linear optics measurements
A. Wegscheider et. al. PRAB 20, 111002 (2017)
 | TbT & tune ampli | TbT & tune phase | orbit & ORM
BPM calibration |  |  | 
BPM synchro. |  |  | 
Nonlinear. & chroma |  |  | 
time consuming |  |  | 
model dependent |  |  | 
DC
AC
@LHC
New formula (with error dk1 between BPMs, model needed)

## Slide 31: Error analysis of linear optics measurements
 | TbT & tune ampli | TbT & tune phase | orbit & ORM
BPM calibration |  |  | 
BPM synchro. |  |  | 
Nonlinear. & chroma |  |  | 
time consuming |  |  | 
model dependent |  |  | 
DC
AC

## Slide 32: Outlines
Understanding & correcting linear coupling (2009-2010)
Nonlinear optics & magnet calibration via turn-by-turn (TbT) BPM data (2010-2013)
Error analysis of linear optics measurements via orbit & TbT analysis (2016-2017)
Applications of AC Orbit data (2016-2019)
Experience of AC dipole & TbT BPM data (2016-2018)

## Slide 33: Applications of AC Orbit data
http://arxiv.org/abs/1711.06589
 | TbT & tune ampli | TbT & tune phase | orbit & ORM
BPM calibration |  |  | 
BPM synchro. |  |  | 
Nonlinear. & chroma |  |  | 
time consuming |  |  | 
model dependent |  |  | 
DC
AC
Orbit response matrix (ORM) @ESRF:
~1 h (DC steerer excitation + numerical response*)
~3’ (AC steerer excitation + analytical response*)
* response : N & S (large matrices)
(AC excitation pioneered @Diamond)
ESRF ORM column: AC Vs DC
measurement
analysis

## Slide 34: Applications of AC Orbit data
 | TbT & tune ampli | TbT & tune phase | orbit & ORM
BPM calibration |  |  | 
BPM synchro. |  |  | 
Nonlinear. & chroma |  |  | 
time consuming |  |  | 
model dependent |  |  | 
DC
AC
Orbit response matrix (ORM) @ESRF:
~1 h (DC steerer excitation )
~3’ (AC steerer excitation )
beam-based measurement of skew-quadrupole fields induced by undulators & skew quad correctors

## Slide 35: Applications of AC Orbit data
Z. Marti e. al. PRAB 23, 012802 (2019)
 | TbT & tune ampli | TbT & tune phase | orbit & ORM
BPM calibration |  |  | 
BPM synchro. |  |  | 
Nonlinear. & chroma |  |  | 
time consuming |  |  | 
model dependent |  |  | 
DC
AC
Digression: fast AC beam-based quadrupole alignment derived & applied to ALBA light source (120 quadrupoles):
  serial DC steerer excitation: 5h, precision ~50 mm
  parallel AC steerer excitation: 10’, precision ~15 mm
  applied to sextupoles too.

## Slide 36: Outlines
Understanding & correcting linear coupling (2009-2010)
Nonlinear optics & magnet calibration via turn-by-turn (TbT) BPM data (2010-2013)
Error analysis of linear optics measurements via orbit & TbT analysis (2016-2017)
Applications of AC Orbit data (2016-2019)
Experience of AC dipole & TbT BPM data (2016-2018)

## Slide 37: Experience of AC dipole & TbT BPM data
Betatron coupling described by two CRDTs
Fxy =(f1001 - f1010*) & Fyx =(f1001* - f1010*)
Measurement with low chroma (0,0) & detuning sext. optics
compare (εy/εx~1‰) ORM model ...
AMPLITUDE
PHASE

## Slide 38: Experience of AC dipole & TbT BPM data
Betatron coupling described by two CRDTs
Fxy =(f1001 - f1010*) & Fyx =(f1001* - f1010*)
Measurement with low chroma (0,0) & detuning sext. optics
compare (εy/εx~1‰) ORM model with TbT harmonic analysis
AMPLITUDE
PHASE

## Slide 39: Experience of AC dipole & TbT BPM data
Betatron coupling described by two CRDTs
Fxy =(f1001 - f1010*) & Fyx =(f1001* - f1010*)
Measurement with large chroma (8,13) operational optics
compare (εy/εx~1‰) ORM model with TbT harmonic analysis
AMPLITUDE
PHASE

## Slide 40: Experience of AC dipole & TbT BPM data
1st experimental observation: AC dipole tuning tedious with high chromaticity: beam lost with setting used for low-chroma optics.
High (8,13) chroma sextupole optics:
RAD OFF & ON (multi-particle simulations)
Qx=0.44
QAC=0.39

## Slide 41: Experience of AC dipole & TbT BPM data
2nd experimental & numerical observation:
synchrotron radiation + diffusion & high chroma => limited accuracy.
AC dipole & data cleaning OK for low-chroma lepton rings.

## Slide 42: Outlines
Understanding & correcting linear coupling (2009-2010)
Nonlinear optics & magnet calibration via turn-by-turn (TbT) BPM data (2010-2013)
Error analysis of linear optics measurements via orbit & TbT analysis (2016-2017)
Applications of AC Orbit data (2016-2019)
Experience of AC dipole & TbT BPM data (2016-2018)
Thank you for your attention