## Slide 1
Presenter Name
Date
EP R&D SEMINAR
Signal formation in detectors with resistive elements
Djunes Janssens
djunes.janssens@cern.ch
Supervisor: F. Blekman, J. D’Hondt , E. Oliveri,
W. Riegler, H. Schindler and R. Veenhof.
Monday June 13th, 2022

## Slide 2: Introduction
  Novel detector structures are proposed regularly, mixing old and new ideas, with detectors containing resistive elements widening the landscape of possible configurations.
  The use of these technologies in experiments makes it necessary to understand and characterize its the response for the design and optimization of the next generation of particle detectors and their application.
T. Alexopoulos et al., Nucl. Instrum. Meth. A 640 (2011) 110.
M. Tornago, R. Arcidiacono, N. Cartiglia et al., Nucl. Instrum. Meth. A 1003 (2021).
AC-Coupled LGAD
Resistive-strips micromegas

## Slide 3: Overview
  We want to use Garfield++ and COMSOL to model the signal formation in detectors with resistive elements by applying an extended form of the Ramo-Shockley theorem.
  Outline:
  Ramo-Shockley theorem extension for conductive media
  Overview of the numerical approach
  Examples of signals induced in various detectors
  Summary
Garfield++: https://garfieldpp.web.cern.ch/garfieldpp/
H. Schindler’s dissertation: Microscopic simulation of particle detectors
COMSOL Multiphysics: https://www.comsol.ch
Electron
Ion
Drift lines of a GEM in Garfield++

## Slide 4: Ramo-Shockley theorem
  The Ramo-Shockley theorem allows the current induced by an externally impressed charge density on any electrode to be calculated by the usage of a so-called weighting potential .
Readout strip
Gas gap
Insulator
Weighting potential for only perfect insulators and electrodes with infinite conductivity.
Cathode/Mesh
S. Ramo, PROC. IRE 27, 584 (1939).
W. Shockley, Journal of Applied Physics. 9 (10): 635 (1938).
This static can be calculated for an electrode i by:
Remove the drifting charges
Put the electrode at potential Vw
Grounding all other electrodes
Vwϴ(t)

## Slide 5: Ramo-Shockley theorem
  Using this framework, the induced current sourced by a point charge q can, for example, be calculated in a single GEM geometry with x- and y-strips. This is done by first calculating the weighting potential of the strips.
GEM
This XYU-Readout design is a project in progress with F. Sauli and K. J. Flöthner.
First results will be presented tomorrow by K. J. Flöthner :
https://indico.cern.ch/event/1138814/contributions/4917313/
x
y
u
XYU Readout image

## Slide 6: Ramo-Shockley theorem extension for conducting media
  For detectors with resistive elements, the time dependence of the signals is not fully given by the movement of the charges in the drift medium but also by the time-dependent reaction of the resistive materials.
Readout strip
Gas gap
R layer
Insulator
Weighting potential for a resistive layer separating the gas gap and insulating layer.
Vwϴ(t)
W. Riegler, Nucl. Instrum. Meth. A 535 (2004), 287-293.
W. Riegler, Signals in Particle Detectors, CERN’s Academic Training Lecture Regular Programme (2019):
https://indico.cern.ch/event/843083/
Cathode/Mesh
This dynamic can be calculated for an electrode i by:
Remove the drifting charge carriers
On the electrode apply a step voltage pulse at time t = 0
Grounding all other electrodes
V

## Slide 7: Ramo-Shockley theorem extension for conducting media
where .
  The time-dependent weighting potential is comprised of a static prompt and a dynamic delayed component:
Examples of systems of which the weighting potential is analytically obtainable see W. Riegler, JINST 11 (2016) no.11, P11002.
Further reading: W. Riegler, P. Windischhofer, Nucl. Instrum. Meth. A 980 (2020)
=
R = 1 kΩ/❑
R = 10 kΩ/❑
R = 100 Ω/❑
Charge has reached the cathode at t = T
250 μm
10 μm
400 μm
Direct induction
Reaction from resistive material
The current induced by a point particle q is given by:
R = 1 kΩ/❑
R = 10 kΩ/❑
R = 100 Ω/❑

## Slide 8: Overview of the numerical methodology
  These weighting potentials can only be obtained analytically for a small subset of the larger group of existing detectors; thus, a numerical method is used.
  COMSOL® :
  Numerically obtain the dynamic weighting potential.
  Garfield++:
  Detailed microscopic simulation of particle detectors based on ionization measurements in gases or semiconductors.
Garfield++: https://garfieldpp.web.cern.ch/garfieldpp/
COMSOL Multiphysics: https://www.comsol.ch /
G. Bencivenni et al., JINST 14 P05014 (2019).
Sketch of the Double-Resistive layout μRWELL:

## Slide 9: Overview of the numerical methodology
  COMSOL is a finite element solver capable of solving the electrodynamics field equations using the Electric Currents module and time solver.
  The ramping time of the step function for the Vw pulse is taken is taken smaller than the reaction time of the resistive material.
Time [s]
Vw pulse [V]
Resistive Stips
Mesh
Insulator
y-Strips
x-Strips
Resistive-strips micromegas

## Slide 10: Overview of the numerical methodology
  Coordinate mapping allows to modelling large area detectors such as a Resistive-strips micromegas.
T. Alexopoulos et al., Nucl. Instrum. Meth. A 640 (2011) 110.
M. Byszewski1 and J. Wotschack, JINST 7 C02060 (2011).
COMSOL coordinate mapping: link.
4 mm
4.8 cm
Image taken at the May-June 2022 SPS test beam
COMSOL model of the geometry

## Slide 11: Overview of the numerical methodology
  The resulting solutions are imported into Garfield++ as a finite collection of time sliced potential maps using its ComponentComsol class.
There is a tutorial on the Garfield++ webpage on the importing of field maps of COMSOL:
https://garfieldpp.web.cern.ch/garfieldpp/examples/comsol/
Weighting potential of a y-strip at y = 0.
v
Resistive strips
x-strips
y-strip
Mesh
z-Axis
x-Axis
Weighting potential of a y-strip at x = 0.
Resistive strip
x-strips
y-strips
Mesh
v
y-Axis
z-Axis

## Slide 12: Overview of the numerical methodology
  Given the trajectories of all charge carriers in your geometry, the induced current on the readout can be calculated.
Drift lines in the induction gap as modelled by Garfield++
Electron
Ion
Mesh
Resistive Stips

## Slide 13: Overview of the numerical methodology
  With the assurance of the accuracy of the methodology based on toy model examples which enjoy an analytic solution, we are deploying it to characterize the signals obtained from a wide variety of resistive particle detectors.
Examples of systems of which the weighting potential is analytically obtainable see W. Riegler, JINST 11 (2016) no.11, P11002.
1 mm
400 μm
500 μm
= 8
= 100 kΩ/❑

## Slide 14: Signal formation in a MicroCAT detector
  The MicroCAT’s two-dimensional interpolating readout structure allows for a reduced number of electronic readout channels without loss of spatial resolution.
  This resistive readout concept recently has enjoyed renewed interest within the development of a DC-Coupled LGAD device
F. Bartol et al. J. Phys. III France, 6 (1996), p. 337
A. Sarvestani et al., Nucl. Instrum. Meth. A 410 (1998) 238–258
H. Wagner et al. Nucl. Instrum. Meth. A 482 (2002) 334–346
Weighting potential map for one readout node
DC-coupled LGAD: N. Cartiglia, The 39th RD50 Workshop (Valencia) (17-19 November 2021).

## Slide 15: Diamond 3D Pixel Detector
A 3D geometry with thin columnar resistive electrodes orthogonal to the diamond surface, is expected to provide significantly better time resolution with respect to the extensively studied planar diamond sensors.
With the team of the INFN TimeSpot project, we are exploring the modelling of signal induction on the readout columns.
Weighting potential of a readout column at z = 250 μm.
Preliminary
Electron
Hole
Pion
Bias Column
Readout Column
Drift lines as modelled by Garfield++
Anderlini L. et al., Frontiers in Physics 8 (2020)
For timing measurements and first modelling results see talk by M. Veltri:
“A 4D diamond detector for HL-LHC and beyond”.
x
y
v

## Slide 16: Signal formation in AC-Coupled LGAD
In collaboration with INFN Torino group of N. Cartiglia, we are currently looking at simulating the currents induced in the AC-Coupled Low Gain Avalanche Diode (LGAD) geometry.
When successfully benchmarked, it can be used to understand and explore novel readout designs.
M. Tornago, R. Arcidiacono, N. Cartiglia et al., Nucl. Instrum. Meth. A 1003 (2021).
See N. Cartiglia’s Friday VCI talk: “4d-tracking, LGADs, and fast timing detectors”.

## Slide 17: Some of the detectors containing resistive elements
Spatial resolution study:
MicroCAT’s two-dimensional interpolating readout
μ-Resistive-WELL
Small-pad resistive Micromegas
Resistive-strip bulk Micromegas
AC-Coupled LGAD
Timing resolution study:
Multigap Resistive Plate Chambers (MRPC)
Resistive Picosec Micromegas Detector
Diamond3D sensor
AC-Coupled LGAD
We are working on extending the list of detectors geometries that contain resistive elements.
M. Iodice et al., Nucl. Instrum. JINST 15 C09043 (2020).

## Slide 18: Summary
  We want to use Garfield++ and COMSOL to model the signal formation in detectors with resistive elements by applying an extended form of the Ramo-Shockley theorem.
  The extension of the Ramo-Shockley theorem for conductive media allows for an efficient way to calculate the signals induced in resistive detectors.
  A numerical method for obtaining the time dependent weighting potentials is used to increase the range of applicability of the framework to a larger set of geometries (COMSOL and TCAD).
  Various induced signals were calculated for a variety of readout structures.
  Outlook:
  Use a general-purpose circuit simulation program to describe the front-end electronics, e.g., Spice®.
  Measurements and simulation for resistive-bulk strip Micromegas, resistive plane Micromegas, Picosec Micromegas and RWELL.
  Including Johnson thermal noise into the simulations.
SPICE: http://bwrcs.eecs.berkeley.edu/Classes/IcBook/SPICE/