## Slide 1: Future accelerators
Roderik Bruce

## Slide 2: Outline
Introduction
  Considerations for collider design: particle type, energy, circular/linear…
  Limitations for future colliders
  European strategy for particle physics
ILC (International Linear Collider)
CLIC (Compact Linear Collider)
HL-LHC (High-Luminosity Large Hadron Collider)
FCC-hh (Future Circular collider, hadrons)
FCC-ee (Future Circular collider, e+e-)
CEPC/SppC (Chinese Electron-Positron Collider / Super proton-proton Collider)
Other future accelerator projects (briefly)
Linear
Circular

## Slide 3: Particle colliders
Particle colliders have been instrumental for scientific discoveries in high energy physics for more than half a century
  Key for establishing the standard model in particle physics
Technological innovation made it possible to increase energy at a much faster pace than the costs
LHC has the highest energy among colliders built so far
  Circular collider, designed to collide 7 TeV protons and heavy ions
“Livingstone plot” of collider energy vs time (source)

## Slide 4: LHC timeline
Present LHC will operate for a few more years
High-Luminosity LHC (HL-LHC) upgrades foreseen for next long shutdown (LS3) for Run 4
HL-LHC planned to operate at least until ~2038
What happens next?
  Nobody knows, but there are many ideas on the table
It took ~25 years to design and build the LHC, so need to start thinking now about future options
Tentative schedule, could well change
Run 3
Run 3
Run 4
Run 4
Run 5
Run 6
HL-LHC installation
HL-LHC
HL-LHC

## Slide 5
3 main complementary ways to search for (and study) new physics at accelerators
e.g.: Higgs production at future e+e- linear/circular colliders
at √s ~ 250 GeV through the HZ process
 need high E and high L
look for (tiny) deviations from SM expectation from quantum effects (loops, virtual particles)
sensitivities to E-scales Λ>> √s  need high E and high L
production of a given (new or known) particle
Direct
E.g. K+  π+νν decay (NA62 experiment)
Proceeds via loops  suppressed in the SM : BR~ 10-10
Can be enhanced by new particles running in the loop.
Theoretically very clean.
Rare processes
suppressed in SM  could be enhanced by New Physics
Indirect
precise measurements of known processes
X*
 -
 +
E.g. top mass predicted by LEP1 and SLC in 1993:
mtop = 177  10 GeV; first direct evidence
at Tevatron in 1994: mtop = 174  16 GeV
√s ~ 90 GeV
e.g. neutrino interactions, rare decay modes  need intense beams and/or ultra-sensitive (massive)
detectors (“intensity frontier”)
Slide from
F. Gianotti
Main focus

## Slide 6: Considerations for new colliders
So, we want high energy and high luminosity
  When we say high luminosity, we implicitly mean high event rate
  Reminder: The luminosity directly determines the event rate
How do we get there? Several choices to be made:
  What to collide: lepton vs hadron
  How to collide:
    fixed target or colliding beams
    linear vs circular collider
  Acceleration technology
    DC, RF, wakefield…
  Magnet technology
    Superconducting (what conductor?), normal conducting
  Acceptable cost of construction, power consumption, site
Think about various limitations to energy and luminosity and how to overcome them
Event rate
Luminosity
(determined by
and collider design:
can be influenced)
Cross section
(given by physics,
cannot be
influenced)
Notes: Cross section for hadronic Higgs production is order of pico barn

## Slide 7: Leptons vs hadrons
Hadrons (protons or ions)
Mix of quarks, anti-quarks and gluons:
  variety of processes
  not all nucleon energy available in collision
  Energy spread between partons – spread in collision energy
  huge QCD background
Can typically achieve highest collision energy
Good for discoveries at the frontier of new physics
p
p
LEP II e+e- collision, DELPHI
LHC Pb-Pb collision, CMS
Leptons (electrons, positrons, maybe muons)
Elementary particles colliding - very well defined centre-of-mass energy
Low background
Good for high-precision measurements
Higher energy loss from synchrotron radiation influences accelerator design  see next slides
e+
e-

## Slide 8: Synchrotron radiation
Classical electrodynamics: an accelerating charge radiates
  Radiation carries off energy, which is taken away from the kinetic energy
  Radiated energy needs to be replenished by accelerating RF cavities => could lead to very high power consumption
  Radiated photons impact on vacuum chamber => causes heating, maybe even damage for high power loads
Radiation also leads to shrinking emittance (and beam size) – lost momentum replenished only in longitudinal direction: “radiation damping”
Radiation in longitudinal acceleration negligible
Radiation loss for transverse acceleration (bending) can be large: depends on particle mass, energy, and bending radius:
Much stronger effect for leptons!
Imposes limitations on
collider design
force
force
Longitudinal
acceleration
Transverse
acceleration
Notes: Griffiths p11:16 p481 pdf,
Jackson p688 eq 14.13-14.14

## Slide 9: Collider vs fixed target experiments
To achieve the highest possible centre-of-mass energy, need a collider
Fixed Target
Collider

## Slide 10: Circular vs linear collider
source
main linac
N
S
N
S
accelerating cavities
Circular Collider
multi-pass => Accelerate beam in many turns, let beam collide many times
many magnets, few accelerating cavities
Bending of beam trajectory => synchrotron radiation losses
Linear Collider
single pass => need to be very efficient
few magnets, many accelerating cavities
Not limited by synchrotron radiation – promising choice for reaching highest lepton energies

## Slide 11: Increasing beam energy
Hadron beams: energy limited by ability of to keep particle on circular orbit
  Maximum achievable dipole field (superconductor technology)
  Radius of ring (cost, site)
Lepton beams: radiation losses
  RF power consumption
  Disposal of radiated power
  Radius of ring (cost, site)
Circular Collider
Linear Collider
Energy depends on
  Accelerating gradient (RF technology)
    Plasma wakefield acceleration promises large advancement, but not yet mature to produce required beam quality
  Length (cost, site)
To push energy boundary: improve technology (B-fields, RF gradient) or build a larger machine
For protons:
Ecm ≈ Llinac Gacc
Notes: 9 gev lost per turn in FCC-ee 182.5 GeV

## Slide 12: Increasing luminosity
Increase F: shorter bunches, smaller crossing angle
Smaller β*
Smaller emittance
Smaller beam size
Higher intensity
Increase number of bunches
Increase bunch intensity
Reminder: luminosity depends on beams and optics
Expression for round beams:
In addition:
Potential limitations on luminosity from losses and showers from the collisions

## Slide 13: Considerations for future collider choices
Physics potential
The collider energy
The collider luminosity
Particle type
Feasibility
The technical maturity
The risk
The schedule
Affordability
The collider cost
The collider power consumption
Availability of site
D. Schulte

## Slide 14: European strategy for particle physics
Common strategy worked out in Europe to guide future decision-making in field: “European strategy for particle physics”
  endorsed by the CERN council
Based on bottom-up approach:
  physics community is invited to submit proposals for near-term, mid-term and longer-term projects  community discussion in open symposium, Physics briefing book
  Based on this input, the European Strategy Group formulates the strategy
    consists of scientific delegates from CERN Member States, Associate Member States, directors of major European laboratories, representatives of various European organizations, some invitees from outside the European Community
Initiated in 2006, updated in 2013 and 2020, next update foreseen in 2026/2027
  2020 update: Key takeaway messages

## Slide 15: Some recommendations in European strategy
Some points relevant to future high-energy colliders - see full document here
[about LHC] “The successful completion of the high-luminosity upgrade …. should remain the focal point of European particle physics, together with continued innovation in experimental techniques. The full physics potential of the LHC and the HL-LHC …. should be exploited. “
“An electron-positron Higgs factory is the highest-priority next collider”
“Europe, together with its international partners, should investigate the technical and financial feasibility of a future hadron collider at CERN with a centre-of-mass energy of at least 100 TeV and with an electron-positron Higgs and electroweak factory as a possible first stage. “
“The particle physics community should ramp up its R&D effort focused on advanced accelerator technologies, in particular that for high-field superconducting magnets, including high-temperature superconductors”
Notes: Summary from DG presentation to personnel, sept 2020

## Slide 16: Future high-energy colliders studied at CERN
HL-LHC: luminosity upgrade of the LHC.
  Approved and financed - production and installation of upgrades already in full swing
  14TeV pp CMS and heavy ions as in LHC, 27 km
Future Circular Collider (FCC) in different stages
  Conceptual design report released
  Circular e+e- collider in 100 km tunnel, up to 365 GeV CMS: FCC-ee
  Re-use tunnel for 100 km hadron collider, 100 TeV pp CMS: FCC-hh
  2-step approach inspired by successful LEP – LHC programs at CERN
  Alternative approaches:
    energy upgrade of the LHC using stronger magnets: High-Energy LHC (HE-LHC)
    Hadron-electron collisions at the FCC: FCC-he
    Lower-field version of FCC-hh
Compact Linear Collider (CLIC)
  Linear e+e- collider, conceptual design report released
  Up to ~50 km and 3 TeV CMS energy
Other projects that are being studied
  Muon collider
  LHeC (hadron-electron collisions at the LHC)
LHC
FCC
CLIC

## Slide 17: Initiatives in the rest of the world
International Linear Collider (ILC)
  Linear e+e- collider, technical design report released – mature design
  up to 500 GeV CMS, 31 km
  Potentially hosted by Japan – waiting for political decisions
Chinese initiative for circular collider
  First: e+e- collider (CEPC), up to 240 GeV CMS energy, 100 km ring
  followed by a 100 km hadron collider (SppC), 75 TeV CMS energy (proposals for extensions to ~150 TeV)
Electron-Ion Collider (EIC) to be built at Brookhaven, US
  Circular, up to 140 GeV CMS energy, ~3.4 km
  Range of ions: p-U
  Use existing RHIC with some upgrades for ions
  New electron storage ring and injector
  Project approved, announced timeline to completion of ~10-15 years
ILC
CEPC / SppC

## Slide 18
ILC

## Slide 19: ILC basics
International Linear Collider: e+e- collider, aiming at 100-250 GeV beam energy (up to 500 GeV centre of mass)
  Extendable to 1 TeV (requires doubling the length)
Foreseen length at 500 GeV CMS energy of 31 km
Possibly to be built in Japan – waiting for political decisions and agreements on funding

## Slide 20: ILC layout and concept
Undulator
CC BY-SA 3.0, https://commons.wikimedia.org/w/index.php?curid=537945
First, create e- (photocathode DC gun)
Accelerate, send to circulate in 3.2 km damping ring
  Shrinking emittance under radiation damping
e- sent to main linac, accelerate
To create e+: Electrons pass undulator – magnets with many periodic bends
  Radiated photons impact on Ti-alloy target, creating e+e- pairs.
  Capture e+, accelerate, send to damping ring
Send e+ to main linac, accelerate
Collide e+e- inside detector
From ILC design report

## Slide 21: Luminosity comparison
Comparing luminosity between different future lepton colliders
  Circular and linear
At high energies, linear lepton colliders can achieve higher luminosity than circular ones
  Intensity in circular colliders limited by synchrotron raditaion

## Slide 22: Further documentation
ILC technical design report

## Slide 23
CLIC

## Slide 24: CLIC basics
Linear e+e- collider, to be built in stages of increasing centre-of-mass energy:
  3 stages: 380 GeV – 3 TeV
  Length between ~11 km and ~50 km
Aiming at highest lepton energies
30 MW of beam power at 3TeV

## Slide 25: CLIC layout
Concept: beam generation  pre-acceleration  damping rings  booster linac  main linacs collisions
CLIC aims at gradients of 100 MV/m, 20 times higher than the LHC
  Compare 30 MV/m at ILC
Different acceleration concept in main LINAC from ILC :
  drive-beam acceleration, with RF power taken from another e- beam

## Slide 26: Two-beam acceleration scheme
The high-current drive beam is decelerated in special power extraction structures (PETS)
Generated EM field can be transferred in RF waveguides to the other beam => power is used to accelerate the main beam

## Slide 27: CLIC Test Facility (CTF3)
Experimental tests carried out in test facility at CERN to demonstrate drive beam concept
Accelerating gradient of >100 MV/m achieved

## Slide 28: CLIC power consumption
Power and energy consumption at 380 GeV is well within the existing parameters and installations at CERN
At 1.5 TeV: power will surpass the current CERN usage (2017) by ~30%
At 3 TeV the energy consumption will be a factor two of the current CERN usage (2017)
Development work ongoing to further improve energy efficiency
Estimated power consumption of CLIC in MW at 380 GeV (total: 252 MW)
https://clic.cern

## Slide 29: CLIC reference documents
More information:
  Conceptual design report (2012)
  Updated CLIC baseline document (2016)

## Slide 30
HL-LHC

## Slide 31: Reminder: LHC
27 km synchrotron, built to collide 7 TeV proton beams at 4 experiments
  Largest collider and highest energy to date
About 1 month per year: heavy-ion collisions
About 1200 superconducting dipole magnets (NbTi) with 8.3 T field, operating at 1.9 K
So far collected in total about 190 fb-1 of integrated luminosity at the high-luminosity experiments (ATLAS, CMS)
Switzerland
France
LHC
CMS
ALICE
LHCb
ATLAS

## Slide 32: HL-LHC
  High-luminosity LHC: Major upgrade of the LHC
  Main goals:
    Target an integrated luminosity of at least ~250 fb-1 per year
    Achieve a total integrated luminosity of 3000 fb-1 over the project lifetime, a factor ~15 higher than what has been achieved so far at LHC
    Prepare machine for operation from 2029 and at least up to ~2038
 | LHC 2018 | HL-LHC
Protons per bunch | 1.1 x 1011 | 2.2 x 1011
Number of bunches | 2556 | 2750
Normalized emittance | 1.8 micron | 2.5 micron
Beta* | 25-30 cm | 15 cm
Full crossing angle | 320 microrad | 500 microrad
Geometric reduction factor F | 0.6 | 0.35
“Virtual” luminosity |  | 2.4 x 1035 cm-2s-1
Levelled luminosity | 2.1 x 1035 cm-2s-1 | 5 x 1034 cm-2s-1

## Slide 33: Compensation of geometric reduction factor
Bunches experience electromagnetic force from the opposing beam at the collision point (head-on beam-beam) or nearby in common beam pipe (long-range beam-beam)
  Need crossing angle, not only to avoid parasitic collisions
Crossing angle at HL-LHC must be larger than at LHC, due to higher intensity
  Would cause very large loss in luminosity: F≈0.35
To compensate: use “crab cavities” that tilt the bunches longitudinally and ensure overlap at the collision point
Long-range
Head-on

## Slide 34: Crab cavities
Create a oscillating transverse electric field
Kick head and tail of the bunch in opposite directions

## Slide 35
FCC-hh

## Slide 36: FCC-hh general goals
European strategy: “Europe, together with its international partners, should investigate the technical and financial feasibility of a future hadron collider at CERN with a centre-of-mass energy of at least 100 TeV and with an electron-positron Higgs and electroweak factory as a possible first stage. “
FCC-hh: collide 50 TeV protons (or heavy ions of equivalent magnetic rigidity) in tunnel of ~100 km
  Factor 7 higher energy than LHC, factor ~3 longer tunnel
  International FCC collaboration (CERN as host lab)
More than an order of magnitude higher peak luminosity than LHC; factor 6 higher than HL-LHC
Goal: Achieve integrated luminosity of 20 000 fb-1 per experiment collected over 25 years of operation (vs 3000 fb-1 for HL-LHC)

## Slide 37: FCC-hh layout
Insertions in FCC-hh
  Two high-luminosity experiments (A and G)
  Two other experiments (B and L), combined with injection
  Two collimation insertions (F and J)
  One extraction insertion (D)
  One RF insertion (H)
Insertions are 1.4/2.8 km long
Compatible with LHC or SPS as injector

## Slide 38: FCC-hh magnets
Need 16 T dipole magnets – not feasible with today’s technology  big challenge for technological development!
  In LHC, 8.3 T, with NbTi superconductors
  Cannot reach 16 T with NbTi: to be superconducting, need working point below “critical surface” in space spanned by temperature, current density and magnetic field
For 16 T, rely on future developments of Nb3Sn superconductor technology
  Alternatively, bet on high-temperature superconductors – significant technology development and cost reduction needed
Advanced research program on high-field magnets going on!
Critical surface
for NbTi

## Slide 39: Research program on 16T Nb3Sn magnets
Cos-theta
Blocks
Common coils
Short model magnets (1.5 m lengths) will be built until ~2025
Swiss contribution
Canted
Cos-theta
INFN
CEA
CIEMAT
PSI
LBNL
FNAL

## Slide 40: Next challenge: FCC-hh machine protection
0.6 MJ
HL-LHC: 680 MJ - kinetic energy of TGV train cruising at 215 km/h
FCC-hh: 8.3 GJ – kinetic energy of Airbus A380 (empty) cruising at 880 km/h

## Slide 41: Beam dump
Need beam dump to safely extract and dispose of beam in case of any failure, or the remaining beam a the end of luminosity production
  Extract beam in separate dump channel using very fast dipole magnets
Need to dispose of 8.3 GJ!
  Enough to drill 300m long hole in copper
FCC-hh CDR

## Slide 42: Beam dump
Solution: as for LHC, distribute (“paint”) beam transversely, but over much larger surface than in LHC
  Beam-dump made of low-density graphite sheets, should not exceed 1500 deg C
LHC pattern (same scale)
1m
D. Schulte, W. Bartmann

## Slide 43: Synchrotron radiation in FCC-hh
FCC-hh first hadron collider where synchrotron radiation power has potentially limiting effects
  About 5 MW power loss per beam, lost continuously around the ring!
Need about 12 MW of RF power per beam to replenish lost energy
Need to cool away the 5MW heating power of lost photons around the ring - need much more cooling power than 5 MW (Carnot process – look back at thermodynamics)
  If beamscreen kept at 2K : 3500 MW
  If beamscreen kept at 50 K: 100 MW  choose this option!
  Special beam screen design to intercept photons in a slit
FCC-hh conceptual design report

## Slide 44
FCC-ee

## Slide 45: FCC-ee
European strategy: “An electron-positron Higgs factory is the highest-priority next collider”
FCC-ee is a high-luminosity, high-precision e+e- circular collider
Several different operational energies are foreseen to perform precision measurements of Z, W and H bosons and the top quark
  Goal: provide samples of 5× 1012 Z bosons, 108 W pairs, 106 Higgs bosons and 106 top quark pairs.
Beam energy: 45-182 GeV

## Slide 46: Luminosity comparison
To reach the physics goals, need to significantly increase luminosity w.r.t. previous lepton colliders
Can reach higher luminosity than linear colliders at lower energy
  The higher the energy, the more severe limitations from synchrotron radiation

## Slide 47: FCC-ee layout
Two-ring layout with two collision points and two RF insertions
Follows footprint of FCC-hh, except around interaction points (IPs)
  Need a crossing angle at IP - cannot bend beams close to IP - this would generate photons/background
  Special layout with last bend far from IP
presently versions with 2 IPs or 4 IPs under study

## Slide 48: Synchrotron radiation in FCC-ee
Design choice: limit radiation power to 50 MW per beam (still huge!)
  RF cavities have a certain (in)efficiency  total RF power consumption for both beams up to about 160 MW
  Lower intensity at higher energy => lower luminosity
  Not critical for cooling – normal-conducting magnets
At highest energy, 182.5 GeV, loss of 9 GeV or ~5% per turn
  Not enough to replenish energy once per turn  use two RF insertions to control energy in collisions at both Ips
  Also: particles that have lost energy are overbent by the dipoles => accumulate large transverse offsets, “saw tooth” orbit if nothing is done
Example horizontal orbit with radiation
B. Härer, A. Doblhammer, and B.J. Holzer, IPAC16, THPOR003

## Slide 49: Tapering
  To avoid large transverse offsets due to over-bending: “Tapering scheme”
  Vary magnetic strengths along the ring, so that we always match the beam energy
No tapering (note: positive energy offset)
Tapering: adjusting magnetic field to beam energy
B. Härer, A. Doblhammer, and B.J. Holzer, IPAC16, THPOR003

## Slide 50: Beamstrahlung
Particles radiate not only in magnets, but also due to electromagnetic field of opposing beam: “beamstrahlung”
FCC-ee will be the first collider where beamstrahlung plays a significant role in beam dynamics
  Collider must have sufficiently large momentum acceptance to hold a particle that loses its energy in a single photon emission due to beamstrahlung.
    A particle with 2% momentum deviation must still stay within the beampipe without touching it
Power of radiated photons reaches almost 400 kW!
  Photons hit downstream vacuum chamber in localized spot – engineering challenge to dispose of heat without material damage
`
A. Ciarma

## Slide 51: FCC-ee power consumption
Beam energy (GeV) | 45.6 Z | 80 W | 120 ZH | 182.5 ttbar
RF (SR = 100) | 163 | 163 | 145 | 145
Collider cryo | 1 | 9 | 14 | 46
Collider magnets | 4 | 12 | 26 | 60
Booster RF & cryo | 3 | 4 | 6 | 8
Booster magnets | 0 | 1 | 2 | 5
Pre injector | 10 | 10 | 10 | 10
Physics detector | 8 | 8 | 8 | 8
Data center | 4 | 4 | 4 | 4
Cooling & ventilation | 30 | 31 | 31 | 37
General services | 36 | 36 | 36 | 36
Total | 259 | 278 | 282 | 359
Notes: Yearly consumption about 1.9 TWh (compare 1.2 TWh for CERN in 2016)

## Slide 52: Overall FCC timeline
Foreseen FCC timeline spans several decades
Remember: it took ~25 years from the start of the LHC design to the start of operation

## Slide 53: FCC design report
FCC-Conceptual Design Reports (completed in 2018):
  Vol 1 Physics, Vol 2 FCC-ee, Vol 3 FCC-hh, Vol 4 HE-LHC
  CDRs published in European Physical Journal C (Vol 1) and ST (Vol 2 – 4)
  EPJ C 79, 6 (2019) 474 , EPJ ST 228, 2 (2019) 261-623 , EPJ ST 228, 4 (2019) 755-1107 , EPJ ST 228, 5 (2019) 1109-1382
Summary documents provided to EPPSU SG
  FCC-integral, FCC-ee, FCC-hh, HE-LHC
  Accessible on http://fcc-cdr.web.cern.ch/

## Slide 54
CEPC / SppC

## Slide 55: CEPC (Circular Electron Positron Collider)
Chinese proposal for e+e- collider 90-240 GeV, 100 km ring
Focus on Higgs production
Two collision points, two RF insertions
Limit synchrotron radiation power to 30 MW per ring
More info: conceptual design report
CEPC design report

## Slide 56: SppC (Super proton-proton Collider)
100 km hadron collider to later be installed in the same tunnel as CEPC
Design report scenario:
  use 12 T high-temperature iron-based superconductors for high field dipole magnets => centre of mass energy of 75 TeV
  “ultimate” upgrade: 24T field, 150 TeV CMS energy
  Operating at 4.2 K
  Luminosity of 1035 cm–2 s–1
Baseline layout with 8 insertions for experiments, collimation, extraction, injection, RF
More info in conceptual design report

## Slide 57
Other Accelerator Studies

## Slide 58: Physics beyond colliders
Physics Beyond Colliders study group set up in 2016 to explore the opportunities offered by the
CERN accelerator complex and other scientific infrastructure to get new insight into some of
today’s outstanding questions in particle physics through projects complementary to high-energy
colliders (i.e. projects requiring different types of beams and experiments) and other initiatives in the world.
Projects should exploit the uniqueness of CERN accelerator complex and infrastructure.
Rare decays and precise measurements
KLEVER (K0L  π0𝜈𝜈)
TauFV@BDF: 𝜏  3μ
REDTOP (𝜂 decays)
MUonE (hadronic vacuum polarization for (g-2μ))
Proton EDM
QCD measurements
COMPASS++, DIRAC++
NA61++, NA60++
Fixed target (gas, bending crystals) in ALICE and LHCb
Non-accelerator projects
Exploit CERN’s technology (RF, vacuum, magnets, optics, cryogenics) for
experiments possibly located in other labs.
E.g. axion searches: IAXO (helioscope), JURA (Light Shining through Wall)
Long-lived particles from LHC collisions
FASER, MATHUSLA, CODEX-b, milliQAN
Hidden sector with “beam dump”
NA64++ (e,μ)
NA62++
Beam Dump Facility at North Area (SHiP)
LDMX@eSPS
AWAKE++
Report submitted
to the ESPP
Other facilities:
𝛾-factory from Partially Stripped Ions; nuSTORM

## Slide 59: LBNF/DUNE
American project, with proton accelerator at Fermilab, sending neutrinos through the Earth to a detector 1300 km away
Status:
  Far site: Construction at started Nov 2018. Currently building or refurbishing ~100 year old rock handling systems at former gold mine to be able to move ~800k tons of excavated rock to surface
  Near Site: site preparation construction contract awarded last month, design of facilities and neutrino beamline underway.
  DUNE: two prototype detector models constructed and operating at CERN.
DUNE & LBNF & PIP-II
Notes: See HL-LHC annual meeting 2019
See https://www.symmetrymagazine.org/article/november-2012/how-to-make-a-neutrino-beam

## Slide 60: ESS Neutrino Super Beam (ESSnuSB)
Doubling the ESS beam power for a second target
  linac duty cycle doubling to 8 % (RF sources, cooling)
    using new H- source
  accumulator ring (~400 m circ.) compress 2.86 ms beam pulse to few µs
    multi-turn injection, stripping H- → H+
  2nd target station with magnetic horn (350 kA)
    to deliver ~300 MeV neutrinos
Injection
Extraction
Collimation
RF

## Slide 61: Summary (1)
LHC will be upgraded to HL-LHC, and operate until 2035-2040
  Future collider projects on the table, but no decision yet
Main projects studied at CERN
  FCC-ee: circular e+e- collider
    e+e- Higgs factory is highest priority it European strategy
    conceptual design report exists; studies are ongoing to give more inputs to next European strategy
  FCC-hh: circular pp collider with ion option
    High priority by European strategy
    conceptual design report exists; studies are ongoing to give more inputs to next European strategy
  CLIC: Linear e+e- collider
    Also fulfills priority on a Higgs factory in European strategy
    Conceptual design report exists, technology and concept demonstrated
  Also: HE-LHC, FCC-eh, muon collider, LHeC
  All these machines have many interesting beam physics aspects – I could cover only a few!
Initiatives in other parts of the world
  ILC: Linear e+e- collider, possibly hosted by Japan
    Mature design with technical design report; ready to be built. Awaiting political decisions
  CEPC / SppC: circular e+e- collider followed by hadron collider, Chinese initiative
    Conceptual design report exists. China will decide
  EIC: circular electron-ion collider, to be built in the US
    Approved project with conceptual design report

## Slide 62: Summary (2)
Project | Type | Energy [TeV] | Int. Lumi. [ab-1] | Oper. Time [y] | Power [MW] | Cost
ILC | ee | 0.25 | 2 | 11 | 129 (upgr. 150-200) | 4.8-5.3 GILCU1 + upgrade
 |  | 0.5 | 4 | 10 | 163 (204) | 7.8 GILCU
 |  | 1.0 |  |  | 300 | ?
CLIC | ee | 0.38 | 1 | 8 | 168 | 5.9 GCHF
 |  | 1.5 | 2.5 | 7 | (370) | +5.1 GCHF
 |  | 3 | 5 | 8 | (590) | +7.3 GCHF
CEPC | ee | 0.091+0.16 | 16+2.6 |  | 149 | 5 G$
 |  | 0.24 | 5.6 | 7 | 266 | 
FCC-ee | ee | 0.091+0.16 | 150+10 | 4+1 | 259 | 10.5 GCHF
 |  | 0.24 | 5 | 3 | 282 | 
 |  | 0.365 (+0.35) | 1.5 (+0.2) | 4 (+1) | 340 | +1.1 GCHF
LHeC | ep | 60 / 7000 | 1 | 12 | (+100) | 1.75 GCHF
FCC-hh | pp | 100 | 30 | 25 | 580 (550) | 17 GCHF (+7 GCHF)
HE-LHC | pp | 27 | 20 | 20 |  | 7.2 GCHF
D. Schulte, 2019
1United States dollar as in January 2012
2019 – with reservation for updates
Notes: FCC-hh power: 100 MW cooling to absorb 5 MW synchrotron radiation, 30 MW to cool losses from rest-gas scattering. RF power: 12 MW / beam

## Slide 63: Future colliders?
Particle collisions 50 years ago
Particle collisions today
Particle collisions in 50 years
574 TeV Pb beams colliding at ALICE, LHC
32 cm bubble chamber with liquid hydrogen, 16 GeV pion interacting with proton
https://cds.cern.ch/record/39474

## Slide 64: Backup

## Slide 65: Some limitations on intensity and beam size
Intensity
  Limitations in beam production scheme
  Collective effects and instabilities, e.g. space charge, impedance effects, beam-beam effects
  Beam-beam effects (detrimental non-linear electromagnetic field acting on opposing beam)
  In circular lepton machines, limitations on RF power (compensate synchrotron radiation losses)
  Detrimental effects of beam losses
Beam size
  β* limited by magnet focusing strength and aperture in final focus quadrupoles
  Emittance: limitations in beam production, larger risk for instabilities, blowup (intra-beam scattering); not easy to reduce emittance of existing beam, need dedicated cooling etc
    Lepton machines: equilibrium emittance determined by accelerator lattice
    Can use damping rings to shrink emittance
  Beam-beam effects
(not exhaustive list)
Long-range
Head-on

## Slide 66: Radiated power
For full derivation, see e.g. Jackson, Classical electrodynamics, chapter 14
Very short summary
  Write down electric and magnetic fields of moving point charge (at relativistic speed)
  Power radiated is given by integral of Poynting vector over closed surface around charge, let R∞ (only 1/R terms in fields contribute)
  Integrate …. don’t be in a hurry
Result:
  Energy loss is negligible for longitudinal acceleration, except for extreme (unphysical) gradients
  For transverse acceleration (as in circular colliders), energy loss could be significant - 4th power dependence on energy and mass
  Effect is much more limiting for light particles, such as electrons/positrons
    Electrons are 2000 times lighter than protons!
… meaning…
force
force
Longitudinal
acceleration
Transverse
acceleration

## Slide 67: Radiation damping
Emitted photons along betatron trajectory – (almost) no change in angle of particle
Energy losses compensated by RF, giving purely longitudinal momentum kick
  Increases longitudinal momentum and not transverse => decrease in angle
  Smaller betatron amplitudes => smaller emittance, “radiation damping”
    Remember: emittance determines phase space area occupied by beam
On the other hand: photon emission gives small random energy (and very small angle) change => blowup, “quantum excitation”
Equilibrium between radiation damping and quantum excitation exists: equilibrium emittance
  Time needed for the beam to reach the equilibrium emittance: “Damping time”
  Equilibrium emittance is typically smaller in vertical than horizontal plane => “flat” lepton beams
M. Sands, SLAC-121 UC-28

## Slide 68: Geometric reduction factor
Bunches must collide with an angle, ”crossing angle” – otherwise we get unwanted collisions outside interaction point
  Crossing angle need to be large enough so that bunches are not perturbed by electromagnetic field at parasitic encounters (long-range beam-beam effect)
Fewer collisions when overlap is not perfect – geometric reduction factor
  Depends on crossing angle, bunch length, and transverse size
Long-range
Head-on

## Slide 69: ILC main parameters
From ILC design report

## Slide 70: CLIC parameters
Parameter | Symbol [unit] | ILC 250 | CLIC | CLIC
Centre of mass energy | Ecm [GeV] | 250 | 380 | 3000
Luminosity | L [1034cm-2s-1] | 1.35 | 1.5 | 6
Luminosity in peak | L0.01 [1034cm-2s-1] | 1 | 0.9 | 2
Gradient | G [MV/m] | 31.5 | 72 | 100
Particles per bunch | N [109] | 20 | 5.2 | 3.72
Bunch length | σz [μm] | 300 | 70 | 44
Collision beam size | σx,y [nm/nm] | 516/7.7 | 149/2.9 | 40/1
Vertical emittance | εx,y [nm] | 35 | 30 | 20*
Bunches per pulse | nb | 1312 | 352 | 312
Bunch distance | Δz [mm] | 554 | 0.5 | 0.5
Repetition rate | fr [Hz] | 5 | 50 | 50
D. Schulte

## Slide 71: Flat beams in lepton colliders
Naturally smaller vertical beam size from radiation damping
  Often true also for linear colliders due to horizontal bending in damping rings, transfer lines etc.
Beam-beam effect
  Focusing of e+e- beams due to each others’ fields => higher luminosity
  Bending of particles => synchrotron radiation, “beamstrahlung” => unwanted energy spread in collisions
To avoid energy spread and keep luminosity high: collide “flat” beams, with much smaller beam size in one plane
M.A. Valdivia García et al.,
doi:10.18429/JACoW-IPAC2019-MOPMP035
M. Sands, SLAC-121 UC-28
average number of photons per collision depends on sum of beam sizes:
Luminosity depends on product of beam sizes:

## Slide 72: CLIC cavities
To reach 100 MV/m: different type of cavity from ILC
12 GHz, 23 cm long, normal conducting
  Much worse conductor than SC, but allows reaching higher fields
  Problem: power is very rapidly lost in the walls
  Need to put in very intense and short RF pulses timed to the passage of the beam
Power flow
1/3 lost in cavity walls
1/3 in filling the structure and into load
1/3 into the beam
Average RF power about 3 kW/m
About 1 kW/m into beam
D. Schulte

## Slide 73: ILC Cavities
Superconducting cavity (Ni at 2 K)
RF frequency is 1.3 GHz, 23 cm wavelength
Length is 9 cells = 4.5 wavelengths = 1 m
Standing wave structure, achieving gradients of 31.5 MV/m
Theoretical field limit around 50-60 MV/m
  In reality, reaching about 30-40 MV/m with imperfections
Need about 8000 cavities

## Slide 74: CLIC Staged Scenario
Central complex on Prevessin site
Luminosity evolution
3 stages foreseen:

## Slide 75: Drive beam acceleration
To produce very rapid pulses: use two-beam acceleration scheme
A very long beam pulse at 4A, 140 us produced in LINAC
Use combiner rings to decrease bunch spacing of drive beam => produce very short and intense 100 A pulse
Send to decelerating structure
Drive Beam Accelerator
efficient acceleration in fully loaded linac
Power Extraction
Drive Beam Decelerator Sector
Combiner Ring x 3
Combiner Ring x 4
pulse compression &
frequency multiplication
pulse compression &
frequency multiplication
Delay Loop x 2
gap creation, pulse compression & frequency multiplication
RF Transverse
Deflectors
140 µs train length - 24 x 24 sub-pulses - 4.2 A
2.4 GeV - 60 cm between bunches
240 ns
24 pulses – 100 A – 2.5 cm between bunches
240 ns
5.8 µs
Drive beam time structure - initial
Drive beam time structure - final
R. Ruber

## Slide 76: LHC layout
8 bent sections, arcs, and 8 straight sections, “insertion regions (IRs)”
4 experiments where beams collide (ATLAS – IR1, ALICE – IR2, CMS – IR5, LHCb – IR8)
2 IRs for beam cleaning (collimation), one for RF, one for beam extraction

## Slide 77: LHC main parameters
Design luminosity of 1×1034 cm-2s-1 surpassed by more than a factor 2
Collected in total about 190 fb-1 of integrated luminosity at the high-luminosity experiments (ATLAS, CMS)
Parameter | 2018 | Design
Energy [TeV] | 6.5 | 7.0
No. of bunches | 2556 | 2808
p/bunch (typical value) [1011] | 1.1 | 1.15
Max. stored energy per beam (MJ) | 312 | 362
β* [cm] | 3025 | 55
Typical normalized emittance [μm] | ~1.8 | 3.75
Peak luminosity [1034 cm-2s-1] | 2.1 | 1.0
year

## Slide 78: Luminosity leveling
Experiments can only cope with a certain maximum event rate before saturating
In HL-LHC, the achievable peak luminosity gives a significantly higher rate
Solution: artificially reduce luminosity to stay within limit of experiments – ”leveling”
  Can be done by changing offset between beams, β* (beam size – chosen option in HL-LHC) or crossing angle
Separation
leveling
β*-leveling

## Slide 79: Collimation and machine protection
Losses from the beam are inevitable, and could cause magnet quenches or even damage
With higher intensity in the HL-LHC, need to enforce machine protection
New collimators to be installed to better protect the machine
680 MJ =
Total energy in one HL-LHC beam =
kinetic energy of TGV train at 215 km/h

## Slide 80: FCC-hh collimation
The loss of even a tiny fraction of the beam could cause a magnet quench or even damage
To safely intercept any losses and protect the machine: use collimation system
  Should be the smallest aperture limitation in the ring
500 kW of continuous losses from collisions, downstream of experiments
Design requirement: must safely handle beam loss power of 11.6 MW
  For beam lifetime of 12-minute during ~10 s from instabilities, operational mistakes, orbit jitters….
  Collimators must digest these losses without breaking, while protecting the superconducting magnets
Deploying multi-stage collimation system inspired by LHC
P. Hermes
Beam lifetime: usually defined as time needed for reduction of intensity by factor 1/e assuming losses proportional to intensity (often true, but not always)
Beam lifetime:

## Slide 81: Current working hypothesis on FCC placement
Overall layout and placement optimisation process: Many options being studied
Current baseline position based on:
  lowest risk for construction, fastest and cheapest construction
  feasible positions for large span caverns (most challenging structures)
  Total length is 97.75 km, 83 km for arcs
  12 surface sites with few ha area each

## Slide 82: FCC-hh parameter comparison
parameter | FCC-hh |  | HL-LHC | LHC
collision energy cms [TeV] | 100 |  | 14 | 14
dipole field [T] | 16 |  | 8.33 | 8.33
circumference [km] | 97.75 |  | 26.7 | 26.7
beam current [A] | 0.5 |  | 1.1 | 0.58
bunch intensity [1011] | 1 | 1 | 2.2 | 1.15
bunch spacing [ns] | 25 | 25 | 25 | 25
synchr. rad. power / ring [kW] | 2400 |  | 7.3 | 3.6
SR power / length [W/m/ap.] | 28.4 |  | 0.33 | 0.17
long. emit. damping time [h] | 0.54 |  | 12.9 | 12.9
beta* [m] | 1.1 | 0.3 | 0.15 (min.) | 0.55
normalized emittance [mm] | 2.2 |  | 2.5 | 3.75
peak luminosity [1034 cm-2s-1] | 5 | 30 | 5 (lev.) | 1
events/bunch crossing | 170 | 1000 | 132 | 27
stored energy/beam [GJ] | 8.4 |  | 0.7 | 0.36

## Slide 83: Road to 16 T magnets
For HL-LHC:
  Three full-scale Nb3Sn quadrupoles for HL-LHC built and successfully tested (US)
  Four 11T Nb3Sn dipoles initially scheduled for installation in LS2 (2019-2022) postponed due to performance issues
Small demonstrator for 14.5 T Nb3Sn dipole at Fermilab, but still a long way to go for operational magnets and industrial production
FNAL demonstrator
14.5 T Nb3Sn
from
LHC technology
8.3 T Nb-Ti
via
HL-LHC technology
11 T Nb3Sn

## Slide 84: Robustness studies
Use carbon-based materials for highest robustness, with hardware design based on LHC but developed further
Very important to study material response to the high loads
Typically 3-stage simulations:
  Generation of impact coordinates of lost particles
  Energy deposition studies
  Thermo-mechanical study using e.g. ANSYS of dynamic material response
    Study peak temperatures, deformations, melting, detachment of material
Very challenging engineering task to design these collimators

## Slide 85: Electron cloud effects
Electrons inside vacuum chamber accelerated by field from passing bunch
Electrons hit inside of vacuum chamber, releasing more electrons, in turn accelerated => ever increasing cascasde of electrons
Causes heating, potential beam instabilities, worse vacuum...
Big challenge for LHC, even more for FCC-hh
Mitigations:
  Beam screen design, surface treatment, coatings
  If nothing else helps: increase spacing between bunches
a-C
LESS
G. Iadarola
Notes: Laser ablation surface engineering (LASE), or laser-engineered surface structures (LESS) are techniques that can be applied to the beam-facing surfaces of the beamscreen in order to mitigate the electron cloud

## Slide 86: FCC-ee baseline parameters
parameter | Z | WW | H (ZH) | ttbar
beam energy [GeV] | 45 | 80 | 120 | 182.5
beam current [mA] | 1390 | 147 | 29 | 5.4
no. bunches/beam | 16640 | 2000 | 393 | 48
bunch intensity [1011] | 1.7 | 1.5 | 1.5 | 2.3
Synchrotron radiation energy loss / turn [GeV] | 0.036 | 0.34 | 1.72 | 9.21
total RF voltage [GV] | 0.1 | 0.44 | 2.0 | 10.9
long. damping time [turns] | 1281 | 235 | 70 | 20
horizontal beta* [m] | 0.15 | 0.2 | 0.3 | 1
vertical beta* [mm] | 0.8 | 1 | 1 | 1.6
horiz. geometric emittance [nm] | 0.27 | 0.28 | 0.63 | 1.46
vert. geom. emittance [pm] | 1.0 | 1.7 | 1.3 | 2.9
bunch length with SR / BS [mm] | 3.5 / 12.1 | 3.0 / 6.0 | 3.3 / 5.3 | 2.0 / 2.5
luminosity per IP [1034 cm-2s-1] | 230 | 28 | 8.5 | 1.55
beam lifetime rad. Bhabha / Beamstrahlung [min] | 68 / >200 | 49 / >1000 | 38 / 18 | 40 / 18
F. Zimmermann. M. Benedikt

## Slide 87: FCC-ee vacuum and beamscreen
Need absorbers to intercept radiated photons (present design: ~6 m spacing)
  ”winglets” in the plane of the orbit to capture photons
Continuous impact of photons can cause heating, outgassing and bad vacuum
Challenging beam screen design
  Use NEG (Non Evaporable Getter) pumps next to photon absorbers – pump away emitted gas molecules
R. Kersevan

## Slide 88: Top-up injection
Even with a 2-3% momentum acceptance, resulting beamstrahlung losses give ~18 minute beam lifetime at highest energy
  Remember: Beam lifetime is time needed for reduction of intensity by factor 1/e
  In addition, losses from radiative Bhaba scattering
Very short beam lifetime => use “top-up injection”
  Inject beams at collision energy, while colliding
    Compare hadron machines: inject at low energy, then accelerate to top energy, then put beams in collision
  Requires a booster ring – to be built in the same tunnel
Injector chain: source, LINAC(s), positron target, damping ring, pre-booster, booster

## Slide 89
Higgs cross section:

## Slide 90: Coffee break – some fruit?
Source: https://xkcd.com/1949/