## Slide 1: Brain storming HL-LHC valves in Q4
G.Bregliozzi, R. De Maria

## Slide 2: VACUUM SECTOR VALVE location
Alignment during YETS & LS
FRAS
Static
D1
Q6
CRAB
Q5
Q4
D2
Valve D1
Valve D2
Valve D2
Valve CRAB
Valves Q4
Valves Q5
Valve Q6

## Slide 3: Sector valves apertures
D1
ID 150
CRAB
ID 80
D2
ID 100
Q4 – Q5 – Q6
ID 63

## Slide 4: Available margins
D1
ID 150
CRAB
ID 80
D2
ID 100
Q4 – Q5 – Q6
ID 63
Margins calculated by WP2, thanks to R. De Maria

## Slide 5: Detailed calculations
 | VABCKNAF | VABCDDAE | VABCEEAK | CRAB1 | CRAB2 | VABCBMAB | VABCBMAC | VABCBMAB | VABCBMAC | VABTB
Diameter sector valve [mm] | 150 | 100 | 100 | 80 | 80 | 63 | 63 | 63 | 63 | 63
Minimum Aperture due RF fingers | 145.1 | 96 | 96 | 80 | 80 | 63 | 63 | 63 | 63 | 63
Concentricity Flanges [mm] | 0.25 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2
Circularity [mm] | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2 | 0.2
VSC Alignment margin [mm] | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
FRAS | 2 | 0 | 0 | 0 | 0 | 2 | 2 | 2 | 2 | 2
Aperture separation [mm] | 0 | 184.0 | 194 | 194 | 194 | 194 | 194 | 194 | 194 | 194
Final Aperture | 141.65 | 94.6 | 94.6 | 78.6 | 78.6 | 59.6 | 59.6 | 59.6 | 59.6 | 59.6
DCUM % IP5 (mm) | 83118 | 136870 | 152772 | 155062 | 161655 | 172586 | 183474 | 202742 | 211695 | 224251
Position | D1 | D2 | D2 | CRAB1 | CRAB2 | Q4 | Q4 | Q5 | Q5 | Q6
Nearby apertures [mm] | 119 | 80 | 80 | 70 | 70 | 58 | 50 | 45.1 | 45.1 | 45.1
Beam separation [mm] | 16.8 | 178.3 | 194.0 | 194.0 | 194.0 | 194.0 | 194.0 | 194.0 | 194.0 | 194.0
Offset beam – aperture [mm] | 8.4 | 2.9 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Margins w.r.t to nearby apertures [mm] | 7.1 | 5.9 | 7.3 | 4.3 | 4.3 | 0.8 | 4.8 | 7.3 | 7.3 | 7.3
The margin in Q4 is not a strong limitation, but it is not ideal because it will likely requires more re-alignments and extra care compared to the other valves.

## Slide 6
Color code:
DRF
LRM (VMTIA type bellow with standard or improved RF bridge)
RF (standard bellow and RF bridge)
Remote Alignment
Alignment during YETS / LS
CRAB-Q4
(Unless specified otherwise, assume Ø80)
Any improvement on the aperture
should not increase impedance (no DN100)
should not increase peak dose in MCBY (no increased distance with Q4)
In addition WP5 is considering TCLMB aperture reduction due to peak dose to MCBYs concerns

## Slide 7: Potential options
Mask
Valve
Q4
Fras
Fras
Today: Valves manually aligned;
2 flexible bellows, 2 platforms needed;
small aperture margins in the valves
Valves aligned once;
1 flexible bellow, 2 platforms needed;
? kCHF
1)
2)
3)
Valves and TCLMB aligned once
No flexible bellow, 1 platforms needed
? kCHF
Valves aligned once;
1 flexible bellow, 2 platforms needed
? kCHF