## Slide 1: Progress on Comparison to X-band Klystron-based CLIC Option
D. Schulte for the CLIC team
Special thanks to A. Grudiev, B. Jeanneret, Ph. Lebrun, G. McMonagle, I. Syratchev
CLIC-ACE February 3rd, 2010

## Slide 2: Rational
Two concerns exist
  A klystron-based machine can more easily demonstrate the basic RF unit
  A klystron-based machine may be cheaper at lower energies
Want to address these issues with no prejudice
Focus on 500GeV machine since this is the point where concerns are most relevant

## Slide 3: Strategy
Use current CLIC 500GeV design and simply replace the drive beam with klystrons
  Minimal changes
  May not be the optimum klystron based design
Optimise the CLIC 500GeV design for klystron, using heavily damped structures and remaining compatible with up-grade
  We limit ourselfs to structures which have been developed in the process of the CLIC 500GeV optimisation
Full optimisation of CLIC for klystrons
  Not done
  Significant amount of work
Obviously profit from JLC-X/NLC work

## Slide 4: Luminosity Comparison to NLC
 |  | CLIC 500GeV | NLC (TRC II)
Luminosity | 1034cm-2s-1 | 2.0 | 2.0
Beam Power | MW | 9.62 | 12.8
Horizontal/vertical emittance | nm | 2400/25 | 3600/40
Particles per bunch | 109 | 6.8 | 7
Bunches per pulse |  | 354 | 192
Repetition rate | Hz | 50 | 120
Lower beam current per luminosity is due to smaller vertical emittance in CLIC
Smaller horizontal emittance in CLIC allows to run at smaller bunch charges
beamstrahlung fixes optimum N/σx

## Slide 5: RF Comparison to NLC
 |  | CLIC 500GeV | NLC (TRC II) | NLC later
Loaded gradient | MV/m | 80 | 50 | 52
Structure length | mm | 230 | 900 | 600
Energy gain per structure | MV | 18.4 | 45 | 31.2
Structure input power | MW | 74.2 | 75 | 54
Inst. input RF power per GeV | GW | 4.03 | 1.666 | 1.89
RF pulse length | ns | 242 | 400 | 400
Number of bunches / spacing | ns | 354 x 0.5 | 192 x 1.4 | 192 x 1.4
Beam current in pulse | A | 2.2 | 0.8 | 0.8
RF input energy / pulse / GeV | J | 975 | 666 | 666

## Slide 6: Replacing Drive Beam with Klystrons

## Slide 7
X3.16
2x
Anticipated =0.6 for klystron
30 meters
54 MW / structure
250 MeV/unit
=0.92

## Slide 8: NLC Initial Baseline Design
75 MW Klystron (approx 2000 per LINAC)
  Solenoid focussing (25kW per klystron)
  55% efficiency
  0.0002 duty cycle (120 Hz, 1.6µs)
    Average RF output power of klystron 14.4kW
  1 kW heater power per klystron
Line type modulator
  Pulse transformer 20% wasted power with rise and fall time
  Thyratron switch, 600 W per thyratron
Overall Power Requirement per Klystron/Modulator
  55.3 kW
  246 MW/two linac (2264 klystrons)
This technology is known and works

## Slide 9: NLC Baseline Design circa 2002
75 MW Klystron (approx 2000 per LINAC)
  ppm periodic permanent magnet focussing (no solenoids)
  55% efficiency
  0.0002 duty cycle (120 Hz, 1.6µs)
    Average RF output power of klystron 14.4kW
  1 kW heater power per klystron
Solid State Modulator (1 per two klystrons)
  Pulse transformer 20% wasted power with rise and fall time
Overall Power Requirement per Klystron/Modulator(0.5)
  37.5 kW (would at 50Hz be 16.2kW)
  167 MW/two linacs
Klystron development was not finished, some problems with pulse width and high rep rate, peak power achieved
Modulators
  Many iterations were done on different types of solid state switches, but still with pulse transformer. Only recently can we confidently say that this technology is properly developed
This will be our baseline, even if work is needed to fully demonstrate it

## Slide 10: Pulse Compression Efficiency
240
480

## Slide 11
Efficiency
Efficiency [%] | NLC | CLIC | achieved
Modulator | 70 | 70 | 60
Klystron | 55 | 55 | 53-56
SLED II | 81 | 65 | (78)
Waveguide | 92 | 92 | 77
total | 28.3 | 23 | 19.5
 | Design | ready
Modulator | 90* | 86?
Klystron | 70 | 66
Waveguide 1GHz | 95 | 
Structure | 97 | 95.3
Power extraction | 87 | 
Waveguide 12GHz | 99 | 98
total | 50 | 
Consider drive beam based machine up to roughly twice as efficient
But more work to be done at 500GeV drive beam based CLIC
some inconsistencies between Igor and Bernard
Need to include other systems in comparison
e.g. magnets of drive beam complex
Drive beam
Klystron
*strongly depends
on rise and fall time

## Slide 12: Klystron Number
We use
No parameter adjustment for
  Integer number of structures per klystron pair
  Integer compression factor
To be done done once we fix a design
  But will not change the conclusions very much
  Will adjust other parameters a bit, e.g. klystron power, RF pulse length
7200 klystrons for CLIC 500 baseline

## Slide 13: Wall Plug Power
Drive beam CLIC 500
  Average total RF input power 24.3MW
  Wall plug 53.5MW (Igor), 89MW (Bernard)
Klystrons-based CLIC 500
  Average total RF input power 24.3MW
  112 MW wall plug (7200 klystrons)
NLC
  Average total RF input power 47.3MW
  Wall plug 167MW (4464 klystrons)
Note: 10% overhead included

## Slide 14: Semi-optimised Structure

## Slide 15: Reminder: 500 GeV Structure Choice
Structure has been optimised for luminosity per unit power
  Figure of merit: Lbx / N ηRF->beam
Larger emittances than at 3TeV have been assumed
Upgrade potential has been included by requiring
  Structure length be 23 or 48 cm
    i.e. a 500 GeV structure replaces 1 or 2 3TeV-structures
  RF pulse length be 240 or 480 ns
    240ns for 23cm long structures
    i.e. for 48cm long structures the drive beam decelerator can be 2 times longer
  Input power per structure is similar to 3TeV
    Did not quite make it but came close

## Slide 16: Luminosity at 500GeV
Short range wake limits bunch charge
Calculate:
Bunch charge N(G,a,f)
Luminosity L0.99(G,a,f)
Limit on long-range wake at second bunch
Depends on assumptions on
emittances
beta-functions

## Slide 17: Figure of Merit

## Slide 18: Cost Calculation
Klystron-based machine has some cost reduction
  No drive beam generation complex
  No drive beam turn-arounds
  No decelerators
But some cost increase
  Second tunnel is needed for klystron, modulators and pulse compressors
  Klystrons, modulators, pulse compressors etc.
Do not yet have a cost comparison of klystron-based vs. drive beam based machine
  More work needed
But we have an estimate of the relative linac cost for the klystron-based machine
  Allows to identify the best klystron-based machine

## Slide 19: Cost versus Gradient

## Slide 20: Linac Cost versus Luminosity per Power
CLIC drive beam baseline
Interesting structures
3
2
5
NLC is at FoM 1.7/2.15
for Εy=40/25nm

## Slide 21: Structure Parameters
Case | 2 | 3 | 5 | basel. | NLC
Average accelerating gradient: <Ea> [MV/m] | 57 | 67 | 57 | 80 | 52
rf phase advance: ∆φ[o] | 120 | 120 | 150 | 150 | 150
Average iris radius/wavelength: <a>/λ | 0.145 | 0.14 | 0.16 | 0.145 | 0.17
Str. Length: l [mm] | 480 | 480 | 480 | 229 | 600
Bunch separation: Ns [rf cycles] | 6 | 6 | 6 | 6 | 16
Bunch population: N | 5.49×109 | 4.95×109 | 7.01×109 | 6.8×109 | 7×109
Number of bunches in a train: Nb | 382 | 335 | 337 | 354 | 190
Pulse length: τp [ns] | 242 | 242 | 242 | 242 | 400
Input power: Pin [MW] | 76 | 84 | 89 | 74.2 | 54
Max. surface field: Esurfmax [MV/m] | 215.6 | 260 | 260 | 250 | 
Max. temperature rise: ΔTmax [K] | 27.6 | 43 | 42 | 56 | 
Structure efficiency: η [%] | 49.5 | 41.9 | 48 | 39.6 | ~31
Figure of merit: ηLb× /N [a.u.] | 3.41 | 2.79 | 3.81 | 3.3 | 1.7/2.15
Relative lumi in peak @ 50 Hz | 0.73 | 0.55 | 0.94 | 1.0 | 1.0
Number of 75MW-klystrons per linac | 2520 | 2358 | 2934 | 3600 | 2232
Number of structures per klystron | 4.4 | 4 | 3.75 | 4.5 | 4
Power / two linacs [MW] | 78.6 | 73.6 | 91.4 | 112 | 167
Linac cost [arb. units] | 5107 | 4559 | 5521 | 5443 | ?

## Slide 22: Structure Parameters
Case | 2 | 3 | 5 | basel. | NLC
G [MV/m] | 57 | 67 | 57 | 80 | 52
Str. Length: [mm] | 480 | 480 | 480 | 229 | 600
Δz [RF cycles] | 6 | 6 | 6 | 6 | 16
Bunch population: N [109] | 5.49 | 4.95 | 7.01 | 6.8 | 7
Bunches per train: nb | 382 | 335 | 337 | 354 | 190
Pulse length: τp [ns] | 242 | 242 | 242 | 242 | 400
Input power: Pin [MW] | 76 | 84 | 89 | 74.2 | 54
Structure efficiency: η [%] | 49.5 | 41.9 | 48 | 39.6 | ~31
Figure of merit: ηLb× /N | 3.41 | 2.79 | 3.81 | 3.3 | 1.7/2.15
Rel. lumi in peak @ 50 Hz | 0.73 | 0.55 | 0.94 | 1.0 | 1.0
Klystrons per linac | 2520 | 2358 | 2934 | 3600 | 2232
Power / two linacs [MW] | 78.6 | 73.6 | 91.4 | 112 | 167
Linac cost [arb. units] | 5107 | 4559 | 5521 | 5443 | ?

## Slide 23: Future
Documenting the current status
  Report is being prepared
  Some inconsistencies need to be fixed
    E.g. power efficiency
Establish some cost model for 500GeV
  Also needed for drive beam based machine
  Based on CLIC cost evaluation
Further work once we have a scenario for CLIC energy staging
  Emittances at 500GeV have strong impact on structure choice
  Upgrade will place many constraints

## Slide 24: Conclusion
Using current CLIC 500 design with klystrons requires 7200 klystrons
  Prediction for wall plug to RF efficiency could indicate that drive beam is twice more efficient
  But needs careful detailed evaluation on drive beam side
  RF to beam efficiency is about 33% larger than for NLC structure due to heavy damping
Reducing the gradient to reduce the klystron number leads to about 5000 klystrons
  But cost cannot be reduced strongly (<20% for main linac)
The cost for the different options does not seem to vary very strongly
  Error of the model is still large
Comparison of cost klystron vs. drive beam remains to be done