## Slide 1: CTF3 program completion and upgrade to CTF3+
Introduction
CTF3 program completion
CTF3+
Conclusion

## Slide 2
Drive Beam Generation
  Bunch train recombination 2 x 4 in DL and CR (from 3.5 to 28 A)
  Transverse rms emittance < 150 π mm mrad (combined beam)
  Bunch length control to < 1 mm rms (combined beam)
  Beam current stability ~ 0.1 % for combined beam
RF Power Production
  20.8 A beam-powered test of a single PETS (without re-circulation) in the TBTS
    135 MW (with 28 A potentially available in CLEX, the peak power can reach 240 MW)
    140 ns total pulse length
    A measured breakdown rate in the range of 10-4 or lower
    Operation of a few hundred hours at 1 Hz
  7.4(10) A beam-powered test of a single PETS with external recirculation in TBTS
    135 (81) MW circulating power or 65 (65) MW available for accelerating testing
    250 ns total pulse length, 100 (170) ns flattish-top
    A measured breakdown rate in the range of 10-4 or lower
    Operation of a few hundred hours at 5 Hz
    On/off/adjust will be demonstrated using the external reflection/recirculation system mounted on one of the PETS in TBL.
Two Beam Acceleration issues
  TBTS
    Improved measurements of power and energy loss.
    Breakdown transverse kick measurements.
    Probe Beam energy gain and beam loading tests.
  TBL
    The current schedule is to have 8 PETS installed as well as a spectrometer dump for energy spectrum studies, toward the summer 2010. This will allow to verify transport of a beam with up to 30% of the energy extracted.
CTF3 2010 main goals (feasibility demonstration)
done in 2009 – to be reestablished
close in vertical – horizontal to be done
ok in linac – to be done for combined beam
ok in linac – to be done for combined beam
up to >17A
no BDR measurements
up to >12A
no BDR measurements
operation at 1 Hz – 5 Hz tests
first measurements done – power meas. to be improved
>100 MV/m measured
only 1 PETS

## Slide 3: 2011 CTF3 main goals
Drive beam generation
  DL+CR recombination with higher current (MKS13 back)
  <150 π mm mrad emittance of combined beam
  Bunch length control to < 1 mm rms (combined beam)
  Beam current stability ~ 0.1 % for combined beam
  The above at 28 A combined beam in CLEX
Power production
  20.8 A beam-powered test of a single PETS (without re-circulation) in the TBTS
    135 MW (with 28 A potentially available in CLEX, the peak power can reach 240 MW) 140 ns total pulse length A measured breakdown rate in the range of 10-4 or lower Operation of a few hundred hours at 1 Hz
  7.4 (10) A beam-powered test of a single PETS with external recirculation in TBTS
    135 (81) MW circulating power or 65 (65) MW available for accelerating testing 250 ns total pulse length, 100 (170) ns flattish-top A measured breakdown rate in the range of 10-4 or lower Operation of a few hundred hours at 5 Hz On/off/adjust will be demonstrated using the external reflection/recirculation system mounted on the PETS in TBTS
Two Beam Acceleration issues
  TBTS
    Consistent power and energy loss measurements
    Probe Beam energy gain and beam loading tests
    Breakdown transverse kick measurements
  TBL
    Current schedule: 4 PETS installed as well as a spectrometer dump for energy spectrum studies, 8 toward the summer 2011 This will allow to verify transport of a beam with up to 30% of the energy extracted

## Slide 4: Drive Beam generation
DL+CR recombination
  set up the beam with MKS13 (rematch optics)
<150 π mm mrad emittance of combined beam
  optimize dispersion
  verify DL/CR orbit closure
  verify DL/CR optics
Bunch length control to < 1 mm rms (combined beam)
  R56 tuning in Frascati chicane and TL2 arc
  streak camera measurements in CLEX
Beam current stability ~ 0.1% for combined beam, improve slow variations
  optimize combined emittance
  systematically analyze jitter sources, find correlations
  improve overall klystron stability (at least up to best performing klystrons)

## Slide 5: TBTS 12 GHz RF installation
Accelerating structure retuned (TD24) or exchanged (T24)
12 GHz network simplified
VPA suppressed

## Slide 6: RF power
Careful calibration of 12 GHz power measurements
Breakdown rate measurements (at high BD rate - extrapolation to lower rates)
Operation w/out recirculation – may have different breakdown rate…
Test of new PETS on-off scheme (components and concept)

## Slide 7: Two beam issues
  TBTS
    Two-Beam test – 100 MV/m, at nominal structure temperature consistency between power & beam energy gain
    Drive beam, deceleration, power produced
    Probe beam, power delivered to accelerating structure, energy gain
    Beam Loading compensation experiment - by varying fast phase switches – check control of RF pulse shape with probe beam acceleration
    Measurement of breakdown kicks
    Measurement of effect of beam loading on breakdown rate
  TBL
    Measurement of deceleration / produced power
    Goal: deceleration by 30% (need 8 PETS installed) Measurement of energy spectrum
    Optics, steering algorithm studies

## Slide 8: Other issues
CALIFES
  Fully reach nominal parameters (total charge)
  Bunch length measurements (RF defl. & screen)
PHIN
  2011: test of phase coding with beam
Other
  First measurements of phase stability (PETS output, RF pickups…)
  Operation at 5 Hz (or more)
  Control of beam losses
  Coherent Diffraction Radiation (RHUL collaboration)
  …

## Slide 9: PETS on/off
Components under construction
High power tests of components and concept validation (slow movement, external reflector at input coupler) can be done from summer 2011 in the TBTS PETS
replaces recirculation loop (lower losses, faster recirculation)
PETS coupler design with integrated RF reflector
OFF, full
ON
-6dB
Reflection=0 dB
-1 dB
-3 dB
Stroke 7.7 mm
Power attenuation vs. piston position
(full reflection in OFF position)
PETS output (steady state)
Structure input
ON
OFF, full
Stroke 7.7 mm
0.26
ON
OFF

## Slide 10: TBL completion
4 tanks installed by March 2011
4 more installed in summer 2011 => Demonstration with 8 PETS >30% deceleration
Another 4 PETS in shutdown 2011-2012
4 more with input coupler for priming
Perform full experimental program afterwards >50% deceleration
Detailed program in talk by Steffen Döbert

## Slide 11: Schedule 2011
Early start of Linac + CR/DL (combination setup + studies)
Initial PHIN run for phase coding demonstration
CLEX stop in summer for installation of
  4 more PETS
  PETS ON/OFF mechanism
  different accelerating structure ?

## Slide 12: Increased run-time
need higher statistics for BDR measurements
=> increase repetition rate
  test of 5 Hz running with 4x beam to CLEX TL2 spectrometer successful
    klystrons OK at 5 Hz
    radiation well within limits (to be verified when machine drifts)
  shielding in CLEX towards CTF2 added
  BPM readout at 5 Hz not operational, CO work in progress
=> running over nights and week-ends
  RF compression feedback reduced slow machine drifts drastically
  interlocks (losses, radiation) are in place
  CCC supervision for beam started
  could develop repetition rate feedback

## Slide 13: Validation of DB scheme
Parameter | Unit | CLIC nominal | Present state | Objective 2011 | Objective 2012
I initial | A | 7 | 5 | 5 | 5
I final | A | 100 | 28 | 30 | 30
Qb | nC | 8.4 | 4 | 2.5 | 2.5
Emittance, norm rms | p mm mrad | ≤ 150 | 100 (end of linac) ~ 150 (y, comb. beam) | ≤ 150 (comb. beam) | ≤ 150 (comb. beam)
Bunch length | mm | ≤ 1 | ≤ 1 (end of linac) | ≤ 1 (comb. beam) | ≤ 1 (comb. beam)
E | MeV | 2400 | 120 | 120 | 150
Tpulse initial | µs | 140 | 1.4 | 1.4 | 1.4
Tpulse final | ns | 240 | 140 (240) | 140 (240) | 140 (240)
Beam Load. Eff. | % | 97 | 95 | 95 | 95
Deceleration | % | 90 | 3 | 30 | 50
Phase stability @ 12 GHz | degrees | 0.2 | 1 | ? | 
Intensity stability |  | 7.510-4 to few 10-5 | 6 10-4 (linac) few 10-3 (DL) 10-2 (combined beam) | 10-3 (combined beam) | 

## Slide 14: CTF3 limitations
Combined beam current, limited to ~ 30 A (possibly more for shorter pulses)
Pulse length limited to 140 ns (instead of 240 ns) @ 30 A – alternative: 15 A, < 280 ns
Total drive beam peak power (now ~ 3.5 GW – CLIC 240 GW)
DBA
CR
DL
TBTS
CLEX
CTF3
CTF2
#1
#2
#3
<30A
14 A
4 A
140 ns
< 280 ns
~ 1200 ns

## Slide 15: CTF3 beam power upgrade
Present
2
3
4
5
6
7
8
9
10
11
12
13
14
15
girder
Ultimate ?
2
3
4
5
6
7
8
9
10
11
12
13
14
15
girder
About 120 MeV
for final beam current of about 28 A
Total beam power 3.3 GW
e.g., enough to feed
24 accel. structures
(final drive beam energy 50 MeV)
About 200 MeV
for final beam current of about 28 A
Total beam power 5.7 GW
e.g., enough to feed
50 accel. structures
(final beam energy 50 MeV)
45 MW
35 MW

## Slide 16: CTF3 beam power upgrade
Assumptions
  Need 3 additional power stations
  All modulators/klystrons upgraded to 45 MW nominal power
  RF pulse compression factor ~ 2 (about 38 MW/SICA input, including operational limits and losses)
  1.3 µs long RF pulse (needed for combination factor 8)
  Keep girder 10 for diagnostics (emittance, momentum, energy spread)
  Need new drive beam acc. structures
Further possibilities ?
  Add other power stations & structures (girder 10, CT line ?)
  Further upgrade klystrons
  Combine klystrons by two, double their number (space problem, maybe exceed structure limits…)

## Slide 17: CLIC modules in CLEX
Integration of test modules in CLEX
A. Solodko
3 modules to be tested with beam and RF
module layout compatible with CLEX requirements:
  double length PETS feeding two accelerating structures
  accelerating structures with all technical systems and damping features
First module to be ready by end of 2011

## Slide 18: PROTOTYPE Module - CLEX: Phase 3
3.1 / Nominal power and pulse length for 1 PETS and 2 AS
Recirculation
12 A and 240 ns
3.2 / No modifications on the module type 0 HW
No Recirculation
Current increase from 12 A to 19.2 A
Pulse length reduced from 240 ns to 140 ns
Phase 3 foresees the installation and testing of 1 module type 0: AS equipped with WFM (5 um accuracy / few WFM in the 1st powered AS)

## Slide 19: PROTOTYPE Module - CLEX: Phase 4
No modifications on the module type 0
Addition of new modules - type 1 and 4
Increase of current from 19.2 A to 22 A
Modification on the module type 1
(2 CLIC PETS)
Needed klystrons and PC

## Slide 20: Plans for TBL beyond 2012
Upgrade to TBL+ as a test facility relevant for CLIC TDR work
12 GHz power production for structure conditioning
  less pulses than klystron test stand but:
    use of ON/OFF mechanism of PETS
    precondition with klystron and then with beam
    => develop conditioning scenario for CLIC conditioning with beam
    conditioning of PETS
Working experience with a real decelerator
  Power production as a function of beam parameters, alignment, stability, pulse shape, phase stability, beam loses, failure modes
Test bed for PETS development, ON/OFF, new designs, etc
Beam dynamics studies, pulse shaping, feedbacks, etc
=> more in talk by Steffen Döbert

## Slide 21: Phase measurements & feed-forward
DRIVE BEAM
LINAC
CLEX
CLIC Experimental Area
DELAY
LOOP
COMBINER RING
10 m
Phase & energy measurement
Fast feed-forward kicker in final compression line
Phase monitor being developed (FP7) for 2012
=> more in following talk of Piotr Skowronski

## Slide 22
 | 2010 |  |  |  | 2011 |  |  |  | 2012 |  |  |  | 2013 |  |  |  | 2014 |  |  |  | 2015 |  |  |  | 2016 |  |  | 
 | 1 | 2 | 3 | 4 | 1 | 2 | 3 | 4 | 1 | 2 | 3 | 4 | 1 | 2 | 3 | 4 | 1 | 2 | 3 | 4 | 1 | 2 | 3 | 4 | 1 | 2 | 3 | 4
CTF3 TBTS operation | inst. | 1-2 structures, beam loading, breakdown kick |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
CTF3 TBL operation | inst. |  | Deceleration 8 PETS |  | final decelerator test (16 PETS, 50%) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Modules lab | initial tests, installation 2 modules |  |  |  | further tests, installation 4 modules |  |  |  | testing |  |  |  |  |  |  |  | pre-series production, industrialization |  |  |  |  |  |  |  |  |  |  | 
Modules CTF3 |  |  |  |  |  |  |  | 1 module inst. |  | testing 1 module |  | 3 modules inst. |  | testing 3 modules |  |  |  |  |  |  | > upgrades? |  |  |  |  |  |  | 
CTF3 phase feedback | design, hardware tests |  |  |  |  |  |  | installation |  | testing |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
CTF3 TBL+ |  |  |  |  |  |  |  | installation |  | commissio-ning |  | RF testing, potential upgrades |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
CLIC DB injector & linac / CLIC 0- | design |  |  |  |  |  | component construction (injector) |  |  |  |  | installation (inj) |  | commissioning (inj) |  |  | staged upgrade & testing |  |  |  |  |  |  |  |  |  |  | 
RF structures construction | precision metrology, fabr. procedures |  |  |  | up to 40 structures built, establish precision machining at CERN or elsewhere, 5 mm tolerances achieved |  |  |  |  |  |  |  |  |  |  |  | more than 200 structures built, final cost optimization, pre-series with industry |  |  |  |  |  |  |  |  |  |  | 
RF test infrastructure | CERN test stand inst. |  | CERN test stand testing and upgrades (at least two slots) |  |  |  |  |  | continue testing with increased capabilities, CERN or elsewhere, up to 10 slots |  |  |  |  |  |  |  | testing, up to 200 accelerating structures plus PETS and RF components |  |  |  |  |  |  |  |  |  |  | 
Prototypes of critical components | technical choices, design |  |  |  |  |  |  |  | construction, hardware tests |  |  |  |  |  |  |  | finalization, performance & cost optimization, industrialization for large scale components |  |  |  |  |  |  |  |  |  |  | 
Other systems, Civil Engineering… | detailed program definition |  |  |  | first phase (CDR baseline) |  |  |  |  |  |  |  |  |  |  |  | second phase (new baseline ?, project implementation plan) |  |  |  |  |  |  |  |  |  |  | 
Beam physics studies | CDR activities, feasibility studies |  |  |  |  |  | Performance and cost optimization |  |  |  |  |  |  |  |  |  | new baseline? Preparation for commissioning, operational scenarios… |  |  |  |  |  |  |  |  |  |  | 
TD phase - Preliminary schedule

## Slide 23: Beyond CTF3
Plan to build one full-scale drive beam injector (up to ~ 30 MeV).
  Thermionic + bunching system solution preferred w.r.t. photoinjector (possibly build both)
  Time scale around 2013 => see Steffen Döbert’s talk
Need as well at least a few drive beam accelerator modules (klystron/modulator/structure) => see talks by Erk Jensen + ?
Present plan – add modules to arrive gradually at about 200 MeV (first bunch compression stage / 10% of average CLIC beam power))
Total cost: ~ 100 MCHF (including manpower)

## Slide 24: Resources for CTF3+
Project | Time- span | Estimated budget (MCHF) | 
Energy upgrade | 2011-2013 | 5 | 2 MKS +2 ACS
Rep. rate | 2011-2013 | 3 | 10 Hz
Consolidation, stability, operation | 2011-2016 | 8 | feedbacks, spares, etc
Phase feedback + monitor | 2011-2014 | 2 | 
TBL+ | 2011-2016 | 4 | Modified tanks + testing infrastructure
Two-beam modules | 2013-2016 | 14.5 | 17 modules
CLIC DB injector | 2011- 2016 | 28 | 12 x1 GHz rf stations
Warning: Very rough estimates for time being

## Slide 25: Conclusion
We have a plan to complete CTF3 and extend it for TDR type of studies
Some choices have to be made how much beam power is needed,
how many modules are reasonable
how many testing slots in TBL
do we want a production facility or dedicated experiments
We would like your input for this !

## Slide 26: Spares

## Slide 27: Phase coding for PHIN
NEW scheme
Modulator 1
Switching with one modulator
280 ns
Clean cutting between pulses
Optimization of 2 modulator scheme by end of January/2011
Integration into laser system for test planned in PHIN February/2011
Streak measurements on laser and electron beam February/ 2011
Delay optimization with <1ps accuracy
M. Csatari Divall

## Slide 28: Feasibility demonstration
R1: Feasibility
  R1.2: Validation of drive beam generation scheme with fully loaded linac operation
  R1.1: Test of damped accelerating structure at design gradient and pulse length
  R1.3: Design and test of damped ON/OFF power extraction structure