## Slide 1: Beam Gas Curtain (BGC) Design and Plans
Gerhard Schneider for BGC Collaboration Team
Beam Gas Curtain (BGC):
baseline instrument for on-line monitoring of the overlap between proton and electron beams in the hollow e-lens and as a general non-invasive profile measurement diagnostic
12th HL-LHC collaboration meeting 20 09 2022 Uppsala

## Slide 2: Content
BGC Collaborations
BGC v3 Tunnel installation Phase 1
BGC v3 on Electron Beam Test Stand (EBTS)
BGC v3 Tunnel installation Phase 2
BGC v4 final instrument
Notes:
BGC v3: Demonstrator instrument
BGC v4: Final instrument for Hollow Electron Lens
Presentation Share
My presentation: Hardware, Installations and Planning
Presentation Ondrej Sedlacek: Tests and Physics

## Slide 3: BGC Collaborations
BGC Collaboration with deliverable v3
  Liverpool University/Cockcroft Institute: KE3298/BE/HL-LHC Addendum Nr. 3
  GSI: KE3036/BE Addendum Nr. 10
BGC v4 final instrument
  In-kind contribution Liverpool University/Cockcroft Institute (UK2), CERN EDMS 2369616
  CERN supply: HL-LHC infrastructure for LHC operation

## Slide 4: Beam Gas Curtain principle
5 bar gas
Expansion after nozzle to supersonic jet
Background pressure 10-3 mbar
1st Skimmer: Background pressure 10-5 mbar
2nd Skimmer: Background pressure 10-7 mbar
3rd Skimmer: Background pressure 10-9 mbar
Interaction with Proton/Electron beam
4th Skimmer
(Gas return blockage)

## Slide 5: BGC tunnel installation today (Phase 1)
Optical system
3x Gate valves
BGI gas injection system
Local BGI Penning
Gas injection for distributed gas
Local Racks
BGC cables for Phase 2
Phase 2 gas injection valves

## Slide 6: Summary LHC tunnel installations (Phase 1) resulting from approved ECRs
ECR 2025553 + ECR 2363497 = LS2 + YETS 21/22
Done in LS2 and YETS 21/22
BGC Installed in the LHC
Gas line is pulled from the gas bottle to the BGC (for Phase 2)
Gas line valves installed
Compressed air for the valves pulled
Power cables pulled
Fibre optics cable pulled and rack installed
BGI gas system and control rack now operational on BGC, Injection made
Optical system installed and operational

## Slide 7: V3 Phase 1: Operational for distributed gas injection (more see Ondrej)
Penning VGPB.368.5L4.B | Penning BGC | Penning VGPB.443.5L4.B
1.1E-9 mbar | 1.5E-9 mbar | 6.2E-10 mbar
9.0E-9 mbar | 1.0E-8 mbar | 4.4E-9 mbar
2.0E-8 mbar | 2.2E-8 mbar | 1.0E-8 mbar

## Slide 8: A big thanks to all of you helped that we now can take data with the LHC beam and with distributed gas in the 2022 Run!! First Neon gas injections with LHC beam were done with the BGC via the BGI gas injection system, looking forward for more data!

## Slide 9: Phase 2 instrument with Gas Curtain delivered from Cockcroft Institute/Liverpool University to CERN in March 2022  This is the real thing…
Dump side between beam pipes
Interaction chamber  Sister/Brother chamber already installed in the LHC
E-gun in lab instead of LHC beam or EBTS beam
Gas injection chamber  Passage side in tunnel
Optical system  parallel system already installed in LHC
3x Gate valves

## Slide 10
16 mm
22 mm
22.5 mm
Measurements
Simulation
… and it works
Courtesy: Ondrej Sedlacek
Observed E-beam v3 at CERN

## Slide 11: Phase 2: Go from Laboratory Vacuum system to LHC compatible Vacuum System
TE-VSC and EN-CV colleagues actively working on:
BGC vacuum aspects relevant for LHC operation (Gas loads, pump-down times…)
LHC compatible operation (Start, operation and stop…)
Implementation in the LHC (last cables requested)
Ordering PLC and other control equipment ongoing
Assure safe operation (separate compressed air arrival for BGC valves, local solution without de-pressurisation the compressed air mains)

## Slide 12: Before installation in the LHC: Test on Electron Beam Test Stand (EBTS) Current situation; Electron Gun & Collector Current
Notes: Current phase of the EBTS. Primary assets are the Electron Gun, BDB and Collector.
There is also a Sector Valve and x4 Solenoid magnets.

## Slide 13: BGC on Electron Beam Test Stand (EBTS)
Install BGC on EBTS. Foreseen installation: October 2022 followed by operation
(Operational Programme  see Ondrej)

## Slide 14: Phase 2 Installation in LHC
Remove:
  BGI gas system
  BGI control rack
Install:
  6 primary pumping units
  Gas injection system
  Gas dump chamber
  5 TMPs:
    Gas injection system with 3 TMPs
    Gas dump chamber with 1 TMP
    1 TMP directly on the interaction chamber
  Compressed air line to the valves
  3 solenoids for the gas injection valves
  Add independent compressed air supply for BGC vacuum pumping system
Connect everything to power and controls

## Slide 15: Phase 2 to be installed in green
12th HL-LHC Collaboration Meeting Uppsala 20 09 2022

## Slide 16: Timeline v3
Phase 2 BGC validation operation ongoing
Change from laboratory vacuum system to LHC compatible system ongoing. Objective: Finish by Q4 2022. Challenging controls supply due to global events.
Validation on EBTS as from October 2022. Foreseen operation about 2 month
Very challenging but not impossible objective for YETS 2022/23 tunnel installation, not all cards in our hands. Alternative installation in YETS 23/24, which is the more likely scenario

## Slide 17: BGC V4: Design constraints
Space
Notes: QRL – cryogenic Ring line. Cryogenic supply line to supply helium to the magnets in the tunnel.
For Colling system
What is inside? Cold Helium

## Slide 18: BGC V4 Installation environment P4 right
BGC location
HEL CryoMagnets
QRL
2nd beam pipe
Helium reservoir
Notes: QRL – cryogenic Ring line. Cryogenic supply line to supply helium to the magnets in the tunnel.
For Colling system
What is inside? Cold Helium

## Slide 19: BGC V4 Space constraints Point 4 Right
QRL
HEL Top view
200mm
4x Rods in Bellows to compensate for magnets force
2nd beam pipe
793mm
HEL cut in BGC location
412mm
381mm
525mm
679mm
Helium reservoir
Girder
QRL
2nd beam pipe
Notes: QRL – cryogenic Ring line. Cryogenic supply line to supply helium to the magnets in the tunnel.
For Colling system
What is inside? Cold Helium

## Slide 20: BGC V4 Space constraints Point 4 Right
Edge welded Bellow
Rod
Thermal shield
Thermal shield
≈ -269 ℃
≈ 20 ℃
≈ 20 ℃
Insulation vacuum
Notes: QRL – cryogenic Ring line. Cryogenic supply line to supply helium to the magnets in the tunnel.
For Colling system
What is inside? Cold Helium

## Slide 21: BGC V3/V4 Space comparison
104mm
3rd skimmer
IP
2nd skimmer
1st skimmer
nozzle
155mm
222mm
135mm
Version 3
Version 4 proposal
3rd skimmer location range
IP
3rd skimmer
2nd skimmer
1st skimmer
nozzle
17
17
4mm
4mm
Nozzle to IP: 280mm
Nozzle to IP: 378mm
Notes: QRL – cryogenic Ring line. Cryogenic supply line to supply helium to the magnets in the tunnel.
For Colling system
What is inside? Cold Helium

## Slide 22: V4 related to Space: Optimise conductances to remove injected gas
2nd beam pipe
10-3 mbar
10-5 mbar
10-7 mbar
Notes: QRL – cryogenic Ring line. Cryogenic supply line to supply helium to the magnets in the tunnel.
For Colling system
What is inside? Cold Helium

## Slide 23: BGC V4 in HEL
Gas Injection Chamber
Dump Chamber
Central Chamber
Optical System
(possibly with mirror)
Beam direction
Gate Valve
Gate Valve
TMP
TMP
3x Turbo Molecular Pump (TMP) (3rd not shown)
Helium reservoir
2nd beam pipe
QRL
Gate Valve
4x Rod
Notes: QRL – cryogenic Ring line. Cryogenic supply line to supply helium to the magnets in the tunnel.
For Colling system
What is inside? Cold Helium

## Slide 24: BGC V4 Installation Mock-up: Procedure checked
Notes: QRL – cryogenic Ring line. Cryogenic supply line to supply helium to the magnets in the tunnel.
For Colling system
What is inside? Cold Helium

## Slide 25: Summary v3
Phase 1 BGC installation objectives for distributed gas fully achieved, operation with Neon injected with LHC beam has started.
Phase 2 BGC installation underway
  BGC v3 Phase 2 instrument delivered to CERN and fully operational for laboratory use
  EBTS test required prior to installation
  Change to LHC compatible vacuum system under way
  Approval by LHC management after proof of vacuum compatibility
  Additional cable request by VSC for YETS 22/23 done, minor activity
  Additional compressed air connection in tunnel addressed
  Objective for full installation in YETS 22/23, very challenging. Alternative YETS 23/24

## Slide 26: Summary v4
In-kind contribution from Liverpool/Cockcroft institute (UK2)
Engineering well advanced
Further challenges to optimise conductance on gas injection side

## Slide 27: Questions?

## Slide 28: BGC Phase 1

## Slide 29: BGI Gas injection system next to BGC

## Slide 30: Final BGC version (V4) in HEL, here 4R

## Slide 31: Design of final instrument (V4) for HEL well in Progress Challenge: Space