## Slide 1: ITER History and Layout Fusion Technology for ITER Part 1 (ITER at CERN Lecture 3)
Scientific Lectures
CERN
14. April 2011
Guenter Janeschitz
ITER Organization, Route de Vinon, CS 90 046 13067 St Paul Lez Durance Cedex, France
Notes: 1

## Slide 2: Outline Lecture 3 (14th April 2011)
A short History of ITER
Basic Parameters and Features of a Tokamak
The Layout of a Reactor Class Fusion Machine
  The large ITER Machine (1.5 to 3.0 GW Fusion Power)
  The reduced size ITER of today (0.5 GW Fusion Power)
Fusion Technology, Challenges, ITER Design
  Magnets
  Vessel & In Vessel Components
  Remote Maintenance & Hot Cell
Summary of lecture 3

## Slide 3: Outline Lecture 4 (15th April 2011)
Fusion Technology, Challenges, ITER Design continue
  Cryostat and Thermal Shield
  The D-T Fuel Cycle
  Plasma Heating Systems and Plasma Diagnostic Systems
  The Cryo system
Status of the ITER Project
Which Technologies are needed for a DEMO Reactor
  The T- Breeding Blanket & a He Cooled Divertor
  Structural and Functional Materials for the In Vessel Components
  Improvements in H&CD, in RH, and possibly in Magnets
What if Mankind needs Fusion Faster ?
  The Apollo like program – the Ultra Fast Track to Fusion Energy
Summary

## Slide 4
A short History of ITER

## Slide 5: ITER Cooperation
1978 (November): First “Steering Committee of the INTOR Workshop” convenes in Vienna. INTOR was the first attempt at building a truly international fusion programme. INTOR was very close to ITER in its concept.
1985 (November): At Geneva Superpower Summit in 1985 US president Reagan and Secretary General Gorbatchev propose an international effort to develop fusion energy... "as an inexhaustible source of energy for the benefit of mankind". This is the first political step to the ITER programme

## Slide 6: ITER Cooperation
1988-1990 ITER CDA ( Garching)
1992-1999 ITER EDA ( San Diego, Garching, Naka).
USA leaves ITER cooperation .The EU ,Japan and Russia decide to continue.
1999-2001 Redesigning of ITER from Ignition to Q=10 ( 21MA to 15 MA)
2001: ITER Council approves design of the ITER machine. Symbolically, the meaning of ITER is changed. It is not the acronym of International Thermonuclear Experimental Reactor anymore, but the Latin word “iter” which means “the way”.
2005 (June): Decision on building ITER in Cadarache is reached on 28th June at ministerial meeting in Moscow
21/11/2006: ITER Agreement is signed at Elysée Palace in Paris by the seven Parties: China, Europe, India, Japan, Korea, Russian Federation and the United States of America

## Slide 7
21/11/2006: ITER Agreement Signed

## Slide 8
Basic Parameters and Features of a Tokamak

## Slide 9: Basic parameters of a Tokamak
R = Major Radius (distance machine center to plasma center
a = minor radius ( radius of plasma)
e = Aspect Ratio is R/a
k = Elongation is b/a (plasma center to top or bottom / minor radius)
d = Triangularity Ratio of c / a – see picture
TF = Toroidal Field
PF = Poloidal Field
S = Separatrix
CS = Central Solenoid – Transformer
VS = Vertical Stability (e.g VS – coils)
tE = Energy Confinement Time (1/e time)
ne = Density (1020 m-2)
Ti = ion temperature
R
b
a
c

## Slide 10: A Modern Tokamak – Magnetic Field Structure
Divertor
Transformator
Poloidal field coils
Vertical Field
Magnetic well
Radial control
Radial Field
vertical control
TF- Coils
VS-Coils

## Slide 11
antenna
wave guide
HIGH FREQUENCY HEATING
plasma current
OHMIC HEATING
ion source
neutraliser
„ion cemetery“
high energetic atoms
accelerator
transmission line
source: Forschungszentrum Jülich
ICRH
ECRH
HEATING BY NEUTRAL BEAM INJECTION
ionized atoms
Methods for the heating of a tokamak plasma

## Slide 12: Energy and particle Transport is governed by turbulence
Radial size of turbulent structures can be reduced by ExB shear, by magnetic shear and by zonal flows produced by the turbulence itself
Ion Turbulent energy transport sets in at a critical temperature gradient which depends on the local temperature

## Slide 13: Confinement Scaling Relation
Extrapolation of global thermal confinement time to ITER-FEAT (R = 6.2 m), using the IPB98(y,2) scaling (tE=3.9s)
  Only Q= 10 possible, no ignition
  For ignition R~ 8 m and tE >5.7 sec needed
ITER represents an extrapolation of a factor ~4 beyond existing database

## Slide 14
The Layout of a Reactor Class Fusion Machine
  The large ITER Machine
  The reduced size ITER – present ITER

## Slide 15: How do we size a Reactor class Fusion machine (1)
Trippel Product Diagram

## Slide 16: How do we size a Reactor class Fusion machine (2)

## Slide 17: A System Code finds self-consistent Design Options
A typical flow diagram of such a system code can be seen on the right side
The system code combines physics rules with engineering design knowledge
It can only be used if a more detailed design of a particular type of machine has been done and the experience / knowledge has been implemented
Beside a set of non linear equations representing physics and engineering rules / knowledge, the system code contains also a cost algorithm which is based on the industrial cost estimates established for ITER-1998

## Slide 18: Typical results from the System Code Study
The main machine parameters and the cost change with increasing aspect ratio in the following way:
  The toroidal Field, the Magnetic Energy increase with Aspect Ratio
  The minor radius, The major Radius and the Plasma Current decrease with Aspect Ratio
  However, the cost of the machine stays constant over most of the Aspect Ratio range investigated

## Slide 19
The Large ITER Machine 1998

## Slide 20
The Large ITER Machine

## Slide 21: Requirements for ITER-98 and present RC-ITER
Inductive Performance ITER-1998:
  achieve controlled ignition and extended burn (>1000 sec)
  An average neutron wall loading of > 1 MWm-2
    i.e. ~ 1.5 GW of fusion power
Steady State Performance:
  Demonstrate Steady State as an ultimate Goal (~ 10000 sec)
Demonstrate Fusion Technology :
  Super Conducting Coils
  High Heat Flux Components
  Shielding / Breeding Blanket
  Remote Handling
Inductive Performance ITER-FEAT:
  Driven burn with Q = 10 for > 400 sec, (ignition not precluded)
  Neutron wall loading > 0.5 MWm-2
    i.e. ~ 0.4 GW of fusion power
  Cost < 50% of ITER-1998
Steady State Performance:
  Achieve Steady State with Q = 5 as a goal (~ 3000 sec)
Demonstrate Fusion Technology :
  Super Conducting Coils
  High Heat Flux Components
  Shielding / (Breeding Blanket)
  Remote Handling

## Slide 22: Comparison of ITER-98 with a typical RC-ITER
In order to reduce
the cost by ~ 50%
and to achieve
Q = 10 the machines
major radius is
reduced from 8.2 m
to ~ 6 m
The general concepts for the main machine components remains largely unchanged which allows to make full use of the R&D performed during the EDA
However, a simple downscaling of ITER-98 is not possible !!

## Slide 23: Cross section of ITER and machine parameters
Parameters of ITER-FEAT
Inductive pulse length ~ 400 sec

## Slide 24: What were / are the major Challenges in Physics ?
The solution to the divertor peak heatflux problem (solved / ongoing)
  The development of the radiative divertor heatflux from 40 MWm-2 to < 20 MWm-2
The prediction of the ITER Energy Confinement and thus the definition of its size (solved / ongoing) –> major radius = 6.2 m
  Shortfalls of scaling as a predictive tool => Physics understanding needed !
The impact of magnetic ripple on energy confinement (solved / ongoing)
  Impact low at ripple < 0.5% at separatrix, however, not understood !!
The developing understanding of ELMs and RWM and their stabilisation (solved / ongoing)
  In vessel coils foreseen in ITER – physics not understood – risk !
The definition of a credible steady state scenario (solved / ongoing)
  Development needs new generation of Tokamaks (EAST, KSTAR, JT60SA, ITER)

## Slide 25
ITER Operation Space in H-mode
-> Integrated Plasma Model
  G. Pacher, H. Pacher, Y. Igitkhanov, M. Sugihara, G. Janeschitz
Q=5, LH transition, low temperature limit on alpha power, auxiliary power, edge density limit
ELM Control / Mitigation
ELM Mitigation by edge ergodization
  by RMP coils
  see foreseen ELM- coil layout below

## Slide 26: In-Vessel Coils for VS and ELM control
ELM Coils
(3 per sector)
Upper VS Coil
ELM Feeders
(27 sets in Upper Ports)
Upper VS Feeders
(1 set in 4 upper ports)
Lower VS Feeders
(2 sets in 2 lower ports)
Lower VS Coil
Purpose: Vertical Stability, ELM suppression
See also Lecture 2 ( D. Campbell) – H-mode

## Slide 27
The Technological Challenges which had to be overcome
The resulting ITER Design
The ongoing Procurement - Construction

## Slide 28: The ITER Tokamak (500 MW of Fusion Power)
Central Solenoid (6)
(Nb3Sn)
Toroidal Field Coils (18)
(Nb3Sn)
Poloidal Field Coils (6)
(NbTi)
Feeders
(NbTi)
Cryostat
(29 m high x 28 m dia.)
Thermal Shield
(4 sub-assemblies)
Vacuum Vessel
(9 sectors)
Blanket
(440 modules)
Divertor
(54 cassettes)
In-vessel Coils
Feeders (31)
(NbTi)

## Slide 29: ITER Technology Challenges / Developments
The development of high field large superconducting magnets
  Requirements seemed unfeasible 20 years ago (ongoing / solved)
The development of Divertor High Heatflux Components
  A large step in development to achieve 20 MW/m² (ongoing / solved)
The development of Remote Maintenance
  Thought to be impossible by engineers from nuclear industry (ongoing / solved)
The development of the DT fuel Cycle
  A key for ITER and DEMO – a challenge up to today (ongoing / solved)
The development of Heating and Current Drive systems
  A challenge for all systems envisaged, not fully solved today
The development of ITER compatible Diagnostics
  A step from laboratory type systems to a reliability similar to space

## Slide 30
Magnets

## Slide 31
The ITERMagnet System
6 PF Coils (EU & RF)
CS Coils – Stack of 6 (US)
31 Feeders (CN)
9 Pairs of Correction Coils (CN)
18 TF Coils
(EU & JP)
Facts
- 48 superconducting coils (~9800 tons)
- 11.8 T (peak TF field)
- 68 kA (peak current)
- Stored energy – 51 GJ
Technical Challenges
- Large size
- Tight tolerances
- High field performance
- Conductor and magnet manufacturing

## Slide 32: Magnet Development: Current-Field-Chart (Lorentz-Force)
TFMC = Toroidal Field Model Coil CSMC = Central Solenoid Model Coil
Superconducting coils from earlier experiments
0
1
0
0
0
0
2
0
0
0
0
3
0
0
0
0
4
0
0
0
0
5
0
0
0
0
6
0
0
0
0
7
0
0
0
0
8
0
0
0
0
Current
[
A
]
4
5
6
7
8
9
1
0
1
1
1
2
1
3
1
4
Field
[
T
e
s
l
a
]
J
a
p
a
n
J
a
p
a
n
J
a
p
a
n
J
a
p
a
n
J
a
p
a
n
J
a
p
a
n
U
S
G
e
r
m
a
n
y
F
r
a
n
c
e
E
U
,
S
c
h
w
e
i
z
J
a
p
a
n
,
U
S
W
7
-
X
T
F
-
I
T
E
R
T
F
I
C
T
F
M
C
-
P
h
a
s
e
I
C
S
-
I
T
E
R
C
S
M
C
G
e
r
m
a
n
y
Phase II
Situation at the beginning of the 90th
Situation today – gives confidence to be able to built the ITER magnets

## Slide 33
ITER Conductors
Cooling Spiral
ITER coils are wound from Cable-In-Conduit Conductors (CICC’s), relying on superconducting multifilament composite strands mixed with pure Cu strands/cores.
Fakts:
~90 km / 400 t of Nb3Sn conductor
(The biggest Nb3Sn conductor procurement in history)
- ~150000 km of strand (15 x around Earth)
- Operates at ~5 K
- 11.8 T (peak TF field)
- 68 kA (peak TF current)
Stainless Steel Conduit
X-section of 70kA ITER TF Conductor (CEA)
Final-Stage Cable
(ASIPP)
(NFRI)

## Slide 34
Jacketing Lines Status
CN, JA and RF have set up their jacketing lines; EU and US will award contracts in oncoming 2 months; KO is negotiating with JA.
CN Jacketing Line
at ASIPP
JA Jacketing Line
at NSE
RF Jacketing Line
at UNK

## Slide 35
TF Conductor Production Status
JA has completed jacketing of 760 m Cu dummy cable and first three superconducting cables (100m and 2 x 420m).
Welding
& Leak Checking
Cable Insertion
Compaction
& Spooling
Notes: 35

## Slide 36
TF Winding Pack
TF Coil Design (1)
Inner Leg Cross Section
TF – conductors are embedded in radial plates
force on isolation is only from one conductor and not from winding pack
second insulation around radial plates – double pancake
radial plates are embedded in a strong casing which provides the backbone of the machine
Radial plate mock-up at CNIM
(Forged segments jointed by EB welding)

## Slide 37
TF Coils Design (2)
~ 900 mm

## Slide 38: ITER Toroidal Field Magnets Manufacturing

## Slide 39: TF Coils Progress – JADA
Pictures courtesy JAEA & Contractor Toshiba
Completed one third scale 3-turn winding trials at Toshiba
Winding & Bending Rollers
Winding Support Jig
Notes: 39

## Slide 40: TF Coil Structures Progress – JADA
Pictures courtesy JAEA & Contractors Toshiba & KHI
A1 Segment
B3 Segment
Manufacturability study of large TF coil components by Toshiba and its sub-contractor KHI
Inter-coil Structure - Forging
Pre-compression Ring Flange
Notes: 40

## Slide 41
TF Coils Progress (KHI-JA)
TF Coil Case Straight Leg
~ 900 mm
Welding Trials for attachment of Pre-compression Ring Flange to TF Coil Case

## Slide 42
ITER Central Solenoid
Single CS module
CS Conductor
Peak Field 12.5 T

## Slide 43
Terminals
Support clamps
He inlets
Poloidal Field Coils
Conductor
Winding
Facts
• So big (23 m) must be manufactured on site!
• Building is 250 m long x 45 m wide and will be the first on site!

## Slide 44
CS Coil
ITER Magnets Feeders

## Slide 45
Vacuum Vessel & In Vessel Components

## Slide 46
Design inputs for VV and PFCs
Electromagnetic loads. During a plasma instabilities eddy currents are induced in the PFCs. These currents interact with the toroidal magnetic field thus resulting in extremely high forces applied to the PFCs. These forces (several MN) can generate mechanical stresses up to a few hundreds of MPa with a consequent strong impact in the design of the supporting structures.
Toroidal field
Plasma current
Eddy currents
In PFCs
Poloidal field

## Slide 47
Plasma current in MA
Plasma radial position in m
Plasma vertical
position in m
Vertical Displacement Events (VDE)
can cause large currents to flow through the blanket, divertor and VV
cause large vertical forces on the BL, Div, VV >150 MN

## Slide 48
VV Status
ELM & VS Coils
(VV interfaces implemented)
Status
• VV sector and port PA’s signed (EU, KO, IN, & RF)
• KO - VV & port contract awarded to Hyundai Heavy Industries
• EU - VV contract awarded
• Manufacturing schedule is on critical path!!!
Technical Challenges
• Large Size
• Tight tolerances
• High quality components
• Part of safety boundary
Facts
- First safety barrier for ITER
- SS 316 LN-IG
- ~5300 tons (VV, ports, shielding only)
- 19.4 m (63 ft) torus outer diameter
- 11.3 m (37 ft) torus height

## Slide 49
Full Size Prototype of the ITER Vacuum Vessel (2001) (JA Domestic Agency)
Vacuum Vessel Prototypes
VV Mock-up of Electron Beam welding on the inner shell (EU Domestic Agency)
Mock-up of E-beam Welding for Key and
Blanket Manifold Support
(KO Domestic Agency & HHI)
Notes: 49

## Slide 50: VV Assembly Scheme, In Wall Shielding, VV-Support
Triplet #2
Triplet #1
Reference
Triplet
- The space between the double walls of the VV is filled with in-wall shielding (IWS), which is mainly made of an austenitic stainless steel containing 1-2% weight boron to improve the neutron shielding efficiency.
VV-Support

## Slide 51
Principal in-vessel components
First wall/blanket  heat exhaust, impurity management, nuclear shielding
Divertor  particle and heat exhaust
Be
Carbon fibre composite (CFC) and W

## Slide 52
In Vessel System Integration

## Slide 53
Integrate ELM/VS Coils and Blanket Manifolds
Electrical Straps
Flexible attachments
In Vessel System Integration

## Slide 54
Start-up: q|| ~ 25 MWm-2, lq|| ~ 5.0 cm Several seconds Confinement transients q|| ~ 250 MWm-2, ~2-3 secs
Start-up and rampdown: q|| ~ 40 MWm-2, lq|| > 1.2 cm Several seconds
VDE (up): q|| ~ 70-270 MJm-2, lq|| > 3.0 cm t = 1.5-3.0 ms
VDE (down): q|| ~ 90-300 MJm-2, lq|| > 3.0 cm
Steady state: q|| ~ 8 MWm-2, lq|| > 4.0 cm q|| ~ 24 MWm-2, lq|| > 2.5 cm (ELMs) Disruptions q|| ~ 45-120 MJm-2, lq|| > 20 cm t = 3.0-6.0 ms
Radiation: SS: 0.5 MWm-2 (photon+CX)
Disruptions
TQ: ~0.5 MJm-2 t ~ 1 ms (mitigated)
CQ: ~0.9 MJm-2 t ~ 10 ms
ITER Thermal Load Specifications: resumé

## Slide 55
A generic shaping solution
Top
Outboard
BM #1-6 Central column HFS start-up Toroidal & poloidal shaping
BM #7-10 Secondary divertor region Toroidal & poloidal shaping
BM #11-18 Outboard LFS start-up/ramp-down Toroidal shaping
Inboard

## Slide 56
First wall: blanket modules (BM)
Two main components
Plasma-facing surfaces: separable shaped First Wall (FW) Panel
Armoured with Be tiles
Neutron shielding: Semi-permanent massive Shield Block (SB): ~3.50.5 tonnes
Total number of BMs: 440 Total mass: ~1800 tonnes All water cooled
1.4 m
1.0 m
0.5 m

## Slide 57: The first ITER divertor – now in procurement phase
54 divertor assemblies (~8.7 tonnes each)
4320 water cooled heat flux elements
Bakeable to 350C
Cost > €100 million
Must sustain steady heat fluxes of ~10 MWm2 Guarantee sufficient He exhaust and retention of impurities

## Slide 58
Vertical target monoblocks
59184 CFC monoblocks 193,428 W monoblocks
No front surface shaping on first divertor.
Toroidal gaps: CFC: 1.0 mm (max) W: 1.3 mm (max)
Poloidal gaps: CFC: 0.7 mm (max) W: 1.0 mm (max)
Inner target
W
CFC
28-30 mm
27-32 mm
15
8
20 mm
12 mm

## Slide 59
Divertor Qualification Prototypes
All the 3 Domestic Agencies have qualified
CFC Armoured Areas
  1000 cycles at 10 MW/m2
  1000 cycles at 20 MW/m2
W Armoured Areas
  1000 cycles at 3 MW/m2
  1000 cycles at 5 MW/m2

## Slide 60: Plasma transients – biggest threat to ITER
Disruptions & VDEs
ELMs
“Natural” ELMs expected to expel ~6% of Wplasma at 1-2 Hz  peak energy densities on ITER divertor of 2-10 MJm-2 on timescales of 250-500 ms
Worst case full energy disruptions  peak energy densities on the divertor of 5.0-20 MJm-2 on timescales of 1.5-3 ms (thermal quench)
Current quench: runaway electron currents up to 12 MA with 10-20 MeV in localised areas on timescales of a few 10’s of ms
No material can tolerate these energy densities  reliable ELM and disruption avoidance and mitigation mandatory

## Slide 61
Divertor Target Behaviour under ELM Loads
Thermal exposure at QSPA facility (RF)
Pre-heating of samples at 500 °C
60 degree inclination
Plasma pulse duration: 500 μs
Peak absorbed energy density: from 0.5 to 1.5 MJ/m2
Total number of simulated ELMs: 100 cycles
CFC erosion starts at > 0.6 MJ/m2 (~1µm/pulse at 1 MJ/m2)
Tungsten cracking occurs at > 0.2 MJ/m2; melting of tile edges at > 0.4 MJ/m2

## Slide 62
Remote Maintenance & Hot Cell, Assembly

## Slide 63
Tokamak
building
Hot Cell
building
ITER Remote Handling / Hot Cell
PBS 23-3
Transfer cask
PBS 23-6
Hot Cell RH
PBS 23-5
NB RH

## Slide 64: Cask & Plug Handling System – Cask transfer

## Slide 65
Module / Tool transporter
Tractor
Cable Handling Equipment
Transfer frame for Cable Handling Equipment
Rail Support Equipment
Rail
Vehicle Manipulator
Blanket RH System Rail Support Equipment and Module Transporter
Payload: 7ton - (max. 10 ton at limited location)
Reach: 1.3 – 3.8m from the rail center - Rail location: R6.2m from machine center

## Slide 66: Blanket Handling – Transfer Casks
Vehicle manipulator
Intermediate Cask
Rail positioning arm
Vehicle fixing arm
Tractor
Sliding beam
Rail storage table
Cask base Plate
Rail connecting
equipment
Rail
BM transport
IVT deployment
IVT Cask

## Slide 67
Full scale 180° rail deployment test (1998)
In-port rail connection
2008-2009
2 decades of development to provide demonstration of feasibility and reliability
RH system for blanket has shown its ability to perform the job
Some issues remain

## Slide 68: Divertor Handling – Divertor RH System
Toroidal Subsystem
Radial Subsystem

## Slide 69
The import / export facility,
The docking station of transfer casks to the red zone,
The reception/cleaning workstations,
The refurbishment workstations (port plugs, TBM, other vacuum vessel components),
The testing workstations (port plugs, TBM, other vacuum vessel components),
The buffer storage for port plugs,
The HCF remote handling preparation, decontamination and repair area;
Link to Neutral Beam cell.
Hot Cell Facility layout level L1

## Slide 70: Hot Cell RH System – Building Overview – B2/B1
Rad waste RH
Equipment
Hot Remote Handling Test Facility
Cask park
(partial)
Cask maintenance
IVT TESTING
Scope of Hot Cell RH System
Procurement Package

## Slide 71: Machine Assembly
TF Coil / Sector Assembly
~1400 ton
Tokamak and Assembly Building
Status
• Detailed assemble plans developed
• Assembly tool PA signed with Korea

## Slide 72: Summary of Lecture 3 (14th April 2011)
ITER is a political as well as a high tech Project
  Makes the execution more difficult and more expensive
A Tokamak Reactor is a highly integrated machine
  Everything is linked – Physics and Technology
  Difficult to separate into different systems
  Even more difficult to procure systems in different countries
ITERs technology has been developed during last 2 decades
  Every part is underpinned by R&D and qualification prototypes
Manufacturing has started for Major Tokamak Systems
In Lecture 4 peripheral Systems and DEMO Technology will be presented