## Slide 1
Mar CAPEANS
“CERN Year of Environmental Awareness: outcome and future perspectives”
15 September 2022

## Slide 2
IMPLEMENTATION AXIS IN SCE
GHG Emissions
Reduction by 28%
Energy Consumption
Limit raise by 5%
Water Consumption
Limit raise by 5%
Noise
Restrict
Biodiversity
Protect
Commuting
Constant
Waste
Increase recycling rate
3
Sustainability integrated into operations
Projects of large impact
Pilots of scalable projects

## Slide 3
Sustainability integrated into operations
GHG Emissions
Reduction by 28%
Energy Consumption
Limit raise by 5%
Target: 5% reduction of electricity & gas consumption on campus operations
Actions: optimization of district heating, reduced public lighting, accelerated replacement to LED lighting, sleep-mode for unoccupied infrastructures…
Energy saving on Campus
40% invested into environmental actions:
Global renovation of 2 buildings/y with energy efficiency improvement >60%
Building envelope actions: roofs, windows, facades
Change of indoor and public lighting, HVAC systems, automation, monitoring
Site Consolidation programme
The mission is to plan capital investments and carry out, in a rolling time window of 10 years, the pre-emptive repairs and improvement of infrastructures assets that are essential for CERN’s scientific programme

## Slide 4
Sustainability integrated into operations
Biodiversity
Protect
Ozone water treatment
The cleaning process begins with the creation of ozone in a generator which is then injected into water, and immediately starts oxidizing and eliminating contaminants, such as bacteria and rust.
Piloted in Prévessin, moving to Meyrin at the end of 2022
Chemical-free cleaning
Analysis of impact on Biodiversity for all construction projects
Green compensation fund
Biodiversity conservation included into every new project

## Slide 5
Projects of large impact
GHG Emissions
Reduction by 28%
Energy Consumption
Limit raise by 5%
Net-zero/passive buildings as compared to conventional buildings:
5% more expensive at construction
25-35% less energy consumption
15% lower maintenance costs
20-85% less GHG emissions
Sustainable buildings
Prévessin: up to 4 MW recovered from the new PCC (~100% reduction of CO2 emissions at full capacity)
Meyrin: up to 10 MW recovered from LHC cooling towers at Point 1 (~80% reduction of CO2 emissions at full capacity)
Sustainable heating plants from 2026/27
Average figures in the field

## Slide 6
Pilots of scalable projects
GHG Emissions
Reduction by 28%
Reduce, Reuse, recycle
Central collectors of office waste (8 buildings)
Laboratory waste pilot (2 buildings)
Biowaste pilot (R3 and 2 office buildings)
Coffee capsules
Measure
Waste: global and local actions
2022
3 kyburz e-Trolley for mail delivery
2 e-transit vans for internal transport
1-2 shuttles for people transport
1 truck for waste collection
5 to 8 e-cars for the sharing scheme
Gradual replacement of thermal cars by e-cars
80 shared e-bikes
Car Fleet reduction (25% target) in 2024
-15.4 tCO2e
- 500 tCO2e/y

## Slide 7
SCE AMBITIONS
2021
2022
2023
2024
2027
2025
2026
25% Reduction of car fleet
-500 tCO2e/y
Sustainable heating plants
(heat recovery)
Prévessin -1’900 tCO2e/y
Meyrin ~6’000tCO2e/y
Control water effluents Retention basins FR & CH
100% Inventory of CERN areas of biological interests
40’000 m2 Green buildings
40’000 m2 Renovated buildings
5% Energy reduction for Campus activities